## Slide 1
High efficiency and high power klystron development in EDR(P-band and C-band)
Zusheng Zhou
On behalf of CEPC high efficiency klystron team
2024 European Edition of the International Workshop on the Circular Electron-Positron Collider (CEPC)

## Slide 2: Content
R&D status
  P band high efficiency klystron
  Multi-beam klystron
  C band klystron
EDR task
  P band klystron and test stand for superconducting cavity horizontal test
  C band klystron and test stand for accelerator structure conditioning
Future plan

## Slide 3: R&D status

## Slide 4: Total power and cost consumption
Cost consumption
Chart: 
| 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 576 | 460.8 | 384 | 329.1429 | 288 | 256 | 230.4
CEPC at 800 RMB/MWh and 6000 hours/year
Excessive electricity bill, M RMB
1 year
Efficiency, %
70 M RMB
84M RMB
CEPC synchrotron radiation power is 60MW of 2 beams.
Efficiency impact on operation cost is very serious.(Only considering operation efficiency of klystrons).
PAST
1st tube
62%
NOW
2nd tube
77%
FUTURE
3rd tube
80%
Save Money

## Slide 5: Design consideration for Collider RF sources
Considering klystron lifetime, power redundancy and cost, the 2 cavities will be powered with one CW klystron capable to deliver more than 800 kW.

## Slide 6: Requirement list
System components requirement list:
Klystron | 96 | 650MHz/700kW | Higher efficiency
PSM Power Supply | 96 | 130kV/16A | Mature product
Circulator | 96 | 650MHz/700kW | Mature product
Load | 96 | 650MHz/700kW | Mature product
Phase shift | 96 | 650MHz/700kW | Mature product
Waveguide | 96 | Power divider/directional coupler | Mature product
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1% | Mature product
Pre-amplifier | 96 | 650MHz/200W | Mature product

## Slide 7: Requirement list
System components requirement list:
Klystron | 96 | 650MHz/700kW | Higher efficiency
PSM Power Supply | 96 | 130kV/16A | Mature product
Circulator | 96 | 650MHz/700kW | Mature product
Load | 96 | 650MHz/700kW | Mature product
Phase shift | 96 | 650MHz/700kW | Mature product
Waveguide | 96 | Power divider/directional coupler | Mature product
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1% | Mature product
Pre-amplifier | 96 | 650MHz/200W | Mature product

## Slide 8: Design consideration for Linac RF sources
The main high power RF sources components are 33 units of 80MW S-band klystron, 236 units of 50MW C-band klystron and related modulators.
Type | QTY | Freq.(MHz) | Structure type
S-band klystron | 33 | 2860 | 1 1-to-1，standard-bunch 3 1-to-2，standard acc. structure. 8 1-to-2，large aperture acc. structure 21 1-to-4, standard acc. structure.
C-band klystron | 236 | 5720 | 1-to-2，standard acc. structure.

## Slide 9: System components list
Requirement list of baseline:
S band klystron | 33 | 2860MHz/80MW
Modulator of S band klystron | 33 | 400kV/500A
C band klystron | 236 | 5720MHz/50MW
Modulator of C band klystron | 236 | 350kV/400A

## Slide 10: System components list
Requirement list of baseline:
S band klystron | 33 | 2860MHz/80MW | Mature product
Modulator of S band klystron | 33 | 400kV/500A | Mature product
C band klystron | 236 | 5720MHz/50MW | Mature product
Modulator of C band klystron | 236 | 350kV/400A | Mature product

## Slide 11: C band 80MW klystron
Why we need do R&D of C band 80MW klystron?
  Only C band of 50MW klystron is mature product in the world.
  So, 1 klystron only power to 2 accelerator structures (CEPC Linac baseline).
  QTY of C band klystron is very large (236 set).
IF output power of C band klystron is up to 80MW, the number of klystron will be reduced by half. (1 klystron power to 4 accelerator structures)
System cost will be decreased more than 40%.

## Slide 12: R&D Strategies
650MHz/800kW klystron with higher efficiency design for CEPC Collider.
5720MHz/80MW klystron for CEPC Linac cost reduction.

## Slide 13: 650MHz/800kW-1st klystron prototype
Oct. 2017 Design report
Mar. 2020 High power test at IHEP
Parameters | Design | Test
Operating frequency (MHz) | 650 | 650
Beam Voltage (kV) | 81.5 | 80
Beam Perveance (μA/V3/2) | 0.65 | 0.7
Efficiency(%) | 65 | 62
Saturation Gain(dB) | ≥45 | 47
Output power(kW) | 800 | 800
1 dB Bandwidth(MHz) | ≥1 | 1.8

## Slide 14: 650MHz/800kW-2nd klystron prototype
Jan., 2021: Klystron manufacture started
Feb., 2024: 800kW(Pulsed), 77.2% efficiency

## Slide 15: 650MHz/800kW-3rd prototype (MBK)
Dec., 2021: Klystron beam tester manufacture started
Oct., 2023: Accomplishment of klystron beam tester high voltage conditioning and beam emission.
Jan. 2024: Klystron manufacture is in progress.

## Slide 16: 5720MHz/80MW-Design progress
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Pulsed width | 3us
Repetition rate | 100Hz
Gain | 54 dB
Efficiency | 47%
bandwith | ±5MHz
Beam voltage | 420 kV
Beam current | 403 A
Focusing field | 0.27 T
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Pulsed width | 3us
Repetition rate | 100Hz
Gain | 54 dB
Efficiency | 47%
 | ±5MHz
Beam voltage | 420 kV
Beam current | 403 A
Focusing field | 0.27 T
Main parameters
Beam dynamics

## Slide 17: Design progress
RF Power Combiner & Collector Connected with
80 MW C-band Klystron
RF Power combiner

## Slide 18: EDR task

## Slide 19: P band klystron and it’s platform
P band klystron
  800kW CW operation
  >80% efficiency
  Klystron prototype become klystron product (optimization……)

## Slide 20: P band & C band LLRF
P band LLRF for SC cavity horizontal test
Schematic drawing of P band LLRF
PAPS P band LLRF

## Slide 21: P band & C band LLRF
C band LLRF for NC accelerator structure and C3 structure
Schematic drawing of C band LLRF
HEPS S band LLRF

## Slide 22: P band platform
Based on PAPS 2A hall, to design power distribution and transmission system

## Slide 23: C band klystron and it’s platform
C band klystron
  80MW pulsed power with 100Hz operation
  With NC accelerator structure and C3 structure conditioning
  Another choice of CEPC Linac baseline

## Slide 24: C Band platform
Based on BEPCII high power test stand

## Slide 25: Future plan

## Slide 26: Energy recovery klystron
If 60MW SR power (e+&e-) of CEPC, RF power demands 109.5MW, waster power is still about 49.5MW. (Klystron efficiency~70% @linear region and ~80%@saturate region).
The energy recovery klystron recovers energy from the spent electron beam by multi-depressed collector, thereby reducing the power demand from the grid and significantly lowering operation.
Typical klystron
Energy recovery klystron
RF OUT

## Slide 27: PPM klystron
Small volume, light weight, and does not require water cooling and power supply.
It saves the power consumption and cost of power supply, and on the other hand, it avoids the risk of power supply failure and water leakage.
 | E37212 | E37302A
Frequency(MHz) | 5712 | 2998
Output Power (MW) | 51 | 47
Beam Power (MW) | 118.3 | 123.5
Average Power (kW) | 35.5 | 24.7
Solenoid Power (kW) | 8.4 | 3.4
RF efficiency (%) | 43.1 | 38
Overall efficiency(%) | 34.9 | 33.5

## Slide 28: Klystron protection with long cable operation
Design parameters：
  Protection time: <10μs；
  Energy limitation: <20J；
  Crowbar /solid state device

## Slide 29: P band & C band resonant ring
High power conditioning for klystron window
High power conditioning for SC cavity coupler

## Slide 30: Summary
Much higher efficiency and much less power consumption and system cost.
The high power test of 650MHz high efficiency klystron is being done at IHEP PAPS test stand.
Design of C band 80MW klystron is almost accomplished design and will be manufactured in the near future.
Energy recovery klystron and PPM klystron are also being developed at IHEP.

## Slide 31
Thanks for your attention