## Slide 1
IHEP Beam driven plasma accelerator
and efficiency study
07-11 April 2024, Marseille, International workshop on CEPC (EU Edition)
Prof. Wei Lu, Dr. Dazhang Li, et al. On behalf of the IHEP-THU-BNU AARG team

## Slide 2: Content
Plasma-based Linear Collider
CPI studies during TDR
IHEP PBA TF proposals and current status
Summaries and prospects

## Slide 3
Plasma-based Accelerator
RF Cavity：< 100MeV/m
Driver:
High power laser  LWFA
High energy e-  PWFA
…………
PBA：1-100 GeV/m

## Slide 4
Conceptual design of LWFA/PWFA collider
LWFA collider conceptual design
PWFA collider conceptual design
Ultimate goal for PBA: to build a much cheaper, more compact and green collider
These two conceptual designs were presented ~ 2010, not updated for 15 years
Significant progress has been achieved, while some key issues still need be addressed
Parameters upgrade  Stability improve  application attempts  cost & power optimization

## Slide 5
Conceptual design of LWFA/PWFA collider
Size:
  LWFA LC << PWFA LC << LC
  But NOT 1000 times smaller
Power consumption
  In principle, PBA LC < LC, smaller size means smaller vacuum, magnet, SC ……
  PWFA LC < LWFA LC, due to higher ηwall plugdriver and ηdrivertrailer efficiency
  PBA’s estimation is not accurate compared with conventional LC. How to estimate?
Construction
  PBA’s cost is in a big range due to technique uncertainty
  May not be ready for colliders in next 20 yrs
A 5~10 year mid-step: an injector for a real machine Vs. a 5-10-100 GeV PBA module

## Slide 6: Content
Plasma-based Linear Collider
CPI studies during TDR
IHEP PBA TF proposals and current status
Summaries and prospects

## Slide 7
CEPC Plasma Injector (CPI)
Plasma Injector
10 GeV
Linac
100 km
Booster
10 GeV e-/e+ beam in a 100 km ring
Minimum magnetic field = 28 Gs
Field error < 28 Gs*0.1% = 0.028 Gs
Field reproducibility < 29 Gs*0.05% = 0.014 Gs
The Earth field ~ 0.2-0.5 Gs, the remnant field of silicon steel lamination ~ 4-6 Gs.
10 GeV linac + CT coil magnet, or 30 GeV linac + iron-core magnet ? Both lead to significant cost rise ~ 1 B RMB
Collider
Rings

## Slide 8
Collaborated team on CPI since 2017
Proposed by Prof. Gao and Prof. Lu on 2017.01
First collaborated group meeting on 2017. 03
Till now, IHEP+THU+BNU, 15+ staffs and 20+ PhDs

## Slide 9
Electron PWFA for TR ≥ 3.5
beam | Driver | Trailer
Driver energy () | 10 | 10
Normalized emittance | 20 | 100
Length (u) | 600 | 77
(matched) Spot size(u) | 3.89 | 8.65
Charge (nC) | 5.8 | 0.84
Beam distance (u) | 149 | 
beam | Driver | Trailer
 | 10 | 10
 | 20 | 100
 | 600 | 77
 | 3.89 | 8.65
Charge (nC) | 5.8 | 0.84
 | 149 | 
Accelerating distance (m) | 10.65
Trailer energy () | 45.5
Normalized emittance | 98.44
Charge(nC) | 0.84
Energy spread | 0.56
Efficiency (%) (driver  trailer) | 59.1
Accelerating distance (m) | 10.65
 | 45.5
 | 98.44
Charge(nC) | 0.84
 | 0.56
Efficiency (%) (driver  trailer) | 59.1
V2.0 TR≥3.5
For CPI V1.0 and V2.0
TR ≥ (45.5-10)/10=3.55
ideal case
non-ideal case
The noise is over estimated because the simulation particle number is much smaller than real particle number

## Slide 10
Electron PWFA for TR ~ 2
TR ≤ 1.8 seems acceptable () if no extra damping mechanism is adopted.
CEPC injector’s baseline was changed: 10 GeV  30 GeV  TR ≥ 2
Ion motion can significantly decrease the hosing instability

## Slide 11
Tilt angle | 10 μrad | 100 μrad | 1 mrad
Bunch charge [nC] | 1.197 | 1.197 | 0.903
Energy [GeV] | 30.01 | 30.01 | 30.24
RMS energy spread | 0.41 | 0.41 | 0.65
Offset (x direction) | 4 μm | 12 μm | 20 μm | 30 μm
Bunch charge [nC] | 1.197 | 1.197 | 1.174 | 1.079
Energy [GeV] | 30.01 | 30.04 | 30.16 | 30.37
RMS energy spread | 0.43 | 0.41 | 0.22 | 0.72
θ
driver
trailer
driver
trailer
offset_x
tilt angle =1 mrad
offset_x =20μm
Preliminary error tolerance analysis

## Slide 12
e+ PWFA in TDR: asymmetric electron driver

## Slide 13
e+ PWFA in TDR: high quality
Plasma parameters |  | 
Density (cm-3) | 1.133e15 | 
Inner radius () | 158 | 
Outer radius () | 711 | 
Beam parameters | Driver | Trailer
Charge () | 6.45 | 1.1
Energy (GeV) | 30 | 3
Transverse size (μm) | 32 | 6
Normalized emittance (mm⋅mrad) | 32 | 16
Length (μm) | 237 | 153
Energy spread (%) | 0 | 0
Beam longitudinal distance (μm) | 885 | 
Plasma parameters |  | 
Density (cm-3) | 1.133e15 | 
 | 158 | 
 | 711 | 
Beam parameters | Driver | Trailer
 | 6.45 | 1.1
Energy (GeV) | 30 | 3
Transverse size (μm) | 32 | 6
 | 32 | 16
Length (μm) | 237 | 153
 | 0 | 0
Beam longitudinal distance (μm) | 885 | 
Positron beam parameters | 
Charge (nC) | 1.1
Energy (GeV) | 30.1
Normalized emittance (mm⋅mrad) | 41.6 (x)
 | 18.7 (y)
Energy spread (%) | 0.68
Acceleration properties | 
Acceleration length (m) | 20.8
Acceleration gradient (GV/m) | 1.3
Beam loading efficiency (%) | 22.6
Positron beam parameters | 
Charge (nC) | 1.1
Energy (GeV) | 30.1
 | 41.6 (x)
 | 18.7 (y)
 | 0.68
Acceleration properties | 
Acceleration length (m) | 20.8
Acceleration gradient (GV/m) | 1.3
Beam loading efficiency (%) | 22.6

## Slide 14
e+ PWFA in TDR: Energy compression
Parameter | Symbol | Unit | Value
Beam charge | Qe+ | nC | 1.1
Beam energy | Ee+ | GeV | 30.1
Energy spread | σe | % | 0.68
Emittance | εn | mm·mrad | 151(x) / 35.1(y)
Bunch length | σl | mm | 0.322(rms)
Peak Current | I | kA | 0.647
Parameter | Symbol | Unit | Value
Beam Charge | Qe+ | nC | 1.05
Beam energy | Ee+ | GeV | 30.0
Energy spread | σe | % | 0.156
Emittance | εn | mm·mrad | 131 (x) 76.2 (y)

## Slide 15
Parameter | Driver | Trailer | Total
Energy E (GeV) | 11.23 | 10.94 | 11.16
Normalized emittance (mm-mrad) (H/V) | 20.6/20.2 | 10.6/10.2 | 18.8/18.0
Bunch length (μm) | 339.9 | 88.9 | 599.2
Beam size (μm) (H/V) | 192/132 | 178/97 | 189/124
Charge (nC) | 3.87 | 1.19 | 5.06
Energy spread | 1.14% | 0.34% | 1.5%
Beam distance (μm) | 170.4 |  | /
Parameter | Driver | Trailer | Total
Energy E (GeV) | 11.23 | 10.94 | 11.16
 | 20.6/20.2 | 10.6/10.2 | 18.8/18.0
Bunch length (μm) | 339.9 | 88.9 | 599.2
Beam size (μm) (H/V) | 192/132 | 178/97 | 189/124
Charge (nC) | 3.87 | 1.19 | 5.06
Energy spread | 1.14% | 0.34% | 1.5%
Beam distance (μm) | 170.4 |  | /
Linac (e- driver) design & optimization for CPI

## Slide 16
Final Focus design & optimization for CPI
Driver’s transverse emittance need further optimization. Plasma matching section as in e+ PWFA can be helpful

## Slide 17
Energy compression with plasma dechirper
Interaction
chamber
Compressor
Chicane
Deflecting
cavity
Dipole
S-band
linac
RF gun
beam
Yipeng, Wu et al., PRL 122 204804 (2019); Dr. Shuang Liu’s PhD Thesis (2020)

## Slide 18
e+ beamline design & optimization for CPI
 | BCI | BCII | BCIII
Initial energy (MeV) | 400 | 400.1 | 405
inj (%) | 0.054 | 0.367 | 2.17
Initial z (mm) | 4.4 | 600 | 100
fRF (GHz) | 2.860 | 5.712 | 5.712
Voltage(GV) | 0.0056 | 0.12 | 4.18
Gradient (MV/m) | 20 | 40 | 40
L (m) | 0.28 | 3 | 104
RF (degree) | 89 | 88 | 61.5
R56 (mm) | 1200 | 27.6 | 5.5
Final energy(MeV) | 400.1 | 405 | 2400
ext (%) | 0.367 | 2.17 | 1.83
final z (μm) | 600 | 100 | 20
Beam distribution @ FF (~20μm）

## Slide 19
Key issues need to be addressed

## Slide 20: Content
Plasma-based Linear Collider
CPI studies during TDR
IHEP PBA TF proposals and current status
Summaries and prospects

## Slide 21
Hall 10 @ IHEP used for detector calibration
2023.12.03

## Slide 22
束流中心
2.5 GeV e-/e+ beamline + PW-level high performance laser system
~ 661 MeV
e- gun
e+ target, ~240 MeV
PWFA lab
Diagnostics
BEPCII-based PWFA TF design V1.0

## Slide 23
BEPCII-based PWFA TF design V2.0

## Slide 24
BEPCII-based PWFA TF design V2.0
2024.03.24

## Slide 25
BEPCII-based PWFA TF design V2.0
L-band e- Gun (> 5 nC): ~ CPI requirement
Beams combination: similar to CPI
High quality e+ beam: NO
Final Focus: even harder than CPI
HTR e- acc.: easier than CPI (~CPI @ SXFEL)
High rep. rate plasma source: > CPI
e+ PWFA acc.: 1st exp. result, < CPI
Cascaded/staging: 1st exp. result, < CPI

## Slide 26
Budget & timetable of BEPCII-based PWFA TF
2023.10-2024.03: Clear Hall 10
2024.05-2024.10: Construction and re-decoration
2024.07-2024.10: Install BL-I (outside hall 10)
2024.11-2025.06: Install BL-I (inside hall 10)
2025.02-2025.08: Install PW Laser system
2025.07-2025.12: Install BL-II
2026.01-2026.06: Beam and laser commissioning
Since 2026.06: PBA experiments
~ 10 million €

## Slide 27
PBA TF based on LPA + Storage Ring @ HN
L-band e- Gun (> 5 nC): NO
Beams combination:  beam manipulation
High quality e+ beam: similar to CPI
Final Focus: NO
HTR e- acc.: NO
Plasma source: ~ CPI
e+ PWFA acc.: ~ CPI
Cascaded/staging: NO

## Slide 28
Budget & timetable of PBA TF @ HN
The total budget is 10-15 million € from Henan Province
2024.01-2024.12: Lab construction (2024.4.24, opening ceremony)
2024.01-2024.06: Overall design for both LPA, transport line and SR
2025.01-2025.06: Laser system installation and LPA experiments
2025.07-2025.12: Accelerator installation
2026.01-2026.06: Laser and beam commissioning
2026.07-2027.06: LPA injector experiments and SR light source optimization
2027.07- : Polarization and other novel accelerator physics / techniques studies

## Slide 29: Content
Plasma-based Linear Collider
CPI studies during TDR
IHEP PBA TF proposals and current status
Summaries and prospects

## Slide 30
Summary and prospect
Thank you!
Conceptual design of CPI has been carried out since 2017
A series of simulation progress has been made during the last 5-6 years
We’ll focus on the TF construction in the next 2-3 years
Linac + PWFA (Beijing) and LPA + Ring (Henan), totally complementary
Not only PBA TF, but also accelerator physics / technique
Test the CPI feasibility on these 2 TFs and push PBA to a real machine

## Slide 31
Conceptual design for a dedicated PWFA TF
high charge, longitudinal shaped
Lower energy for lower cost
accumulate, compress and damping e+
High resolution beam/field diagnostics
PWFA-based FEL
Total Budget: ≥ 300,000,000 RMB