## Slide 1: GATE activities Medical University of Vienna
Hermann Fuchs
Department of Radiation Oncology

## Slide 2: What you see is what you treat
Making MR guided particle therapy a reality

## Slide 3: Motivation and Vision
At the treatment table only X-Ray/CBCT available
  On line MR images
  Advance adaptive treatment strategies

## Slide 4: Motivation and Vision
Integrated systems for photon-MR clinically available
For particles much research still to be done
Making on-line MR-guidance for particle therapy a reality

## Slide 5: Dosimetry
Measurements with dosimetry detectors in magnetic fields (0 - 1 T)
Characterization of detector response
MC modelling of an ionization detector

## Slide 6: Proton beams in magnetic fields
MC beam model
  Clinical beamline IR1@MedAustron
Custom magnetic field maps
  From G4 Purging Magnet
  Steppers and chord reconstruction
  parameters from Geant4 available in GATE
  Experimental benchmarking
Nozzle
Magnet

## Slide 7: Beam model validation
In-depth & lateral dose profiles
  EBT3 Films:
    Averaged dose LET correction
  Single energy fields and SOBP
  B fields 0 and 1T
Padilla-Cabal et al., Med. Phys. 2019.

## Slide 8: Future steps
Extend to custom electric + magnetic field implementation.
  Homogeneous
  3D maps
Submit to GitHub
Modelling dosimetric detectors - response function

## Slide 9: Film corrections
EBT3 films
  Multiple positions in SOBP
  No magnetic field effects detected
Correction on film quenching using GATE actor
Padilla-Cabal et al., Med. Phys 46, 2019
Resch et al., submitted to Med. Phys
corrected
original

## Slide 10: Beam modelling
Fast generation of beam models

## Slide 11: Beam modelling - Status
Publication in preparation
Beam modelling scripts working well
  Proton and carbon ions
  >10 Beam modells created
Will become part of GATE tools

## Slide 12: Expanding capabilities
Non-dedicated eyline at MedAustron

## Slide 13: Feasibility study of uveal melanoma treatment Non-dedicated eye beamline at MedAustron
Collimator
  Material
  Geometry
  Particles
    Proton & 12C
    Range in water: 3 cm
Arrangement of passive elements
 Simulation study using GATE
Hao Chen et al 2014 Phys. Med. Biol. 59 5043

## Slide 14: Lateral dose profile before and after collimator in air

## Slide 15: Preliminary results: Lateral dose profile in water
Dose fall off sharper for 12C
Parameter to quantify: p8020
- Distance from 80% to 20% dose

## Slide 16: Penumbra 80-20% over depth in water
Protons
  Lateral dose characteristics similar to other proton eye beam lines
  Further optimization
Carbon ions
  Considerably sharper
  Relative biological effectiveness ?

## Slide 17: Summary
GATE extended to magnetic and electric field maps
  Validated
  Pull request on-going
Tool set for fast beam model generation
  Publication in preparation
  Will become part of GATE tools
Use of GATE for design process of eye-line at MedAustron