## Slide 1
Challenges and issues about nuclear data for fuel cycle applications
28/06/2022
V. Vallet, D. Bernard, A. Chebboubi, G. Noguère, O. Serot, G. Kessedjian, O. Bouland, et tous les autres…

## Slide 2: Illustrated examples of ND needs and impacts on fuel cycle applications
Decay Heat:
  TAGS experiments
  Correlations in Fission Yields and Decay Data
  Np239 decay data: need for a re-evaluation?
Dose rate:
  Example of 136Cs
Outline

## Slide 3: TAGS data for Decay Heat
Test on Fission Burst Experiments
JEFF-3.1.1 versus JEFF-3.1.1 + 9 TAGS: better agreement with exp. data
New TAGS data on mean β/γ decay E are included in JEFF-3.3
Phys. Review Letters, 105 (202501), 2010
Phys. Review C, 95 (024320), 2017
Phys. Review Letters, 115 (102503), 2015

## Slide 4: TAGS data for Decay Heat
Impact of new <E>gamma TAGS on the gamma contribution compared to Jurney’s exp. data
Impact of new JEFF-3.3 TAGS data on 239Pu thermal Fission Burst with long irradiation
Jurney: irradiation time of 2e4 sec (~5.6 h)
Chart: s
| 29 | 128 | 284 | 538 | 1218 | 2530 | 3930 | 5010 | 23760 | 59320 | 96840 | 146500
JEFF311 | -14.2355 | -9.4522 | -8.4373 | -9.6205 | -7.1377 | -2.3724 | -0.76923 | -0.83333 | 5.1515 | 6.8293 | 6.25 | 4
JEFF311 + 9 TAGS | -6.7839 | -2.589 | -1.723 | -3.5153 | -2.5543 | 0.22069 | 0.60038 | -0.022523 | 5.1515 | 6.8293 | 6.25 | 4
exp. Unc. (1 std) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lower C/E discrepancies for time < 1e4 s
E. T. Jurney, LA-7620-MS, 1979

## Slide 5: TAGS data for Decay Heat
Impact of new <E>gamma TAGS on the gamma contribution compared to Friesenham’s exp. data
Impact of new JEFF-3.3 TAGS data on 239Pu thermal Fission Burst with long irradiation
Friesenham : irradiation time of 8.64e4 sec (1 day)
Lower C/E discrepancies for time < 1e4 s
S. J. Friesenham, EPRI-NP-180, 1976

## Slide 6: TAGS data for Decay Heat
Impact of new JEFF-3.3 TAGS data on 239Pu thermal Fission Burst with « long irradiation »
Comparison of relative DH isotopic contributions to the total DH of a PWR UOX fuel at 100 s of cooling
Fission bursts
Fission bursts with « long Irrad. Time »
PWR UOX
T1/2 [s] | Irrad. Time | no | 5.6 h | 1 d
55.7 | BR_87g | 1.09 | 0.23 | 0.21
16.5 | BR_88g | 0.17 | 0.01 | 0.01
35.6 | MO105g | 2.69 | 0.36 | 0.33
4.492 | RB_92g | 0.00 | 0.00 | 0.00
2.702 | RB_94g | 0.00 | 0.00 | 0.00
1098 | TC104g | 0.88 | 5.17 | 4.64
456 | TC105g | 1.31 | 2.55 | 2.29
36 | TC106g | 5.01 | 0.68 | 0.61
21.2 | TC107g | 0.78 | 0.06 | 0.06
 | Total | 11.93 | 9.06 | 8.14
The DH emitted by a« fission burst with long irradiation » is closer to what’s happening in a real fuel.
Use those exp. data to quantify the impact of new TAGS measurements
review the list of Pandemonium candidates, provide sensitivity profiles

## Slide 7: Illustrated examples of ND needs and impacts on fuel cycle applications
Decay Heat:
  TAGS experiments
  Correlations in Fission Yields and Decay Data
  Np239 decay data: need for a re-evaluation?
Dose rate:
  Example of 136Cs
Outline

## Slide 8: Decay Heat uncertainty: importance of correlation/covariances data
Decay Heat: Cooling times ~from 0 s to geological times (accidents, storage, transport, reprocessing…) / Burnups ~from 0 to 100 GWd/t / Fissile content [ 1-5% 235U], [2-11% Pu]
Not enough integral experimental data to assess bias and uncertainties on the whole domaine of application
Nuclear data covariance propagation is of paramount importance and a key element in the safety demonstration but the results (and then the safety margins) strongly depend on covariance reliability, completeness and accuracy
  → 2 examples : FY and DD cov
A need for reliable and accurate ND covariances
UOX exp. coverage
MOX exp. Coverage
= la tête à toto
Integral DH exp. for ND+code validation

## Slide 9: Decay Heat uncertainty: Fission Yields covariances
Reduce the dependency to phenomenological models,
ensure consistency between all fission yields quantities (independent, cumulative,…)
Produce full covariance matrices consistent with nominal values
  Correlations come from pure experimental mass yield analysis, conservation laws (no correlations from isotopic model parameters at this moment)
New CEA/NNL evaluation for 235U(nth,f) FY -> 3 main goals
235U fission burst
Fission Yields were the main contributors to the total DH uncertainty
With new eval+cov -> strong reduction of the uncertainty, around 1% at 1 std !
JEFDOC-2128 (2022)

## Slide 10: Decay Heat uncertainty: Decay data covariances
Covariance evaluation: not performed at the moment during Decay Data evaluations
As an illustration, arbitary correlation (=0, -1 ou +1) between mean Eβ and Eγ are tested
With the strong reduction of the uncertainty due to FY cov, other sources are to be consolidated
With FY cov: other uncertainties are to be considered

## Slide 11: Illustrated examples of ND needs and impacts on fuel cycle applications
Decay Heat:
  TAGS experiments
  Correlations in Fission Yields and Decay Data
  Np239 decay data: need for a re-evaluation?
Dose rate:
  Example of 136Cs
Outline

## Slide 12: Decay Heat: 239Np decay data
Until 15 days, DH = FP + 239U/239Np contributions
Decay Heat of an UOX fuel (3.25% 235U, 33 GWd/t)
A preliminary study of the decay data of 239Np in JEFF-3.1.1 / JEFF-3.3 and ENDF/B-VIII.0 show some inconsistencies and underline the need for a new evaluation!
See JEFDOC-2063 (Nov-2021) (D.Bernard)

## Slide 13: 239Np/DD: central value deviations btw evaluations can inform on uncertainty quality
Mean deposited energy [keV]
JEFF-3.1.1: A. L. Nichols nov-2007 (rev2/1991) from UKHEDD25
JEFF-3.3: V.P. Chechev, N.K. Kuzmenko from ensdf/jul-2006
ENDF/B-VIII.0: from ensdf/feb-2018
DM(AME2016) = 722.746 272(3) keV
*: reconstructed
40keV  10%
JEFDOC-2063

## Slide 14: Analysis of 239Np/DD difference btw evaluations
239Np Decay Data/detailed deposited energy
Averaged deposited energies [keV] | JEFF-3.1.1 | ENDF/B-VIII.0
Light particles (b- + conversion + eA + e+/-) | 262.840 ± 13.837 | 230.583 ± 6.146
Electromagnetic particles (g+X) | 182.189 ± 7.235 | 174.346 ± 3.253
Total (quadratic unc. for DARWIN…) | 445.029 ± 15.614 | 404.929 ± 6.954
-40.100 keV btw ENDF8 vs JEFF-3.1.1 :
  -32.257keV light particles
  -7.843 keV EM particles
JEFDOC-2063

## Slide 15: Conclusion of 239Np/DD difference btw evaluations: 40keV on deposited energy
ENDF/B-VIII.0 is more rigorous than JEFF-3.1.1 but the analysis of the spectrum of light particles shows that b- lines are incorrectly normalized (+2.4%) and the file is incomplete versus total Qb-: Atomic Mass Evaluation (-6.3%)…
Still work to de bone for Decay Data files !!!
239Np is not the only isotope candidate for a review of its decay data and uncertainties: 242Cm,238Pu, 140La, 106Rh, 144Pr, 95Nb, 132I …

## Slide 16: Illustrated examples of ND needs and impacts on fuel cycle applications
Decay Heat:
  TAGS experiments
  Correlations in Fission Yields and Decay Data
  Np239 decay data: need for a re-evaluation?
Dose rate:
  Example of 136Cs
Outline

## Slide 17: Dose Rate: the 136Cs example
Too large uncertainty on its isotopic concentration due to nuclear data covariance propagation (11% at 1 std)
Sensitivity/variance analysis
Example of 136Cs, in the TOP’10 of the main contributors of the integrated dose received by the equipments in accidental scenarios

## Slide 18: Dose Rate: the 136Cs example
After re-analysis by U. Koster and thanks to measures at ISOLDE@CERN:
RIT = 0.996 ± 0.005
+ new decay scheme of 136mCs
<Eγ> = 501 keV (JEFF311= 816.6 keV)
D. Bernard, A. Chebboubi, U. Koster

## Slide 19: Dose Rate: the 136Cs example
New evaluation of 135Cs(n,g) -> -10% sur [136Cs]
and 135Xe(n,g)
-> not tested yet
New evaluation of RB as a function of incident neutron E and spin/parity of the coumpound sys. before desex γ -> FIFRELIN + new decay scheme
RB = 0.0 ± 0.0 (=0.16 dans JEFF-3.0/A)
(G. Noguère , O. Bouland)-> JEFF-4)

## Slide 20: Dose Rate: the 136Cs example
Improvement of isomeric FY (FYg/m) with FIFRELIN
+
New experimental campaign at Lohengrin@ILL in june 2021 : 239Pu(nth,f)136Cs
New measurement method! …Analysis in progress (A. Chebboubi, et al.)

## Slide 21: Dose Rate: the 136Cs example
Some analysis are still in progress, the total impact has to be assessed
A reduction of the 4/5% of the isotopic concentration of 136Cs in depleted calculation is expected
A reduction of its uncertainty is expected thanks to the new measurement of the 239Pu(nth,f)136Cs fission yield (35% in JEFF-3.1.1)

## Slide 22: To conclude
Needs in fuel cycle applications (decay heat, dose rate, fuel reprocessing, …) are a strong source of interesting studies involving needs in nuclear data
Sensitivity analysis / experimental validation / data assimilation are powerful tools to identify and drive improvements in nuclear data
The 136Cs is a good example of the work we do:
  Identification of an “industrial”/”application” need
  Study of the nuclear data involved, identification of the possible improvements
  Action! New experiment / evaluation / theoretical calculation / etc…
  Feedback, JEFF project
Shopping list: 129I (period, branching of its precursors), 235U(nth,f)137Cs (new measurement)

## Slide 24: Comparaison avec les bibliothèques des données évaluées et les données expérimentales
Cas du 137-Cs-55
Préconisation d’A. Rizzo sur Yc(137-Cs, 235U):
Pas compatible avec JEFF-3.1.1
Pas compatible avec les autres évaluations
Pas compatible avec les données expérimentales
  Nouvelle mesure par spectrométrie g recommandée
Préconisation d’A. Rizzo sur Yc(137-Cs, 239Pu):
Compatible avec JEFF-3.1.1
Compatible avec les autres évaluations
Compatible avec la plupart des données expérimentales
  Conserver JEFF-3.1.1 pour JEFF-4.0