## Slide 1
A detection unit designed for the study of the UHECRs from space
Sylvie Blin
Alexandre Creusot
Guillaume Prévôt
Étienne Parizot
APC & Omega (IN2P3 France)

## Slide 2
1 part/m2/year
1 part/m2/s
1 part/m2/billions years !
Quelles particules ? Et quelles sources ?

## Slide 3: JEM-EUSO space mission detection principle
Ability to detect UHECR from above (fast signal: 50-150 μs), through the UV fluorescence light and the Cherenkov
3
Photon-couting
MAPMT + ASIC ( + FPGA)
Wide dynamic > 100 pe
Time resolution < 10 ns
GTU = 1 μs
(i.e. time for an event to cross one pixel on ground)
Previous EUSO UV
camera prototype (2012-2017)
2304 pixels
(20 x 20 x 20 cm):
Detection area : 200 000 km2

## Slide 4: SPACIROC 3 ASIC chip
Developed by OMEGA IN2P3 for the experiment
64 channels photon counting
Single photon counting 100% trigger efficiency: 1/3 pe (~50 fC when MaPMT gain = 10 6)
Internal 8 bits counter (in order to minimize the consumption)
Wide linear dynamic: 1 to 130 pe
MAPMT adjustment trigger by individual threshold for each pixel
Double pulse resolution : 6 ns
Data acquisition & Readout to be done every 1 µs (GTU)
Readout Clock : 80 MHz
Output: 8 multiplexed data lines (to minimize interconnection with the FPGA)
Radiation Hardness By Design : TMR (Triple Module Redundancy)
Power budget : < 0.8 mW/pix
4

## Slide 6: History: previous pathfinders
EUSO-Ballon (France)
Un pathfinder dans un ballon stratosphérique ouvert
2011-2014
36 SPACIROC1
Mini-EUSO (Russie+Italie)
Un pathfinder dans l’ISS
2016-2019
36 SPACIROC 3
EUSO-TA (Japon)
Un pathfinder au sol (Utah)
2015-2018
36 SPACIROC1
EUSO-SPB (US)
Un pathfinder dans un ballon super-pressurisé
2015-2017
36 SPACIROC 3
EUSO-SPB2 (US)
Avril 2023
25 avril 2017
22 août 2019
6
NEXT STEP

## Slide 7: Previous pathfinders main results
EUSO-TA 2015
EUSO-Balloon 2014
EUSO-SPB 2017
7

## Slide 8: EUSO-SPB2 for 2023
  Prototype de l’EC-ASIC
6 FM EC-ASIC in mechanical structure
FM PDM
Z
Z
Antenna Boom (CSBF antennas)
Battery-Box (GCC+batteries)
SIP
Fluorescence Telescope (FT)
Cherenkov Telescope (CT)
Science solar panels
CSBF solar panels
(4 each side)
EUSO-SPB2 Operational Requirements –Flight
  We collect data at night, looking down and looking at the Earth Limb.
  Need dark sky, and minimal light pollution, ULDB
Wanaka NZ launch site is best option by far.
X

## Slide 9: New design: need a more compact detection unit
To minimize the dead zones on the new focal surface, it is mandatory to integrate the ASIC boards inside the unit.
Previous height: 200mm -> new one: height = 55mm (flat camera)
64 pixels MAPMTs
dynode PCB
kapton (anodes to ASIC board)
ASIC board
HVPS board
100 pins connector (to FPGA board)
kapton (output signals)
9
55 mm
to FPGA board
55 mm
HVPS
Dynode board

## Slide 10: SPACIROC3 BGA serial test
SPACIROC3 BGA:
  Packaging: BGA 12 x 12 mm , 353 balls, pitch 0,5
  Socket Yamaichi Y-red BN0353 MI 0-H-S
SPACIROC3 ASIC automatic test:
  Dedicated test bench: power supply, labview, pulse generator, keithley
  130 SPACIROC3 BGA tested: functionality, linearity of DAC, charge injection
  Good yield = 94%
Issue: need 180 BGA ASICs ( SPB2 and K-EUSO and Spares)
=> Novapak bankrupt
=> Japanese company for packaging
previous
new
  BGA packaged Spaciroc 3 ASIC
10

## Slide 11: Routing and Dimensions of the new ASIC board
A complicated board:
A board uneasy to integrate inside the EC_Unit
A board challenging to route (inner micro-vias, density)
A board complicated to produce (PCB/kaptons, hard to find a manufacturer, bad yield)
SAMTEC 100 pins
155 mm
EC_anode boards
Kapton 1
BGA ASIC
Kapton 2
50 mm
11
PCB designer= Pierrick Dinaucourt (OMEGA)
Xray campaign + modification process
only one manufacturer accepted: SOS electronic for PCB
=> 100 boards June 2018 (K-EUSO: 18, EUSO-SPB2: 54)
1st batch in October 2018:
8 PCB: Yield=50% (delaminated between rigid PCB and Flex)
2nd batch in March 2019:
rigid Kaptons 12 boards with 10 boards OK but intermittent failure or even permanent after some time

## Slide 12: ASIC board PCB issues: X ray campaign
Discussion with experts and with companies
3rd batch : 22 PCB
4th batch: 45 PCB
Selection PCB by X ray before cabling
IPC-600A norm
PCB scans
Faulty EC-ASIC boards due to imperfect manufacturing: shifts between different PCB layers
Thanks to Xavier de La Bernardie at Subatech
Yield=80% => enough for production

## Slide 13: First prototype of our new EC_Unit
  A light (500g) compact (55mm x 55mm x 55mm) detection unit:
  256 pixels
  photocounting
  GTU = 1μs
  consumption = about 250mW
  including HVPS & safety switches
  potted (arathane resin)
  two 100 pins output connectors
13

## Slide 14: SPACIROC and EUSO boards
TEST_EC_ASIC (1212)
EC-ASIC (SPACIROC1) v1 (1206)
EC-ASIC v2 (SPACIROC3) (1606)
EC_ASIC v3 mini-EUSO (1620)
EC_ASIC_BGA (1801)
test_SPACIROC3_BGA
test_EC_UNIT_SPB2
Elementary Cell test
EC_asic test
EC_asic test
BGA ASIC test and MAPMT

## Slide 15
Fluorescence Telescope Camera Development and Fabrication

## Slide 16: MAPMT Test
16
MAPMT test with full illumination
  Histogram of DAC positions of the inflexion points
  Efficiencies of the 64 pixels of 1PMT
  Efficiency map of 1 PMT

## Slide 17: EC test and PDM test
Automatic scan for 1 line
Total efficiency (MAX of the light seen for every position)
Detailed scan of the photo-sensitive surface:
We use small steps (about 0.5mm) so we can evaluate the varying sensitivity inside a pixel)
Spot size = 1.5mm (pixel = 2.9 mm x 2.9 mm)
Automatic scan for EC #34 (SPB2)
Total efficiency
17
1 PDM

## Slide 18: Conclusion
3ème génération:
  Détecteur de K-EUSO (mission ROSCOMOS, phase A)
  Détecteur de POEMMA (sélectionné par NASA) et son démonstrateur est EUSO-SPB 2 (2023)
REX:
- 130 ASICs en BGA chez Novapak (113 pour SPB2 et 36 K-EUSO et Spare)
=> dépôt de bilan de Novapak => manque ~50asics
=> packaging par une compagnie japonaise
- PCB fabrication: délai non prévu => chemin critique du projet pendant quelques semaines
Prospectives:
projet détection de débris au sol (collaboration japonaise de EUSO)
=> SPACIROC3 BGA packaging et production des EC_ASIC_BGA
projet POEMMA ou K-EUSO production
=> stock pour les prochaines missions
=> nouveau design d’ASIC
18