## Slide 1
STARE
(Serial Transfert Acquisition and Readout over Ethernet)
un transfert de données à 4*10Gb/s pour
AGATA
Electronic : C. Esnault (CE), L. Gibelin (LG), N. Karkour (NK), X. Lafay (XL), D. Linget (DL)
Computing : N. Dosme (ND), S. Elloumi (SE), E. Legay (EL), M. Taurigna
Students: M. Cahoreau (MC), G. Vinther-Jørgensen (GV)

## Slide 2: AGATA project
180 segmented crystals (60 triple clusters)
362 kg of Ge
82 % solid angle
50 kHz Ge crystal counting rate
Energy resolution & range: ~0.2%, 5 keV-180 MeV
Angular resolution : ~1º
Efficiency: 35 % (Mγ=1) , 20% (M γ =30)
Pic/Total: 50%(Mγ=1), 40% (Mγ=30)
Mobile detector
Large inner radius to accommodate ancillary devices
http://www.agata.org
http://agata.in2p3.fr

## Slide 3: Tracking ingredients
36-fold segmented +
CORE
Preprocessing
Identified interaction points
(x,y,z,E,t)i
Reconstruction of photon trajectories by tracking algorithms
100 Mhz, 14 bit sampling of segment and central contact signals
1
2
3
4
reconstructed -ray energies,
emission & scattering directions
7600 MB/s/crystal
50 kHz event rate/detector
100-sample traces/segment
200 MB/s/segment
900 MB/s
<100 MB/s
1,3 TB/s/detector

## Slide 4: Pre processing 1 crystal phase_0
2 * Carrier (3 FPGAs)
1 * GTS (1 FPGA)
7 * Mezzanines (1 FPGA)
1 Linco (1 FPGA)

## Slide 5: Pre processing 1 crystal new electronics
STARE
INFN & U. Milano
Hardware: IFIC Valencia
Firmware: IPHC Strasbourg
IJCLab Orsay

## Slide 6: Firmware developments February – September 2019
Based on code provided by David Sidler (ETH Zurich) and IPBus firmware from CERN (VC709)
=> tested with the CSNSM 10 Gbps network data flow and validate the UDP for AGATA DAQ.
Port the code from the VC709 to the KCU105
As decided by the FEE WG, the future AGATA electronics will be based on the SOM technology plus dedicated carrier boards.
STARE will be composed of a KU040 SOM module plus an FMC based dedicated carrier board.

## Slide 7
STARE characteristics
FMC vita 57.1
Input data rate from pre-processing : 4 x 10 Gbps (Aurora).
2 Power supply sources (Internal and external PSU using hot swap mux)
Spare LVDS I/O with the pre-processing for future use
Full clock management inside the SOM and the FMC carrier (SI5338).
Network Bandwidth up to 4 x 10 Gbps in parallel.
1 Gbps IPBus for slow control or slow control coming through SPI.
With this configuration it is absolutely easy to achieve continuous and comfortable 10 Gbps with monitoring and online analysis using multiple 10 Gbps Tx/Rx.

## Slide 8
STARE characteristics
4 x 10 Gbps Tx/Rx
STARE FPGA
KINTEX7
KCU040
UDP External Memory
10 Gb Transceiver
Readout data
IPBUS Slow Control
Monitoring data
Futur use data flow
Power Manager & Muxs
LVDS lines & IPbus
PACE - FMC Interface
EXT Power
System On Module
CLK generator
CLK generator

## Slide 9
STARE prototype

## Slide 10
STARE Prototype Design
Steps during 2020 (Covid constraints):
Design schematic (DL, NK, XL, CE) : Power management, Reset management, SOM-FMC Interface (meetings with PACE people), Mechanical constraints (meetings with PACE People)  During the first confinement - Spring 2020.
PCB placement, footprints creation, PCB routing (LG, DL, NK)  Summer 2020
PCB manufacturing and purchase components  Autumn 2020
PCB cabling  Winter 2020-2021
First delivery : first 5 prototypes  beginning February 2021.
Second delivery: last 5 prototypes  Middle March 2021.
Due to Covid19 : company in 60% of FTE mode

## Slide 11
STARE prototype
Top side
Bottom side

## Slide 12
STARE prototype
Power
management &
Debug facilities
SOM
Network
SFP+ cage
4 x 10 Gb/s
FMC
Conn.

## Slide 13
STARE production
Top side
Bottom side

## Slide 14
STARE Prototype Testbench
Xilinx Evaluation board: VC709
STARE
Firmware Dev: MC, CE, XL, (GV)
Optical fibers: 10 Gb/s
Ethernet câble: IPbus
Xilinx Evaluation board: KCU105

## Slide 15: Data processing
UDP interface
(David Zidler – Munich)
Data manger
Splicer
Aurora interface
10 Gb/s
Aurora
64 bit
@156,25 Mhz
Paquets de X KB
64 bit
@156,25 Mhz
X Paquets de 1 KB
10 Gb/s
Ethernet SFP
_ Slow control
_ EEPROM
_ Clock manager
X.LAFAY

## Slide 16: Results
Transfert @10Gb/s
=> 5 hours test : packets loss < 1.10-6 ; no bit error
Transfert @5Gb/s
=> 5 hours test : no packets loss ; no bit error
X.LAFAY

## Slide 17: Reliability mechanisms
Go Back N
  Using memory Efficiency
Selective Repeat
  Complexity
  Window size
  Better for debugging
  No data loss between FPGA and server
  Generates back
X.LAFAY

## Slide 18: Diagramme de l’œil et article de Rohde et Schwarz

## Slide 19
STARE Prototype
Difficulties in purchasing SOM Modules: IJCLab constraints, Covid constraints, global shortage on integrated circuits  only 4 modules are delivered (2 IJCLab & 2 from Andres), 10 modules ordered (delivery August 2021) (for reminder : 10 STAREs are available).
STARE with SOM Module (from Andres) will be sent to Valencia for Mechanical Integration with PACE board and crate.
STARE ready for integration test : from now until begin April…
Integration tests: PACE status, Covid constraints??
PACE Board
STARE Area

## Slide 20
STARE Prototype status
10 prototypes Working and tested completely in standalone mode
Integration tests started with Valencia PACE board
2 test benches were prepared by IJCLAB engineers to Valencia
Standalone data transfer from STARE to Server using PACE board is working to the computer server.
PACE firmware is ongoing to send data from PACE to the server
UDP Software is developped using basic data structure mode.
10 Gbps transfer is working during few hours
5 Gbps is fully working
Server configuration is needed
STARE Firmware for the first phase is working completely