## Slide 1
N. Karkour and the SIRIUS Collaboration
Projet SIRIUS
Digital Feedback Charge Sensitive Preamplifier for the Tunnel detector (DFCSP)

## Slide 2: Outline
SIRIUS Presentation (collaboration, funds, WP Structure)
DFCSP Front End Electronics for the Tunnel detector,
SIRIUS Si detector Back End Electronics
DFCSP Tunnel Firmware
Conclusion and Future roadmap

## Slide 3: SIRIUS in S3 Hall
Final focal plane Selection & Identification
Time of flight + Energy measurement
Beam
momentum achromatic
Mass spectrometer
2015-2021 : SIRIUS Construction phase Funded from CPIER Contract (La region Basse Normandie Vallée de la Seine)
Partners : IRFU - GANIL – IN2P3 (CSNSM- IPHC-IPNO)

## Slide 4: SIRIUS Technical challenges
Si detectors technical specifications
  Total detector Counting rate 10 kHz (100 Hz/channel)
  High energy : 10 MeV to 200 MeV Resolution FWHM 1 %
  Low energy : 100 keV to + 15 MeV FWHM < 20 keV @ 8 MeV.
  Timing resolution 1 ns between TOF and FP
  Electron and escaped alpha detection and identification
Gamma detection: 5 EXOGAM clovers with electronics
Trigger system and architecture :
  Triggerless system with Time stamping

## Slide 5
SIRIUS WP
Structure
2 Focal plane
F. Le Blanc (IPHC)
2.2 Front end DSSD
T. Chaminade (IRFU)
2.3 Silicium Tunnel
O.Dorvaux (IPHC)
2.4 Front end Tunnel detector
N. Karkour (CSNSM)
2.6 Mechanics infrastructure
T Goeltzenlichter(IPHC)
3 Back-End
K. Hauschild (CSNSM)
3.1 Tracker
(BEAST)
G. Wittwer (GANIL)
4 Data Acquisition system
F. Saillant (GANIL)
4.1 Electronic control core
S. Coudert (GANIL)
4.2 Run Control
F. Saillant (GANIL)
4.3 Data Flow
C. Maugeais (GANIL)
4.5 Daq Infrastructure
G. Lebertre (GANIL)
5 Assembly, Integration & test in S3 Hall
J. Piot / S. Herlant (GANIL)
5.1 Detectors mechanical integration
(Tracker & Focal plane & Ge)
F. Lutton (GANIL)
5.2 Control command and Vacuum system (GANIL)
6 Simulation & Data analysis
A. Lopez-Martens (CSNSM)
6.1 Simulation & performances
K. Hauschild (CSNSM)
3.4 DSSD Firmware
H. Leprovost (IRFU)
5.3 EMC and power supply
N.Karkour
6.3 Data analysis
J. Piot (GANIL)
3.3 FADC-DAC development
D. Linget (CSNSM)
3.2 Production Hardware Numexo2
A. Boujrad (GANIL)
3.5 Tunnel Firmware
X. Lafay (CSNSM)
3.6 GTS & Trigger
A. Boujrad (GANIL)
2.1 Detector DSSD& Veto Detector
Theisen/Sulignano (IRFU)
2.5 Germanium detector
K.Hauschild (CSNSM)
5.4 Test & Commissioning of the whole system
J. Piot / S. Herlant (GANIL)
6.2 System validation for physics
A. Lopez Martens (CSNSM)
4.4 Data analysis tool
L. Legeard (GANIL)
SIRIUS Management
Project coordinators: B. Sulignano (IRFU)
Project Manager: F. Le Blanc (IPHC)
Technical coordinator: N. Karkour (CSNSM)
Spokespersons (GANIL, IPHC,CSNSM,IRFU)
1.2 Front end electronic
J. Pancin (GANIL)
L. Caceres (GANIL)
1 Tracker/Diagnostic Box
J. Pancin/L. Cáceres (GANIL)
1.1 Detector
S. Herlant (GANIL)
L. Caceres (GANIL)
1.3 Mechanics
F. Lutton (GANIL)
S3 collaboration
board
SIRIUS collaboration board
O. Dorvaux IPHC
K. Hauschild CSNSM
J. Piot GANIL
B. Sulignano IRFU
S3 MB

## Slide 6: SIRIUS Instrumentation Architecture
BEAM

## Slide 7: WP2 WP3: Focal Plane Instrumentation
4 x 64 pixel Si Detector
DSSD Instrumentation 256 Channels (FPCSA)
Tunnel instrumentation 96 Channels (DFCSP)
6 * 16 channels Numexo2 boards
WP 3.6:
Trigger SYSTEM
GTS tree:
GTS NIM Carriers
GTS V3 Mezzanine
WP 3.2 : Numexo2 modules
WP3.4 et WP 3.5 FW DSSD and Tunnel
WP3.3: FADC-DAC
CMPAC50
DFCSP
CSP
FPGA
DFCSP block
Low gain resolution | 65kev
High gain resolution | 21keV
Linearity | <1.5%
Dead time | 2,5µs
Power by detector | 30W
CSP Output
Feedback Control
WP2.3: Tunnel
WP2.1: DSSD
WP2.2: DSSD FEE
WP2.4: Tunnel FEE
CSP Output
HI/LO Gain Switch
switching a feedback capacitor for changing the gain as a function of output signal level
High Energy resolution using DFCSP From 20 to 500 MeV | < 0,1 %
Linearity on overall range | < 1.5%
Dead time | < 5 µs
High gain resolution @ 8 MeV | 13,5 keV
High gain resolution @ 500 keV | 9,5 keV
Linearity | < 0,8 %
Dead time using MWD | < 8 µs

## Slide 8: DFCSP FEE for the Tunnel detector
From Tunnel detector to Numexo2
V. Alaphilippe, L. Gibelin, N. Karkour, and lot of Internship

## Slide 9: DFCSP basic principle
QHE
QLE
Rf
Cf
Cc
VLE
15MeV < EHE < 500 MeV
-7,5 MeV < ELE < 20 MeV
Cc = 20 pF = > G ≈ 2mV/MeV
Cf = 1 pF = > G ≈ 44 mV/MeV
Rf = 50 MΩ => τ = 47 μs
High Energy charge compensation stage
IN
TEST
- QHE
50Ω
Cd
I
FPGA
DAC
14 bits
100 MHz
PACS3
FADC DAC plus Numexo 2
Constraints :
2 signals par channel OUT to ADC and In from DAC.
Very high Integration and low coupling between input and output signals
Extreme Low noise signal integrity (few 10s of µV per LSB 14 bits)
Differential signal transmission over 10 m from FEE to BEE

## Slide 10: PAC S3
21 / 10 / 16
200 CSP produced
Low Energy Spectra 6 MeV alpha source @ IPHC
44 mV/MeV
Range: 30 keV to 60 MeV
< 5keV intrinsic resolution
@ 300 keV electron energy :
9 keV Si detector total resolution is 10.3 keV with the CSP
@ 6 MeV alpha energy :
12 keV detecor resolution 13 keV with the CSP.
Collaboration with GANIL

## Slide 11: CMPAC 50
48 CSP Mother board
48 Feedback input
48 detector signal processing from vacuum side
signal integrity and Xtalk in a small area of 110 x 160 mm
Top side is in the air bottom side is in vacuum.
20 layers 7 drill sequences 120 µ isolation
6mm thickness with 0.4 mm via !.
All vias are filled for vacuum (10-7 mbar) constraints.
Mixed types of components very small SMD next to huge 80 mm 200 pin BGA like connecteurs.
Complex Assembly solder thermal cycle (connectors and pcb flatness issue, 12 plane layers).

## Slide 12: INTERCONNECTIONS
21 / 10 / 16
Detector connections

## Slide 13
Si Focal plane Backend Electronic
Flash ADC-DAC Mezzanine development
D. Linget, N. Karkour, L. Gibelin, V. Alaphilippe, X. Lafay and Internships

## Slide 14
14
2 Hardware configurations using solder jumpers
Numexo2 card
16 channels
Tunnel detector BEE Configuration
Constraints :
Very high integration board, XTalk and Low noise
Components >80% of pcb Area.
Collaboration with GANIL and IFIC Valencia Spain

## Slide 15
Flash ADC and DAC Mezzanine
Production:
Test bench designed
100 FADC DAC produced tested and mounted.
FADC DAC Production Test Bench

## Slide 16: BANC DE TEST DFCSP FEE and BEE
21 / 10 / 16

## Slide 17: Firmware tunnel
Firmware numexo2 + ADC_feedback

## Slide 18: DFCSP basic principle
QHE
QLE
Rf
Cf
Cc
VLE
15MeV < EHE < 500 MeV
-7,5 MeV < ELE < 20 MeV
Cc = 20 pF = > G ≈ 2mV/MeV
Cf = 1 pF = > G ≈ 44 mV/MeV
Rf = 50 MΩ => τ = 47 μs
High Energy charge compensation stage
IN
TEST
- QHE
50Ω
Cd
I
FPGA
DAC
14 bits
100 MHz
PACS3
FADC DAC plus Numexo 2
Constraints :
2 signals par channel OUT to ADC and In from DAC.
Very high Integration and low coupling between input and output signals
Extreme Low noise signal integrity (few 10s of µV per LSB 14 bits)
Differential signal transmission over 10 m from FEE to BEE

## Slide 19: feedback IP Block
Etot = n x Step + residual

## Slide 20: IP feedback
Saturating CSP @ High Energy.
DFCSP retrieves that charge
Charge retrived . CSP is discharged to 0 level
Autocontrol Zoomed image
DAC
1 ms
ADC
Step_coeff
20 µs
max
Coefficient Calculation for residual charge left
8192 pulses are sent and 8192 ADCmax values obtained and added.

## Slide 21: Baseline Spectra measurements to see the Hardware effect
75 MeV
110 MeV

## Slide 22: Tests de résolution et de fonctionnements annexes
Random events using alpha source
Digital data processing events
DAC
ADC
Vin_Preamp = 18.86mV @ channel 1736
Vin_Preamp = 19.02 mV @ channel 1751
10.53µV par LSB.
FWHM = 4 canaux sur 16000
Précision = 1/4000 (pour un cdc à 1/100)
High energy followed by a low energy
High energy followed by another High energy

## Slide 23
Tests avec attenuateur entrée géné fixe :
Att: 30 dB E = 139 MeV FWHM 110 keV
Att : 40 dB E = 46,1 MeV FWHM 36 keV
Att : 50 dB E = 16,4 MeV FWHM 27 keV
Linéarité : -15% 
Linéarité : -8%
Resolution and Integral non linearity avant correction

## Slide 24: Energy Correction IP
The CSP decaytime is 50 µs The exponential equation V=V0 e-tRC .
During DFCSP algorithm there is an energy loss.
calculation of the lost energy and add it to the raw energy.
  Eraw is the feedback energy injected through the DAC.
  V0 = Eraw* etRC)
RC = 50 M * 1 p, Find t. t= number of steps *timereg *clock period. Deduce etRC
Energy Loss
Raw Injected Energy
Total Energy
INL < 1,2 % after correction
Linearity is submitted to huge number of iterations and acquisitions to choose the right parameter. Each channel has its own calibration value. Automatic calibration is needed before each run to make sure that the signal measurement is perfectly calibrated

## Slide 25
Results of the qualification of the code for step 300

## Slide 26: Existing V6 from Exogam2 Firmware modifications Collaboration with GANIL
IP Feedback
4 channels
FPGA V6
ISERDES IP
Deserialized
RAW SAMPLES
DSP IP
COMPUTED Information :
Energy
Time
Shape
Mirror charges
OSCILLOSCOPE IP
4 circulars buffers of 32KB
triggered
INSPECTIONS IP
ANALOG &
DIGITAL INSPECTIONS
EVENT DATA
REGISTERS VALUES
OSCILLOSCOPE DATA
RAW DATA
READOUT IP
BUILD of FRAMES:
event
oscilloscope
DAC FEEDBACK
SYNCHRONOUS (8bits)
ASYNCHRONOUS
(16 bits)
< 100 Mb/s
SPI (Serial link)
400 MB/s
TRIGGER
REQUESTs (16)
LOW SPEED
DATA FLOW
HIGH SPEED
DATA FLOW
SETUP_IP SIRIUS

## Slide 27
Internship was important in the project progress

## Slide 28: SIRIUS Now
IRFU 2020
GANIL 2021

## Slide 29: QUESTIONS
21 / 10 / 16