## Slide 1: MICROCHAnNEL COOLING
Prospectives for future detectors
24 January 2020

## Slide 2: OUTLINE
Thermal management problematic
Improving cooling with Si microchannel
Silicon microchannel cooling applications
Aida 2020 ongoing developments
Silicon microchanel cooling optimization @IN2P3

## Slide 3: Thermal management problematic
Future pixel sensors will require more and more cooling
Micro/nano technologies progress
Etching size reduction
Consumption reduction
Densification
Time resolved pixel
Consumption increase
Current Trend
Thermal management issues
  Lifespan > 10 years - Availability and reliability : 7/7
  High magnetic field – High radiation
  Sensor T<<0°C
  Material must be minimal
  Coolant T cannot be lowered at will : low TFM
E. Anderssen et al., Advanced Materials and Tools Research, Forum on Tracking Detector Mechanics 2015 (Amsterdam, NL): https://indico.cern.ch/event/363327/contribution/34
P= 2W/cm2 & Tfluide = -35 °C
 Tsensor > - 9°C
TFM=
Tfluide
Tsensor
LHCb : 0.5 W/cm2
LHCb upgrade I (2022) or ITK : ~2 W/cm2
LHCb upgrade II (2034) : ~ 3 - 5 W/cm2 (estimation)

## Slide 4: Improving cooling with Si microchannel
Minimizing TFM
Silicon wafer
Etching (DRIE)
Si-Si direct bonding (1200°C-200b)
Thinning
Typically TFM for Si cold plate circulating boiling CO2 is lower than 3 K.cm2/W
Locally distributed cooling
Large thermal exchange surface
Minimal path of thermal resistances
Low X0
Temperature Homogeneity
Radiation hard
Compatible with “HEP fluids”
Microchannel etched on Si wafer
m-fluidics (microchannel) device as heat exchanger for thermal management of heat source
Equivalent Diameter < 1 mm
Single or dual (boiling) phase flow

## Slide 5: Si microchannel cooling applications
2 independent networks of 75 µchannels
inlets and distribution manifolds (1.6 x 0.28 mm)
outlets
Advantage
Low TFM (~3Kcm2/W)
Minimum material budget: very thin coldplate (250-500mm)
No CTE mismatch with Si sensor
Channel failure has little impact on cooling
Silicon microchannel production on LHCb
Microchannel on NA62-GTK
No defect
Channel defects
Drawback:
  Expensive process (>120 steps)
  Size limitation
  Few competent subcontactors
  Direct bonding difficult
  Bad prod. Output
  Simulation not enough predictive
(Liquid C6F14)

## Slide 6: Aida 2020 Ongoing development
Alternative process
Céramic 3D printing
  Lighter than metal
  Flexibility
  CTE compatible
Ti 3D printing
  Low mass
  Cheap
  Easy to integrate
Carbon microvascular
  Ultralight
  Can be very long
Microchannel back to sensor
  CMOS Compatible
  Silicon advantage
  No bonding
Condenser
Evaporator
60 mm
Micro oscillating heat pipe
No pump
Self-contained and self-actuated.
Eliminate connectors

## Slide 7: Silicon microchanel cooling optimization @IN2P3
Objectives
  Cost reduction
  Production time reduction
  Material reduction
  Design optimization
 Kaizen approach instead of technological breakthrough
  Process optimization
    Laser etching & cutting
    Direct bonding replaced by anodic bonding coated glass
  Optimization of the connections
      Ceramic connector
      Anodic bonding
      Serialization of colling plate
  Design optimization
    Predictive Simulation
    Caraterisation : heat engineering
Inexpensive, flexible
and fast process
TFM optimization
Material optimization
Fast design

## Slide 8: Silicon microchanel cooling optimization @IN2P3
Process optimization :
  Laser etching
  Anodic bonding Si wafer coated (electron beam) with 5mm of glass
Wafer Si
Thin layer of glass (5mm)
Etching (DRIE)
Anodic Bonding
Thining
Glass deposition
4 inch wafer with a thickness of 500 mm
Pressure tests 06/2020
Tests in progress
Low cost for a prototype (<1k€)
Fast prototyping and optimization
Freedom on engraving and cutting
Complementary to chemical etching
Low cost (<1k€)
Fast production
Mature technology
Bonding can be done at home
Possibility to do complex structure
5cm

## Slide 9: Silicon microchanel cooling optimization @IN2P3
Process optimization possibilties:
  Anodic bonding of connector on cooling plate
  Anodic bonding of sensor/electronic on cooling plate
  In chip 3D etching
Onur et al., In chip microstructures and photonics devices fabricated by nonlinear laser lithography deep inside silicon. Nat Photon 11, 639-645 (2017)
 Cost & time saving
 Time & material saving
Call for tender
in September
Thesis in co-tutuelle?

## Slide 10: LAPP EXPERIENCE from CO2 COOLING OF FUTURE ATLAS PIXEL
Metallic tube of 2-3 mm diameter
New parametrisation of CO2 heat exchange in High Heat Flux regime

## Slide 11: LAPP CONTRIBUTION FOR MICROCHANELS DEVELOPMENTS
Thermo-fluidic di-phasic CO2 simulation
Prototype measurement
Current studies : 3D thermal models + 1D fluid models
New studies : 3D thermo-fluidic models (ANSYS FLUENT)
1- Validate the simulation with Pierre Barroca data
2- Perform simulation + mesurements for critical parameters (roughness, …)
3D simulations seems pretty difficult to manage
Expertise from OPTIFLUIDES company (https://www.optifluides.net/)
New insights on boiling carbon dioxide flow in mini- and micro-channels for optimal silicon detector cooling
DEPFET pixel detector for future e-e+ experiments
Publications :

## Slide 12: LPNHE Experience from CO2 COOLING OF FUTURE ATLAS PIXEL
Thanks to Reflecs* & Reflecs2* proj. (CNRS-Defi instr. 2014&15) it was possible to:
Realize prototypes of µ-channels etched in silicon and sealed with pyrex
Connectors in 3D-printed ceramic:
* PI: M. Bomben
D. Hellenschmidt, M. Bomben, G. Calderini et al.
Nucl. Instrum. Meth. (2019) 162535.
6”
CO2 boiling enhanced
at restrictions
Round single channel to
study 2-phase fluid at high-pressure
(50-100 bar) in micro-channels: valuable data to improve simulations
Ceramic conn.
Silicon µ-chann’s

## Slide 13: LPNHE CONTRIBUTION FOR MICROCHANELS DEVELOPMENTS
New production being prepared at C2N (Saclay)
  Test of different walls rugosity to see the influence on boiling
Continue prototype testing – e.g soldering
More work on connectivity among building block samples
Pressure test  no leak until 600 bar
Leak test with Helium: taux de fuite: 9x10-10 mbar l/s
“Rallonges” to be inserted somehow between one inlet unit and one outlet one
Using existing ceramic connectors?
To be continued...

## Slide 14: Conclusions
Strong interest in microchannel cooling for tracker detectors :
  NA62 GTR wishes to use microchannels by anodic bonding in 2021.
  Reflection to participate in the writing of the LHCb TDR framework
  FCC, BELLE, AIDA2020 …
Complementary skills on :
  LAPP: simulation, tests
  CPPM: process
  LPNHE: connectors, tests
Adapted tests means and samples are available
Industrial transfer potential (computers, biology, space, microreactors, etc.)
Technical theses possible
We can play a major role in the development of microchannel if we intensify our efforts
Funding are required