## Slide 1: Synergies between dynamic vacuum issues in accelerators and GW instrumentations.
Luisa Spallino1, Marco Angelucci1, Andrea Chincarini2, Riccardo Musenich2, Stefania Farinon2, and Roberto Cimino1
1 LNF-INFN Frascati, Italy. 2 INFN Genova, Italy.

## Slide 2: Motivation:
There are clear synergies in vacuum, cryogenics plants and installation between ultimate accelerators and Gravitational Waves Observatories.
Are recent R&D for (cryogenic) dynamic vacuum of interest too?
Can a “Material and Surface Science laboratory” and the competences developed in recent years to tackle unconventional “dynamic” vacuum be of some use for the running of existing GW interferometers and for the proposed ones?

## Slide 3: (Personal) Motivation:
“... The only common items between LHC vacuum and The Einstein Telescope are..... the pumps!!” V.B.
“... Vacuum in accelerators has nothing to do with the one needed for the the Einstein Telescope. There, being absent the particle beams, only static vacuum issues are of interest, while, in ultimate accelerators, dynamic vacuum phenomena are dominating and attracting the most recent R&D. ” N.F.

## Slide 4: Common Standard vacuum issues
Installations and running of huge vacuum and cryogenic systems.
Joints, flanges, valves etc. R&D.
Pumps and diagnostic (gauges, mass spectrometers and related R&D)
Vacuum calculations.
R&D on new materials, material’s coatings (NEGs?) and/or surface treatments to reduce surface degassing to limit vacuum pumps and contain vacuum costs!

## Slide 5: Unconventional GWO issues:
1. Electrostatic charge of mirrors
  Both VIRGO and LIGO optics undergo to inhomogeneous electrostatic charging of variable (or unknown) sign that may induce unwanted noise.
   procedures are undertaken for neutralization with positive/neg ions. (time consuming and risky)
2. Cryosorption on cold optics (frost):
  KAGRA GWO suffers from gas cryosorbed on the mirror surface inducing detrimental effects on the optics.
   Warming up should be avoided (time consuming)
Anything to do with accelerator Dynamic Vacuum?

## Slide 6: Unconventional issues: dynamic Vacuum
1. The beam interacts with the rest gas in the vacuum chamber causing:
  reduced beam lifetime - and/or emittance.
2. The vacuum system plays an important role for beam stability:
  Its material(s) conductivity, shape, coating and transitions determine machine impedance.
3. The vacuum chamber also affects beam stability and lifetime otherwise
  Its inner wall surface properties, in particular electron induced desorption and electron yields, are critical
   High desorption yields can lead to pressure runaway.
   High electron yields can lead to electron cloud formation

## Slide 7: e- cloud formation
Generation of electrons inside the vacuum chamber
(primary, or seed, electrons)
E
q
secondaries
elastically reflected
Acceleration of primary electrons in the beam field
Secondary electron production when hitting the wall
(F.Zimmermann)
Primary e-
After bunch passage
R. Cimino et al PRL 2004
SEY Study the number of electrons emitted by the surface when hit by an electron of given energy.
See for instance: R. Cimino and T. Demma “Electron cloud in Accelerators” Int. J. Mod. Phys. A 29 (2014) 1430023.
Photoelectrons from synchrotron radiation
Desorption from the losses on the wall
Residual gas ionization
Electrons from Ion pumps and gauges
Electrons from cosmic rays etc...

## Slide 8: e- cloud formation
Generation of electrons inside the vacuum chamber
(primary, or seed, electrons)
Acceleration of primary electrons in the beam field
Secondary electron production when hitting the wall
Avalanche electron multiplication
Tx to F. Ruggiero
The presence of an e-cloud inside an accelerator has consequences on the machine (pressure rise, outgassing, heat load, etc.) and on the beam Needs to be mitigated!
Tx to G. Rumolo
See for instance: R. Cimino and T. Demma “Electron cloud in Accelerators” Int. J. Mod. Phys. A 29 (2014) 1430023.

## Slide 9
SEY depends on the electron impinging energy
Material and surface conditions:
= 1 -
On a dielectric, the charge left on the surface depends on the energy of the impinging electrons
R.Cimino et al PRL 2004

## Slide 10
For non conductive surfaces (Ar ice on Cu; MgO,Al2O3):
SEY of 83 ML Ar on Cu
1
1
This can very well explain the mirrors electrostatic charge, its inhomogeneity and sign uncertainty.
Jokela et al. TIPP 2011
SEY < 1
= 1 -

## Slide 11: SEY not only can explain the charging phenomenon but suggests how to cure it! Using electrons of a given (low) energy just above or below SEY=1 to neutralize a dielectric.
Ongoing:
Measure detailed SEY from realistic samples representative of the various surfaces composing the mirrors.
Study the effect of electrons (very low doses and energy) on the mirror surface. (Much less penetrating than UV photons and much less disruptive than Ions)
Study the effect of electrons impinging on a charged surface.

## Slide 12: Design a testbench, where, with an e-gun, we can deliver to a mock-up mirror a given positive or negative charge.
We can than charge the mirror locally (by focusing / defocusing the gun) and set a “smart” system to measure the effect of such charging on the mirrors.
Having a Feed back seems very useful in this approach. We can define and validate the approach to estimate charging.
We can induce and neutralize this charge!
If validated, electrons can be delivered to actual mirrors without breaking UHV, efficiently reducing down-time.

## Slide 13: On Cryogenic mirrors this method can be used not only to neutralize them, but also to “clean” them. In fact, at LT a cryosorbed gas layer grows on mirrors influencing reflectivity and adding unwanted thermal noise. Jessica Steinlechner and Iain W. Martin PRR 1, 013008 (2019)
Need to be mitigated.

## Slide 14: Electrons are efficiently inducing desorption from cryogenically adsorbed gas!
Much more efficient than Photons (factor 100 – 1000)
Much less penetrating.
Mirror
R. Dupuy et al. J. Appl. Phys. 128, 175304 (2020)

## Slide 15: Electrons may see only the cryogenic overlayer (few mm are needed to be detrimental) and not the mirror surface!

## Slide 16: Some “back of the envelope” estimates.....
If Peff ~ 1 10-10 (H2O,CO,CO2, etc) mbar;
sticking coefficient = 1
1 monolayer (~ 1015 mol/cm2 ~ 0.3 nm) will be cryosorbed in 10.000 s. (~ 2.5nm/day ~ 10 times less than in KAGRA)
If we assume a mean ESD h= 0.1 mol./electron (as for H2O) @ 100eV. (R. Dupuy et al. J. Appl. Phys. 128, 175304, 2020)
To remove 1 ML we need an el. current of:
~ 1 mAmps/cm2 in one second (104 faster)
~ 100 mAmps/cm2 in 10 seconds (103 faster)
~ 10 mAmps/cm2 in 100 second (102 faster)
.....
and deposit, in total, less than 100 mW/ML/cm2
All in UHV, with marginal heating up of the mirrors and (possibly) reduced downtime.
Deserves further investigation!

## Slide 17: LNF-INFN MaSSlab “Material and Surface Science laboratory”
Two “state of the art” UHV set-ups equipped with cryogenic manipulators for hosting small samples (10x10mm2) at <20 K, electron guns, XPS, SEY, QMS and other spectroscopies to perform (with minor upgrades):
Proof of principle SEY and surface characterization of mirrors materials at RT and LT before and after cryosorption of gases.
03/12/2020

## Slide 18: Conclusion
There are many conventional vacuum issues in common between GWO and Accelerators.
There are also some “unconventional” vacuum studies were both communities can learn from each other.
A lot of R&D is ahead and have to be tackled as soon as possible to be included in the final design.