## Slide 1: Development of Electronics and its Synchronization System for the Hyper-Kamiokande
Japanese PI Yoshinari Hayato
(Kamioka Obs., ICRR, The Univ. of Tokyo)
hayato@suketto.icrr.u-tokyo.ac.jp
French PI stefano russo
(LPNHE/IN2P3)
srusso@lpnhe.in2p3.fr

## Slide 2
71ｍ
68ｍ
Super-K
Hyper-Kamiokande
Neutrino research and Hyper-Kamiokande
Secrets of neutrino are gradually revealed since the discovery of non-zero neutrino mass
in 1996 at Super-Kamiokande.
However,
we still don’t know which neutrino is heaviest. (Mass hierarchy problem)
Also, we don’t know whether neutrino and
anti-neutrino oscillations are same or different,
i.e. CP is conserved or violated.
Current analyses are statistically limited!
Super-Kamiokande can detect a tens of atmospheric, solar and accelerator neutrinos from J-PARC (@ 500kW neutrino mode).
Upgrade the J-PARC accelerator and build gigantic detector, Hyper-Kamiokande.

## Slide 3: Hyper-K Electronics and Synchronization System
Total number of PMTs are up to 55,000.
# of front-end electronics boards is > 2,000.
All the front-end boards must be synchronized.
Need accurate synchronization system, better than 100ps.
Hyper-K is expected to be operated for >20 yrs.
Long term stability and durability are essential.
Interaction position of particles in the detector
Reconstructed using timing.
Accurate timing measurement is essential.

## Slide 4
1 Gbps Eth*
Time dist. element
FE
…
24
FE
…
24
…
DAQ
Time dist. element
FE
…
24
FE
…
24
8*
…
* These numbers depend on the bandwidth
…
clock distribution edge
Time distribution architecture
1 Gbps Eth*
8*
Each time distribution element is synchronized to the local base and accorded to UTC.
Clock is sent to FEs embedded into data stream. Each FE reconstructs it and use as reference.
R&D focus to define the best way to distribute the clock.
Two scheme under evaluation: CERN White Rabbit and custom solution. Both based on FPGA serialiser-deserialiser.

## Slide 5
R&D program
R&D already started. Preliminary jitter tests performed on evaluation boards
Next steps are:
  Perform time distribution tests on FE electronics at an earlier stage.
  Test the UTC synchronization scheme is situ on the real orography.
  Test the prototypes on the existing similar detectors like Super-Kamiokande

## Slide 6
Founding requests
Founding request from France |  |  |  | 
Description | €/unit | Nb of units | Total (€) | Request to
Visit to Japan | 100/day | 30 days | 3000 | IN2P3
Travel | 1000 | 2 travels | 2000 | IN2P3
Visit to Japan | 100/day | 5 days | 500 | CEA/IRFU
Travel | 1000 | 1 travels | 1000 | CEA/IRFU
Total |  |  | 6500 | 
Founding request from KEK |  |  |  | 
Description | k¥/Unit | Nb of units | Total (k¥) | Request to
Visit to France | 20/day | 20 days | 400 | KEK
Travel | 150 | 3 travels | 450 | KEK
Total |  |  | 850 | 
Additional founds from France |  | 
Provided by | Type | €
JENNIFER2-RISE IN2P3 | Travel | 5000
JENNIFER2-RISE IN2P3 | Travel | 1500
Total |  | 6500
Additional founds from KEK |  | 
Provided by | Type | k¥
JSPS | Travel | 450
Total |  | 450

## Slide 7
backup slides

## Slide 8: Hyper-Kamiokande detector
Start operation in 2027

## Slide 9
Wide variety of Hyper-Kamiokande physics program
Atmospheric neutrino
Neutrino mass hierarchy
Accelerator neutrinos
CP violation
Solar neutrinos
Interior of the sun
Supernova neutrinos
Evolution of the universe
Proton decay
Grand Unification

## Slide 10
Tokai
Kamioka
J-PARC
L2VPN (SINET)
Distance = 295km
Neutrino arrives at SK in ~1ms.
Accelerator produces neutrino every ~1 sec.
Record the neutrino production time with GPS.
Send information via L2VPN.
Record the data around the beam arrival timing
Detection of accelerator neutrinos
GPS systems in both sites need to
provide “correct” time.

## Slide 11
GNSS receiver
Time distribution
Atomic
clock
Local time reference and UTC
A very small jitter (1 ps), small drift local time base is generated by an atomic clock system.
The local time base is accorded to UTC by means of Global Navigation Satellite System (GNSS) network.
The UTC reference is used to select particles events from the accelerator and to corelate astrophysical events with other telescopes
The system architecture depends on the site orography