## Slide 1: ALTIROC, a 25 ps time resolution ASIC for ATLAS HGTD
N.Seguin-Moreau*1, S. Conforti1, C. de La Taille1, P. Dinaucourt1, G. Martin-Chassard1, A. Dragone2, B. Markovic2 , L. Ruckman2 , A. G. Schwartzman2, D. Su2, C. Agapopoulou3, N. Makovec3, S. Sacerdoti3, L. Serin3, D. Gong4, J. Ye4, W. Zhou4
TWEPP 2019
1
2
3
4

## Slide 2: ATLAS High Granular Timing Detector in HL-LHC
In the forward region, between the Inner Tracker and the End Cap of EM Calorimeter
• 2.4 < η < 4.0 ( 120 mm < R < 640 mm), ΔZ = 75 mm (+50 mm moderator)
• TID up to 9.5 MGy (SF 2.25) at R = 120 mm after 4000 fb-1 (1016 n/cm2 SF =1.5) => Ring 3.1< η < 4.0 replaced half the HL-LHC lifetime = 32 % of modules.
• σt ~ 30 ps/track at start, 50 ps/track at the end, dominated by electronic jitter and < 10% occupancy
- Si (Low Gain Avalanche Diodes) sensors
- 1.3 x 1.3 mm2 granularity
- 2 hits/track η< 3.2 ; 3 hits/track η> 3.2
• Use as counting detector at 40 MHz for luminosity measurements
MIP signal (10 fC) with LGAD sensor
thickness = 50 µm and G = 20
2 disks, 2 layers/disk
equipped on both sides with
Low Gain Avalanche Diodes (LGAD)
Sensor overlap: 20% for r>320 mm and 80% for r<320 mm

## Slide 3: HGTD module
Module = LGAD sensor (450 PADs of 1.3 x1.3 mm2) + 2 ASICs (225 channels/ASIC) bump bonded to sensor + Flex to peripheral electronic boards (LpGBT, DC-DC, flex connectors)
  - 2 ASICs =2 x 2 cm x 2 cm (15x30 channels) with 1.3 x 1.3 mm2 pads granularity
Flex: wire bonded to sensor (bias voltage) and to ASICs (signals and power)
See Marisol Robles’ poster (144) :
« Test results of a flexible printed circuit for the ATLAS HGTD »

## Slide 4: Requirements for the ASIC
HGTD key requirement: Time resolution per track, combining multiple hits, is 30 ps at the start of lifetime
to 50 ps after 4000 fb-1 => Time resolution /hit must be < 40 ps at start and 85 ps (70 ps) at the end of lifetime
for the inner radius (outer radius)
Main contributors:
Maximum jitter (σelec) | 25 ps at 10 fC at the start of the HL-LHC and 70 to 85 ps after 4000 fb-1 for 2.5 fC
TDC contribution | < 10 ps
Time walk contribution | < 10 ps
TDC conversion time | < 25 ns
PAD size | 1.3 x 1.3 mm2 x 50 µm => Cdet = 4 pF
ASIC size and channels /ASIC | 2x2 cm2 225 channels/ASIC
Single PAD noise (ENC) | < 1500 e- or 0.25 fC
Minimum threshold | 1 fC
Dynamic range | 2.5 fC to 100 fC
TID Tolerance | Inner region (R<320 mm): 4.7 MGy (Modules replaced after 2000 fb-1) Worst case at R=320mm: 5.1 MGy
Voltage and Power dissipation per ASIC | 1.2V and 300 mW cm-2 => 1.2 W/ASIC (225 ch) or 4.4 mW/channel and 200 mW for the common part
+ +
with = + +
ASIC designed in CMOS 130 nm

## Slide 5: ALTIROC1 single channel FE readout
ALTIROC1 FE integrates:
A preamplifier followed by a discriminator: Time walk correction made with a Time over Threshold (TOT) architecture
Two TDC (Time to Digital Converter) to provide digital Hit data =Time of Arrival (TOA) + Time Over Threshold (TOT) measurement
  TOA TDC: range of 2.5 ns and a bin of 20 ps (7 bits)
  TOT TDC: range of 20 ns and a bin of 40 ps (9 bits)
One Local memory (SRAM): to store the 17 bits of the time measurement (Hit data) until L0/L1 trigger (~ 1 MHz) => trigger latency = 35 µs
Altiroc1 integrates a standalone phase shifter designed by SMU

## Slide 6: ALTIROC Preamp: Voltage configuration (Baseline)
  Id tuneable: Id (M1) = Id1 (150 µA) + Id2 (tuneable up to 850 µA)
  BW tuneable with Cp: 1 GHz down to 200 MHz
  R2=25K: for DC bias, Rin ~ 1.6 KΩ, Fall time= 2.2 RinCd
  I leakage sensor: absorbed by R2
    ~ gm1 x R1 and gm1 ~ 20 * (Id1 + Id2)
Noise independant of Cd, depends of √BW and of 1/√Id
  with en given by:
Signal rise time is the convolution of signal duration td and amplifier risetime t10-90_PA
V step from internal pulser
70 ps
~ α Id
Chart: noise spectral density
| 0.1 | 0.2 | 0.4 | 0.8 | 1.6 | 3.2
 | 2.0372 | 1.4405 | 1.0186 | 0.72024 | 0.50929 | 0.36012

## Slide 7: TOA TDC Architecture (Simplified): Vernier Delay Line
1
2
3
4
128
F1
F2
F3
F4
F128
120ps
120ps
120ps
120ps
120ps
1
2
3
4
128
S1
S2
S3
S4
S128
140ps
140ps
140ps
140ps
140ps
Q1
Q2
Q3
Q4
Q128
Bin2
Q2
Q1
Bin3
Q3
Q2
Bin4
Q4
Q3
Bin128
Q128
Q128
Bin1
Q1
0
Time-to-Digital Converter (TDC)
START
STOP
Simplified Block Diagram:
STOP signal propagates
in the Fast Delay Line
(Delay of one cell = 120 ps)
START signal propagates
in the Slow Delay Line
(Delay of one cell = 140 ps)
The START pulse comes first and initializes the TDC operation.
The STOP pulse follows the START with a delay that represents the time interval to be digitalized.
At each tap of the Delay Line the STOP signal catches up to the START signal by the deference of the propagation delays of cells in Slow and Fast branches of the delay line: i.e. 140ps – 120ps = 20ps that represents the LSB of time measurement.
The number of cells necessary for STOP signal to surpass the START signal represents the result of TDC conversion
Cycling configuration used in order to reduce the total number of Delay Cells.
TDC range is equal to 128*20ps = 2.56ns
2.5ns
Clock
STOP
Event
Detection
2.5ns Measurement Window
START
ToA
Differential shunt capacitor voltage-controlled delay cells
TOA TDC
Resolution: 20 ps
Range: 2.5 ns
7 bits
@ Bojan Markovic, SLAC
TDC Power consumption 0,4 mA *1.2V = 0,5 mW @ 10% occupancy

## Slide 8: TDC for TOT measurement
TOT TDC
Resolution: 40ps
Range: 20 ns
9 bits
TOT: coarse delay line (160 ps) + TOA TDC
@ Bojan Markovic, SLAC
TDC Power consumption 0,4 mA *1.2V = 0.5 mW @ 10% ocupancy

## Slide 9: PROTOTYPES DONE SO FAR (all CMOS 130 nm)
ALTIROC0: contains only PA + discriminator – for 2x2 1x1 mm2 sensors
  Altiroc0_V1 (Dec 2016): 4 channels for 2 pF (1x1 mm2 sensor) and 4 channels for 20 pF (3x3 mm2 sensors), Voltage PA (=VPA) for all channels
  Altiroc0_V2 (December 2017): 4 channels with faster VPA preamp and and 4 channels with TZ preamp. All for Cd ~ 2pF
  Testbench and testbeam measurements
ALTIROC1_V1 : 5x5 complete readout channels (PA, discri, TDC, SRAM) to readout 1.3 x 1.3 mm2 LGAD pixels , 15 channels with VPA, 10 with Transimpedance amplifier (TZ)
  Testbench measurements (debug) since beg. of Dec. 2018
  Irradiation tests
ALTIROC1_V2: submitted March 2019 (CMS eng run ) but thinned/diced dies received beg of July => first tests begun mid July 2019
  Minor modifications between V1 and V2: 1.2V MOSCAPs used to filter DLL Vctrl voltages changed to 2.5 MOSCAPs to get rid of the leakage current on these nodes
  Testbeam 19-25 August @DESY
  => measurements shown with Altiroc1_V2 are quite preliminary
Altiroc1 tesboard
~ 7,7 mm
2 mm
2 mm
Altiroc0
Wire bonding and bump bonding done by IFAE, CNM and IHEP

## Slide 10: ALTIROC1
~ 8 mm
Altiroc1 layout
Submission :
V1 13 June 2018, V2 March 2019
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
ZOOM of one pixel
VPA: Voltage preamp
TZ: Transimpedance preamp
Measurements shown in this presentation only with VPA

## Slide 11: SETUP for ALTIROC1 measurements
Altiroc1 die
Wire bonding @

## Slide 12: ALTIROC1 TOA measurement setup
Injection of charge (0 fC up to 50 fC) using the ASIC internal pulser controlled by cmd_pulse input
cmd_pulse signal generated by the FPGA, synchronous to 40 MHz clock
External trigger pulse to characterize the TOT TDC alone (as well as TOA TDC)
ALTIROC FPGA Board (C01):
Using SY89295UMG as a programmable delay, the cmd_pulse can be delayed by software with steps ~10 ps in ~10 ns range
Cmd_pulse
Ext_trig

## Slide 13: ALTIROC1_V2: TOA Measurements using PA+Discri
2.5ns
2.5ns
40 MHz clock
cmd_pulse
cmd_pulse
Altiroc1_V2
LSB= 22 ps
Range = 2.7 ns
In Altiroc1_V1, LSB was 28 ps and range 1.8 ns (due to Ileakage in MOS filtering Cap used in the DLL): corrected in Altiroc1_V2 by replacing 1.2V MOS transitors capacitors by 2.5V MOS transistors

## Slide 14: ALTIROC1_V2: TOT measurement using external trigger
ALTIROC1_V2
LSBc= 163 ps
LSBf= 35 ps
Range = 20 ns
Jitter = 10 ps
TOT TDC of Altiroc1_V1: range was only 5 ns. Due to a larger than expected initial pulse-width (higher parasitics)
of signals circulating within the cyclic delay lines => corrected in Altiroc1_V2 with a better control the initial pulse width

## Slide 15: Jitter and LSB uniformity of ALTIROC1_V2 meas. , wo sensor
Measurements done
on the 15 VPA channels only
Qinj=10 fC, Cd =0
Individual tunings of the pixel TDC not done
VPA: Voltage preamp
TZ: Transimpedance preamp
LSB
JITTER

## Slide 16: ALTIROC1_V1: Jitter vs Qinj measurement (Cd=3.5 pF)
5fC, σ = 36 ps (33 ps afetr floor substraction)
10fC, σ = 23 ps (19 ps after floor substraction)
Measurements done with the internal TOA TDC
Floor (~ 13 ps) from clock, command pulse and TDC bin not substracted

## Slide 17: TOA vs TOT of ALTIROC1_V1 measurement
Measurements done with scope as TOT TDC didn’t work properly in Altiroc1_V1

## Slide 18: CK tree measurement
Clock tree (pulser command, clocks): good distribution for 4x4 channels
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
VPA
VPA
VPA
VPA
VPA
VPA: Voltage preamp
TZ: Transimpedance preamp
Ch 0
Ch 2
Ch 1
Ch 3
Ch 4
Ch 5
Ch 7
Ch 6
Ch 8
Ch 9
Ch 10
Ch 12
Ch 11
Ch 13
Ch 14
Ch 15
Ch 17
Ch 16
Ch 18
Ch 19
Ch 20
Ch 22
Ch 21
Ch 23
Ch 24
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
VPA
ck0
ck1
ck2
ck3
ck4
ck5
ck6
ck7
ck8
ck9
ck11
ck11
ck10
ck10
VPA
VPA
VPA
VPA
RMS = 18 ps ± 4ps
Ch8: to be checked on another ASIC

## Slide 19: TEST BEAM measurements with Altiroc0_V2 (Oct. 2018)
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
Time resolution of a 2x2 x1x1 mm2 LGAD array bump bonded on an Altiroc0 ASIC as a function of the discri threshold (DAC Units) before (black points) and after TW correction (red points)
Time reference given by SiPM
with a time resolution = 40 ps ,
which has been substracted
30 % improvement after TW correction
Jitter around 35 ps

## Slide 20: TEST BEAM measurements with Altiroc1_V2 (19-25 Aug. 2019)
LSB =20 ps

## Slide 21: Irradiations tests with Altiroc1_V1 (June 28- July 8, 2019)
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
CERN facility, TID up to 340 Mrad
Chart: Altiroc1_V1: Internal pulser before and after 340 Mrad
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 12 | 16 | 24 | 32 | 48 | 63
after 340 Mrad | 0.26 | 1.016 | 1.854 | 2.6 | 3.6 | 4.34 | 5.18 | 5.92 | 6.88 | 10.2 | 13.2 | 19.8 | 26 | 38.94 | 51.2
Before irrad | 0.3 | 1.06 | 1.9 | 2.66 | 3.64 | 4.4 | 5.24 | 6 | 6.978 | 10.32 | 13.4 | 20.08 | 26.32 | 39.46 | 51.78
20 Mrad
340 Mrad
V bandgap
DC internal pulser
7 bit DAC (Threshold correction)
10 bit DAC (Threshold setting)
20 mV
0.3 mV
20 mV
20 mV
Slope bef and after irrad: - 0,4 mV/DACU
Chart: Altiroc1_V1: 10-bit DAC (Threshold) after 340 Mrad
| 0 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 800
10-bit DAC after irrad | 671.5 | 672 | 672.7 | 673.3 | 675.1 | 678.4 | 685.9 | 700 | 727 | 782 | 891 | 1015

## Slide 22: Irradiation tests with Altiroc1_V1 (June 28 – July 4, 2019)
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
TOA jitter could be measured up to 23 Mrad but then water pb on the setup … => TDC didn’t work anymore
=> Measurements (after 340 Mrad) of the jitter vs Qinj performed on scope (using discri output) and compared to measurements performed with the TDC done on the very same channel before irrad: 45 ps jitter @ Qinj=5 fC after TID to be compared with 35 ps obtained before irrad.
Test of PLL (designed by OMEGA) used in the phase shifter after irrad. Ref clock = 40 MHz. After 340 Mrad, PLL can still lock up to 50 MHz

## Slide 23: Summary and next steps
  ALTIROC0 and ALTIROC1 prototypes crucial to measure the analog performance, which is rather good (25 ps @ 10 fC) but still a lot of measurements to be done in particular with the sensor (testbench and testbeam)
  Still points to be understood:
    Leakage currents in the DLL and the internal pulser
  Next steps: ALTIROC2 with 225 channels (1.3 x 1.3 mm2 LGAD pixels) to be submitted in Jan. 2020
    Digital part quite complicated (IFAE, IHEP and LPC Clermont)
    Analog part performance vs 2x2 cm2 ASIC
    Plan to combine « Digital On Top » for matrix part (with an exclusion area for 1/3 of the pixel = PA + Discri + TDC) and « Analog On Top » design for off pixel electronics and the floorplan (distribution of the power supplies)
See Raimon Casanova’s poster (152):
« ALTIROC2, a readout ASIC for the HGTD in ATLAS »

## Slide 24: BACKUP

## Slide 25: ALTIROC1 prototype (June 2018 submission)
ALTIROC1 = Second ALTIROC ASIC prototype with 25 complete FE channels to readout 5 x 5 sensor cells of 1.3 mm x 1.3 mm (6.5 mm x 6.5 mm) + Phase shifter
3 Labs involved: OMEGA (analog Part, floorplan), SLAC (Digital part: TDC and FIFO), SMU (Phase shifter)
ASIC size: 7,5 x 7 mm² taking into account the pads on the right side of the ASIC (7.5 mm) and also pads (for bias, probes ...) on the top side for debug (top pads only for this prototype version)

## Slide 26: Voltage-Controlled Delay Cell
@ Bojan Markovic, SLAC
Differential Shunt-Capacitor Delay Cell:
  Differential architecture: reduced jitter and improved supply noise rejection.
  Additional source transistors for supply noise rejection.
  Compared to Current-Starved approach, the Shunt-Capacitor approach guarantees a more contained and linear Voltage-Delay characteristic with benefit of reducing jitter due to control voltage noise and ripple.
  The MOS diodes in parallel to MOS capacitors prevent leakage currents from altering the capacitor voltage, thus improving delay accuracy.
  Additional delay-control transistors for trimming/calibration purposes.
  Separate buffered outputs for time measurement operations.

## Slide 27: Local FIFO 19x400 (SRAM)
SRAM Cell (10T configuration):
Standard 6T cell Configuration
Additional buffers in order to allow for simultaneous Read/Write operation within the same clock period.
Dimensions:
6.57um x 2.18um = 14.3226um^2
Layout:
+
+
+
+
SRAM word length: 19bits
  1 HIT bit
  7 TOA bits
  9 TOT bits
  2 extra debugging bits:
    TOA overflow bit
    1 extra Vernier TDC bit for TOT measurement
SRAM depth: 400 (10µs data)

## Slide 28: ALTIROC1: jitter and out_pa amplitude vs Cd Vth = 1 fC
Amplitude goes as 1/Cd as expected
Jitter increases with Cd as expected

## Slide 29: ALTIROC1: TOA jitter vs Qinj (VPA), Cd=3.5 pF Vth = 1 fC and 2 fC
Jitter decreases with Qinj and is better for larger Vth as expected

## Slide 30: VPA jitter vs TZ jitter (Altiroc0_V2)

## Slide 31: Single-channel readout in ALTIROC2

## Slide 32: POWER CONSUMPTION
Power consumption requirement: MAX= 300 mW/cm2 => 1.2W/ASIC (2X2 cm2)
200 mW for the common digital part
=> Max 1W /225 = 4,4 mW / channel
PA + Discri + 2 TDC of one channel = (570 +60) µA + 350 µA + 2* 0,4 mA = 1,8 mA or 2,2 mW (= vdda)
2.2 mW (= vddd) for all the digital part of the channel (Hit buffer, ck trees, lumi block etc)

## Slide 33: Requirements
@ Cd= 4 pF
=> Cd ~ 4 pF
9.5 MGy
2.7 MGy
=> ~ 4 mW/channel

## Slide 34: Connections between ASIC and DAQ
Peripheral boards: flex connectors, DC DC converters for LV and HV voltages. LpGBT for data transmission and optical modules. 3 sets of optical links. Down links for slow control (in red) connected to the FELIX boards in USA15 and up links for the offline data. The uplinks for the lumi data go to dedicated back-end boards