Physics performance of a DHCAL with various absorber materials
Jan BLAHA
CALICE Meeting, 16 – 18 Sep. 2009, Lyon, France

---
Introduction
Motivation:
Better understanding of DHCAL generally
The first qualitative view on DHCAL global performance
Study performed:
Study of the main calorimeter characteristics such as:
Response
Linearity
Energy resolution
Shower shape
Containment
Comparison of various absorber materials: Fe, W, Pb
Comparison of analog and digital readout
Dependency on the readout threshold
Simulation tools:
SLIC (Geant4) simulation tools with LHEP physics list
lcsim.org analysis framework
Generated data: π-: 3, 10, 50, 100, 150, 200 GeV

---
Calorimeter configuration
µMegas DHCAL
Calorimeters description:
Sampling calorimeter with 80 layers (9 λ)
Active medium: Gas (3 mm of Ar/Isobutane)
Passive medium: Fe or W or Pb
1x1 cm2 cell size
Readout: - analog (dep. energy or charge)
 - digital (nb of hits above threshold)
Calorimeter with Fe absorber:
Passive material: total 9 λ (including 4 mm thick steel cover)
Active layer: 6 mm (3 mm of gas + 3 mm detector materials)
Dimension: 200 x 200 x 200 cm3
Calorimeter with W and Pb absorbers:
Passive material: 9 λ (absorber material only)
Active layer: 6 mm (3 mm of gas + 3 mm detector materials) + 4 mm of Al cover (32 cm in total (0.8λ))
Dimensions: - W: 200 x 200 x 170.16 cm3
- Pb: 200 x 200 x 239.44 cm3
100 GeV Pions

---
Analog vs digital readout, W abs.
analog
σ = 8.4 %
 Edep [MeV] in calorimeter
 Nb of counted hits
analog
σ = 14.9 %
analog
σ = 26.2 %
digital
σ = 10.8 %
digital
σ = 15.7 %
digital
 Edep [MeV] in calorimeter
 Edep [MeV] in calorimeter
 Nb of counted hits
 Nb of counted hits
σ = 20.2 %

---
Analog vs digital readout, Fe abs.
analog
analog
analog
σ = 13.7 %
σ = 22.6 %
σ = 10.4 %
 Edep [MeV] in calorimeter
 Edep [MeV] in calorimeter
 Edep [MeV] in calorimeter
digital
digital
digital
σ = 17.5 %
σ = 11.3 %
σ = 8.7 %
 Nb of counted hits
 Nb of counted hits
 Nb of counted hits

---
Response for various abs.
More visible energy is for the Fe due to its longer X0 and RM in comparison with W and Pb absorbers
Number of counted hits is well correlated with Edep. Digital readout can be used in a wide energy range
The saturation effect is seen for higher
energy → semidigital readout must be	considerd
Fe abs.
analog readout
digital readout

---
Response vs threshold, Fe abs.
1 MIP MPV
1 MIP MPV

---
Response vs threshold, W abs.
1 MIP MPV
1 MIP MPV

---
Calorimeter linearity
Fe abs.
W abs.

---
Linearity vs threshold
W abs.
1 MIP MPV
Fe abs.
1 MIP MPV
W abs.
1 MIP MPV
Fe abs.
1 MIP MPV

---
Energy resolution
Fe abs.
W abs.

---
Resolution vs threshold
Fe abs.
Fe abs.
1 MIP MPV
1 MIP MPV
W abs.
W abs.
1 MIP MPV
1 MIP MPV

---
Longitudinal shower profile
Fe abs.
100 GeV pions
Shower profile behaves as expected for different absorbers
Analog and digital readouts have	almost identical shower profile in a	low energy range
With increasing energy the shift between analog and digital shower profiles increase
W abs.

---
Lateral shower profile
Fe abs.
100 GeV pions
Difference between analog and digital readout is seen for all the energies
More hits, in comparison with deposited energy, are counted in the core and less in the tail
The difference is significantly larger	in case W in comparison with Fe	absorber
W abs.

---
Mean shower radius
Fe abs.
Pb abs.
W abs.
100 GeV pions

---
Longitudinal containment
50 GeV
Fe abs.
W abs.
50 GeV pions
Fe abs.
For Fe absorber, 95 % energy is contained in 50 layers (~5.6 ) for 50 GeV pions
In case of W absorber, 95 % energy is contained in 45 layers (~5 ) for 50 GeV pions
As the consequence the W absorber needs less s for the same containment
50 GeV
W abs.

---
Lateral containment
digital
Fe abs
?
W abs
analog
50 GeV
50 GeV pions
Fe abs
Large difference in containment is seen between analog and digital readout
For analog readout, 95 % is contained in a radius 23 (27) cm for Fe (W) absorber for 50 GeV pions
In case of digital readout, 95 % is contained in a radius of ~21 (19) cm for Fe (W) absorber for 50 GeV pions
This can leads to underestimation in case that only digital information is considered
digital
analog
50 GeV
W abs

---
Summary and conclusions
Linearity has been found similar for all three absorbers and is within 1 % for analog and 5 % for digital readout. The linearity is stable over whole studied thresholds (from 0.0 to 2.0 MIP MPV)
Energy resolution for digital in comparison with analog readout tends to be superior for lower and inferior for higher energy. The best energy resolution, over whole energy range, has been found for Fe absorber. The resolution is stable in a range from 0.0 to 1.0 MIP MPV for both readouts
The significant difference in longitudinal and lateral shower profiles has been found between analog and digital readout. The difference can lead to incorrect estimation of the calorimeter dimension if only digital information is considered
A difference in performance between analog and digital approaches has been identified and will be a subject of further investigation. The study will be also extended from digital (1 bit) to semi-digital (2 bit) readout.

---
Spare slides

---
Properties of absorbers
absorber	Z	ρ [g.cm-3]	X0 [cm]	λ [cm]	RM [cm]	1 abs. [cm]	80 planes [cm]
Fe	26	7.87	1.76	16.78	1.77	1.9	200
W	74	19.30	0.35	9.97	0.92	1.127	170.16
Pb	82	11.35	0.56	17.6	1.60	1.993	239.44

---
Stochastic and constant term
Fe abs.
Fe abs.
W abs.
W abs.