## Slide 1: Recent Achievements on Time Distribution System R&D
stefano russo LPNHE Paris,
Fabrizio Ameli INFN Roma,
HK meeting 04/03/2021

## Slide 2: Proposed Architecture
The time distribution system consists of 2 main parts:
A system that generates the local time base correlated to the Universal Time Coordinated (UTC).
A distribution network that delivers the clock to all the front-end nodes and establish a communication link for critical slow control.
For each of the two I’ll present the actual R&D status and future plans

## Slide 3: The Local Time Base

## Slide 4: GNSS/UTC
Thanks to the close and fruitful collaboration with SYRTE (https://syrte.obspm.fr) colleagues we are working to define the architecture most suitable for HK.
GNSS receiver
Time distribution
Atomic
clock

## Slide 5: GNSS/UTC – Key components
Atomic Clock
Multi GNSS receiver and Antenna
Distribution system between Atomic Clock and GNSS receiver
Software correction for UTC correlation (if needed)
GNSS receiver
Time distribution
Atomic
clock

## Slide 6: Atomic Clock
The atomic clock is the foundation of the local time base
Needs to be as stable as possible
A good tradeoff between cost and performance could be a “Passive Hydrogen Maser”
  Frequency stability: 5-13s @ 1s, 4-15s @ 1day
  Jitter equivalent: 0.5 ps on RF signals, <40 ps on PPS
  Frequency Drift: 1-15s per 1day (many 1-13s in a year)
The main problem of this kind of atomic clocks is the medium-long term frequency drift
(can be mitigated by the GNSS receiver)
GNSS receiver
Time distribution
Atomic
clock

## Slide 7: Multi GNSS Receiver and Antenna
The GNSS receiver is driven by the atomic clock to enhance stability.
The performances are heavily dependent by the antenna field of view (site orography).
The less satellites are available the less precision is achieved (position and corrections).
A multi GNSS receiver provides a larger satellites catalog (not only GPS but also GALILEO and QZSS/ Michibiki (みちびき))
A common view technique could be developed to “trigger” the far detector when the beam is active
A mobile system is needed to study the orography (before start) and check the ”resident” system (every 2/3 years)
GNSS receiver
Time distribution
Atomic
clock
The GNSS receiver is needed to:
  accord the local base to UTC
  Correct the medium/long term drifts of the atomic clock

## Slide 8: Summary and next steps
We have purchased a Septentrio PolaRX5TR multi GNSS receiver and an antenna.
We’ll characterize the system against a “level 1 UTC station” (SYRTE) as soon the pandemic will allow (delayed).
After a first R&D phase we are planning to test it in situ at Super-Kamiokande site (details under discussion).
To better exploit the Japanese constellation we could benefit of a contact with the Japan institute responsible for UTC (NICT?)
To be done:
  It would be great to exchange ideas with T2K colleagues so we can learn from them and study the compatibility with the JPARC equipment for common view.
  Early access to the HK site to study its characteristics and test the satellite signals.

## Slide 9: The Time distribution Network

## Slide 10: Requirements
Clock to all FE synchronous and phase deterministic with the source.
Jitter at FE < 100 ps.
Bidirectional data exchange link for critical slow control (100 Mbps minimum).
Extra bandwidth can be useful.

## Slide 11: Time Distribution Basic Concepts
Two concepts are subject of our R&D:
  Direct distribution SK-like (see Izumiyama-san talk).
  Clock embedded into data (clock and data recovery concept)
    Custom solution
    White Rabbit

## Slide 12: CERN White Rabbit
A possible architecture
WR switch
FE
…
24
FE
…
24
8*
…
DAQ
8* links
WR switch
FE
…
24
FE
…
24
8*
…
…
8* links
* These numbers depend on the bandwidth
clock distribution edge

## Slide 13: Custom Solution - 1
A possible architecture (same as WR)
Custom Concentrator
FE
…
24
FE
…
24
8*
…
DAQ
1 Gbps Eth
Custom Concentrator
FE
…
24
FE
…
24
8*
…
1 Gbps Eth
* These numbers depend on the bandwidth
…
clock distribution edge

## Slide 14: Custom Solution - 2
A possible architecture (clock fanout)
Custom Concentrator
FE
…
24
FE
…
24
8*
…
DAQ
1 Gbps Eth
Custom Concentrator
FE
…
24
FE
…
24
8*
…
1 Gbps Eth
Alternative CLK fanout
* These numbers depend on the bandwidth
clock distribution edge

## Slide 15: Custom Solution
Possible connection schemes
FE
…
FE
…
16
…
Custom Concentrator
TE0808
16 connections to FE
1 up to 10 Gb Ethernet for slow control
FPGA cost ~1000 euros
Board cost ~1500 euros
Total of 53 concentrator for the Inner detector.
~130 keuros
~10 distributors for OD ~15keuros

## Slide 16: Custom Solution
Possible connection schemes
FE
…
FE
…
32/48
…
Custom Concentrator
Zynq
32/48 connections to FE
2 up to 10 Gb Ethernet to slow control
A7200
A7200
A7200
FPGA cost ~1500 euros
Board cost ~2500 euros
Total of 18 concentrator for the Inner detector.
~75 keuros
~5 distributors for OD ~12keuros

## Slide 17: Board Set for the Custom Solution
This board set will allow to build a time distributor module connected to 6 FEs.
It could be used for the IWCE at CERN.
The firmware development has started.
Trenz TE080
Xilinx Ultrascale+ ZU9EG
Motherboard with 2 SFP+ and RJ45
Expansion with 4 SFP+

## Slide 18: Summary of the Test Campaign

## Slide 19: Test on Custom Solution

## Slide 20: First Jitter Test on Custom Solution
The clock is sent embedded into data from the board on the right and reconstructed by the board on the left
Test done with 2 Xilinx EVB KC705
And the Lecroy scope
Wavepro 760Zi 6 GHz 40Gsps
TX board
RX board
Tx clk
Rx clk

## Slide 21: TX clock Time Interval Error
Time Interval Error 32 ps rms
RMS noise 29.5 ps
Noise at 500 kHz
and its harmonics
Time Domain
Frequency Domain

## Slide 22: RX clock Time Interval Error (time domain)
Time Interval Error 61.5 ps rms
RMS noise 50.1 ps
More noise at 500 kHz and its harmonics
due to DC\DC modulation
Time Domain
Frequency Domain

## Slide 23: Custom solution: Jitter Test on KC705-Waveboard
The TX board is the same KC705 while the RX board is a custom board developed by INFN-Roma for BDX experiment (zynq 7000)
TX board
RX board

## Slide 24: RX clock Time Interval Error (Frequency Domain)
RMS noise 40.6 ps (with KC705 was 50.1)
Still noise at 500 kHz due to the TX side. There are no spurious from the RX board.

## Slide 25: RX clock Time Interval Error Cleaned by PLL
RMS noise 2.4 ps
The received clock is sent to the jitter cleaner PLL SI5345 and its output is measured

## Slide 26: Phase Stability After Reset Test
The phase difference between TX and RX remains constant after each reset
TX clock
RX clock
RX clock after PLL

## Slide 27: Test on White Rabbit

## Slide 28: White Rabbit R&D
PPS total jitter = 17.96 ps
Measured sustained bandwidth > 953Mbps

## Slide 29: White Rabbit R&D
The total jitter on reconstructed clock is 67.26 ps RMS
The biggest part is concentrated between 1 and 10 Hz

## Slide 30: White Rabbit R&D
The total jitter on reconstructed clock is 67.26 ps RMS
The biggest part is concentrated between 1 and 10 Hz

## Slide 31: Conclusions
The R&D program is almost concluded. The proof of concept test has shown that our technology is perfectly fitted for the requirements
The last phase has started (according to the schedule):
  Test our distribution against the FE. Work in progress with QTC and discrete. The other 2 groups are welcome to join
  The final prototype for the custom solution is under design. The distributor EVB delivery is a bit late due to difficulty in producer stock (autonomous drive market?) but still on schedule
  WR switch already available to make the final test
  We should discuss about the time distribution end point in the vessel. An intermediate step could be temporary end-point board
We look forward to start travelling again so we can speed up the integration and final tests

## Slide 32: One Last thing…
We would like to better evaluate the impact of the time distribution on the final charge and time measures to:
  Justify and cross check the actual experimental constraints.
  Have a better understanding of our instrument (before and during operation).
To do that we are thinking to build/use a very simple simulation tool to study that.
All ideas, suggestions and help are very welcome!!!

## Slide 34: GNSS to local time distribution link
The local atomic clock drives the GNSS receiver with 10 MHz and 1 PPS signals.
This link must be synchronous and phase deterministic to have good stability results.
A system able to compensate a very long fiber path is needed (same R&D as the local time distribution).
The final choice will be taken once the antenna and receiver location will be decided.
GNSS receiver
Time distribution
Atomic
clock

## Slide 35: Software correction for UTC correlation
The time base will be correlated to the UTC using the GNSS receiver.
If a great precision is needed software algorithms can be used to correct satellites data using “time products” distributed by the UTC consortium.
These “time products” and therefore the corrected data would be available every week.
The need of this kind of techniques will be defined once we’ll establish the experimental constraints and study the site (antenna position).
GNSS receiver
Time distribution
Atomic
clock

## Slide 36: Cost estimation (updated)
As today the price of the system is:
Atomic clock: 60/70 KEuro
GNSS receiver: 13 Keuro
Antenna + cable: 5 Keuro
Clock distribution system: 6 KEuro
TOTAL: ~100 Keuro
Prices and performances may vary in the future so we’ll buy the equipment just before deployment
GNSS receiver
Time distribution
Atomic
clock

## Slide 37: Direct distribution
Clock is sent directly on one dedicated fiber.
Time information is sent on another fiber in form of counters.
0x0B
0x16
Master
Clk ? MHz*
Data
0x0B
0x16
Data
Clk ? MHz*
0x0B
0x16
Clk ? MHz*
Data
Slave

## Slide 38: Clock embedded into data
Clock, time information and payload data are sent on the same fiber encapsulated in a protocol
0x0B
0x16
Clk 125 MHz*
Data 8bits
1101001011
8b10b
encoder
Serializer
Clk 125 MHz*
Data 10bits
Clk 1.25 GHz*
0110101011
1101001011
0110101011
Serial data 1.25 GHz*
10 possible
phases
0x0B
0x16
Data 8bits
Deserializer
(clock recovery)
8b10b
decoder
The link’s lock is established and the reconstructed clock is generated after power-up or reset
The clock is reconstructed from the data stream but there are 10 possible phases to lock on
*Not in scale
Clk 125 MHz*

## Slide 39: Clock and data recovery - Custom solution
0x0B
0x16
Clk 125 MHz*
Data 8bits
1101001011
8b10b
encoder
Serializer
Clk 125 MHz*
Data 10bits
Clk 1.25 GHz*
0110101011
1101001011
0110101011
Serial data 1.25 GHz*
10 possible
phases
0x0B
0x16
Data 8bits
Deserializer
(clock recovery)
8b10b
decoder
The phase distance is only dependent on the lasers and fiber that connect the master and slave.
Temperature variations are negligible in our case
*Not in scale
Clk 125 MHz*

## Slide 40: Clock and data recovery – white rabbit
0x0B
0x16
Clk 125 MHz*
Data 8bits
1101001011
8b10b
encoder
Serializer
Clk 125 MHz*
Data 10bits
Clk 1.25 GHz*
0110101011
1101001011
0110101011
Serial data 1.25 GHz*
10 possible
phases
0x0B
0x16
Data 8bits
Deserializer
(clock recovery)
8b10b
decoder
The phase distance between the sent and reconstructed clock is continuously compensated
*Not in scale
Clk 125 MHz*

## Slide 41: Clock and data recovery – comparison
Custom Solution
White Rabbit
No external circuit required on FE (only FPGA ser-des).
The phase difference is not compensated.
Custom design (but we have expertise).
Distribution custom boards needed (EVB could be used).
Link speed and the data protocol are flexible
  defined by FPGA configuration.
An external circuit to compensate the phase is required on the FE.
Phase difference is compensated.
Design provided by CERN.
Distribution boards are off-the-shelf (WR switches).
Link protocol is 1 GbE (the data flow can be lower).