## Slide 1: Systematic tests on fast pigtails DWV Test and Budget Resistance Test May, 2021 Monday the 10th

## Slide 2: Dielectric Withstanding Voltage test
Pre-setting of 750V
Observation of the leakage current over 1 minute
Test of the pigtails X -
Time = 2h20
Test of the pigtails X +
Time = 2h
BM25 plug
BM25 plug

## Slide 3: Dielectric Withstanding Voltage test
Results :
Continuity test = validated for each pigtails on the first time
the first thirty seconds, we notice a leakage current around 0.0010 / 0.0020uA which eventually stabilizes and disappears at the end of the minute (between 0 and 0,0003 uA)

## Slide 4: Budget Resistance Test : procedure
Temperature probe
BM25 plug

## Slide 5: Budget Resistance Test : results and notes
Pigtail X- | 
Average | 25,2857576 mΩ
Variance | 0,39512519
Standard deviation | 0,62858984
Maximal Value | 27,12 mΩ
Minimal Value | 24,57 mΩ
Pigtail X+ | 
Average | 24,7248485mΩ
Variance | 0,31658201
Standard deviation | 0,56265621
Maximal Value | 25,99 mΩ
Minimal Value | 23,64 mΩ
- Uniform values on a same set of measure
- Between two sets : some differencies between values of the same DUT

## Slide 6: Budget Resistance Test
Board resistance = 9,36mΩ
Plug resistance = 4mΩ
Flex + Z-ray resistance | X- | X+
Average | 11,92mΩ | 11,36mΩ
Maximal value | 13,76mΩ | 12,63mΩ
Minimal value | 11,21mΩ | 10,28mΩ