## Slide 1: Full System Proposal for the Hyper-Kamiokande Experiment Time Distribution System IN2P3-INFN
stefano russo LPNHE Paris, Fabrizio Ameli INFN Roma HK meeting 30/04/2021

## Slide 2: Motivation
Our time distribution R&D is almost completed: the proof of concept has been established and the integration test with digitizers is ongoing (QTC, discrete and HKROC soon).
At this stage we are ready to present our complete proposal that includes all the parts. This will leave plenty of time for review and comments (if any).

## Slide 3: Full System Block Scheme
Clock Generation &
UTC
Clock Generation &
UTC
Time distribution endpoint
GNSS
Atomic clock
Time quality measure
High speed clock generation
Time Distribution Board
DAQ connection infrastructure
Clock recovery module
Slow control manager
FPGA firmware update module
External lab/
electronics hut
Electronics huts
Frontend vessel

## Slide 4: Full System Block Scheme
Clock Generation &
UTC
Clock Generation &
UTC
Time distribution endpoint
GNSS
Atomic clock
Time quality measure
High speed clock generation
Time Distribution Board
DAQ connection infrastructure
Clock recovery module
Slow control manager
FPGA firmware update module
External lab/
electronics hut
Electronics huts
Frontend vessel

## Slide 5: Clock Generation & UTC
GNSS (x2)
Atomic Clock (x2)
Local time
Freq comparator
Local time/GNSS
Freq comparator
10 MHz and PPS
10 MHz and PPS
Clock conditioning Board
125 MHz and PPS
To TDM
Computing/
Monitoring system
GNSS: Septentrio PolaRx 5 (acquired)
Atomic clock: SRSFS725/ (ordered)
Freq. comparator: Keysigth 53230A (1 acquired)
Clk conditioning board: custom (under design)
Cavern
Time data and UTC
To TDM

## Slide 6: Clock Generation & UTC
The commercial components have been identified and acquired (only redundancies are missing).
The final atomic clock choice will be done after performance evaluation.
The clock conditioning custom board is under design and will be fabricated before the final review.

## Slide 7: Full System Block Scheme
Clock Generation &
UTC
Clock Generation &
UTC
Time distribution endpoint
GNSS
Atomic clock
Time quality measure
High speed clock generation
Time Distribution Board
DAQ connection infrastructure
Clock recovery module
Slow control manager
FPGA firmware update module
External lab/
electronics hut
Electronics huts
Frontend vessel

## Slide 8: Time distribution Module (TDM)
Sync links to the FE
125 MHz and PPS
From Clk Gen
Two possible TDM solutions:
WR and custom
TDM
Ethernet switch to DAQ
Slow control &
Time/UTC data
To DAQ
Sync links to the FE

## Slide 9: Time distribution Module (TDM)
WR solution
In case the collaboration will decide to use WR
our production proposal for the TDM is the WR switch.
It’s a commercial product already used in many
Experiments so its reliability is known.
The actual system is 1Gbps but a new 10 Gbps solution
is under development and the two will be compatible.
16 connections to FE if we decide to have an external fiber redundancy or
8 connections to FE if we decide to have an internal fiber redundancy.
Ready to be reviewed and “produced”

## Slide 10: Time distribution Module (TDM)
CUSTOM solution – 8 links
In case the collaboration will decide to use CUSTOM
our production proposal for the TDM is a Trenz system.
It’s a commercial product ready to be purchased and
based on a ZYNQ 7000. No hardware development
is needed.
8 connections to FE with external fiber redundancy.
Ready to be reviewed and “produced”

## Slide 11: Link Risk mitigation – spare links 2
FE
Time distribution module (TDM)
Two lasers on FE and one on TDM plus an active splitter
Pros:
Reduce the cost/complexity on the TDM side
The FE active link can be selected by software
Cons:
A failure on the TDM laser requires in-person intervention.
Active optical switch
2 fibers (tx, rx)
2 fibers (tx, rx)
2 fibers (tx, rx)

## Slide 12: Link Risk mitigation – spare links 1
FE
Time distribution module (TDM)
Two lasers on both ends to implement a full bidirectional redundancy
Pros:
Two identical links (only one active at a time). High reliability
FE link choice is made with a sw command after power up
Cons:
Expensive.
2 fibers (tx, rx)
2 fibers (tx, rx)

## Slide 13: Time distribution Module (TDM)
In case the collaboration will decide to use CUSTOM
our production proposal for the TDM with 8 redundant links is based on the custom board.
The 8 link prototype is ready to be reviewed and only a small modification is required to add redundant optical ser-des.
8 connections to FE with internal fiber redundancy.
Ready to be reviewed
CUSTOM solution – 8 links redundant

## Slide 14: Time distribution Module (TDM)
In case the we go for external redundancy we can consider 16 link per TDM
Our is ready for the final TDM review
Numerology
 | total number of PMTs | PMT per FE | Total number of FE (Time distribution nodes) | Number of nodes per distributor | Number of distributors
outer detector | 10 000 | 72 | 139 | 8 | 18
Inner detector | 20 000 | 24 | 833 | 8 | 105
MultiPMT | 5 000 | 24 | 208 | 8 | 27
 |  | total FE | 1 181 | total TDM | 150

## Slide 15: Full System Block Scheme
Clock Generation &
UTC
Clock Generation &
UTC
Time distribution endpoint
GNSS
Atomic clock
Time quality measure
High speed clock generation
Time Distribution Board
DAQ connection infrastructure
Clock recovery module
Slow control manager
FPGA firmware update module
External lab/
electronics hut
Electronics huts
Frontend vessel

## Slide 16: Time distribution Endpoint (TDE) preferred solution
Sync link from TDM
As already discussed our preferred solution is to integrate the TDE in the concentrator or the digitizer (if concentrator is not needed) to enhance the reliability and the efficiency
Some consensus is already forming on this idea
Concentrator/digitizer
+
Time Distribution Endpoint
Digitizer
Eth link from DAQ
Slow control data

## Slide 17: Time distribution Endpoint (TDE) Alternative solution
Sync link from TDM
If a digitizer needs a concentrator or the collaboration decides to have separated boards
We have already a developed solution and we are ready to support that
Time Distribution Endpoint
Digitizer
Eth link from DAQ
Slow control data
Concentrator/digitizer
Slow control data

## Slide 18: Time distribution Endpoint (TDE) Alternative solution board
This board is ready to be reviewed and integrated as final prototype
If accepted for final production, a small modification will be needed to host 2 lasers

## Slide 19: Time distribution Endpoint (TDE) final considerations
The time distribution group will support whatever decision will be taken from the collaboration (both for ID, OD):
  In case of integrated solution we’ll support (and pay)
  Lasers, PLL, firmware IP etc. in case of single board.
  In case of 2 boards solution we’ll support (and pay)
  The full board

## Slide 20: Time distribution on IWCD and TE
Our group has offered a contribution also on the IWCD that has been accepted so the same proposal will be implemented on the IWCD and tested during the test experiment at CERN.
This option will be highly beneficial for the FD since it will develop good synergies:
The mPMTs will be ready to use our time distribution system.
The MCC (concentrator board) will host the same time distribution technology. (The integration on the same board is under discussion).
The test experiment will provide an early verification of the proposed design collecting real data.

## Slide 21: Time distribution system total envisioned cost
Including the production and purchase of the described components we estimate a total contribution of 1M Euros.
This is to be considered only related to the time distribution system. The French digitizer contribution is not included.

## Slide 22: Time Distribution System conclusions
We have presented a full proposal for the time distribution system
We think thay the proposal is mature enough to be reviewed.
This will leave plenty of time to address comments and questions but we would like to start this process rather soon to be ready for the final review.