## Slide 1: High-resolution calorimetry for the FCC: Motivations, possibilities and exploration for French involvement
Suzanne GASCON-SHOTKIN
Reunion FCC-Contacts
March 19, 2021 updated April 30, 2021
Remerciements: R. Aleksan, E. Auffray-Hillemanns, C. Dujardin, A. Iyer, K. Lebbou, M.T. Lucchini, C. Tully

## Slide 2
The physics case for a high-resolution calorimeter for FCC (-ee): Measurements
2
What’s behind it: Pairing of photons to accurately reconstruct p0
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021
R. Aleksan, FCC-France Jan 2021
M.T, Lucchini 4th FCC Workshop, Nov 2020
Study of CP with
multiple-neutral modes
High-resolution calorimeter needed to
see signal

## Slide 3
The physics case for a high-resolution calorimeter for FCC (-ee): Searches
3
What’s behind it: Brem recovery enabling Zee to achieve 80% of Zmumu resolution
R. Aleksan, FCC-Physics March 15 2021
M.T, Lucchini 4th FCC Workshop, Nov 2020
Low-mass ALPs : Poor recoil mass resolution could fake a signal
PNGB close in mass to Z (background from ee fakes)
A. Iyer, FCC-France Jan 2021
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021
Notes: .

## Slide 4
Improving the DR concept with a crystal or crystal-fiber ECAL (context: IDEA)
4
M.T, Lucchini 4th FCC Workshop, Nov 2020
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021

## Slide 5
Improving the DR concept with a crystal or crystal-fiber ECAL (context: IDEA)
5
M.T, Lucchini 4th FCC Workshop, Nov 2020
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021

## Slide 6
Improving the DR concept with a crystal or crystal-fiber ECAL: some options
6
Replace bulk crystals with crystal fibers for one or both ECAL layers. Advantages:
  Much higher transverse granularity possible (almost 1 order of magnitude: O(cm) vs O(mm))
  Dual-readout possible with ‘panachage’ of Cerenkov-emitting and scintillating fibers (Dual emission also possible for bulk, R&D ongoing to study best way to separate 2 components either through emission or timing separation) or with doped plastic fibers with dual emission media not dense enough for homogenous calorimeter
  Enables high-precision (10s of ps) timing while conserving excellent stochastic term (~bulk)~3%/sqrt(E) typical of homogeneous ECALs (R0, X0 material-dependent only)
  SiPM or PMT readout, limited degradation of resolution (see later)
  Mechanical ‘alveolar’ structure would have to be developed
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021
Crystal fibers developed in Crystal Clear Collaboration (see later), ‘bundle’ concept for illustration purposes only
PWO from CMS ECAL

## Slide 7
Improving the DR concept with a crystal or crystal-fiber ECAL: Readout with SiPMs
7
M.T, Lucchini 4th FCC Workshop, Nov 2020
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021

## Slide 8
Improving the DR concept with a crystal or crystal-fiber ECAL: Readout with SiPMs
8
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021
M.T, Lucchini IAS2021, Jan 2021

## Slide 9
R&D Efforts at CERN and in France
9
Dr. Etiennette AUFFRAY-HILLEMANNS (Senior physicist, CERN): section leader of EP-CMX-Detector Applications Group and spokesperson Crystal Clear Collaboration (RD18)
E. Auffray-Hillemanns, FCC-Physics March 15 2021+ private communication
R&D in CERN EP-RD WG3 calorimetry for LHCb calorimeter phase II upgrade
Good separation of
Scintillation & Cerenkov
Cerenkov
(LuAG)
Scintillation (LuAG:Ce)
Beam
Dual Readout developments
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021
Simulation,

## Slide 10
R&D Efforts at CERN and in France
10
Institut Lumiere-Matiere (UMR 5306, UCBL-CNRS), Luminescence group: Dr. Kheirreddine LEBBOU (DR), responsible for Crystal Growth activity, and Prof. C. DUJARDIN, responsible for Scintillators & Phosphors characterisation activity
Cutting-edge research in bulk crystal, crystal fiber and nanomaterial scintillator production and characterization, large-scale fiber production capabilities with French industrial partners.
Historical collaboration within Crystal Clear Collaboration, most recenty on DR and SPACAL developments, ANR INFINHI (2010-2014) + ScintLab’ IRP Laureate (2020-2025)
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021

## Slide 11
Going forward: Possible FR participations
11
Historically much expertise in certain French HEP labs in R&D, production test and operation of large homogeneous high-resolution calorimeters: (L3 BGO, CMS PbWO4….)
  IP2I: Development and characterization of photodetection devices and readout electronics (including ASICs)
  LLR: Development of mechanical structures and thermal sensors
  CEA IRFU: Development of sophisticated crystal transparency monitoring systems with lasers
Already a strong history of collaboration with E. Auffray-Hillemanns (CERN-EP-CMX-DA group) on CMS and within Crystal Clear Collaboration (interest in timing from CCC member C.Morel (CPPM))
could join with:
ILM (UMR 5306, UCBL-CNRS), Luminescence group: C. Dujardin and K.
Lebbou, a unique national resource, very interested in participating (invitation wkshp)
Discussions with consequential US community (colleagues from L3/CMS): ‘CALVISION’ Consortium DoE proposal (CALorimetry using cerenkoV and Inorganic Scintillation InnOvatioN)
Note IHEP group from Beijing (mostly working on bulk crystals currently)
S. GASCON-SHOTKIN FCC-Contacts 19/3/2021