## Slide 1: Development of the Electronics and Time Synchronization for Hyper-Kamiokande
stefano russo
2021 Joint Workshop of TYL/FJPPL and FKPPL
11/05/2021
IN2P3, CEA, ICRR, The Tokyo University

## Slide 2: Neutrino Research Motivations
Neutrino’s secrets are gradually revealed.
1998 Discovery of non-zero neutrino mass @ Super-Kamiokande
2011 All three neutrinos are mixing each other.
However, there is a lot of questions still open:
We still don’t know which neutrino is heaviest (mass hierarchy problem).
We don’t know whether neutrino and anti-neutrino oscillations are different (CP violation).
CP violation may be related to the origin of the matter dominant universe.
Neutrinos are also an excellent astrophysical probe to “see” very far events.

## Slide 3
Hyper-Kamiokande physics program
Atmospheric neutrino
Neutrino mass hierarchy
Accelerator neutrinos
CP violation
Solar neutrinos
Interior of the sun
Supernova neutrinos
Evolution of the universe
Proton decay
Grand Unification

## Slide 4: Hyper-Kamiokande
Start operation in 2027
Hyper-K
detection efficiency and timing resolution

## Slide 5: Hyper-K Electronics and Synchronization System
The total number of PMTs is up to 50.000 read with more than 2.000 Front-End board.
Hyper-K is expected to be operated for >20 yrs. Long term stability and durability are essential.
Events are reconstructed from Cherenkov ring by means of PMTs. Time synchronization and digitization are essential.
This development group is presenting the whole chain.

## Slide 6: Time Distribution Full System Block Scheme
Proof of concept established, requirements meet, prototypes under development
Total Jitter 2.4 ps

## Slide 7: First Integration Test France-Japan joint effort
Test still ongoing total Jitter measure coming soon

## Slide 10: Conclusions
IN2P3, CEA and University of Tokyo have established a very strong collaboration in spite of very difficult working conditions (pandemic).
The work is progressing following the plans and great results have already been achieved.
We look forward to restart traveling to speed-up even more our development
and integrated tests.

## Slide 11: Backup

## Slide 13: The Local Time Base
This study in collaboration with SYRTE Lab, part of the Paris Observatory (https://syrte.obspm.fr)

## Slide 14: GNSS/UTC – Key components
Atomic Clock
Multi GNSS receiver and Antenna
Distribution system between Atomic Clock and GNSS receiver
Software correction for UTC correlation
GNSS receiver
Time distribution
Atomic
clock

## Slide 15: The Time distribution Network

## Slide 16: Requirements
Clock to all FE synchronous and phase deterministic with the source.
Jitter at FE < 100 ps.
Bidirectional data exchange link for critical slow control (100 Mbps minimum).
Extra bandwidth can be useful.

## Slide 17: Time Distribution Basic Concepts
Two concepts are subject of our R&D:
  Direct distribution SK-like.
  Clock embedded into data (clock and data recovery concept)
    Custom solution
    White Rabbit

## Slide 18: Direct distribution
Clock is sent directly on one dedicated fiber.
Time information is sent on another fiber in form of counters.
0x0B
0x16
Master
Clk ? MHz*
Data
0x0B
0x16
Data
Clk ? MHz*
0x0B
0x16
Clk ? MHz*
Data
Slave

## Slide 19: Clock and data recovery
0x0B
0x16
Clk 125 MHz*
Data 8bits
1101001011
8b10b
encoder
Serializer
Clk 125 MHz*
Data 10bits
Clk 1.25 GHz*
0110101011
1101001011
0110101011
Serial data 1.25 GHz*
10 possible
phases
0x0B
0x16
Data 8bits
Deserializer
(clock recovery)
8b10b
decoder
The phase distance is only dependent on the lasers and fiber that connect the master and slave.
Temperature variations are negligible in our case
*Not in scale
Clk 125 MHz*
Custom solution
White Rabbit solution
The phase distance between the sent and reconstructed clock is continuously compensated

## Slide 20: CERN White Rabbit
A possible architecture
WR switch
FE
…
24
FE
…
24
14
…
DAQ
2 Gbps Eth links
WR switch
FE
…
24
FE
…
24
14
…
…
2 Gbps Eth links
clock distribution edge

## Slide 21: Custom Solution - 1
A possible architecture (same as WR)
Custom Concentrator
FE
…
24
FE
…
24
14
…
DAQ
2 Gbps Eth links
Custom Concentrator
FE
…
24
FE
…
24
14
…
2 Gbps Eth links
…
clock distribution edge

## Slide 22: First R&D results

## Slide 23: First Jitter Test on Custom Solution
The clock is sent embedded into data from the board on the right and reconstructed by the board on the left
Test done with 2 Xilinx EVB KC705
And the Lecroy scope
Wavepro 760Zi 6 GHz 40Gsps
TX board
RX board
Tx clk
Rx clk

## Slide 24: TX clock Time Interval Error
Time Interval Error 32 ps rms
RMS noise 29.5 ps
Noise at 500 kHz
and its harmonics
Time Domain
Frequency Domain

## Slide 25: RX clock Time Interval Error (time domain)
Time Interval Error 61.5 ps rms
RMS noise 50.1 ps
More noise at 500 kHz and its harmonics
due to DC\DC modulation
Time Domain
Frequency Domain

## Slide 26: Custom solution: Jitter Test on KC705-Waveboard
The TX board is the same KC705 while the RX board is a custom board developed by INFN-Roma for BDX experiment (zynq 7000)
TX board
RX board

## Slide 27: RX clock Time Interval Error (Frequency Domain)
RMS noise 40.6 ps (with KC705 was 50.1)
Still noise at 500 kHz due to the TX side. There are no spurious from the RX board.

## Slide 28: RX clock Time Interval Error Cleaned by PLL
RMS noise 2.4 ps
The received clock is sent to the jitter cleaner PLL SI5345 and its output is measured