## Slide 1: ROC ASICs for timing at OMEGA RD51 workshop 15 jun 2021
Christophe de La Taille
OMEGA CNRS/IN2P3 Ecole Polytechnique

## Slide 2: Timing optimization : common view
Jitter due to electronics noise:
also presented as j = tr / (S/N)
dV/dt prop to BW, N prop to √ BW => jitter prop to 1/√BW
« the faster the amplifier, the better the jitter ? »
« High speed preamps need to be low impedance (50 Ω or less) ? »
  minimize RPA : small time constant RPA.Cd « Minimize « charge time transfer »
NB : tr = t10-90% = 2.2 tau.
f-3dB = 1/2πtau = 0. 35 / t10-90
f-3dB = 1 GHz <-> t10-90% = 300 ps
1 ps = 300 µm in vaccum

## Slide 3: Detector impedance and input voltage
1 GHz, Cd=few tens of pF, input signal width <1ns
Cd>1 pF, Zs@1GHz dominated by Cd
Rise time: tr= td when td<< RS Cd and tr= RS Cd when td>> RS Cd
1pF
10 pF
100pF
50Ω
1 GHz
At HF : difficult to beat the capacitance => signal integrated on Cd

## Slide 4: Examples of pulse shapes
SiPM pulse : Q=160 fC, Cd=100 pF, L=0-10 nH, RPA=5-50 Ω
Sensitivity to parasitic inductance
Choice of RPA : decay time, stability
Small RPA not necessarily the fastest
Convolve with current shape… (here delta)
RC
L/R
Q/Cd
C=100 pF
L=10 nH
R=50 Ω
C=100 pF
L=10 nH
R=5 Ω

## Slide 5: High speed amplifiers
Response to very short pulse
Broadband : voltage sensitive
  Zin=Rs (50 Ohm)
  Vin = Q/Cin
  =
Transimpedance
  Zin ~ Zf/G ~ 1/gm
Same response at High Frequency
For highest speed : go to broadband. Faster, less stability issues

## Slide 6: Signal and noise in Broadband amplifiers
Jitter is given by :
Optimum value: t10-90_PA= td (current duration)
Gives ps/fC as scales with 1/Qin : « factor of merit »
Electronics noise en given by the input transistor transconductance gm:
Jitter optimum is rather shallow with preamp risetime
But noise and minimum threshold goes up quickly with speed (as sqrt)
Dominated by sensor
Electronics only gives en
Cd: detector capacitance
t 10_10_PA : rise time of the PA
td= detector current duration
e n preamp noise density

## Slide 7: OMEGA timing chips
See also presentation by Stéphane Callier on Thursday (Hardroc et al.)

## Slide 8: PETIROC2A
Detector Read-Out | SiPM, SiPM array
Number of Channels | 32
Signal Polarity | Positive or Negative
Sensitivity | Trigger on first photo-electron
Timing Resolution | ~ 35 ps FWHM in analogue mode (2pe injected) - ~ 100 ps FWHM with internal TDC
Dynamic Range | 3000 photo-electrons (106 SIPM gain), Integral Non Linearity: 1% up to 2500 ph-e
Packaging & Dimension | TQFP160 – TFBGA353
SiPM read-out for time-of-flight PET
SiGe 350 nm

## Slide 9: Petiroc2A bandwidth measurement
Preamp + discriminator bandwidth
reconstruction of pulse by discriminator
tr 10%-90% = 300 ps,
BW = 0.35 / tr ~ 0.9 GHz
can also use BW = 0.1 / (t50% - t10%)

## Slide 10: SPTR measurement : Petiroc2A trigger outputs
Source : Laser
SiPM : Various model (FBK, Hamamatsu, Sensl)
HV : Various value
FBK NUV 1x1 mm2 : 90.7 ps FWHM
1.3x1.3mm2 MPPC
1x1mm2 NUV
3x3mm2 JDO
90 ps
3x3mm2 MPPC
SPTR : 90 ps FWHM (40 ps rms)

## Slide 11: Petiroc2 for CMS RPC readout [I. Laktineh et al.]
.

## Slide 12: LIROC : SiPM read-out for Lidar
Collaborative design between Weeroc & Omega
Funding from ATTRACT EU H2020 Research & Innovation Program
SiPM read-out for LIDAR
TSMC 130 nm

## Slide 13: Parameters & Performances
Detector Read-Out | SiPM, SiPM array
Number of Channels | 64
Signal Polarity | Positive or Negative (selectable ASIC-wise)
Sensitivity | Trigger on 1/3 of photo-electron
Timing Resolution | Better than 20 ps FWHM on single photo-electron Better than 5ns double-peak separation on single photo-electron
Dynamic Range | Over 100MHz photon counting rate
Packaging & Dimension | BGA 20x20 mm2 Flip-Chip low inductance packaging technology
Power Consumption | 210mW – Supply voltage : 1.2 V
Inputs | 64 analogue inputs with independent SiPM HV adjustments
Outputs | 64 low-common-mode LVDS triggers (CLPS) – compatible with CERN picoTDC and all LVDS FPGA I/Os
Internal Programmable Features (I2C) | 64 HV adjustment for SiPM (64 x 6 bit), trigger threshold programming (10bits), 64 x 7 bit channel-wise threshold adjustment, ASIC-wise polarity selector, preamp pole-zero cancellation adjustment, individual trigger masking and cell powering.

## Slide 14: Jitter and timewalk
Chart: Jitter - Threshold 1/4 Photoelectron (40fC)
| 39.81071705534972 | 44.668359215096316 | 50.118723362727224 | 56.234132519034908 | 63.095734448019329 | 70.794578438413794 | 79.432823472428154 | 89.125093813374548 | 100 | 112.20184543019636 | 125.89254117941672 | 141.25375446227542 | 158.48931924611136 | 177.82794100389231 | 199.52623149688799 | 223.87211385683395
stev(ps) | 114 | 78 | 38 | 25 | 18 | 14.4 | 13 | 12 | 11 | 10 | 10 | 9 | 10 | 9 | 9 | 9
1 photoelectron - Gain 106
Threshold: 40 fC
Metrology chain limit. 6.2ps rms
Chart: Timewalk - Threshold 1/4 Photoelectron (40fC)
| 39.81071705534972 | 44.668359215096316 | 50.118723362727224 | 56.234132519034908 | 63.095734448019329 | 70.794578438413794 | 79.432823472428154 | 89.125093813374548 | 100 | 112.20184543019636 | 125.89254117941672 | 141.25375446227542 | 158.48931924611136 | 177.82794100389231 | 199.52623149688799 | 223.87211385683395
mean(ns) | 26.22 | 26.09 | 25.94 | 25.85 | 25.76 | 25.7 | 25.63 | 25.57 | 25.52 | 25.48 | 25.44 | 25.4 | 25.35 | 25.36 | 25.3 | 25.4
TW : 800 ps

## Slide 15: Time Over Threshold – Measuring amplitude
Chart: Time over Threshold
| 1 | 2 | 3 | 4 | 5 | 10 | 15 | 20
ToT(ns) Positive injection | 3.85 | 5.62 | 6.47 | 7.29 | 7.65 | 8.81 | 9.23 | 9.7
ToT (ns)Negative injection | 3.38 | 5.17 | 6.38 | 7.25 | 7.78 | 8.99 | 9.33 | 9.53
Trade-off beetween double peak separation (see consecutive photons) and time over threshold. Tuneable.
Optimized for double-peak separation in that measurement (3ns separation measured)

## Slide 16: ALTIROC : ATLAS LGAD ReadOut Chip for HGTD
ALTIROC0 (2017) : contains only PA + discriminator – for 2x2 1x1 mm2 sensors
  4 channels VPA and 4 channels TZ analog readout optimized for Cd=2pF
  Bandwidth tunable (0.3-0.8 GHz)
  Power : 2 mW/ch TSMC 130 nm
ALTIROC1 (2018) : 5x5 complete readout channels (PA, discri, TDC, SRAM) to readout 1.3 x 1.3 mm2 LGAD pixels , 15 channels with VPA, 10 with Transimpedance amplifier (TZ)
ALTIROC2 (2021) : 15x15 final size and functionnality
Altiroc1 tesboard
~ 7,7 mm
2 mm
2 mm
Altiroc0
C. de La Taille RD51 workshop 15 jun 2021

## Slide 17: ALTIROC0 measurements
VPA
TZ
VPA
TZ
Testbench (left) and testbeam (right) measurements
VPA
VPA
VPA
30 % improvement after TW correction
Jitter around 35 ps
ALTIROC0_V2
Time resolution of a 2x2 x1x1 mm2 LGAD array bump bonded on an Altiroc0 ASIC as a function of the discri threshold (DAC Units) before (black points) and after TW correction (red points)
C. de La Taille RD51 workshop 15 jun 2021

## Slide 18: ALTIROC1
~ 8 mm
Altiroc1 layout
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
VPA
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
TZ
ZOOM of one pixel
VPA: Voltage preamp
TZ: Transimpedance preamp
C. de La Taille RD51 workshop 15 jun 2021

## Slide 19: ALTIROC1_V2 - TDC performance
<TOA> vs delay
LSB /<LSB> vs channel
<TOA_LSB> = 22.5 ps
<TOT_LSB> = 171 ps
ASIC + sensor
TOA_LSB and TOT_LSB can be adjusted to 20 ps and to 160 ps (respectively) using per channel Slow Control parameters
Some of the DLLs don’t lock properly => use of external R to set control voltages of the TDC
<TOA> vs delay: Small discontinuities due to LSB bin size that can be calibrated with Random Programmable Generator
ASIC + sensor
=> Altiroc1_V3: integrates a Random Programmable Generator
Specifications:
TOA: 20 ps ± 10%, range 2.5 ns
Specifications:
TOT: 160 ps ± 10%, range 20 ns

## Slide 20: ALTIROC1_V2- performance at system level
ALTIROC1_V2
+ LGAD sensor
e ~100% for ASIC alone and ASIC+Sensor at 4fC
Jitter ~ 25 ps (55 ps) for ASIC alone (ASIC+sensor) at 4fC
Estimated jitter using LGAD signal,
using calibration data and simulation
LGAD input
Dirac input
out_preamp simulation
Specifications:
Minimum Vth <2 fC

## Slide 21: HGCROC2 : CMS HGCAL readout chip
Overall chip divided in two symmetrical parts
1 half is made of:
  39 channels: 18 ch, CM0, Calib, CM1, 18 ch (78 channels in total)
  Bandgap, voltage reference close to the edge
  Bias, ADC reference, Master TDC in the middle
  Main digital block and 3 differential outputs (2x Trigger, 1x Data)
Measurements
Charge
  ADC (AGH): peak measurement, 10 bits @ 40 MHz, dynamic range defined by preamplifier gain
  TDC (IRFU): TOT (Time over Threshold), 12 bits (LSB = 50ps)
  ADC: 0.4 fC resolution. TOT: 2.5 fC resolution
Time
  TDC (IRFU): TOA (Time of Arrival), 10 bits (LSB = 25ps)
Two data flows
DAQ path
  512 depth DRAM (CERN), circular buffer
  Store the ADC, TOT and TOA data
  2 DAQ 1.28 Gbps links
Trigger path
  Sum of 4 (9) channels, linearization, compression over 7 bits
  4 Trigger 1.28 Gbps links
Control
Fast commands
  320 MHz clock and 320 MHz commands
  A 40 MHz extracted, 5 implemented fast commands
I2C protocol for slow control
Ancillary blocks
Bandgap (CERN)
10-bits DAC for reference setting
11-bits Calibration DAC for characterization and calibration
PLL (IRFU)
Adjustable phase for mixed domain

## Slide 22: Test boards and signal
HD BGA board
Flip-Chip on mezzanine
HD BGA on mezzanine
Version 2
125 fC
Gain = ~0,18 fC/ADCU
Separates effects from the BGA substrate and PCB
Rising time (10-90 %): ~ 15 ns
Falling time (10-90 %): ~ 30 ns, < 20 % at BX+1
Good uniformity over the channels
Digital 40 MHz clock coupling on the analog signal on the HD BGA board: digital noise (slide 11)

## Slide 23: Charge ADC (0 – 160 fC)
Two 10b-DAC to globally set the pedestal to a wanted level
5b-DAC to reduce dispersion per channel
  From ~ 100 ADCu dispersion to ~ 5 ADCu
Good linearity within +/- 0.5%
  1.6 fC (~1 MIP) linearity for the typical gain
~ 0.3 fC resolution with 50 pF input capacitor
~ 0.3 fC

## Slide 24: Charge: TOT range (160 fC – 10 pC)
Charge measurement from TOT when preamplifier saturates
160 fC to 10 pC (for the typical preamplifier gain)
  12 bits over 200 ns
  50 ps binning
Linearity
  < 2% linearity
  Better with input capacitor (as expected)
  Small residual wiggles on TOT due to digital noise on preamplifier input
Resolution around the LSB (~ 50 ps)
  Some peaks due to outliers (understood and fixed)
1 LSB
150 ns
0,1 %

## Slide 25: Noise
Measured noise with 50 pF input cap = 0.3 fC (~ 2000 electrons) (0.7 nV / √Hz)
Very low correlated noise contribution: ~ 0.1
Coherent noise extracted by comparing direct and alternate sums on n channels (n = 72):
;
  Incoherent noise
  Coherent noise
Correlation matrix
Equivalent Noise Charge wrt. sensor capacitance
Coherent vs. incoherent noise
IN: 0.3 fC
CN: 0.06 fC

## Slide 26: Timing performance
Minimum Charge providing a TOA measurement is 20 fC, limited by the digital coupling
: 2.5 ns w/o detector cap., ~ 5 ns with 50 pF input capacitor
Time Walk
Timing jitter
20 fC

## Slide 27: Timing performance – S-curve
S-curves show the ToA efficiency as a function of the charge
Minimum charge providing ToA events is 20 fC
  Limited by the digital coupling

## Slide 28: Analog Channel Overview: SiPM version
H2GCROC2 (SiPM version) = HGCROC2 + input current conveyor
  Heidelberg university design
2.5 V input stage for overvoltage adjustment

## Slide 29: SiPM version measurements
H2GCROC2 measurements:
Good shape as expected
Adjustable conveyor gain
Dynamic range as expected: TOT (12bit) – 300pC aimed
Single-Photon Spectra (SPS):
  4V overvoltage, conveyor gain = 12
  Gain: ~ 10 ADC counts
ped.
1 pe.
2 pe.
3 pe.
~10 ADC tics

## Slide 30: Conclusion
Lots of interest for ~10 ps timing resolution
Most of our work (so far) focused on Si, LGADs and SiPMs
Studies of PETIROC and LIROC with MGRPCs by Imad et al.

## Slide 31: backup

## Slide 32: voltage vs current sensitive
Example : 10 fC – 1 ns => i = 10 uA
signal from 1-10-100 pF sensors into 50 Ω (current) or 50k (voltage) preamp
C=100 pF
C=10 pF
C=1 pF
100 µV
1 ns
1 mV
10 mV

## Slide 33: Signal : detector current
PN diode w =200µm
Very short rise time : tr~10ps
Relatively long «drift time» : td~2ns
I holes
I SiPM
td=100 ps
tr
SiPM detector (10pe-)
very short rise time : tr~10 ps
Short duration : td~100ps),
  3600x22.5fF (80 pF), Gain=1M, Rquench=125K, Cquench=5fF, CL=10pF
© Harmut Sadrozinski (Santa Cruz) “the beautiful risetime of the detector is spoilt by the electronics”
LGAD sensor w =50µm
rise time : tr~500ps
Decay time» : td~700ps

## Slide 34: Examples [measurements from testbeam studies]
NA62 tracker : PIN diode thickness 300 µm A=0.09 mm²
  Cd = 0.1 pF en = 11 nV/√Hz td = 3 ns σ = 60 ps/Q(fC)
  1 MIP = 3 fC => σ = 20 ps/#MIP (~60-200 ps measured)
CMS HGCAL : PIN diode thickness 300 µm A=25 mm²
  Cd = 8 pF en = 1 nV/√Hz td = 3 ns σ = 420 ps/Q(fC)
  1 MIP = 3.8 fC => σ = 110 ps/#MIP (~200 ps measured)
ATLAS HGTD : LGAD diode thickness 50 µm A= 2 mm² G = 10
  Cd = 2 pF en = 2 nV/√Hz td = 0.5 ns σ = 50 ps/Q(fC)
  1 MIP = 5 fC (G=10) => σ = 10 ps/#MIP (~40 ps measured)
SiPM G = 1E6
  Cd = 300 pF en = 1 nV/√Hz td = 100 ps σ = 3 ns/Q(fC)
  1 pe = 160 fC => σ = 20 ps/#pe (~60 ps measured)
SiGe preamp © N. Spencer (UCSC)

## Slide 35: Digital noise
A 40 MHz modulation is visible on the analog signals
  Comes from digital current spikes on preamp ground node
    10 µV on ground give 1 ADC count
  BGA worse than flip chip
  BGA substrate optimised, improvements made by optimizing decoupling & the pcb ground impedance
  Further improved by removing decoupling caps !
    Reduces digital current spikes (inductance)
This provides recommendations for the Hexaboard design
  Very delicate design!
[ns]
[ns]