## Slide 1
OMEGA ROC ASICs : Integrated Readout Electonics for Gazeous detectors
Salleh AHMAD, Stéphane CALLIER, Selma CONFORTI DI LORENZO,
Frederic DULUCQ, Julien FLEURY, Christophe de LA TAILLE, Gisèle MARTIN-CHASSARD, Ludovic RAUX, Nathalie SEGUIN-MOREAU, Damien THIENPONT
OMEGA microelectronics
Ecole Polytechnique & CNRS IN2P3
http://omega.in2p3.fr
& WEEROC SAS
http://weeroc.com
Notes: I will talk about SPACIROC asic
SPACIROC stands for Spatial…….

## Slide 2: OMEGA ASICs : manufactured & used ASICs
AMS 350nm SiGe
HARDROC
SPIROC
MICROROC
HGCROC
MAROC3
PETIROC
ALTIROC
SKIROC2_CMS
SPACIROC
CITIROC
TRIROC
CATIROC
2021
2006
TSMC 130nm
SKIROC

## Slide 3: HARDROC2 for RPC readout
HARDROC2: 64 channels (RPC DHCAL)
  preamp + shaper+ 3 discri (semi digital readout)
  Auto trigger on 10fC up to 20 pC
  five 0.5 Kbytes memories to store 127 events
  Full power pulsing => 7.5 µW/ch
  Fully integrated ILC sequential readout
  10 000 chips produced to equip 400 000 ch
  SDHCAL technological proto with 40 layers (5760 HR2 chips) built in 2010-2011.
    Successful TB in 2012 : 40 layers in AutoTrigger with Power Pulsing mode
      High Granularity ( PAD size : 1 cm x 1 cm )
@IPNL
Cosmic hadronic shower
Blue : 150 fC
Green : 2 pC
Red : 18 pC
X
Z
Y
Z
X
Y
1 m3 RPC detector, 40 layers
370 000 channels
@IPNL Lyon

## Slide 4: HARDROC3: Simplified schematics
64 channels with current preamplifiers
Trigger less mode (auto trigger 15fC up to 50pC)
Gain correction (max factor 2)
3 shapers + 3 discriminators (encoded in 2 bits for readout)
I2C link with triple voting for Slow Control Parameters
64 Independent channels with zero suppress
Max 8 events / channel with 12-b time stamping
Integrated clock generator: PLL
All bias and reference voltage internal (with power pulsing)
  No decoupling capacitances required on bias and references voltages
Token Ring ReadOut

## Slide 5: Gain correction / Scurves
50% point
± 25fC
Qinj=100fC
50% point
± 5fC
HR2 gain correction
23
FSB0: 5σ noise limit= 15fC
50% trig. Eff. (DAC units) vs Qinj (fC)
ASIC Dynamic range: 15fC - 50pC
HR3

## Slide 6: Zero suppress: Memory mapping
 | HR2 | HR3
1 chn hit | 160 | 48
8 chn hit | 1280 | 272
4 chn hit @ same time | 160 | 144
10 chn hit @ same time | 160 | 336
Chip ID is the first to be outputted during readout (MSB first)
MSB of each word indicates type of data:
  “1”: general data (Hit ch. number and number of events)
  “0”: BCID + encoded data
A parity bit/word
Up to 9232 bits (577x16) during readout
Example of number of bits during readout:

## Slide 7: Power pulsing in HR chips
Power supply | HR3 with LVDS (5M + 40M) µW / channel | HR2 with LVDS (5M + 40M) µW / channel
PowerOnA (Analog) | 1650 | 1325
Only PowerOnDAC | 55 | 50
Only PowerOn D | 725 | 50
Power-On-All | 2430 | 1425
Power-On-All @ 0,5% duty cycle | 12,2 | 7,5
Compared to HR2, HR3 power consumption is higher due to:
  The extended dynamic range (from 15pC to 50pC)
  The integration of the zero suppress algorithm
If the PLL is used, the power consumption is increased by 3% (due to the PLL VCO)
DAC output (Vth)
Trigger
25 µs
PWR ON
HR2
Power pulsing:
  Bandgap + ref Voltages + master I: switched ON/OFF
  Shut down bias currents with vdd always ON
  No decoupling capacitance on bias and voltage references

## Slide 8: MICROROC (GEMROC)
1m² Micromegas detector
144 Microroc : 10 000 channels
@LAPP Annecy
64 channels for µMegas (sDHCAL ILC)
  Very similar to HARDROC except :
    Input (charge) preamp
    Slower shapers (100-150 ns)
    HV Spark protections
  Noise: 0.2fC (Cd=80 pF). Auto trigger on 1fC up to 500fC
  Pulsed power: 10 µW/ch (0.5 % duty cycle)
  4 Micromegas prototypes of 1x1 m2 were constructed in 2011-2012 and tested in particle beams inside the DHCAL steel structure in 2012
  Test Beam :
  Very good performance
  of the electronics
  and detector
  (Threshold set to 1fC)

## Slide 9: MAROC3 : MultiAnode Read-Out Chip
Complete front-end chip for 64 channels multi-anode photomultipliers
  6bit-individual gain correction
  Auto-trigger on 1/3 p.e. at 10 MHz
  12 bit charge output with internal ADC
  SiGe 0.35 µm, 12 mm2, Pd = 5 mW/ch

## Slide 10: MAROC3 performance
Chart: 
| 80 | 100 | 200 | 500 | 1000
 | 36.2 | 33.7 | 30.2 | 27.9 | 26.7
 | 170 | 97 | 60 | 46 | 43
Input charge (fC)
Jitter (ps rms)
Time walk (ns)
Rms = 3.5 fC
Qin = 50 fC = 1/3 pe
Threshold = 50 fC = 1/3 pe
Jitter < 100 ps
crosstalk ~1%
Charge readout 20 pC

## Slide 11: PETIROC2
32 ch SiPM GHz readout ASIC, dual polarity, 100 fC-400 pC, 6 mW/ch
32 trigger outputs and multiplexed data output
Embedded 10-bit ADC and 50 ps TDC
Dual threshold : first photons and energy

## Slide 12: PETIROC2A : SCURVES with and w/o clock
Injection of a step (1mV, 2mV, 3mV, 4mV, 5mV and 10mV)

## Slide 13: PETIROC2A: performance
10%
90%
out_PA (mV)
Time (ps)
Preamp Rise Time reconstruction
300 ps
Jitter (ps)
Vin (mV)
400 ps
TW
Scope measurement
TOT measurement

## Slide 14: PETIROC2: TAC measurement
TAC
Slope dispersion:
~1% rms or 10ps/1ns
or 250ps/25ns
=> Calibration
Intercept dispersion:
~1% rms => Calibration
Non Lin: ~0.25% or ±50ps
Due to digital coupling

## Slide 15: SUMMARY
http://omega.in2p3.fr/
http://www.weeroc.com/

## Slide 16
Notes: I will talk about SPACIROC asic
SPACIROC stands for Spatial…….

## Slide 17: OMEGA ROC chips
Use of Silicon Germanium AMS 0.35 µm BiCMOS technology since 2004
Readout for MaPMT and SiPM for ILC calorimeters and other applications
Very high level of integration : System on Chip (SoC)
HARDROC2
SPIROC2
MAROC3
SPACIROC
SKIROC2
MICROROC1
PARISROC2
http://omega.in2p3.fr
Chip | detector | ch | DR (C)
MAROC | PMT | 64 | -2f-50p
SPIROC | SiPM | 36 | 10f 200p
SKIROC | Si | 64 | 0.3f 10p
HARDROC | RPC | 64 | -2f-50p
PARISROC | PM | 16 | -5f-50p
SPACIROC | PMT | 64 | -5f-15p
EASI/CITIROC | SiPM | 32 | 10f 200p
MICROROC | µMegas | 64 | -0.2f-0.5p
PETIROC | SiPM | 32 | 50f 300p
TRIROC | SiPM | 64 | 50f 300p
GEMROC

## Slide 18: MOS and Bipolar
http://cmp.imag.fr/aboutus/slides/Slides2011/02_Runs_2011.pdf
© K. Torki (CMP)

## Slide 19: SiGe technology
Faster bipolar transistors for RF telecom
  Better mobility and FT
  Better current gain (beta)
  Better Early voltage
  Interesting improvement at low T
  Compact CMOS (0.25 or 0.35µm) for mixed-signal design
© R. Hermel

## Slide 20: Power and speed with SiGe
BJT : best gm /I ratio (1/UT)
  Large transconductance with small devices
Speed goes as FT= gm /2πC
  C~10 fF gm typ mA/V
  FT ~60 GHz for SiGe 0.35µm
  Interesting for fast preamps
Not forgetting 100V Early voltage and matching performance (A~mV*µm)
VBE=VTLn(IC/IS)
Large swing : VCEsat ~3 UT

## Slide 21: Evolution of technologies in practice
Performant design is at transistor level
More and more functions are integrated inside chips (ASICs)
Evolution of technologies make them more and more performant but more and more complex
10 ans d'évolution des spécifications techniques pour la réalisation d' ASIC
G. Deptuch, Fermilab
© G. Deptusch FNAL

## Slide 22
  design groups ≈ 30-40
Design Groups – Current Status
  active designs ≈ 30-40
  Average one design per group
  institutions leading collaborative efforts
  institutions performing R&D on technologies
  One FE-ASIC design currently requires
  2-4 full-time designers and 2-4 years
  average, from concept to ready-for-production
© G.L. de Geronimo (BNL) TIPP2014

## Slide 23: HR3: Analog linearity
FSB0
FSB0: 5σ noise limit= 15 fC
Up to 10 pC
Up to 50 pC
Fast shaper outputs (mV) vs Qinj (fC)
50% trig. Eff. (DAC units) vs Qinj (fC)
Dynamic range: 15fC - 50 pC
FSB1
FSB2

## Slide 24: PETIROC2: efficiency uniformity
Trigger efficiency measurements: Linearity
One 10-bit DAC Unit= 923 µV
10-bit DAC linearity
923µV/DAC code

## Slide 25: PETIROC2: « S-curves »
Trigger efficiency measurements:

## Slide 26: With SiPMs : SPTR [JINST 11 P10016]
SPTR
  FWHM ~200 ps
  Rms ~ 80 ps

## Slide 27: Going to lower SPTR
Expect ~ 20 ps/pe
NINO risetime ~1 ns
Test with PETIROC2 (tr = 300 ps)
  SPTR = 67 ps rms (180 ps FWHM)
Possible effect of stray inductance
Further studies in FAST framework
10%
90%
out_PA (mV)
Time (ps)
Preamp Rise Time reconstruction
300 ps
© J. Fleury TIPP17