## Slide 1: Neutrino CP Violation with the European Spallation Source neutrino Super Beam Marcos Dracos IPHC-Strasbourg
IRN Neutrino meeting December 1-2 2021

## Slide 2: European Spallation Source
under construction phase
(~1.85 B€ facility)
Neutron facility
(equivalent to SNS in the USA)

## Slide 3: Applications of neutrons
Multi-disciplinary science applications
Transmutation of radioactive (waste) material
  Accelerator-driven Systems
Industrial applications:
  materials analysis and non-destructive testing tools in many industries
    heavy mechanical production
    art conservancy
    Medicine
    …
X-Ray Image
Neutron radiograph

## Slide 4: ESS proton linac
The ESS will be a copious source of spallation neutrons.
5 MW average beam power.
125 MW peak power.
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons).
Duty cycle 4%.
2.0 GeV protons
  up to 3.5 GeV with linac upgrades
>2.7x1023 p.o.t/year.
4
8
time (ms)
Brightness (n/cm2/s/sr/Å)
7
5
x1014
UK TS1
128 kW
UK TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
3
4
1
2
6
λ = 1.5 Å
ESS 5 MW
2012 design (TDR)
empty space for energy upgrades

## Slide 5: European Spallation Source
July 2021
European Research Infrastructure Consortium (ERIC) since 2015
target
instruments
utility buildings
linac

## Slide 6: European Spallation Source

## Slide 7: ESS schedule
Linac schedule
Overall schedule

## Slide 8: European Spallation Source as Neutrino Facility for CP violation observation (2nd Oscillation maximum)
νμ→νe

## Slide 9: Oscillation probability (neutrino beams)
"solar"
"atmospheric"
"interference"
matter effect
δCP dependence,
sizable matter effect for long baselines
for antimatter: δCP →-δCP and a→-a
fake matter/antimatter asymetry due to matter effect
Matter-antimatter asymmetry

## Slide 10: δCP and matter-antimatter asymmetry magnitude
(Jarlskog invariant)
Theoretical models predict that if |sinδCP|≳0.7 (45°<δCP<135° or 225°<δCP<315°), this could be enough, under assumptions, to explain the observed asymmetry.
(from the already observed CP violation in the hadronic sector)
(Nucl.Phys.B774:1-52,2007, arXiv:hep-ph/0611338)

## Slide 11: Use all this ESS linac power to go to the second oscillation maximum
but why?

## Slide 12: Neutrino Oscillations with "large" θ13
solar
more sensitivity at 2nd oscillation max.
P(νμ→νe)
L/E
1st oscillation maximum
2nd oscillation maximum
θ13=1º
("small" θ13)
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
(arXiv:1110.4583)
L/E
L/E
solar
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)
(before 2012)
(after 2012)

## Slide 13: Production of a neutrino beam
What can we do with:
5 MW power
2 GeV energy
14 Hz repetition rate
1015 protons/pulse
>2.7x1023 protons/year
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam

## Slide 14: ESSνSB ν energy distribution
at 100 km from the target, per year (in absence of oscillations)
neutrinos
anti-neutrinos
almost pure νμ beam
small νe contamination which could be used to measure νe cross-sections in a near detector
(Nucl. Phys. B 885 (2014) 127)

## Slide 15: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS like Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)
New 20" PMTs with higher QE and cheaper (see JUNO), the detection efficiency will improve the detector performance keeping the price constant, not yet taken into account.

## Slide 16: Neutrinos in the far detector
540 km (2 GeV), 10 years
Below ντ production, almost only QE events, not suffering too much by π0 background.
neutrinos
anti-neutrinos
2 years
8 years
δCP=0

## Slide 17: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.
full coverage of the 2nd oscillation max.

## Slide 18: Required modifications of the ESS accelerator for ESSνSB
Better to go to 2.5 GeV

## Slide 19: ESSνSB Consortium
COST Action EuroNuNet (CA15139): 2016-2020
  https://euronunet.in2p3.fr
  video for scientists: https://www.youtube.com/watch?v=PwzNzLQh-Dw
EU-H2020 Design Study ESSνSB: 2018-2022 (3 months extension due to COVID19)
  https://essnusb.eu
  video for general public: https://www.youtube.com/watch?v=qAnvft0nAlg

## Slide 20: The H2020 ESSνSB Design Study
A H2020 EU Design Study has been submitted March 2017 (Call INFRADEV-01-2017)
Title of Proposal: Discovery and measurement of leptonic CP violation using an intensive neutrino Super Beam generated with the exceptionally powerful ESS linear accelerator.
Duration: 4 years
Total cost: 4.7 M€
EU funding received: 3 M€
15 participating institutions from 11 European countries including CERN and ESS
6 Work Packages
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
COST Action CA15139 (2015-2019)

## Slide 21: ESS modifications to produce a neutrino Super Beam
European Spallation Source Linac

## Slide 22: How to add a neutrino facility?
The neutron program must not be affected and if possible synergetic modifications.
Linac modifications: double the rate (14 Hz → 28 Hz), from 4% duty cycle to 8%.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons),
  space charge problems to be solved.
~300 MeV neutrinos.
Target station.
Underground detector.
Short pulses (~μs) will also allow DAR experiments (as those proposed for SNS) using the neutron target.

## Slide 23: Candidate active mines
Garpenberg mine
  Distance from ESS Lund 540 km
  Depth 1200 m
  Truck access tunnel
Zinkgruvan mine
  Distance from ESS Lund 360 km
  Depth 1500 m
  Truck access tunnel
Granite drill cores
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
Garpenberg
Zinkgruvan
possible location of MEMPHYS in
Zinkgruvan mine

## Slide 24: Which baseline?
~60% δCP coverage at 5 σ C.L.
>75% δCP coverage at 3 σ C.L.
systematic errors: 5%/10% (signal/backg.)
CPV (Nucl. Phys. B 885 (2014) 127)
Zinkgruvan
Garpenberg
Candidate active mines

## Slide 25: Physics Performance (CPV discovery)
little dependence on mass hierarchy,
δCP coverage at 5 σ C.L. up to 60%,
δCP accuracy down to 6° at 0° and 180° (absence of CPV for these two values),
not yet optimized facility,
5/10% systematic errors on signal/background.
540 km

## Slide 26: Physics Performance (accuracy)
5/5 yrs
δCP accuracy down to 6° at 0° and 180°
12° accuracy at δCP= -90° and 10° at δCP= 90°
5/10% systematic errors on signal/background.

## Slide 27: The Linac modifications and operation
P
P
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
Into linac
Into ring
Into horn
14 Hz
14 Hz
14 Hz
~1.4 kHz
Horn 1
Horn 2
Horn 4
Horn 3
100 µs
0.65 ms
~1 µs
~0.75 ms
H- source options
time operation option

## Slide 28: The Accumulator
4 superperiods
FODO cells
injection
RF
extraction
collimation
Dispersion-free straight sections
Switchyard
H- stripping
lattice development

## Slide 29: General Layout of the target station
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
Beam Dump
8 m concrete

## Slide 30: Detectors
Super-FGD like detector
- 1 t target mass
0.5 kt fiducial volume
water Cherenkov detector
NINJA-like water-emulsion detector
Beam
Near Detector
Far Detector
~500 kt
20" PMT
30% photocathode coverage
77 m
75 m

## Slide 31: Latest Improvements
New Magriation Matrices for the far detector compared to those of MEMPHYS
Genetic Algorithm for Target Station optimisation
MEMPHYS WC detector
Phys. Rev. ST Accel. Beams 16, 061001 (2013)
~500 kt
new far detector reconstruction algorithm
(publication is coming)
horn optimisation
x2
20"
77 m
75 m
30% photocathode coverage
(using WCSim and fiTQun)

## Slide 32: Physics Performance Improvement
https://arxiv.org/abs/2107.07585
best version of NF
ESSnuSB
θ12 = 33.44°
θ13 = 8.57°
θ23 = 49.2°
Δm221 = 7.42e-5
Δm231 = +2.517e-3
2nd osc. max.
507 ktons far detector
contribution of atm. neutrinos still to be included
10 years
EUROnu
θ12 = 33.2°
θ13 = 9.2°
θ23 = 45°
Δm221 = 7.64e-5
Δm231 = +2.45e-3
1st osc. max.
initial performance
current
performance
ESSnuSB
Neurino Factory
540 km
360 km

## Slide 33: Improvements (discovery potential)
360 km
540 km
EUROnu performance
discovery potential at the level of the Neutrino Factory!
~more than 70% after 10 years
10 years
initial performance
current
performance

## Slide 34: Improvements (precision measurements)
EUROnu
10 years
360 km
540 km
Precision measurements
initial performance
current
performance
ESSnuSB
Neurino Factory
more in https://arxiv.org/abs/2107.07585

## Slide 35: Choice to be done soon between the two mines
CPV discovery
precision measurement
70% δCP coverage at 5σ!
better than 8° precision on δCP for all values!
https://arxiv.org/abs/2107.07585

## Slide 36: What to do after?

## Slide 37: Muons at the level of the beam dump
muons at the level of the beam dump
(per proton)
y (cm)
x (cm)
4.2x1020 μ/year
(16.3x1020 for 4 m2)
4.1x1020 μ/year
2.7x1023 p.o.t/year
muons/proton
<Eμ>~0.46 GeV
<Lμ>~2.9 km
10-3
input beam for future 6D m cooling experiments (for muon collider),
low energy nuSTORM,
Neutrino Factory,
Muon Collider.
more than 4x1020 μ/year from ESS compared to 1014 μ used by all experiments up to now (1018 μ for COMET in the future).

## Slide 38: Muons at the level of the beam dump
<Eμ>~0.5 GeV
<Lμ>~3 km
() | ( ) | ( ) | ( ) | ()
decay tunnel length

## Slide 39: ESSνSB and (R&D) synergies
Super Beam
Neutrino Factory
Muon Collider
+Decay At Rest and Coherent scat.
(with short pulses)
nuSTORM
nm or nm
nm + ne
ne + nm
2.7x1023 p.o.t/year

## Slide 40: Coming EU Applications
The natural path after a CDR is to focus the work on prototyping and detailed engineering towards full demonstration of the concepts and the production of a TDR.
  this is difficult to obtain at this stage and the EU INFRADEV/DESTINATION calls are not adapted to these requirements.
The ESSnuSB project is too extensive and complex for it to be possible to prepare in only 4 years a sufficient basis for an application to be included in the ESFRI list as required for an INFRADEV-02 application (R&D).
Remaining coming possibilities:
  INFRADEV-01 (taking example of FCC)
  ERC-Synergy grant

## Slide 41: INFRADEV EU Call
HORIZON-INFRA-2022-DEV01
Developing European Research Infrastructures to maintain global leadership
Deadline: 20 April 2022
Topics | Type of Action | Budgets (EUR million) | Expected EU contribution per project (EUR million) | Number of projects expected to be funded
 |  | 2022 |  | 
Opening: 19 Jan 2022 |  |  |  | 
HORIZON-INFRA-2022-DEV-01-01 | RIA | 24.00 | 1.00 to 3.00 | 10
Overall indicative budget |  | 21.80 |  | 7

## Slide 42: What to do more?
Further important studies needed before start ESSnuSB construction.
  new studies must be significantly different to those already done,
  supplementary studies required for the present proposal (according to present WP conclusions),
  site specific civil underground engineering: at ESS-site and far detector site,
  detailed studies of the safety and licensing requirements needed for the later approval by the authorities as well as how to take environmental protective measures into account
  preparation of the R&D phase before TDR,
  Muons (synergies): design studies of an ESS-based low energy nuSTORM and a Muon Collider Proton Complex Test Facility.

## Slide 43: Proposed scenario for 2022-2025
Accumulator ring to be complemented
with a Compressor ring

## Slide 44: Preliminary Design Study Structure
Possible WPs:
Management
Civil engineering at ESS and mine sites, safety, licensing and environment preservation.
Linac, accumulator/compressor and LEnuSTORM race-track.
  muon collider proton complex test facility: 2 ns bunches of 1014 protons at 14 Hz.
¼ Target Station, hadron/muon production and muon extraction for Low Energy nuSTORM, targets for 2 ns proton bunches.
Detectors and physics performance (synergies between ESSnuSB and LEnuSTORM).
preparation of the R&D phase

## Slide 45: ESS site and mine site civil engineering
Design Study of civil engineering
  ESS site, all installations are underground
    design will be done by ESS (free of charge)
  cavern constructions at Garpenberg and/or Zinkgruvan at 1000 m overburden
    diamond drillings at significant cost necessary
Licencing
Safety
Environment protection
WP2
Far Detector

## Slide 46: Linac, accumulator, race-track and muon activities
WP3
Design study of a nuSTORM race-track storage ring located on the ESS site and study how the uniquely high flux of pions and muons from the ESSnuSB targets station can be injected into such a ring to produce a high flux of equal amounts of electron and muon neutrinos of low energy for neutrinos cross-section measurements and sterile neutrino searches using
a dedicated small close nuSTORM near detector and the ESSnuSB Near Detector
as a far detector for the nuSTORM beam.
nuSTORM
Near
ESSnuSB
Near
Detector
study of the muon race-track

## Slide 47: Targetry, hadron production, muon extraction
WP4
+prepare target R&D
muon extraction at the level of the ESSnuSB beam-dump
including studies using 2 ns proton bunches

## Slide 48: Detectors and Physics performance
Near (LEnuSTORM) and Far (ESSnuSB near) detectors
  cross-section measurements
Physics performance
  LEnuSTORM (sterile neutrinos)
astroparticle physics program with the Far Detector
WP5

## Slide 49: Schedule of the application preparation
By November:
  preliminary list of participants
  preliminary WP coordinators
    better definition the WP's contour
    preliminary task definition and sharing among the participants
    preliminary budget sharing
End 2022:
  finalise the list of participants and partners
  preliminary list of deliverables and milestones
  good draft of the application text
February 2022:
  final list of deliverables and milestones
  list of tasks/WP/participant according to deliverables and milestones
  manpower/WP/participant
  budget sharing and subcontracting
April 2022: Finalise the text and Submission

## Slide 50: New participants are welcome

## Slide 51: Conclusions
The ESS proton linac will be soon the most powerful linac in the world.
ESS can also become a neutrino facility (ESSνSB ) with enough protons to go to the 2nd oscillation maximum and increase significantly the CPV sensitivity and precise measurement of δCP.
The European Spallation Source will be ready by 2025, upgrade decisions by this moment.
Rich muon program for future ESS upgrades
  Low energy nuSTORM
  Muon Collider R&D
Excellent conditions for DAR and Coherent Scattering experiments
New applications under preparation,
  please join!

## Slide 52: Backup

## Slide 53: ESSnuSB structure and participating institutions
11 countries
Starting date: 01/01/2018
Ending date: 31/12/2021 → 31/03/2022,
Duration: 48+3 Months,
3 months extension due to COVID19
Kick-off meeting: 15 January 2018, Lund (ESS),
90% of the budget already received,
All deliverables and milestones ready on time (some rescheduling due to COVID19 has been arranged with the EU Project Officer)

## Slide 54: Possible ESSνSB schedule (2nd generation neutrino Super Beam)
2022: End of ESSνSB Design Study, CDR and preliminary costing
2012: inception of the project
2016-2019: beginning of COST Action EuroNuNet
2018: beginning of ESSνSB Design Study (EU-H2020)
2022-2025: Preparatory Phase, TDR
2025-2027: Preconstruction Phase, International Agreement
2027-2035: Construction of the facility and detectors, including commissioning
2035-: Data taking
Nucl. Phys. B 885 (2014) 127

## Slide 55: High Intensity Frontier Initiative (HIFI)
HIFI Uppsala Workshop 2-3 March 2020

## Slide 56: Muon Collider as Higgs Factory
Carlo Rubbia
arXiv:1908.05664

## Slide 57: Muons at ESS (ESSμSB)

## Slide 58: Muons at ESS (ESSμSB)

## Slide 59: Muons at ESS (ESSμSB)

## Slide 60: Low Energy nuSTORM at ESS
Proposed at FERMILAB and CERN (~3.8 GeV muons)
Sterile Neutrino searches
Neutrino cross sections measurements with unprecedented precision
LBL performance improvement by systematic error mitigation
To be adapted for lower muon energies (~0.5 GeV)
preliminar studies for ESS
sterile neutrino searches

## Slide 61: Decay At Rest at ESS
Possible if short pulses (~μs)
A
+
-
~99%
+
e+
p


e
  26 ns
  2.2 μs
Fragments
DAR
capture
Well known neutrino spectra (DAR).
Very high neutrino intensities ~ 5x1015 n/s.
Separate neutrinos of different flavors by time cut.
Role that neutrino-nucleus interactions play in the supernova explosion process and subsequent nucleosynthesis.
Accurate knowledge of neutrino-nucleus cross sections is important (almost no data exist).
This lack of knowledge significantly limits our understanding of supernovae and of terrestrial observations of cosmic neutrinos to probe the deepest layer of these powerful explosions.

## Slide 62: Coherent Scattering at ESS
SNS
sterile neutrinos,
neutrino magnetic moment,
non-standard interactions (NSI) mediated by new particles,
probes of nuclear structure,
improved constraints on the value of the weak nuclear charge,
reduction in neutrino detector mass may lead to a number of technological applications as non-intrusive nuclear reactor monitoring.
CEνNS is also expected to dominate neutrino transport in neutron stars, and during stellar collapse.
…

## Slide 63: Coherent Scattering at ESS
JHEP 02 (2020) 123
ESS can generate the largest pulsed neutrino flux suitable for the detection of Coherent Elastic Neutrino-Nucleus Scattering (CEνNS ).
Innovative detector technologies able to profit from the order-of-magnitude increase in neutrino flux provided by the ESS, along with their sensitivity to a rich particle physics phenomenology accessible through high-statistics, precision CEνNS measurements, are under study.

## Slide 64: How the CPV coverage and resolution curves have been produced
T2HK:
  Same curves that Hyper-K has showed at the Neutrino Town Meeting at CERN and the one that was showed at Neutrino 2018.
  Systematics are said by T2HK to be between 3% to 4%.
  sin2 2θ13 =0.1 and θ23= π /2.
DUNE:
  Public globes file released by the DUNE collaboration with the CDR, the only change is to increase the number of years from 7 to 10.
  sin22θ13 =0.1 and θ23=π/2, to be compatible with the T2HK line.
ESSnuSB:
  Instead of considering as usual “Opt. Snowmass errors" it is only assumed an overall 3% systematic error in the different signal and background channels, more in line with T2HK assumptions.
  sin22θ13 =0.1 and θ23= π /2, to be compatible with the T2HK line.

## Slide 65: Beyond DUNE, JUNO, HyperK: ESSνSB, P2O and Neutrino factory
Roumen Tsenov
Department of Atomic Physics, University of Sofia
European Neutrino "Town" meeting and ESPP 2019 discussion, CERN, 24.10.2018

## Slide 66: Systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 67
ESSνSB 500 kt tank at 540 km.
ESSνSB 500 kt tank at 360 km.
ESSνSB 250 kt tank at 540 km
and 250 kt tank at 360 km.
(degrees)
CPV performance comparison between ESSnuSB, DUNE and Hyper-K
assuming 3% systematic errors for ESSnuSB in line with the other two.

## Slide 68: Fraction of δCP
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
2 active mines aligned…
My personal opinion:
these scenarios are too optimistic for all facilities
(E. Martinez-Fernandez)

## Slide 69: Comparisons
Comparison using the same systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 70: Possible locations for far detector
CERN
ESS
Kongsberg
Løkken
LAGUNA sites

## Slide 71: nuSTORM
Proposed at FERMILAB and CERN (~3.8 GeV muons)
sterile neutrino searches

## Slide 72: Optimisations

## Slide 73: Expected event spectrum

## Slide 74: Expected event spectrum

## Slide 75: Expected event spectrum

## Slide 76: Expected event purity

## Slide 77: Expected event purity

## Slide 78: Coverage

## Slide 79: Systematics
We included additional bin-to bin uncorrelated nuisance parameter for all signal and background channels (uncorrelated)

## Slide 80: Atmospherics
before optimisation
after optimisation

## Slide 81: PMNS Unitarity