## Slide 1
LOREM IPSUM DOLOR
SIT AMET
Automatic procedures for setup optimization of an Eye Tracking System in ocular proton therapy
Andrea Pella, Guido Baroni

## Slide 2
OPT
Active participation of patient
Reproducibility of setup
Point based registration of clips
On line verification during irradiation
OPT @ CNAO
Non dedicated beam line
Treatment chair coupled to PPS
Custom Eye Tracking System
  fixation light
  real time monitoring
Complexity of Setup and integration!
Via R. et Al. Optical eye tracking system for real-time non invasive tumor localization in external beam radiotherapy. Med Phys. 2015 May;42(5):2194-202. doi: 10.1118/1.4915921.PMID: 25979013

## Slide 3
In room position is verified via Optical Tracking System (OTS)
ETS is mounted on a serial manipulator
Preparation of Patient-specific models, relying on surrogates
1. Setup preparation
2. ETS correctly placed along the desired gaze direction
3. Record references on ETS camera
4. Setup Validation

## Slide 4
Real time monitoring of pupil and iris
NB: edge reference manually drown by operator
OK?
Treatment on
1. Setup preparation
2. ETS correctly placed along the desired gaze direction
3. Record references on ETS camera
4. Setup Validation

## Slide 5
From ‘passive’ Setup preparation…
TIME
Via R, Pella A, Romanò F, et Al. A platform for patient positioning and motion monitoring in ocular proton therapy with a non-dedicated beamline.Phys Med. 2019 Mar;59:55-63. doi: 10.1016/j.ejmp.2019.02.020. Epub 2019 Mar 2.PMID: 30928066

## Slide 6
There are a large number of possible solutions for placing the fixation light along the gaze direction…
…But…
ETS-Mask Collision
ETS-Collimator Collision
Proton Beam obstruction
The optimal configuration shall:
1. maximize the minimum distances between the device and other setup elements
2. exclude inclusion in beam field
3. satisfy the clinical requirements

## Slide 7
Patient Specific Standard tools
Mask Brass collimator Holder ETS
Matlab simulator for automatic optimization of ETS positioning in order to:
Respect patient specific geometrical constraints
Satisfy the clinical requirements imposed by the treatment plan

## Slide 8
Patient Specific Standard tools
Mask Brass collimator Holder ETS
Virtualization of Setup

## Slide 9
The optimal configuration shall:
maximize the minimum distances between the device and other setup elements
2. exclude inclusion in beam field
3. satisfy the clinical requirements
Elisei G, Pella A, Ricotti R, et Al. Development and validation of a new set-up simulator dedicated to ocular proton therapy at CNAO. Phys Med. 2021 Feb,82:228-239. doi: 10.1016/j.ejmp.2021.01.070. Epub 2021 Feb 28. PMID: 33657472.

## Slide 10
Verification Clips position and cv
Setup
& DATA!
Treatment
Monitoring Video Frames of eye

## Slide 11
Offline estimation of tumor coverage (clip to clip distance)

## Slide 12
Offline estimation of tumor coverage (clip to clip distance)

## Slide 13
Automatic segmentation of features of interest
Antonioli L, Pella A, Ricotti R, et Al. Convolutional Neural Networks Cascade for Automatic Pupil and Iris Detection in Ocular Proton Therapy. Sensors (Basel). 2021 Jun 27,21(13):4400. doi: 10.3390/s21134400. PMID: 34199068.

## Slide 14
Automatic segmentation of features of interest
?Robust and safe for automatic treatment interlock?

## Slide 15
Next?
Setup alignment outside the CT room \ Bunker
Geometrical calibration of ETS cameras
Eye simulator (estimation of clip coordinates using eye surface information)
Integration of automatic procedures for iris and pupil segmentation in clinical workflow
Thank you!