PCIe400 mechanical specification for cooling solution design
Version	Date	Comment	Author
0.0.1	13/04/2023	Initial version	JL

# PCIe mechanical specification
The board is in compliance with PCIe Add-in Card double slot, full height. The length of the board is 270mm maximum. The edge connector is the “x16” type.

# PCIe400 description
## General aspect
The board embed 8 majors components regarding cooling consideration which are :
- 1x Intel FPGA Agilex 7 M-series
- 4x Amphenol optoelectronic on-board transceiver referred as OBT
- 1x QSFP112 optoelectronic on-edge transceiver
- 2x SFP optoelectronic on-edge transceiver
Other peripheral components (µmodule DC/DC converter for power supply, connectors and logic components) do not require particular attention regarding cooling although they induce constraints on heatsink dimension for the main components.

## Main component description
### FPGA
The FPGA is 56 x 66mm with a contact pad area with heat-sink reduced to 47.86 x 60.96 x 4.82mm.

The absolute maximum junction temperature allowed is 95°C, the target maximum junction temperature is 85°C to keep margins and reduce electronic constraints for logic implementation in FPGA.
Power dissipated by the FPGA depend on configuration cases referred as ‘typical’ and ‘worst’ case, but also depend on junction temperature. The power dissipated by the FPGA increase as the junction temperature rises. It is therefore favorable to have a cooling solution with higher efficiency than what would just be required to maintain Tj at 85°C in order to reduce global cooling system requirements.
### OBT
Power dissipated in function of Tj
Tj (°C)
Power (W)
OBT is 23.45 x 23.45 x 10mm with a contact pad with heat-sink of 2x158mm2. The separation is meant to allow several OBT module aligned with fiber pass through.

The absolute maximum case temperature is 70°C but should be kept under 50°C to prevent potential rapid aging effect.
Power dissipated by modules is between 5.4 and 7.9W in our use case. The total power dissipated by all 4 modules is therefore at a maximum of 31.6W.

### QSFP112
This on-edge transceiver is composed of a cage and connector on-board ans a pluggable module.
The cage is 20.64 x 61.90 x 22.1mm with heat-sink. The contact pad with the heat-sink is 13.6 x 37mm with no Thermal Interface Material (TIM) in between. The pluggable module is not yet available on market but estimations on the dissipated power and maximum case temperature is ~12W and 70°c respectively.

[misssing heat-sink illustration]
### SFP
This on-edge transceiver is composed of a cage and connector on-board and a pluggable module. The cage is 15.12 x 49 x 10.85 mm. The pluggable module is not specific to our board and can be interchanged. Typically, the dissipated power and maximum case tempertaure is 1W and 85°C. No heat-sink are mounted on top of the cage.
## Placement constraints
The placement of main components are as following
[missing top view drawing with datum]
## I/O bracket

# Environment description
## PCIe specification

PCIe specification does only impose a minimal airflow for chassis manufacturer but provide a recommended design space for Add-in card designers. The expected approach air temperature for add-in card plugged into PCIe slot of a server can go from 25 to 60°C.
In order to refine the environment constraint for designing the cooling solution, here are information more specific to our application.
## Server description
The board is hosted by rack mounted GPU servers such as Gigabyte 4U G48x series or Supermicro GPU SuperServer SYS-421GE-TNRT3 or ASRock 3U8G+. These are only example for reference but host serve choice is not yet specified.

Servers are equipped with array of fans ensuring airflow through the server but the speed and direction is not specified neither on direction or speed. The airflow can pass through the board from either side. It is therefore favorable to have a passive heat-sink solution (no fans on board).

### Performance value
[based on Therma400 measures]

# Feasibility study
## Vapor Chamber model
## CFD Simulation and result
### FPGA and OBT
### Fully populated board
## Heat-sink fixing
### FPGA heat-sink
### OBT heat-sink