## Slide 1: Status CE65V2_xx chip
Andrei DOROKHOV,
on behalf of C4Pi and PICSEL,
IPHC, Strasbourg
8/06/2022

## Slide 2
CE65V2_xx (1.5mm x 1.5mm)
8/6/2022 andrei.dorokhov@iphc.cnrs.fr , IPHC, Strasbourg
Versatile exploratory chip using matrix of pixels (48 col x 24 row) output is multiplexed to one analogue channel (matrix rolling shutter readout mode):
share common pads structure, carrier and proxy boards
4 power domains: 3.3V analogue, 1.2 analogue, 3.3 digital, 1.2 digital
3.3 analog and 1.2 analog share same ground AVSS
3.3 digital and 1.2 digital share same ground DVSS
one column reserved for precise charge collecting diode capacitance measurements
11 biases for pixel front-end:
8 X 1.2 analogue biases
3 x 3.3 analogue biases
3 digital input pulses (3.3V): clock, start, calib
Power:
digital (3.3V IO/1.2V CORE): DVDD33, DVDD12,DVSS
analogue (3.3V): AVDD33, AVSS
analogue (1.2V): AVDD12, AVSS
4 unprotected pads: HV, NWELL ,NWELLSUB, PWELL
Output is in 1.2V analogue domain
2 calibration voltages: VHIGH, VLOW
2 biases for output buffer

## Slide 3
Different modifications / chips of CE65V2_xx / design status
8/6/2022 andrei.dorokhov@iphc.cnrs.fr , IPHC, Strasbourg
Modification | Purpose | Pitch, um | Comment | N | status
CE65V2_C_xx | Charge collection (“_C_”) measurements, rolling shutter readout (AC pixel from CE65 is implemented) | 15, 18, 22.5, 18hexsq, 22.5hexsq | For lab and beam test, charge collection node, techno, optimization | 5 chips ( x 3 flavors: no n-implant Blanket n-implant n-implant with gaps) | DRC, LVS are OK for all chips 5 chips x 3 pixel flavors ready : sent to CERN
CE65V2_A_xx | Precise measurements of multiplexed analogue or digital output of pixel FE (“_A_”): pulse duration, gain, FPN, noise, RTS.. | 18 (or 22.5) | For lab only, possibility to explore waveform with oscilloscope: FE optimization/tuning. | 1 (existing FE from MOSS) + versions?.. | If that chips is relevant for tests and not redundant to other chips: need to define which FE (or versions) for precise measurements
GDS sent to CERN, but would be useful to cross-check the designs of all chips by other person, some layers has to be checked by hand, re-verify the simulations
I have already asked that (in mail sent on 1st June to Jerome, cc: to Christine, Claude, Frederic): “It would be very useful to crosscheck what is going to be submitted, I do that from my side. However, obviously, 15 chips are too many to loose, if something went wrong and all are not usable for a "small" mistake -> so better not to neglect the verification by other person...”