## Slide 1
Possible MAPs R&D lines for FCC-ee*
FCC-France contact meeting, Friday 17, June 2022
D. Contardo, IP2I
* State of the Art better covered in talks of A.Besson CMOS MP, M. Barbero DICE MP & C4PI support platform framework in presentation of J. Baudot

## Slide 2
MAPs for Vertex Detector requirements (SoA) / studies
Ballpark requirements* (SoA)
  σhit ≲ 3 μm (WP1.2 TJ 65 nm ER1/ER2 pitch 18 μm - σhit ≃ 5 μm)
    Assuming binary readout (ToT could be a relatively low power consumption alternative)
  Large sensors 12’’ with stitching (main goal of WP1.2)
  Hit rate max ≃ 50 mHz/cm2 (WP1.2 ER1/ER2 ITS3 < 10 MHz/cm2)
  Integration time ≃ 1 μs (FE speed matched) (covered in WP1.2 ER1/ER2)
  Low power dissipation ≃ O(20) mW/cm2 (MOSS (ALPIDE PE synchrone), MOST (MALTA-type asynchrone) in WP1.2 ER1 - not yet defined for ER2 but likely MOSS less risky for ITS3 schedule)
Studies
  Simulate physics/bgd for rates
    Prepare realistic event inputs for architecture simulation
    Study asymptotic effect of σhit on σd0/z (pT, η) - considering overall configuration, X/X0…
  Develop a parameterized model of power consumption scaling in matrix and periphery
    According to #channels & gemoetry (electrode size/capacitance), FE speed/noise, rates
      w/o and w/ precision timing ToA/ToT implementation
  Simulate/evaluate architecture options performance with physics/bgd simulation inputs
* Close to those proposed for ALICE-3 (2034-35) eg 2.5 μm, 35 MHz/cm2 and 70 mW/cm2
Also applying to other systems
(Central Tracker, HGCalo, Timing Layer)

## Slide 3
MAPs for Central Tracker requirements (SoA) / studies
Ballpark requirements (SoA is mostly from pixels)
  σhit (⊥) ≃ 5 μm (achieved in pixels) - pitch can be relaxed in r-z
    Only ex. ? CLICTD 30 x 8 x 37.5 (300) μm2 , a OR of 8 sub-pixels to ToA, ToT, 1st firing pixel σt O(ns)
  Large sensors 12’’
  Hit rate tbd
  Integration time 1 μs (FE speed matched) as for pixels
  Low power dissipation tbd
Studies
  Simulate physics/bgd for rates
    Prepare realistic event inputs for architecture simulation
    Study asymptotic effect of σhit on σpT (pT, η) considering overall configuration, X/X0…
    Study electrode size and pitch (grouping in r-z)
  Develop a model of power consumption impact on cooling and overall X/X0
* In CLICTD a Or of 8 sub-pixels enters ToA, ToT (the timing is given by first pixel above threshold with σt O(ns))

## Slide 4
MAPs for HGCalo requirements(SoA) / studies
Ballpark requirements* (SoA no specific MAPS developments so far)
  Pad (analog) / Pixel (counting)**, size/pitch tbd (5 x 5 mm2 for pads in current hybrid designs)
  Large sensors 12’’
  Hit rate tbd
  Integration time 1 μs as for pixels? FE speed according to σt tbd
  Low power dissipation tbd
Studies
  Benefit of MAPS for compactness
  Study effect of electrode pitch, size and active thickness on energy resolutions
    Including comparing pad analog vs pixel counting
  Study effect of power consumption / cooling on energy resolutions
  Study benefit of timing ns and sub-nanosecond
  Simulate physics/bgd for rates
    Prepare realistic event inputs for architecture simulation
  Simulate architecture according to physics/bgd simulations
* To be covered by HGCalo community
** Amplitude can be provided by ToT if a timing feature is included

## Slide 5
MAPs for Timing Layer requirement (SoA) / studies
Ballpark requirements (SoA)
  Target 10 ps per hit (PID) (≃ 50 ps expected with 1 mm2 pads)
  20 ps still of interest if 3 layers at large tracker radii?
Studies
  σt optimization versus electrode size, pitch, sensor thickness
  Implementation of ToA/ToT
    Granularity as a function of rates and subsequent power consumptions
  Opportunities to implement 3D or amplification in MAPS (current hybrid design alternatives)

## Slide 6
Summary ballpark parameters for subsystem options
Detector | Sensor 12" |  |  | Readout |  | Performance | 
Paramater | Elect. Pitch (μm) | Elec. Size (μm) | Act. thick. | Power | ToA/T | σhit (μm) | σt (ps)
Vertex | ≲ 10 | ≲ 2 | ≲ 10 | +++ | NA | ≲ 3 | NA
Central Tracker | ≲ 20 - ≳ 1000 | ≲ 20 - ≳ 10001) | ≲ 502) | +++ | NA | ≲ 5 | NA
HGCAL anal. Pads | ≳ 1000 x 1000 | Pads ≳ 10001) | ≲ 500 | ++ | (+) | NA | (≲ 1000)
HGCAL Digi. Pixels | ≲ 50 x 50 | ≲ 50 | ≲ 500 | ++ | (++) | NA | ≲ 10
Timing Layer Pads | ≲ 1000 x 1000 | Pads ≲ 10001) | ≲ 500 | + | +++ | NA | ≲ 10
Timing Layer Pixels | ≲ 10 | ≲ 2 | ≲ 10 | + | +++ | ≲ 3 | ≲ 10
Could be small electrodes grouped for lower C? ex. to improve σhit (cluster size with lower threshold) and σt
For X/X0 considering sensor bending
Values are indicative, requiring simulation studies (see previous slides) and inputs from performance depending on sensor parameters (electrode pitch/size, active thivkness)

## Slide 7
R&D options for FCC-ee
Sensitive area
  Large area sensors with stitching  all systems
  Small pitch, thin active layer for ultimate σhit and σt  all systems
  Pads vs small electrode grouping for S/N, in thin/thick sensors for ultimate σt  CT, HGCalo, TL
  3D or amplification designs for ultimate σt  all systems
Readout
  Low power architecture adapted to FCC-ee rates  all systems
    Readout concept, synchronous vs asynchronous…
    Timing implementation FE and ToA/ToT
      FE O(25) ns for σt O(1) ns for HGCalo - O(1) ns for σt O(10) ps for Timing Layer(s) (possibly HGCalo)
      TDC possible implementation and granularity (depending on rates…)
  Investigate implementation in 3D integration
* Several expressions of interest in PEPR project (rejected) CPPM, IJCLab, IPHC, IP2I, IRFU, LLR, LP2I, LPNHE, LPSC, and also CEA/IRFU
These topics could be a basis of discussion to develop a common FCC-ee R&D program
A mini-workshop organised in the C4PI plateform framework by October (see J. Baudot talk)
will be an opprotuinity to identify possible common demonstrator developments
with all groups* interested in MAPS developments

## Slide 8
R&D opportunities on short/medium term
WP1.2 CERN - ER2 (timescale Oct. 2023) in TJ 65 nm
  Mainstream sensor: large size for ITS3 10 x 28 cm2 with stitching
    On-going contribution to design of FE, MOSS(PE) architecture (IPHC so far)
  Periphery components: 0.5 x 28 cm2 available on each side of mainstream sensor
    Could include follow-up of asynchronuous arcitecture MOST(MALTA) implemented in ER1 tbd with CERN
    Could include investigation of ultimate σhit and σt with pixel pitch down to ≲ 10 μm (CE65 extension) ?
      Possibly implementing pixel grouping to study effect on σt ?
      Possibly implementing intial version of a TDC with simple readout architecture ?
    Could include large electrode alternative for σt ?
    Could include small matrix with alternatives toward a low power arcitecture ?
Other process used in ongoing activities, ex. LFoundry 150 nm , TJ 180 nm
(considering they are unlikely to be a final technology choice for small itch and low porwer)
  Study σt as a function of electrode pitch/size, active thickness
  Investigate new sensor designs ex. 3D, amplification
A FCC-ee budget line need to be identified in a dedicated or wider IN2P3 MP
(with CEA/IRFU collaboration)
Access to WP1.2 ER2 outside mainstream (ITS3) will need discussion with CERN and funding
Beyond, a new R&D framework should result from the ECFA detector RD roadmap implementation,
and R&D goals could be targeted by the new PED detector WG for the FCC Feasibility Studies (2024-25)