## Slide 1
Performance of an LGAD readout ASIC
for ATLAS HGTD picosecond MIP timing detector
2 wheels
ALTIROC2
Maxime Morenas/OMEGA on behalf of ATLAS HGTD collaboration
Journées des métiers de l'électronique de l'IN2P3 et de l'IRFU

## Slide 2: High Granularity Timing Detector in HL-LHC
ASIC’S REQUIREMENTS
LGAD sensor
1.3 x 1.3 mm2
Thickness = 50 µm
Cd = 4 pF
225 channels
Minimum charge : 2 fC
Charge dynamic : up to 100 fC
Noise : < 0.5 fC or 3
Cross-talk : < 2 %
Timing precision : 35 ps for 10 fC
(per hit) 70 ps for 4 fC
TOA TDC
Resolution : 20 ps
Measurement window : 2.5 ns
Conversion time : < 25 ns
TOT TDC
Resolution : 120 ps
Dynamic range : 20 ns
Conversion time : < 25 ns
Radiation tolerance
TID : 2 MGy w/SF=2,25
NIEL : 2.5 1015 neq/cm2 w/SF=1.5
SEE : 1015 neq/cm2 w/SF=1.5
SEU rate : < 5 % per hour
ASIC power dissipation < 1.2 W
Per channel :
Analog very front-end : < 2 mW
TDC : 0,5 mW at 10 % occupancy
Digital : < 2 mW
Calibration LGAD-like injection :
Range : 0 – 100 fC
Rise time : 0.5-1.5 ns
Luminosity : Number of hits per bunch crossing for 2 time windows

## Slide 3: ALTIROC’s architecture
Analog front-end pixel
Matrix
Periphery
15 x 15 channels
TSMC 130 nm
Digital part of the pixel
PLL
phase shifter
calibration pulser
End Of Column
Luminosity process unit
320 Mbit/s fast commands decoder
Trigger Processing unit
Hit data transmission up to 1,28 Gbps
Slow Control
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 4: Comparing analog front-end to another timing/tracking pixel ASIC
Ratio minimum charge detectable over detector capacitance
  Altiroc: Qmin/Cd ~ 500 µV with Cd ~4 pF (1300 x 1300 µm²) and Vth min = 2 fC
  Timepix4: Qmin/Cd > 2 mV with Cd ~ 50 fF (50 x 50 µm2) and Vth min=0,1 fC
Preamp BW
  Altiroc: 1 GHz
  Timepix4: ~ 20 MHz
Power dissipation / technology / size
  Altiroc: 300 mW/cm2 + techno CMOS 130 nm + 225 channels
  Timepix4: 600 mW/cm2 + techno CMOS 65 nm + 229k pixels
=
Cd: sensor cap ( ~4 pF)
td: LGAD drift time, 600 ps
Qin: MIP charge ( 10 fC at start, 4 fC at end)
en: noise spectral density of input trans.
ATLAS HGTD Electronics – JME Caen – 13th June, 2023
TDC bin
  Altiroc: 20 ps
  Timepix4: 200 ps

## Slide 5: A challenging integration of the digital functionalities in 130 nm
Hit buffer: SRAM 1536 x 19 bit = Depth of about 38 µs
  Circular buffer to store timing data for each bunch-crossing, until a L1 trigger arrives
  Data = TOT and TOA bits, only in case of hit to save power ; with zero suppress.
Trigger Hit Selector:
  Each received trigger associated to a trigger tag
  If data stored in Hit buffer related to received trigger, TOA/TOT data + trig tag stored into Matched Hit Buffer
Matched Hit Buffer: 32 positions FIFO
  Control Unit: looks for data related to a trigger event when requested by the End Of Column
  Matched flag handled through a priority OR chain. Pixel at the top of the column with highest priority
  Synchronous readout at 40 MHz
Luminosity process unit
  checks if hits are within 2 programmable windows
I2C configuration registers
ATLAS HGTD Electronics – JME Caen – 13th June, 2023
  Altiroc2 pixel: SRAM Latency of 38.4 µs to cope with 0.8 MHz readout bandwidth

## Slide 6: Testbench for ALTIROC2
Setup = ASIC board (ASIC alone or bump bonded onto sensor) + interface board + FPGA board
Front-end calibration : charge injection (0 up to 50 fC) using ASIC internal calibration pulser, controlled by the FPGA, synchronous to 40 MHz clock, ASIC alone: Cd=3,5 pF can be set by SC to mimic sensor capacitor
Designed by Pierrick Dinaucourt (OMEGA)
ALTIROC2 bump bonded onto an HPK LGAD
2 cm
6
ATLAS HGTD Electronics – JME Caen – 13th June, 2023
Wirebonding Altiroc3
Christophe Wabnitz (IPHC)

## Slide 7
ASIC alone
irradiated up to 200 Mrad
All digital ON
15 pixels enabled
ASIC + LGAD
(unirradiated)
Targeted
minimum
charge
Qmin = 1.4 fC
Qmin = 3.1 fC
Transimpedance
preamplifier results
Thresholds aligned at 3.2 fC
Qmin = 2.9 fC
Qmin = 3.8 fC
What is the minimum detectable charge ? (Median at 50%)
ATLAS HGTD preliminary
ATLAS HGTD preliminary
ATLAS HGTD preliminary
ATLAS HGTD preliminary
All digital ON
15 pixels enabled
All digital ON
All TZ pixels enabled
All digital ON
All pixels enabled
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 8
Digital noise injected on the preamplifier ground gets amplified only when the impedance between the detector capacitance and the non-inverting preamplifier input is not zero : when the sensor is connected !
Noise on gnd_pa amplified x20
“differential mode”
Noise on analog gnd amplified x1 “common mode”
ASIC alone = favourable situation
One channel
Sensor effect on noise
ATLAS HGTD Electronics – JME Caen – 13th June, 2023
Can this parasitic inductance be hidden from the preamplifier ?

## Slide 9: Effect of HV decoupling : where is the AC current flowing back to ground ?
10 nF HV decoupling capacitor adds 50% more noise on a TZ output.
With HV capacitor
Bump likely digital coupling inside the asic
amplified by the HV capacitor
Without HV decoupling capacitor
Multiple channels
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 10: Optimal HV impedance is very different for 5x5 and 15x15 sensor
HV resistance :
  varied from 0 to 1kOhm
  Effect on gnd_pa noise amplification
    Goes from 20 to 1
    ~1 for R>100 Ohm
  Current return ensured by the 224 spectator channels
    Was not the case with smaller sensor
HV parasitic inductance :
  Effect of 10 nH in HV
  1 channel, 25 channels, 225 channels
  = Altiroc0/Altiroc1/Altiroc2
Altiroc2 doesn’t suffer from HV parasitic inductance !
Noise x20 when
Noise x1 when
Noise amplified by PA as signal
Pulse
1 channel
25 channels
225 channels
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 11
Digital clock couples on preamplifier gnd input : induces a noise ripple ~ 3 fC = our limit !
Scope trigger
(FPGA calibration)
20 fC injected
Signal = 30 mV
No signal injected
Noise = ± 5 mVpp
Probing one
transimpedance preamplifier :
Signal aligned with noise bump
ASIC+HPK LGAD biased at -80V (B16)
Minimum threshold obtained aligning the signal with the noise bump.
Signal amplitude seen by the discriminator reduces : “hidden” inside the noise ripple !
Fighting against digital activity
Preamplifier
output baseline :
(exaggerated)
40 MHz
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 12
ASIC+HPK LGAD biased at -80V (B16) All TZ ON
Time-walk = convolution of the preamplifier rise time (300 ps) with LGAD rise time (600 ps)
Skew between bottom and top of the column pixel : due to clock tree distribution
TOA versus charge
TOA versus TOT
Offline time-walk correction using TOT
Time-walk = ~750 ps
Correcting time-of-arrival timewalk with time-over-threshold
ATLAS HGTD preliminary
ATLAS HGTD preliminary
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 13
=
Cd : sensor cap
td : LGAD drift time, 600 ps
Qin : MIP charge (10 fC at start, 4 fC at end)
en : noise spectral density of input trans.
Comparing measured time-of-arrival jitter with simulation
ATLAS HGTD preliminary
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 14
ASIC alone with detector capacitance
ASIC + sensor
ASIC alone without detector capacitance
Pulse reconstruction of a voltage preamplifier, between ASIC alone and ASIC + sensor :
Showing same amplitude & falling edge decay time → the internal LGAD-like capacitance corresponds to 3.5 pF.
Showing slightly slowly rising time → partially explains worst jitter with sensor.
=
Cd : LGAD capacitance
with
calibration pulse
Is the internal detector capacitance equivalent to an LGAD’s ?
ATLAS HGTD preliminary
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 15
Time
Amplitude
Higher slope, better jitter
Lower slope, worst jitter
Simulation
Thresholds aligned
at 3,2 fC
Thresholds aligned
at 4,8 fC
Thresholds aligned
at 9,6 fC
Thresholds aligned
at 19,2 fC
Threshold trade-off to maximise pulse slope (dV/dt), thus minimize jitter.
Jitter depends on the charge, but also on the discriminator thres.
ATLAS HGTD preliminary
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 16
Analog performance demonstrated with ALTIROC2 are encouraging !
  Very useful to understand system issues with sensor
  First assembled module has given similar performances than full ASIC testboard
  Jitter (ASIC+sensor) ~ 25 ps at 10 fC with calibration pulse
  Vth (ASIC+sensor) can be set at ~3 fC
  Testbeam results show degraded jitter around 50 ps (~ 20 fC injected by an HPK LGAD)
  Difficulties to correct from timewalk with TOT due to digital coupling
ALTIROC2 : first 225 channels full matrix LGAD readout chip with 1 GHz preamplifier
with 4 pF detector capacitance : new territory in HEP !
Conclusions
16
ATLAS HGTD Electronics – JME Caen – 13th June, 2023
ALTIROC3 is currently under test with improvements :
  Leveraging on bunch crossing synchronicity, using highly skewed digital logic to reduce couplings on analog
  Analog performances relies on floorplan (power distribution, grounding, IR drops, deepNwell) to minimize coupling between analog and digital power domains.
  Fully triplicated digital logic for SEE hardness

## Slide 17
Backup
17
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 18
ASIC alone (B7) Pixels ON : Col 7 (VPA) or 8 (TZ)
TID : 220 Mrad
Dose rate : 3 Mrad/h
Temperature : 22°C
All DC values and TDC bin remain constant along irradiation.
Jitter stability under TID irradiation
ATLAS HGTD preliminary
ATLAS HGTD Electronics – JME Caen – 13th June, 2023

## Slide 19
1
2
3
4
128
F1
F2
F3
F4
F128
120ps
120ps
120ps
120ps
120ps
1
2
3
4
128
S1
S2
S3
S4
S128
140ps
140ps
140ps
140ps
140ps
Q1
Q2
Q3
Q4
Q128
Bin2
Q2
Q1
Bin3
Q3
Q2
Bin4
Q4
Q3
Bin128
Q128
Q128
Bin1
Q1
0
Time-to-Digital Converter (TDC)
START
STOP
Simplified Block Diagram
START pulse comes first and initializes the TDC operation. STOP pulse follows the START with a delay that represents the time interval to be digitalized.
At each tap of the Delay Line, STOP signal catches up to the START signal by the difference of the propagation delays of cells in Slow and Fast branches: i.e. 140ps – 120ps = 20ps (LSB).
The number of cells necessary for STOP signal to surpass the START signal represents the result of TDC conversion
Cycling configuration used in order to reduce the total number of Delay Cells.
TDC range is equal to 128 * 20 ps = 2.56 ns
2.5ns
Clock
STOP
Event
Detection
2.5ns Measurement Window
START
ToA
Differential shunt capacitor voltage-controlled delay cells
TOA TDC
Resolution: 20 ps
Range: 2.5 ns
7 bits
TDC Power consumption : 0,5 mW @ 10% occupancy
STOP (rising edge of signal of 40 MHz) propagates in the Fast Delay Line
Delay of one cell = 120 ps
START (rising edge of the discriminator) signal propagates in the Slow Delay Line
Delay of one cell = 140 ps
TOA TDC Architecture : Vernier Delay Line
ATLAS HGTD Electronics – JME Caen – 13th June, 2023