## Slide 1: PLAS : Mémoire Analogique Multiplexée Tests, Analyses et Optimisations
14 Juin 2023, JME Caen
L. Alvado, S. Drouet, L. Leterrier, G. Martinez

## Slide 2: Sommaire
Quick story of the PLAS Project
PLASv2 features
How to measure resolution (SINAD, ENOB)
Testbench
PLASv2 Effective Resolution
  Measured with the testbench
  Simulation and Improvement
Conclusion

## Slide 3: Quick Story of the PLAS project
PLAS designer : Ramón J. Aliaga from University of Valencia
ASIC designed for GRIT project (PSA analysis)
PLASv1:
  Technology used : AMS 180nm CMOS
  Some results from PLASv1 datasheet [1] :
    Noise Floor = 1,9 mVrms (after voltage calibration)
    ENOB = 7,2 bits @ 4MHz and 1,5Vpp (target = between 11,5 and 12 bits)
PLASv2:
  Ready to be sent to the foundry (resolution improvement)
  No more MPW runs supported by AMS for this technology (180nm CMOS)
  Project transferred to the LPC-Caen microelectronics team
  New foundry found with the same technology: TSI 180nm CMOS
  Sent to the TSI foundry after corrections of DRC and LVS errors
[1] PLASv1 datasheet: “Zero Deadtime, Self Triggered, 32 Channel Analog Memory – PLAS”, Ramón J. Aliaga
PLASv1 Layout
PLASv2 Layout

## Slide 4: PLASv2 Features
PLAS = PipeLined Asymmetric Switched Capacitor Array
Target resolution : 11,5 bits (noise below 110 µVrms if FS=1,1V)
Sampling Features:
  32 inputs with independent trigger
  Samples at 200 MHz (Both edges of 100 MHz clock = Write Clock)
  224 samples captured per pulse
    32 before trigger (pre-trigger samples)
    192 after trigger (post-trigger samples)
  No deadtime
Reading Features:
  8 output queue slots
  Single analog output (differential)
  Serial readout at 50 MHz (Read Clock)
  Needs external ADC
  Designed for triggerless readout
  Generates timestamp for pulses
Pre-trigger samples
Post-trigger samples

## Slide 5: Comment mesurer la résolution
Utiliser la même façon que pour les ADC, c’est-dire:
  Injecter un signal sinusoïdal
  Échantillonner ce signal
  Traitement des échantillons pour extraire l’amplitude efficace et le bruit sur le signal  SNR, SINAD, ENOB
Deux techniques possibles pour extraire l’amplitude efficace et le bruit:
  Par transformée de Fourier (domaine fréquentiel)
    Inconvénient: avoir un échantillonnage cohérent
    Fréquence multiple de 1/(224x5ns)=892,857... kHz
  Par fit sinusoïdal à 3 ou 4 paramètres (domaine temporel)
    Avantage: pas de contrainte sur la fréquence

## Slide 6: PLASv2 Testbench
Schematic of the testbench system
Design and routing of the testbench
Firmware development : FPGA code
Software development :
  Configuration of the testbench (PLAS, ADC,...)
  Generator and voltmeter control
  Data acquisition
  Data process (SNR, ENOB, INL, Calibration parameters, ...)
  Display and save results
PLASv2
Testbench
FASTER
Motherboard
Waveform
Generator

## Slide 7: PLAS ENOB
DC ENOB: For different DC voltage [-600mV; 600mV]
With voltage calibration (2nd degree polyfit):
- average noise = 1,23 mVrms
- average ENOB = 8,14 bits (expected 11,5 bits)
- INLmax ≤ 0,083% ~10,5 bits (expected 0,03% if 12 bits)
AC ENOB: Amplitude range from 100 mVpp to 1,2 Vpp and a frequency of 4MHz
  With voltage calibration:
    Noise = 1,3 mVrms @ 100mVpp (ENOB = 8,06 bits )
    Noise = 5,6 mVrms @ 1,2Vpp (ENOB = 5,95 bits )
With the voltage calibration, ENOB increases from 0,30
to 0,82 bits.
  Need a time calibration
  Check the clock jitter :
  @1,2Vpp: noise=5,62 mVrms  jitter=527ps-rms
  Pas cohérent avec synthétiseur utilisé: jitter=20ps-pp
Results for post-trigger cells only
Input stage gain = 1

## Slide 8: Noise Summary for the sampling and reading stages
 | Sampling Noise [892,857 kHz; 1 GHz] | Reading Noise [200 kHz; 1 GHz] | Total Noise | SNR (FS=1,1V) | DC ENOB | BW
PLASv2 Tests |  |  | 1,23 mVRMS |  | 8,13 bits | 
PLASv2 Schematics | 672 µVRMS | 755 µVRMS | 917 µVRMS | 52,5 dB | 8,43 bits | 165 MHz
Modified Schematics [2] | 178 µVRMS | 282 µVRMS | 293 µVRMS | 62,5 dB | 10,08 bits | 90 MHz
 | Sampling Noise [892,857 kHz; 1 GHz] | Reading Noise [200 kHz; 1 GHz] |  | SNR (FS=1,1V) | DC ENOB | BW
PLASv2 Tests |  |  | 1,23 mVRMS |  | 8,13 bits | 
PLASv2 Schematics | 672 µVRMS | 755 µVRMS | 917 µVRMS | 52,5 dB | 8,43 bits | 165 MHz
Modified Schematics [2] | 178 µVRMS | 282 µVRMS | 293 µVRMS | 62,5 dB | 10,08 bits | 90 MHz
modified
Modified schematic of a channel during sampling phase
x2
Modified schematic of a channel during reading phase
AMP_DIFF: Gain=1,21
Modified Schematics :
    BUF_REF deleted + decoupling Cap added
    Noise improvement of the AMP_IN amplifier
    Stability improvement of the AMP_SCA amplifier
Cmem=540 fF instead of 270 fF
Swap T&H Switches

## Slide 9: Conclusion
Les résultats de simulation sont cohérents avec les résultats de tests: environ 8bits ENOB pas plus...
Alors que ENOB DC annoncé par le concepteur était de 11,5 bits ENOB en simulation.
Contact par mail avec le concepteur mais pas de réponse à cette énorme différence en simulation
11,5 bits de resolution (~110µVrms de bruit) semble impossible à obtenir (Etat de l’Art)
Des solutions ont été trouvées pour diminuer le bruit et atteindre environ 300µVrms de bruit
Tests continuent : calibration temporel, étude et analyse de certains bugs
Nouveau fondeur à trouver:
  TSI : Ne propose plus de run MPW. Il se focalise sur les clients avec des productions.
  AMS 180nm est de retour ou sinon XFAB 180nm (mais Vth différents)
NDA signé avec AMS, en attente du kit...

## Slide 10: Thank you for your attention ! Questions or Comments ?

## Slide 11
Sébastien Drouet
sdrouet@lpccaen.in2p3.fr
https://www.lpc-caen.in2p3.fr/expertise-technique/electronique-microelectronique/