## Slide 1
Main Telescope
Auxiliary Telescope
AuxTel
Hologram recording
Use as disperser
Le telescope auxiliaire (AuxTel)
D. Boutigny, S. Dagoret-Campagne, J. Chevalier, L. Le Guillou, M. Moniez, J. Neveu, M. Rodriguez-Monroy + Observing team (Patrick, Merlin, Tiago, Craig, Erik, Ioana, Alysha & others)
Rubin-LSST France, LPNHE, 30 nov. 2022
Notes: Ne pas rentrer dans les détails

## Slide 2: AuxTel spectrograph mission: measure the atmospheric transmission to derive the expected fluxes for each object under standard atmospheric conditions
Estimate colour corrections, as functions of the atmospheric conditions and of the object UGRIZY in every LSST field
Example below
- Constant airmass, constant O2 and O3. No cloud
- Change only : H2O (PWV), Aerosols
AuxTel spectrometer
Wet/dry
Aerosol/no aerosol

## Slide 3: Some facts about AuxTel
- D = 1.20m, f/D = 18, f = 21.6m
- Depth of focus 1 arcsec (10 pixels) for 1.8mm change in distance (small aperture).
- Secondary mirror (M2) Obturation: 0.3m
- Total collection area : S= 1.06 m2 (taking into account M2 obturation)
- Plate scale: 105µm/arcsec -> about 10 pixels/arcsec.
- Field of view : 6.3 Arcmin.
- Distance entrance window-CCD : 63.85mm. Light beam diameter at this distance : 3.55mm
- Distance disperser-CCD: about 191.4mm (tilted). beam diameter at this distance : 10.6mm
- Distance filter-CCD : 229mm (tilted).
- Saturation (no filter, no disperser, assuming seeing of 1’’): Msat=13.35+2.5Log10(Texp/30s)

## Slide 4: Our spectrograph is slitless equiped with an Holographic Optical Element
Slitless allows
- fast positioning
- spectrophotometry
Limits: sky+stellar background
low resolution (seeing limited)
Phase hologram (dispersion+focus functionalities)
- Excellent focus for all l with convergent beam -> nominal resolution
- More light -> better s/n
+
Incident beam here
Dispersion
CCD
Spectrum

## Slide 5: Our spectrograph is slitless equiped with an Holographic Optical Element
Slitless allows
- fast positioning
- spectrophotometry
Limits: sky+stellar background
low resolution (seeing limited)
Phase hologram (dispersion+focus functionalities)
- Excellent focus for all l with convergent beam -> nominal resolution
- More light -> better s/n
+
Incident beam here
Dispersion
CCD
Spectrum

## Slide 6: How does it look like?
Atmospheric dispersion (x20)
hologram dispersion

## Slide 7: Data available (since 16 feb. 21)
Spectrum extends from ~ 342nm to 1100nm
Dispersion: 2.73 pixels/nm
Resolution: R = l/Dl > 200 (seeing limited)
Raw extraction (1rst+2nd orders superimposed)
O2
Order 1
Order 2
Order 3
Out of atm. SED
Out of atm. SED
O(1000) spectra for
- Commissioning
Geometry
Resolution study
Transmission
2nd/1rst order : finalization
Bouguer lines: finalization for global telescope throughput
- With various
  CALSPEC standards
  atmospheric conditions
- with/without blocking filters
- but not that many with good quality
->The best nights up to now seem to be 30th june and end sept. 2022.
We need to acquire data in the largest domain of atmospheric Conditions.

## Slide 8: Operations for measuring atmosphere transmission
Use a spectrophotometric standard measured out of atmosphere (CALSPEC)
tatm(l,z) = f (l,z)instrumental /f(l)SED-HST
-> in magnitude (for diffraction order p):
mp(l,z)instrumental = m(l)SED-HST - 2.5logTp(l) + Aatm(l).z
Tp(l) = t(l)telescope . tp(l)disperser . eCCD(l)
tTelescope x eCCD
tHologram
(1rst order)

## Slide 9: Operations for measuring atmosphere transmission
Use a spectrophotometric standard measured out of atmosphere (CALSPEC)
tatm(l,z) = f (l,z)instrumental /f(l)SED-HST
-> in magnitude (for diffraction order p):
mp(l,z)instrumental = m(l)SED-HST - 2.5logTp(l) + Aatm(l).z
Tp(l) = t(l)telescope . tp(l)disperser . eCCD(l)
tTelescope x eCCD
tHologram
(1rst order)
Computed from lab. measurements

## Slide 10: Ingredients of throughput
M1 reflectivity vs date (measured)
M2-M3 reflectivity vs l (theoretical)
Loss at window entrance/exit
CCD efficiency (measured)
Hologram transmission
(measured/modelized)

## Slide 11: Throughput is estimated with Bouguer lines technique (1729)
Example in band [485-515]nm (1rst order)
Series of instrumental magnitudes
- of the same source
- for various aimasses (here 1.23 - 2.1)
- during a period with stable atmosphere
Extrapolation of the line to airmass=0
-> get magnitude OUT OF ATMOSPHERE
-> compare with HST spectrum
-> deduce system throughput in the band
Several measurements duplicated
(and almost identical)
per airmass
Only end of night used
(low+stable absorption)
30 june 2022

## Slide 12: Determination of 2nd order/1rst order
Use spectra with blue filter (125)
Extract separately orders 1 and 2
Compute ratio
Projection
Order 1
Order 2

## Slide 13: Spectroscopic reduction: état de l’art
SpecTractor operational tool for spectrum extraction
  Forward modelling, taking into account every instrumental effect:
    dispersion law, PSF(l), focus, 1rst+2nd orders, atmospheric dispersion…
  Separation of 1rst and 2nd diffraction orders now satisfactory
From RAW

## Slide 14: Spectroscopic reduction: état de l’art
- 1
Flux [erg/s/cm2/nm]
- 0
- 0.5
Filter transmission
Ha,b,g etc. stellar lines
O2, H20 atmospheric absorption bands
1st order
2nd order
HST spectrum
Hb
Hg
Hd
He
Ha
O2
O2
H2O
H2O
H2O
U
G
R
I
Z
Y
SpecTractor operational tool for spectrum extraction
  Forward modelling, taking into account every instrumental effect:
    dispersion law, PSF(l), focus, 1rst+2nd orders, atmospheric dispersion…
  Separation of 1rst and 2nd diffraction orders now satisfactory
To REDUCED

## Slide 15: Extraction of atmospheric parameters
After knowing the telescope/hologram/(filter) throughput:
Find atmospheric parameters (LibRadTran) from fit of data with model
  Ozone, aerosols, and PWV=4.55+/-0.03 (Precipitable Water Vapor)
H2O
H2O
H2O(A)
H2O(B)

## Slide 16: Control tool : EQW(O2) should depend only on airmass x pressure
EQW definition
After checking EQW(O2), we will measure
EQW(H2O(A)) and EQW(H2O(B))
H2O(A)
H2O(B)

## Slide 17: Next steps / work in progress
We have now a kind of hygrometer
- Ultimate check by comparing dispersion of measurements after/before correction
We also need to measure aerosols
- Difficulty: no sharp feature
- We have sensitivity (comparison before/after culmination, same airmass shows variations)
- Test using multiband filters with spectro
Special flat-fielding
- derived from standard flat-field
- Obtained through special telescope operations
From atmospheric parameters to color corrections
Color changes induced by water vapor
Color changes induced by aerosols

## Slide 18: Flat-fielding in spectroscopy
Flat-fielding is not standard for spectroscopy
  Ultimately, the CBP will be the best tool
  In the meanwhile,we use approximations :
    Keep only fluctuations due to camera window + CCD (dust & pixel-to-pixel gain variations)
    spatial and wavelength efficiencies factorize
  drifting star to produce a special flat-field to be tested
flat after filtering slow variations due to upstream optics
Blue flat pixel value
Red flat pixel value
Normal flat FELH0600

## Slide 19: Color changes due to water vapor
PWV=1mm
2
3
4
5
6
7
8
9
Color variations follow: Scalar(PWV)xVector(type)

## Slide 20: Color changes due to water vapor
Impact of PWV on colors
- mainly (i-z) and (z-y)
- described by Scalar(PWV)xVector(type)
- with type linked to (ugrizY)
Impact of aerosol on colors
- mainly (u-g) and (g-r)
- work in progress

## Slide 21: COMPLEMENTS

## Slide 22: Spectrograph commissioning results
Objectives of the spectrograph commissioning:
Short term: characterize the spectrograph
- Geometry -> done
- Spectrograph resolution R > 200 within [342, 1100]nm : limited by the seeing (as expected); 2x better for the second order -> ex. H9 absorption line (@383nm) clearly visible. -> OK
- Software: SpecTractor(1) operational, constantly improving -> work in progress
- Checked the equivalent width (EQW) properties -> OK
- Telescope throughputs of 1rst and 2nd orders holographic disperser(2) with Bouguer lines -> work in progress, near to end (needs one « ideal » photometric night to consolidate).
- + a faint V=11.3 standard gives « enough » signal in 30s for spectroscopy
Long term: Estimate colour corrections, as functions of the airmass, atmospheric conditions and the object UGRIZY in every LSST field -> work in progress (Martin Rodriguez-Monroy)
  Either with an atmospheric model established from the follow-up of standards throughout the night
    -> Check the predictivity of the model versus airmass AND versus azimuth
  And / or with simultaneous measurements near the LSST field (needs secondary standards and observation strategy to « follow » LSST)
    -> Rely on GAIA DR of spectra
(1) Paper in preparation (2) MNRAS 506, 5589–5605 (2021). 2nd paper in preparation.

## Slide 23: Hologram for AuxTel
Goal : measure atmospheric parameters by extracting spectrum of standards
Constraints
  Easily switch imager / spectro.
  Incident beam perpendicular to CCD-plane
  Converging beam (not parallel)
Usual gratings:
  Strong defocus due to optical path variations with the diffraction angle
  Distorsion when used with a converging beam
Holographic grating:
  forced focus on the focal plane at all wavelengths: 0th and 1rst order at same focus
  No distorsion by design of hologram

## Slide 24: Holographic element characterization
Geometry: 2 scans (wide and fine meshes); changing position of the 0 order star
Determination of the nominal zero order position (1750, 300) -> determined with < 0.5 mm precision
Transmission is found constant within >1mm from nominal position
Good focus along the full l [342-1100]nm scale -> one of the main improvements w/r Ronchi grating
Transmission efficiency -> up to 3x more than Ronchi (depending on l)
Shows the dispersion direction if zero order is here

## Slide 25: Estimating a lower limit of resolution, using narrow emission lines of Planetary nebula Hen 2-113
656 nm
762 nm
486 nm
O2
656 nm
762 nm
486 nm
907nm
953 nm
967 nm
H𝜸
star
star
star
H⍺
star
O2
CII
star
SIII
SIII
spectrum from
le Bertre et al. 1989, A&A, 225, 417
434 nm
400
500
600
700
800
900
Hologram, Texp=60s
H𝞫
OII
R a 100 (seeing/object size limited)
R a 200 (seeing/object size limited)
-> lower limits on R=l/Dl (because extended object)
-> focus OK for all l

## Slide 26: Transmission efficiency model vs test-bench measurements
Phase delay profile of holographic grating
l=400nm
l=1000nm
l=639nm
Caracteristic curve of holographic emulsion
Transmissions:
Model (lines)
Data (points)
UV transmissions measured on sky (Bouguer lines): in progress

## Slide 27: Variability of the atmospheric transmission (Stubbs et al. PASP, 119: 1163–1178, 2007)
Photometrists use photometric quality nights and narrow band filters
  No cloud
  Low humidity
  Low aerosols
LSST wants to use all nights with wide band filters
  Few clouds (grey absorption)
  Humidity (affects I & Z)
  Aerosol (affects U & G)
After correcting for Airmass:
O2, O3, rayleigh can be extracted
Then determine H2O and aerosol

## Slide 28: Auxtel : First estimates of atmospheric parameters
Variation of EQW for atmospheric lines illustrates sensitivity to atmospheric parameters (EQW)
EQW definition
Stellar lines
EQW independent on atmosphere
Atmospheric absorption lines
EQW depends on atmosphere
H2O
H2O
H2O
  ‘’fit’’ H2O :
  PWV ~ 3.2mm
data/simu(LibRadTran) for several hypothesis (PWV)
O2 atm. absorption lines
O3 atm. absorption bands
H2O atm. absorption bands
Hg
Hb
Ha
H2O
(720nm)
H2O
(820nm)
O2
(760nm)

## Slide 29: Atmospheric studies
Objective of the AuxTel calibration:
Estimate colour corrections to vector (UGRIZY)LSST for each object, as a function of
- the atmospheric parameters (airmass, PWV, tVAOD ) -> the baseline
- or the directly measured atmospheric transmission function Tatm(l, RA, Dec) synchroneously within the LSST field
What are the orders of magnitude of the corrections ?
From simulation: atmospheric fluctuations induce typically less than 10mmag (max. ~30mmag @ airmass=2 for cold stars) residual colour variations per airmass after removing grey common absorption
-> Correction precision dC needs to be such that:
0.010 x dC < wanted resolution
i.e. dC=50% for 5mmag / 10% for 1mmag

## Slide 30: Characterizing the AuxTel throughput with Bouguer lines to measure separately order1 and order 2 transmissions versus l
Spectrum extraction software (SpecTractor) needs the global throughput of the system for each diffraction order p:
Tp(l) = t(l)telescope . tp(l)disperser . eCCD(l)
-> Obtained by the ratio of instrumental out-of-atmosphere flux to HST reference flux (as a function of l)
If constant atmospheric conditions, instrumental magnitude@l follows a Bouguer line in airmass z:
mp(l,z)instrumental = m(l)SED-HST + Aatm(l) . z + 2.5.Log[Tp(l)]
At a given l, extrapolating the line from the series of mp(l,z)instrumental to z=0 airmass gives out-of-atmosphere instrumental magnitude and allows to deduce the throughput from:
mp(l,0)instrumental = m(l)SED-HST + 2.5.Log[Tp(l)]
Requirements
-> (at least) one photometric night (i.e. stable atmosphere) to obtain long series of spectra.
-> The same star needs to be measured during the same night in the widest airmass domain.
-> large # of measurements allows better determination of the slopes and of z=0 extrapolation.
Series of mp(l,z)instrumental
z
l
Extrapolated mp(l,0)instrumental
Slope depends on l

## Slide 31: Measurement of Bouguer lines
Only end of night used
(low+stable absorption)
Instrumental magnitude vs airmass
Out of atm.
SED
Measured
spectra
Example of a
Bouguer line
HD142331 trajectory in airmass
Spectra integrated in bins of 30 nm width
Extrapolated out of atmosphere instrumental magnitudes in narrow [30nm] bandwidth
Notes: The night is not photometric, however we convince ourself that the the second part of the night have lower absorption and seems for stable.
The we remains with few usable exposures to construct Bouguer lines.
Top right : this is and example of Bouguer line, but the chi2 per degree of fredoom is above 6.
Bottom right : this is the set of Bouger lines from which one can reconstruct the Throughputs.

## Slide 32: Sky background has spectrum depending on the position on CCD

## Slide 33: Factorization of the wavelength dependence
Idea:
Evaluate spatial correlation between flats with different filters
See if can factorize out the wavelength dependency on the flats:
  = out of focus artifacts (vignetting, dust on optical components) = slow pixel to pixel variation (real space) or low spatial frequency (Fourier space)
  = focused artifacts (dust on the CCD, pixel surface variations) = fast pixel to pixel variation or high spatial frequency
  We examine the hypothesis of
If ~ true, then we could preliminary use a single flat for spectra reduction
How can we test this?
  By examining the ratio of flat images at different wavelengths (with different filters)

## Slide 34: Factorization of the wavelength dependence: pixel correlation
⍴ = 0.96
Relative dispersion of ratio
ADU Relative dispersion

## Slide 35: Establishing correction procedures
We did predictions from simulations, based on parametrization with (z, PWV, VAOD). But O3 , O2 and cloud absorption (grey) can also be parameters.
The methods have to be systematically checked for every atmospheric situation:
  Predictability of the correction in (airmass, azimuth)
  Needs observation of CALSPEC standards through entire nights (to estimate atm. parameters) AND various fields in (airmass, azimuth) containing standards to test the prediction. « ronde des standards ».
Alternative: directly measure atm. transmission in the same direction than LSST, using secondary spectrophotometric standards measured out of atmosphere by GAIA. We checked that spectra of stars as faint as M=10 are measurable in 30s with s/b>100