## Slide 1: Network between CC-IN2P3 and KEK
Soh Suzuki

## Slide 2: Topology
KEK
SINET
GEANT
RENATER
U-Tokyo
IN2P3
10G (x2)
10G (x2)
7G
Peering of SINET and GEANT is at MANLAN.
The bandwidth from there to JP is shared with traffic for commercial peering (3G).
KEK and U-Tokyo has almost same bandwidth to SINET.

## Slide 3: SINET4
NII which manages SINET, has started the preparation of “SINET4”.
When LHC data transmission had started, they realized the fat traffic of HEP experiment.
  The bandwidth which was allocated to research networks such as ESNET was almost occupied by ATLAS data drill.
Currently they are planning the upgrade the line to the east coast of U.S. to 20G, for the traffic to Europe.

## Slide 4: PerfSONAR at KEK
Belle 2 collaborator in University Melbourne asked us to configure some network bandwidth test at KEK side.
Already they are using PerfSONAR and proposed it.
We configured it as “perfsonar-test1.kek.jp” and it is listed in lhcperf.bnl.gov automatically.

## Slide 5: PerfSONAR at KEK (Cont.)
Low level test via bwctl by hand seemed to work well, between University Melbourne.
  But most of functions provided by PS-toolkit are out of use at the end of last year.
  What versions are preferred for HEP community, it is not clear.
If this is useful to monitor the bandwidth and network conditions, please let me know the parameters…..