## Slide 1
P2IO 1 December 2022
Proof of the principle experiment of Machine Learning based online Characterization and Optimisation of a high intensity LAser pulse (ML-COLA)
Viacheslav Kubytskyi, Moana Pittman
Laboratoire de Physique des 2 infinis Irène Joliot-Curie – IJCLab

## Slide 2: Outline
CPA technology
STC problems in the context of PALLAS
Measurements with multispectral camera
Next steps

## Slide 3
Source: Fabien Quere. Methods for characterisation of high-power femtosecond lasers
Need to focus all spectral components of the pulse into very small temporal and spatial dimensions.
Requires: high level expert, advanced diagnostics and many adjustment iterations.
CPA technology

## Slide 4
Important: Short bunch focusing, intensity at focus.
High energy pulse compressor
Laser control and beam quality in a context of laser plasma experiment PALLAS
Laser control. Real time & integrated
Plasma cell
Diagnostics and transport
Ultrashort laser pulse needs to be broad spectra.
Chromatic optical elements misalignment leads to residual cromaticity.
UHI CPA LASERIX
  40TW 1.6J / 40fs @ 10Hz
Notes: Complete spatial, spectral , temporal(Frog) in real time
MISS 2-spatioo specteral 2d inferommetry
Measure longitudinally , transversally and combine.

## Slide 5
J. Opt. 22 (2020) 103501 (33pp) https://doi.org/10.1088/2040-8986/abad08
Spatio-temporal characterization of ultrashort laser beams: a tutorial
Spencer W Jolly, Olivier Gobert and Fabien Qu ́er ́e
One example of STC: pulse-front tilt
When it is important:
Intensity at the focus is the most critical parameter of a laser pulse.
Misalignment of compressor gratings can lead to STCs such as PFT.
What is STC?
Notes: Measure “length” locally

## Slide 6
Principal idea of the project
Automatization
Laser beam quality, compressor alignment GOOD or BAD?
ML learns automatically, from image details and additional diagnostics.
Decompose imperfections and perform necessary corrections

## Slide 7
Is it possible to measure?
With scan-based technique like Termites/Insight. Very precise, but slow.
Reconstruction algorithms.
In ML-COLA we proposed to use multispectral camera coupled with ML methods in order to perform snapshot measurements for laser characterization.
Spatio-spectral intensity & Spatio-spectral phase

## Slide 8
Measurements with multispectral camera
-0.31 mRad
-0.42 mRad
0.42 mRad
0.31 mRad
0 mRad

## Slide 9
Channel by channel.
Notes: Clearly see misalignments follow spectrum.

## Slide 18
Feature extraction with VGG16
Pretrained model
Similarity between channels.
adapted to 8 channels inputs
classification

## Slide 19
Optimisation and ML tasks.
Structural similarity
Autoencoders
Feature extraction
Measurements dataset for training. Data taking of labelled data.
Robust bounded optimizer
Transfer learning, domain adaptation
DATASET:
Amplitude and phase data: images from multispectral camera and INSIGHT/termite measurements
Compressor and principal laser parameters: (u, v, d), adaptive mirror configuration, timings, temporal length, energy, pointing stability etc.
Categorical labels assigned by the laser expert
Notes: We want ML learns automatically, form image details. GOOD or BAD alignment?

## Slide 20
Camera delivery : December 2021.
Setup, tests and several measurements. Automatization.
PhD student Gueladio Kane
2023: data + ML
Equipment to buy: achromatic objective optics, motorization,
special Notch filter, PC for automatization and ML.
Timeline and next steps

## Slide 21
Outcomes:
Unique diagnostics of ultrashort high intensity laser
Online control and shot to shot stability.
Laser characterization for PALLAS.
Key idea: Snapshot measurement combined/reinforced with ML techniques.
Summary

## Slide 22: LASERIX platform at IJCLab
Equipements : UHI CPA Laser
  40TW 1.6J / 40fs @ 10Hz (37J @ 0.1Hz démontrés en 2007) (*)
    → matériels disponibles et « gros » potentiel d’upgrade
  Base Amplitude Laser « customisé » (flexibilité & performances)
  Contrôle Commande développé avec Amplitude Laser, évolutif
(*) F. Ple et al., "Design and demonstration of a high-energy booster amplifier for a high-repetition rate petawatt class laser system," Opt. Lett. 32, 238-240 (2007)
Activités Scientifiques / Techniques
  R&D sources intenses (laser, XUV) et diagnostics spécifiques
  TP lasers intenses (M2-GI-PLATO, Polytech)
  Applications : Physiques des Plasmas, matériaux, irradiation, expériences résolues en temps (régions XUV - NIR), façonnage de faisceaux XUV, Physique non-linéaire, QED (Dellight) et… accélération par laser : PALLAS
Temps faisceau
  PALLAS 50% (20 semaines)
  Autres 50% (20 semaines)
  Maintenances (7 semaines)
  Arrêt : Août (5 semaines)
Notes: Main characteristics: CPA, energy
Beam lines, experiments (Q, PALLAS)
Nautilus, compression gratings - STC