## Slide 1: Nuclear Emulsion in neutrino precise measurements.
Osamu Sato Nagoya University
For
B02 group in Grant-in-Aid for Scientific Research
on Innovation Areas
“Exploration of Particle Physics and Cosmology with Neutrinos”.

## Slide 2: Nuclear Emulsion detector: 3D tracking device with 50 nm precision
20 m
10 GeV/c 
beam
Sensitivity 36 grains/100 m
Cross-sectional view
Plastic base (200 m)
Emulsion layer (44 m)
Emulsion layer (44 m)
200 nm
Emulsion film
AgBr crystal 1014 crystals in a film
Object lens
Camera
Charm particle (X particle) was detected by emulsion first.
KOBAYASHI Makoto: Nobel Prize Lecture

## Slide 3: Automatic Track recognizing microscope
Emulsion detector contributed to elementary particle physics.
While there was a big problem.
The readout of tracks was time consuming by human eye.
Majority of people gave up and use electronic detector.
Nagoya university pioneered the automatic tracking microscope from 1970 .
Continuous improvements, tack readout speed increased 100 times / 10 years.
The automatic track recognizing
microscope change the story.
Now experiments
with emulsion detector
become comparable scale
with other experiments.
Speed in cm2/h
0.003
0.082
1
72
4500
0.001
0.01
0.1
1
10
100
1000
10000
TS(TTL)
NTS(CPLD)
UTS(FPGA)
SUTS(FPGA)
HTS(GPU)
1000m2/Year
HTSⅡ
3m2
100 Times faster by every 10 years
1983 1994 1998 2006ｰ 2015～ 2022

## Slide 4
4


1mm
Emulsion
鉛
OPERA nmnt
15万個のＥＣＣ 1250 トン
1300トンがニュートリノを待ち構える
730㎞
nm->nt?
2008-2012
Pot = 17.96 1019
< E > ( GeV ) 17
(e + e) /  0.89, 0.06 %
 /  2.1 %
 prompt Negligible
ECC 57 films 56 Pb
2
g1
3
g2
7
5
1
6
8 daughter
τ−→ρ− ντ
ρ−→π0 π-
π0 → γ γ
First nt event in OPERA NEUTRINO2010
Phys.Lett. B691 (2010) 138-145
ECC
56 pb+ 57films
12.5 x 10 x7cm3 8kg
OPERA Full detector 1250 tons 15000 ECC
Notes: 4

## Slide 5: Evolution of Emulsion Scanning Speed and Decline of Photographic Film Industry
Emulsion scanning speed (cm2/h)
Chart: 
| 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
TS | 0.082 | 0.082 | 0.082 | 0.082 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 72 | 72 | 72 | 72 | 72 | 72 | 72 | 72 | 72 | 4700 | 4700
フィルム | 76.0355 | 84.9112 | 90.5325 | 96.4497 | 88.7574 | 98.2249 | 100 | 92.8994 | 94.6746 | 86.3905 | 74.5562 | 70.4142 | 53.5503 | 31.0651 | 19.8225 | 11.8343 | 8.284
Discovery
of nt
in DONUT
1st event of
νμ→ντ
in OPERA
(total 10 events)
Global demand for color film* (relative)
We started the development and supply
of Nuclear Emulsion itself in our laboratory (2010–)
Current system “HTS”
*data from FUJIFILM
1/10
in 10 years
Peak in 2000
Crisis for
future emulsion
experiments !!
→New system “HTS-Ⅱ” (developing)
will be 25000 cm2/h (x5 faster)
5000 cm2/h

## Slide 6: Subject other than track readout
A giant supplier of emulsion, FUJI Film reduced its production. (Digital camera era.)
Then Preparation of Enough emulsion films is subject to promote projects.
Our survival plan
Developing / constructing New Emulsion Production Facility in NAGOYA university.
Scale of a total nuclear emulsion area of several 100 m2 or 1000 m2.
First experiments we supplied or will supply soon the Emulsion films.
DsTau (NA65 CERN SPS), Study for tau neutrino flux. supplied for 2021(22) run
FASERn (LHC), Study of High Energy neutrino from the LHC. supplied for 2022 run
SND@LHC (LHC) , Study of High Energy neutrino from the LHC. supplied for 2022 run and
GRAINE Precise measurement of cosmic gamma rays supplied for 2023-Spring
Balloon flights in 2023 (NOW)
NINJA (J-PARC), Study of sub-GeV GeV neutrino interactions to be supplied 2023 run
Scan Pyramids Muon radiography for Pyramid Considered
Observation from multiple observation site for targets

## Slide 7: Install of 10 times large-scale Gel Production Machine(3rd machine)
New Machine enables the stable & long-term mass-production.
120ℓ
12ℓ
4ℓ
1st
2nd
3rd
We
automatize
preparation,
liquid transfer,
washing, …etc

## Slide 8
achieved production speed
of ~8 m2/day
2021 May.-
Roll-to-roll emulsion film coating facility
started practical operation
(Real production in the dark)
Coating
Drying
Winding
Melting
Double-sided emulsion film
after two processes
2019 Oct.– Start installation

## Slide 9: Result of Mass Production in the new facility
Photo at 100th batch
~125m2/month
(=1500m2/year)
2023/01
2022/01
2022/07
2021/07
2021/05
Start mass production
20230326
200th batch
1 batch ~2Bottle(8m2)

## Slide 10: Performance of Films
Stable quality of Grain Density and Fog Density at long production
Master thesis 2022(Usuda)
20 m
10 GeV/c 
beam
Sensitivity 36 grains/100 m
Signal: Grain Density
High is good
NOISE: Fog Density
Low is good

## Slide 11: DsTau(CERN NA65)
Physics Target
  Precise understanding of ντ production flux
    Measurement of differential (XF, Pt) production cross section of Ds
  Reduction of tau neutrino nucleon cross section uncertainty 50% → 10%
    Update of tau neutrino cross section given by DONUT by new knowledge on tau neutrino flux.
    Inputs for future tau neutrino projects : SHiP ντ
  Byproduct study
    Charm production： forward production, 、 intrinsic charm ?
    Charm hadron’s interaction cross section measurement.
Tau neutrino production study principle
  Double kink decay topology + partner cham.
DsTau web site
https://na65.web.cern.ch/
D+
Ds
τ
ντ
Proton beam
ντ
X
X'
~5 mm
Small kink angle(7mrad)
Ds → τ kink decay
11
Physics run 2021-2023
Notes: 1 mrad = 0.057 deg

## Slide 12
FASER and SND@LHC

## Slide 13
Veto
FASER
Emulsion/tungsten
neutrino detector
Neutrino
beam
FASER spectrometer
Emulsion film
(precision tracker)
1 mm tungsten plate
(neutrino target)
A total weight of 1.1 ton neutrino detector
tungsten and emulsion could chamber
3 neutrino flavors will be detected / studied.
Emulsion films ~55 m2 x 3
replacements/yr
will be identified using the FASER
magnetic spectrometer
The main FASER detector was successfully installed in March 2021.
Interface tracker
First electron neutrino
Candidate in FASER2022
FASERn (ForwArd Search ExpeRiment): neutrinos study in the currently unexplored TeV energy region
LHC Run 3 (2022-2025)
LHC magnets
Charged particles
480m from IP

## Slide 14
A neutral vertex in ECC
5 ECC walls 830kg, 44m2 emulsion total surface.
3 or 4 times replacements /yr. 4 times changes in 2022

## Slide 15: GRAINE Project
Scientific
Balloon Launch
provided by
ISAS/JAXA
Cosmic γ-ray Observation in sub-GeV/GeV
using Balloon-borne Nuclear Emulsion Telescope
GRAINE2018 Demonstrated
Detection of Vela pulsar
Highest Imaging (0.5°,>80MeV)
GRAINE2023 Starts
Scientific Observation
with Large-scale Telescope
Almost Ready for launching !
Total surface of emulsion :250m2
≒GRAINE2018
x 6.5
Dedicated talk
by S. Aoki
16:30- Today
  – High-res imaging of Vela in GeV region
  – Obs. of Gal. center
  – Survey for transient sources

## Slide 16
Neutrino Interaction research with Nuclear emulsion and J-PARC Accelerator
Precise measurement of neutrino-nucleus cross-sections in Sub-Multi GeV
Electron neutrino cross-section measurement
Sterile neutrino search
10μｍ
Nuclear Emulsion
A neutrino interaction in emulsion @J-PARC
Plenary talk today (17:45-)
Proton momentum
Current detectors
Difficult to study
Neutrino-water interactions

## Slide 17: Summary of B02 Emulsion amount for
B02
Emulsion
B02 constructed a new emulsion production facility at Nagoya university.
Started supplying emulsions to REAL projects and producing physics results now !
Together with production, polishing emulsion quality and production process improvement is continued in order to increase the production power and reduce man power ..
Installation / Beam exposure Year | NINJA Total Emulsion surface(m2) | DsTau Total Emulsion surface (m2) | FASERnu Total Emulsion surface (m2) | SND Total Emulsion surface (m2) | GRAINE Total Emulsion surface(m2)
2018 | 10 | 49 | 30 | 0 | 42
2019 | 120 | 0 | 0 | 0 | 0
2020 | 25 | 0 | 0 | 0 | 0
2021 | 0 | 110 | 0 | 0 | 0
2022 | 0 | 110 | 130 | 140 | 0
2023 | 250 | 200 | 180 | 176 | 250（500）
2024 | 400 |  | 180 | 176 | 
2025 | 600 |  | 180 | 176 | 
GRAINE

## Slide 18: Summary
Emulsion readout / analysis is not bottleneck now.
Giant supplier of emulsion, like FUJI, reducing production.
We decided to install large scale emulsion production facility in
Nagoya University and target production speed of several 100 m2 to 1000 m2.
Construction started 2019 and became good shape in 2020 and continue producing emulsion films through the years.
The coated and cut emulsion films supplied from 2021 for (DsTau) and 2022 for (DsTau, FASER, SND@LHC) and ready for (GRAINE) observation.
Currently producing gels for NINJA and DsTau, FASER, SND@LHC fotr2023 run.
Total supplied emulsion film (total surface)
2021 110 (DsTau)m2
2022 110(DsTau)+ 130(FASER) + 140(SND)m2
The supplied amount of emulsion is nearly reached to original plan.
Now it start producing preliminary but good physics results.
We continue producing emulsion films for next experiments ..

## Slide 19: backups

## Slide 20: Use of NAGOYA Emulsions
2nd machine
(x3 scale)
1st machine
(x1 scale)
2010
2010- Install & development started
2013- Supplied self-controlled films to real experiments.
2014- New projects launched. Successfully achieved good results.
2019- All projects plan to expand the scale of experiment
R&D
Dark Matter
Search
SND/SHiP
2023
2014
10
100
1000
10000
1
2019
Use of Film [m2/Year]
3rd machine
(x30 scale)
Next-generation
scanning speed
& Coating machine
Gamma-ray Telescope
Muon Radiography
NINJA
ENPHATIC
DsTau
FASERν
ν
γ
μ

## Slide 21
乾燥10m
13 m
乾燥
乾燥
> 1000 m2/y is possible by this facility!!
Emulsion Coating facility
“Roll-to-Roll
Coater”

## Slide 22: Installation of Roll-to-Roll Coater
2019 Oct.– Start installation

## Slide 23: Film Production for FASER-nu 2022 run
Gel Production
Gel-to-Film (coating & drying)
Cutting into Sheet (250 x 300 mm2)
Resetting process
(humidity control)
Shipping to CERN
✓Installation in Mar.
✓Installation in Jul.
✓Installation in Sep.
Provided 150 m2
Emulsion Film in total.

## Slide 24: The detector structure (~400 modules) 2.3x108 Proton-tungsten interactions （4.6x109 POT）
Target
Detecting about 1000 Ds → τ →X decays
10 Units
(A total of 100 nuclear emulsion films )
Another 2 units for momentum evaluation
(25 films）
400GeV/c
Proton beam
Decay Volume & Tracking detector
Proton beam
105/cm2
Ds
ντ
ντ
D+
X
X'
τ
Plastic plate (200 μm)
Nuclear emulsion film (320 μm)
Tungsten plate(0.5 mm)
DsTau paper:
10.1007/JHEP01(2020)033
tungsten
plastic
emulsion
Tungsten
Emulsion PLASTIC
Notes: 役割を説明
target, decay volume

## Slide 25: Interaction at tungsten Some distribution comparison Data/MC
IP Multiplicity Space angle
IP (um) Multiplicity (本) angle (rad)
It looks EPOS MC reproduce real data well.

## Slide 26: Molybdenum target from 2021 run
The neutrino source , the beam dump of DONuT experiment was tungsten target .
On the other hand, future experiment SHIP will use molybdenum alloy together with tungsten for beam dump.
In 2018 pilot run, we exposed proton only modules with tungsten(0.5mm thick) modules.
From 2021run, also molybdenum (1.0㎜ thick）modules.
A subsample data of molybdenum interactions shows following features.
Charged track multiplicity of proton interaction is less than tungsten target case.
Angle distribution of secondary particle is nearly same with tungsten target case.
IP is bit larger but it is expected by thickness difference of target plate.
Charged track Multiplicity IP to 1ry vertex Angle distribution of 2ry trk

## Slide 27: FASERn (ForwArd Search ExpeRiment): neutrinos study at un-explored energy region
100 m of rock
480 m
Service tunnel
LHC tunnel
Neutrinos (and new particles)
LHC magnets
p-p collision at ATLAS
Neutral hadrons
Charged particles
FASER
Notes: Here, I propose a novel approach to make use of this intense neutrino beam.
Let’s follow what happens after proton collision in ATLAS. A bunch of forward mesons are created and some of them decay into neutrinos. Charged particles are deflected by the LHC magnets. Neutral hadrons stop in the rock. Finally only neutrinos can go further.
What a coincidence, there is a disused service tunnel and a space is available. Let’s put a neutrino detector, LHCnu. Although this is not designed as a neutrino beamline, this setup functions as a neutrino beamline. In this way, I can exploit neutrino beam from the LHC with a negligible cost for infrastructure. This is a big advantage of LHCnu, because if you want to build a dedicated neutrino beamline, it would cost minimum 100 million euro.
In fact, the use of this location was first proposed for the dark photon search by the FASER Collaboration, including myself. LHCnu will be a part of the FASER activity.

## Slide 28
Basic measurements :
0.4 mrad
0.4 mrad
20 mrad
Angular Scatter Plot (2nd module)
0.19 m
Position resolution
2022 2nd module (10.6 fb-1)
1000 m
 | track density (/cm2/fb-1) (within 10 mrad from the peak)
2022 1st module (0.5 fb-1) | 1.2104
2022 2nd module (10.6 fb-1) | 1.3104
 | track density (/cm2/fb-1) (within 10 mrad from the peak)
2022 1st module (0.5 fb-1) | 
2022 2nd module (10.6 fb-1) | 

## Slide 29
Track q/p distribution
Observation of CC interactions by FASER spectrometer

## Slide 30
Ettore Zaffaroni slide at Moriond2023

## Slide 32: GRAINE2018 Balloon Experiment
✓ Detection of Vela pulsar (7.4σ)
✓ World’s Highest imaging 0.51deg 68%radius (>80MeV)
0.4m2 telescope
Balloon Flight in AUS
Flight duration ~17h
JAXA Balloon Program