## Slide 1: Intra- and inter-field imaging of proton therapy with the PETITION PET detector
Keegan McNamara :: Paul Scherrer Institute
24.4.2023

## Slide 2: PET for range verification
Proton therapy gives highly conformal dose distributions and spares healthy tissue
Range uncertainties can lead to over/under dosage of tissue
Positron emitting isotopes can be used for in-vivo validation

## Slide 3: PETITION PET detector
PET for InTensive care and Innovative iON therapy
Open-ring PET detector for in-beam imaging in Gantry 2 at PSI
Current design fixed to 90˚ increments
  Full clinical implementation would require PET scanner to rotate with Gantry nozzle

## Slide 4: Basic imaging protocol
During treatment 12N (t1/2 = 11ms) is formed
  Spot delivery time 5-100 ms
  Energy layer change time 100ms
Post field irradiation imaging 15O, 11C, 38K, etc.
  Couch and Gantry movements take >30s between fields
Notes: Coincidences label

## Slide 5: Simulation workflow
*Keegan McNamara et al 2022 Phys. Med. Biol. 67 244001
TPS
(FIonA)
Dose & activity calculation
(FRED)*
Isotope decay & imaging
(GATE)
Image reconstruction
(SIONARA)

## Slide 6: Energy layer imaging
Pauses between each energy layer allow for imaging
Ideally: ~100 ms energy switching time enough to image 12N (t1/2 = 11 ms)
  Scanner saturation
  Dead time of crystals
  Low SNR
  Build up of longer lived isotopes

## Slide 7: Inter-field imaging
Time between fields ~60 seconds, allowing for direct imaging of each field
Following final field longer imaging time is feasible

## Slide 8: Inter- and post field imaging
Opening of scanner leads to loss of counts and spatial resolution
Normalised root mean square error (NRMSE)
NRMSE=2.70 NRMSE=1.97 NRMSE=2.88

## Slide 9: Inter-field imaging with rotations
In a clinical setting, scanner must be manoeuvrable to next field delivery position
Why not acquire during this period?

## Slide 10: Inter-field imaging with rotations
Moves opening (low sensitivity) away, giving higher count rate
Boost spatial resolution in different regions
Notes: 204’300 fixed, 229’500 rotating 90˚, 281’200 rotating 450˚

## Slide 11: Inter-field imaging with rotations
Symmetric ION therapy Accelerated Reconstruction Algorithms (SIONARA)
Reconstruction of PET images aquired at different angles is memory intensive
  System matrix required for every position
Instead one matrix can generate many others!
Publication in preparation

## Slide 12: Inter- and post field imaging
With 90˚ rotation to next imaging position, spatial resolution is partially recovered
NRMSE=1.40 NRMSE=1.15 NRMSE=1.02

## Slide 13: Inter- and post field imaging, rotating scanner
With 450˚ rotation to next imaging position, spatial resolution is fully recovered
NRMSE=1.32 NRMSE=0.99 NRMSE=0.91

## Slide 14: Summary
In-beam imaging provides verification possibility during delivery of first field
Fixed position inter-field imaging poses challenges due to poor image quality
Rotating scanner between fields drastically improves verification capabilities
Outlook
Incorporating BEV range analysis
And…

## Slide 15: Early measurements
Comparison to simulations upcoming!

## Slide 16: Wir schaffen Wissen – heute für morgen
Acknowledgements
Shubhangi Makkar
Christian Ritzer
Cristian Fuentes
Judith Flock
Marina Beguin
Daniel Lempen
Martina Bochsler
Anne-Sophie Bogaert
Jan Hrbacek
Prof. Damien Weber
Prof. Günther Dissertori
Carla Winterhalter
Prof. Tony Lomax

## Slide 17: Other views

## Slide 18: Other views

## Slide 20: Scanner properties
2.74x2.74x15 mm3 LYSO crystals
Energy resolution: 12% (FWHM)
Timing resolution: 500ps (FWHM)
Spatial resolution: 1.8-2.7 mm
SiPM Board
ASIC Board
Main Board
x 6
x 12
Images courtesy Cristian Fuentes
Notes: If theres time