## Slide 1: Contribution to ITS3 design proposal from IPHC

## Slide 2: Introduction
4 main axes
  Digital flow
  Pixel readout and pixel array
  Power and rails simulations
  Analogue Front-End optimisations
Resources
  Mainly in the digital with strong backend background
    3 FTP: X. Fang, F. Morel, and A. Himmi, G. Bertolone and J. Soudier for 1 ETP
  Expertise in analogue front end
    1 FTP: A. Dorokhov
    Also C. Lemoine with Walter’s thesis

## Slide 3: Digital flow
Digital flow is not unique, the choices can have a strong impact on the design
  Verification capabilities
  Design duration
  Hardware limitation (CPU, RAM)
Stitched sensor is very demanding on the capabilities of the tools
Need to elaborate a strategy on the flow
  We can help with our experience on previous design
  To select and configure most effective verifications

## Slide 4: Pixel matrix and readout 1/2
Experience on column readout
  MIMOSIS chips
  MOSS
Better to assemble the pixel matrix with Innovus
  Best control of the digital (reduce respin)
  Can merge Digital pixel and Column readout
  Can make analysis at early stage with the Blackbox flow
    IR drop, Crosstalk, Timing, Congestion
  Respin of the matrix
Column
Readout
Collection
Diode
Collection
Diode
Collection
Diode
Collection
Diode
Digital
Pixel
Digital
Pixel
Analog FE
Digital
Pixel
Digital
Pixel
Analog FE
Analog FE
Analog FE
22.5 / 25 µm
17 / 18 µm

## Slide 5: Pixel matrix and readout 2/2
Even if the digital tools are used, the same quality can be achieved
  Complex and controlled routing is possible
Xiaochao and Frederic are former analogue designers
Current activities:
  Column readout study has started (Xiaochao)
    Preliminary results: width of 16 µm is achievable with 4 routing metal layers with standard width and spacing
  Flip-flop as memory has not been started (Frederic)
    Further implication on the pixel matrix readout?

## Slide 6: Power and rails simulations
Power and rails simulations are crucial with ER2
Need to start as soon as possible
  Will help sizing power rails
Embedded regulators
  We have started to study power rails on chip with embedded regulators
  OBELIX for BELLEII experiment

## Slide 7: Analogue Front-End optimisations
Andrei's expertise is well established
Andrei and Walter are a good duo