## Slide 1: TIIMM Sensor’s overview
TIIMM0 (second submission)
Chip area: 2.2 mm * 1.5 mm
Matrix: 32 (rows) * 16 (col)
Pixel pitch: 40 μm×40 μm
Corrected from the first
submission
TIIMM1 sensor
Chip area: 2.2 mm * 1.5 mm
Matrix: 32 (rows) * 24 (col)
Pixel pitch: 41.2 μm×40 μm
TIIMM1A sensor
Chip area: 2.2 mm * 1.5 mm
Matrix: 46 (rows) * 32 (col)
New front end
Analog part study only
TIIMM1B sensor
Chip area: 2.2 mm * 1.5 mm
Matrix: 32 (rows) * 24 (col)
Pixel pitch: 41.2 μm×40 μm
  - First submission: preliminary prototype (TIIMM0) submitted in March 2020.
  - Second submission: TIIMM0/TIIMM1/TIIMM1A/TIIMM1B prototypes received in August 2022
CMOS Monolithic Active Pixel Sensor
design in TowerJazz 180 nm process
For position and energy measurements
Thickness | Process | 
25 m Epi High Res. | Standar | Non-uniform N- layer Uniform N- layer + Extra Deep
50 m Epi High Res. | Non-uniform N- layer Uniform N- layer + Extra Deep P | 
100 m Epi High Res. | Non-uniform N- layer Uniform N- layer + Extra Deep P | 
7 sensing layer variants
New front-end
New front-end enhanced

## Slide 2: TIIMM1B: Single pixel Analog Front-end
Pixel pitch: 40 μm × 41.2 μm
ToT (6 bits)
AC coupling
Cf = 3.75fF， Cd = 2fF
Gain=29mV/ke-, ENC: 102 e-（extracted sim）
Threshold=1000e-

## Slide 3: TIIMM1B (Transistor level - simulations only)
TIIMM1 comparator offset
TIIMM1B comparator offset
TIIMM1 vs TIIMM1B
Amplifier structure optimized
for larger input dynamic range
New Comparator structure with
less intrinsic input offset
 | TIIMM1 | TIIMM1B
Range of TOT | Maximum at 250ke- | Maximum at 700ke-
Comparator input offset | 6.6 mV | 2.7 mV
Qin (ke-)
TOT(µS)
TIIMM1B comparator
TIIMM1 comparator

## Slide 4
La comparaison (Réglages typiques)
TIIMM1B
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
TIIMM1.
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
TIIMM0
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
Amplitude du CSA vs Qin (500 e-~150 ke-)
Largeur de signal du comparateur vs Qin (500 e- ~150 ke-)
La partie ~ linéaire du ToT est de 500e- à ~110 ke-.
La partie ~ linéaire du ToT est de 700e- à ~ 250 ke-.
La partie ~ linéaire du ToT est de 1Ke- à ~ 700 ke-.
Amplitude du CSA vs Qin (0,7Ke -~ 300 ke-)
Largeur de signal du comparateur vs Qin (0,7k e- ~300 ke-)
Amplitude du CSA vs Qin
(1Ke -~ 800 ke-)
Largeur de signal du comparateur vs Qin (1k e- ~800 ke-)
4

## Slide 5
La partie linéaire reste sensiblement la même.
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
La partie linéaire reste sensiblement la même.
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
La partie linéaire reste sensiblement la même.
Qin (ke-)
Qin (ke-)
Amplitude of the csa_vout (V)
Pulse width of the comparator (µS)
Amplitude du CSA vs Qin
(500 e-~150 ke-)
Largeur de signal du comparateur vs Qin (500 e- ~150 ke-)
Amplitude du CSA vs Qin
(0,7Ke -~ 300 ke-)
Largeur de signal du comparateur vs Qin (0,7k e- ~300 ke-)
Amplitude du CSA vs Qin
(1Ke -~ 800 ke-)
Largeur de signal du comparateur vs Qin (1k e- ~800 ke-)
Avec 3 courants de bias (ampli) différents : 30nA, 60nA et 150nA
TIIMM1B
TIIMM1.
TIIMM0
5

## Slide 6
TIIMM1B – First Functional test results (single pixel)
Pulse width (s)
TOT counts
Input amplitude (V)
TOT counts
External digital pulse generator (hits emulator)
TOT counting is correct (6bits)
Internal analog injection pulse
(using parasitic capacitor)
The full chain working
Digital part
Full chain
Setup:
ADC – SOC (FPGA: Cyclone V with ARM- A9 running Linux)
Automatic controlled Pulses generator
Sensor prototype wire bonded on custom board
monitoring ADC, biasing DACs, analog outputs readout
Full control acquisition system
TIIMM1B Sensor covered
TOT: Time Over Threshold
TOT: Time Over Threshold

## Slide 7: TIIMM1B – First Laser tests
Pulsed Diode LASER
(Model LDH-P-C-N-1060)
TIIMM1B sensor
Pulse generator
(Model HP 811A)
We can move the laser spot in
x/y direction with 1μm step precision
We are able to inject charge in a single pixel
Positioning and number of laser pulses are remotely controlled
8 analog outputs to perform
different measurements with
the oscilloscope
Selectable repetition frequencies: 3.25 KHz to 80 MHz
Wavelength (average): 1061 nm
Peak power (intensity): from 18 mW to 400 mW
FWHM (time-width): 88 ps to 500 ps
Single pixel CSA output signal
with 2 laser pulses
Width: 5 ns ; Period: 10 ns
Amp: 2 V
Leading-edge: 2ns ; Trailing-edge: 2ns

## Slide 8: TIIMM1B – First Laser tests - Full matrix heat map
5 Laser pulses
50 Laser pulses
180 Laser pulses
130 Laser pulses
130 Laser pulses
180 Laser pulses
880 ke-
660 ke-
440 ke-
220 ke-
0 ke-
Pixel number
Pixel number

## Slide 9
TIIMM1B – CSA output preliminary tests with Fe55 source - Calibration
Fe55
Noise
2 laser pulses
4 laser pulses
Superposition of 3 histograms
Histogram of the output voltage
of the CSA with 2 laser pulses
(single pixel)
Histogram of the output voltage of the CSA with 4 laser pulses (single pixel)
Histogram of the output voltage
of the CSA (single pixel) with a Fe55 source only
9

## Slide 10: TIIMM1B – First Laser tests Energy loss measurement (single pixel TOT)
Qin (ke-)
TOT(µS)
Measurements
9,8 ke-
24 ke-
240 ke-
490 ke-
635 ke-
880 ke-
Simulation
Range of measured charges on single pixel: ⁓ [500e- , 900Ke-]
Charge Sensitive Amplifier output voltage (oscilloscope)

## Slide 11
TIIMM1B – First Laser tests Energy loss measurement (single pixel TOT)

## Slide 12
Merci de votre attention