## Slide 1
Main Telescope
Auxiliary Telescope
AuxTel
Hologram recording
Use as disperser
Le telescope auxiliaire (AuxTel)
D. Boutigny, S. Dagoret-Campagne, J. Chevalier, L. Le Guillou, M. Moniez, J. Neveu, M. Rodriguez-Monroy + Observing team (Patrick, Merlin, Tiago, Craig, Erik, Ioana, Alysha & others)
Rubin-LSST France, LPNHE, 30 nov. 2022
Notes: Ne pas rentrer dans les détails

## Slide 2: AuxTel spectrograph mission: measure the atmospheric transmission to derive the expected fluxes for each object under standard atmospheric conditions
Estimate colour corrections, as functions of the atmospheric conditions and of the object UGRIZY in every LSST field
Example below
- Constant airmass, constant O2 and O3. No cloud
- Change only : H2O (PWV), Aerosols
AuxTel spectrometer
Wet/dry
Aerosol/no aerosol

## Slide 3: Some facts about AuxTel
Telescope
- D = 1.20m, f/D = 18, f = 21.6m
- Depth of focus 1 arcsec (10 pixels) for 1.8mm change in distance (small aperture).
- Secondary mirror (M2) Obturation: 0.3m
Total collection area : S= 1.06 m2 (taking into account M2 obturation)
Zero point : M(no filter nor dispersor) = 27.8 – 2.5 Log10(Flux in ADU/s)
Detector
- Plate scale: 105µm/arcsec -> about 10 pixels/arcsec.
Field of view : 6.3 Arcmin.
CCD gain ~ 1.1 -> 1.3 (from 2022/09/22) photoelectron/ADU
Light distribution
For a sky background of 20 mag/(‘’)2 (~ full moon): expect 13 ADU/pixel/s
For a sky background of 22 mag/(‘’)2 (~ new moon): expect 2 ADU/pixel/s
Saturation (no filter, no disperser, assuming seeing of 1’’): Msat=13.35+2.5Log10(Texp/30s)
Geometry
- Distance camera window-CCD : 63.85mm. Light beam diameter at this distance : 3.55mm
- Distance dispersor-CCD: ~ 191.4mm (tilted). beam diameter at this distance : 10.6mm
- Distance filter-CCD : 229mm (tilted)

## Slide 4: AuxTel observation ecosystem newcomers welcome
3000-4000 spectra taken since feb. 2021
One 3-night run per month (new moon)
Now two runs/month
One contact person for each run
Sometimes online participation
  From 2am (Paris-time)
Strategy updated (JIRA ticket) for each run
Data reduction -> Sylvie
Check (direct or the day after) with Rubin-TV
https://roundtable.lsst.codes/rubintv/summit/auxtel
Slack channels
  Run preparation: auxtel-operations
  Control room: summit-auxtel
  Data reduction: auxtel-computing
  Analysis: desc-pc-auxtel

## Slide 5: How does it look like?
Atmospheric dispersion (x20)
hologram dispersion

## Slide 6: AuxTel: chantiers en cours
Image reduction
- Flat-fielding in spectroscopy : analysis -> Martin
- Hardware: flat-fielding in spectroscopy / mitigate impact of field stars : -> Marc
Spectrum Extraction
- Full understanding of order2/order1
- Understanding of telescope throughput
Atmospheric studies
  Fit of atmospheric parameters
  - Known –constant- atmospheric effects (not measured): Rayleigh
  - Variable atmospheric parameters : water, ozone, aerosols, clouds
  Estimated at airmass=1
Compensation of the color variations due to atmosphere (Discussion). Color changes induced by water vapor / aerosols

## Slide 7: Flat-fielding in spectroscopy
Flat-fielding is not standard for spectroscopy
  Ultimately, the CBP will be the best tool
  In the meanwhile,we use approximations :
    Keep only fluctuations due to camera window + CCD (dust & pixel-to-pixel gain variations)
    spatial and wavelength efficiencies factorize
  A line of light to produce a special flat-field
flat after filtering slow variations due to upstream optics
Blue flat pixel value
Red flat pixel value
Normal flat FELH0600
Vignetting affects direct image but not spectrum

## Slide 8: Factorization of the wavelength dependence
Idea:
Evaluate spatial correlation between flats with different filters
See if can factorize out the wavelength dependency on the flats:
  = out of focus artifacts (vignetting, dust on optical components) = slow pixel to pixel variation (real space) or low spatial frequency (Fourier space)
  = focused artifacts (dust on the CCD, pixel surface variations) = fast pixel to pixel variation or high spatial frequency
  We examine the hypothesis of
If ~ true, then we could preliminary use a single flat for spectra reduction
How can we test this?
  By examining the ratio of flat images at different wavelengths (with different filters)

## Slide 9: Factorization of the wavelength dependence: pixel correlation
⍴ = 0.96
Relative dispersion of ratio
ADU Relative dispersion

## Slide 10: Flat-fielding in spectroscopy
Difference (normal flat) vs (special flat):
Visible on large-scale only
-> spots from upstream optics are out-of-focus and impacts only the direct light of a normal flat
Inter-register gap
Impact of flat-fielding on a segment of pixels on the crest of the spectrum (around a spectral line)
-> smaller pixel-to-pixel variations

## Slide 11: Hardware to mitigate field star contamination
Simple hardware to be installed in the filter wheel (less than 3cm distance to the hologram)
  For special flat-fielding: cylindrical lens
  To mitigate the field stars: collimator -> already (successfully) tested with the first hologram prototypes at CTIO and Pic du Midi -> reduces both sky background and 0th order field stars. The structure of the sky background (section orthogonal to the dispersion) remains invariant by translation along the dispersion axis with a squared collimator
No source
With source
62
65
15
17
window

## Slide 12: Optical setup
Filter wheel
Disperser wheel

## Slide 13: Optical design
Filter
Disperser
Cylindrical lens

## Slide 14: Optical design
Filter
Disperser

## Slide 15: Optical design
Filter
Disperser
Light profile shape invariant with l
-> Deviations are attributable to defects in the input window and the CCD

## Slide 16: Frame conception
62
65
62

## Slide 17: Frame conception for cylindrical lens
dispersion
62
light entrance
side
62
65
2.5
15
15
17
Cylindrical lens
window
plane face behind (side of the detector)
Frame center
Edmund

## Slide 18: Frame conception

## Slide 19: More hardware -> easier analysis for hologram and notch spectra…
Planning:
Cylindrical lens ordered (on the shelve)
Special frame to be inserted in the filter wheel produced with 3D-printer (as the hologram)
tests with these objects should take place on-site at the end of august/september

## Slide 20: Spectroscopic reduction: état de l’art
SpecTractor operational tool for spectrum extraction
  Forward modelling, taking into account every instrumental effect:
    dispersion law, PSF(l), focus, 1rst+2nd orders, atmospheric dispersion…
  Separation of 1rst and 2nd diffraction orders now satisfactory
From RAW

## Slide 21: Determination of 2nd order/1rst order
Use spectra with blue filter (125)
Extract separately orders 1 and 2
Compute ratio
Projection
Order 1
Order 2

## Slide 22: Rapport 2/1 avec Mu-Col en UV
Spectre image 2021110400553_postisrccd.fits : MuCol avec filtre BG40, z = 1.13, seeing = 1.3’’, FWHM spectre autour de 25 pixels.
Rapports flux boite2/boite1
Soustraction bandes latérales
Pas 149.85 traits/mm recalculé à partir de la raie Hg (à 1 pixel près)
Relation exacte pixel - longueur d’onde
Positionnement précis
Pas de déflatage

## Slide 23: Ingredients of throughput
M1 reflectivity vs date (measured)
M2-M3 reflectivity vs l (theoretical)
Loss at window entrance/exit
CCD efficiency (measured)
Hologram transmission
(measured/modelized)

## Slide 24: Throughput is estimated with Bouguer lines technique (1729)
Example in band [485-515]nm (1rst order)
Series of instrumental magnitudes
- of the same source
- for various aimasses (here 1.23 - 2.1)
- during a period with stable atmosphere
Extrapolation of the line to airmass=0
-> get magnitude OUT OF ATMOSPHERE
-> compare with HST spectrum
-> deduce system throughput in the band
Several measurements duplicated
(and almost identical)
per airmass
Only end of night used
(low+stable absorption)
30 june 2022

## Slide 25: Control tool : EQW(O2) should depend only on airmass x pressure
EQW definition
After checking EQW(O2), we will measure
EQW(H2O(A)) and EQW(H2O(B))
H2O(A)
H2O(B)

## Slide 26: Color changes due to water vapor
PWV=1mm
2
3
4
5
6
7
8
9
Color variations follow: Scalar(PWV)xVector(type)

## Slide 27: Color changes due to water vapor
Impact of PWV on colors
- mainly (i-z) and (z-y)
- described by Scalar(PWV)xVector(type)
- with type linked to (ugrizY)
Impact of aerosol on colors
- mainly (u-g) and (g-r)
- work in progress

## Slide 28: COMPLEMENTS

## Slide 30: Variability of the atmospheric transmission (Stubbs et al. PASP, 119: 1163–1178, 2007)
Photometrists use photometric quality nights and narrow band filters
  No cloud
  Low humidity
  Low aerosols
LSST wants to use all nights with wide band filters
  Few clouds (grey absorption)
  Humidity (affects I & Z)
  Aerosol (affects U & G)
After correcting for Airmass:
O2, O3, rayleigh can be extracted
Then determine H2O and aerosol

## Slide 31: Spectrograph commissioning results
Objectives of the spectrograph commissioning:
Short term: characterize the spectrograph
- Geometry -> done
- Spectrograph resolution R > 200 within [342, 1100]nm : limited by the seeing (as expected); 2x better for the second order -> ex. H9 absorption line (@383nm) clearly visible. -> OK
- Software: SpecTractor(1) operational, constantly improving -> work in progress
- Checked the equivalent width (EQW) properties -> OK
- Telescope throughputs of 1rst and 2nd orders holographic disperser(2) with Bouguer lines -> work in progress, near to end (needs one « ideal » photometric night to consolidate).
- + a faint V=11.3 standard gives « enough » signal in 30s for spectroscopy
Long term: Estimate colour corrections, as functions of the airmass, atmospheric conditions and the object UGRIZY in every LSST field -> work in progress (Martin Rodriguez-Monroy)
  Either with an atmospheric model established from the follow-up of standards throughout the night
    -> Check the predictivity of the model versus airmass AND versus azimuth
  And / or with simultaneous measurements near the LSST field (needs secondary standards and observation strategy to « follow » LSST)
    -> Rely on GAIA DR of spectra
(1) Paper in preparation (2) MNRAS 506, 5589–5605 (2021). 2nd paper in preparation.

## Slide 32: Hologram for AuxTel
Goal : measure atmospheric parameters by extracting spectrum of standards
Constraints
  Easily switch imager / spectro.
  Incident beam perpendicular to CCD-plane
  Converging beam (not parallel)
Usual gratings:
  Strong defocus due to optical path variations with the diffraction angle
  Distorsion when used with a converging beam
Holographic grating:
  forced focus on the focal plane at all wavelengths: 0th and 1rst order at same focus
  No distorsion by design of hologram

## Slide 33: Holographic element characterization
Geometry: 2 scans (wide and fine meshes); changing position of the 0 order star
Determination of the nominal zero order position (1750, 300) -> determined with < 0.5 mm precision
Transmission is found constant within >1mm from nominal position
Good focus along the full l [342-1100]nm scale -> one of the main improvements w/r Ronchi grating
Transmission efficiency -> up to 3x more than Ronchi (depending on l)
Shows the dispersion direction if zero order is here

## Slide 34: Estimating a lower limit of resolution, using narrow emission lines of Planetary nebula Hen 2-113
656 nm
762 nm
486 nm
O2
656 nm
762 nm
486 nm
907nm
953 nm
967 nm
H𝜸
star
star
star
H⍺
star
O2
CII
star
SIII
SIII
spectrum from
le Bertre et al. 1989, A&A, 225, 417
434 nm
400
500
600
700
800
900
Hologram, Texp=60s
H𝞫
OII
R a 100 (seeing/object size limited)
R a 200 (seeing/object size limited)
-> lower limits on R=l/Dl (because extended object)
-> focus OK for all l

## Slide 35: Transmission efficiency model vs test-bench measurements
Phase delay profile of holographic grating
l=400nm
l=1000nm
l=639nm
Caracteristic curve of holographic emulsion
Transmissions:
Model (lines)
Data (points)
UV transmissions measured on sky (Bouguer lines): in progress

## Slide 36: Auxtel : First estimates of atmospheric parameters
Variation of EQW for atmospheric lines illustrates sensitivity to atmospheric parameters (EQW)
EQW definition
Stellar lines
EQW independent on atmosphere
Atmospheric absorption lines
EQW depends on atmosphere
H2O
H2O
H2O
  ‘’fit’’ H2O :
  PWV ~ 3.2mm
data/simu(LibRadTran) for several hypothesis (PWV)
O2 atm. absorption lines
O3 atm. absorption bands
H2O atm. absorption bands
Hg
Hb
Ha
H2O
(720nm)
H2O
(820nm)
O2
(760nm)

## Slide 37: Atmospheric studies
Objective of the AuxTel calibration:
Estimate colour corrections to vector (UGRIZY)LSST for each object, as a function of
- the atmospheric parameters (airmass, PWV, tVAOD ) -> the baseline
- or the directly measured atmospheric transmission function Tatm(l, RA, Dec) synchroneously within the LSST field
What are the orders of magnitude of the corrections ?
From simulation: atmospheric fluctuations induce typically less than 10mmag (max. ~30mmag @ airmass=2 for cold stars) residual colour variations per airmass after removing grey common absorption
-> Correction precision dC needs to be such that:
0.010 x dC < wanted resolution
i.e. dC=50% for 5mmag / 10% for 1mmag

## Slide 38: Characterizing the AuxTel throughput with Bouguer lines to measure separately order1 and order 2 transmissions versus l
Spectrum extraction software (SpecTractor) needs the global throughput of the system for each diffraction order p:
Tp(l) = t(l)telescope . tp(l)disperser . eCCD(l)
-> Obtained by the ratio of instrumental out-of-atmosphere flux to HST reference flux (as a function of l)
If constant atmospheric conditions, instrumental magnitude@l follows a Bouguer line in airmass z:
mp(l,z)instrumental = m(l)SED-HST + Aatm(l) . z + 2.5.Log[Tp(l)]
At a given l, extrapolating the line from the series of mp(l,z)instrumental to z=0 airmass gives out-of-atmosphere instrumental magnitude and allows to deduce the throughput from:
mp(l,0)instrumental = m(l)SED-HST + 2.5.Log[Tp(l)]
Requirements
-> (at least) one photometric night (i.e. stable atmosphere) to obtain long series of spectra.
-> The same star needs to be measured during the same night in the widest airmass domain.
-> large # of measurements allows better determination of the slopes and of z=0 extrapolation.
Series of mp(l,z)instrumental
z
l
Extrapolated mp(l,0)instrumental
Slope depends on l

## Slide 39: Measurement of Bouguer lines
Only end of night used
(low+stable absorption)
Instrumental magnitude vs airmass
Out of atm.
SED
Measured
spectra
Example of a
Bouguer line
HD142331 trajectory in airmass
Spectra integrated in bins of 30 nm width
Extrapolated out of atmosphere instrumental magnitudes in narrow [30nm] bandwidth
Notes: The night is not photometric, however we convince ourself that the the second part of the night have lower absorption and seems for stable.
The we remains with few usable exposures to construct Bouguer lines.
Top right : this is and example of Bouguer line, but the chi2 per degree of fredoom is above 6.
Bottom right : this is the set of Bouger lines from which one can reconstruct the Throughputs.

## Slide 40: Establishing correction procedures
We did predictions from simulations, based on parametrization with (z, PWV, VAOD). But O3 , O2 and cloud absorption (grey) can also be parameters.
The methods have to be systematically checked for every atmospheric situation:
  Predictability of the correction in (airmass, azimuth)
  Needs observation of CALSPEC standards through entire nights (to estimate atm. parameters) AND various fields in (airmass, azimuth) containing standards to test the prediction. « ronde des standards ».
Alternative: directly measure atm. transmission in the same direction than LSST, using secondary spectrophotometric standards measured out of atmosphere by GAIA. We checked that spectra of stars as faint as M=10 are measurable in 30s with s/b>100