## Slide 1
Optical readout for gazeous detectors
Antoine Cools
Outline
Scintillation study and optical readout
Applications
Glass Micromegas

## Slide 2
Outline
Scintillation study and optical readout
  Optical readout overview
  Argon/CF4 scintillation
  Readout
Applications
Glass Micromegas

## Slide 3
Optical readout
Use of camera (high granularity, large number of pixels, use of lens for large field of view)
Easy handling of the data (light intensity matrix)
Real-time imaging thanks to very low data processing and light integration approach
  Optical readout overview
Gazeous detector
Large dimensions (several m2)
Not expensive
Radiation hard (10s year of LHC)
Compatible with magnetic field
Gas active medium low density

## Slide 4
  Optical readout overview

## Slide 5
F.M. Brunbauer
F.M.F Fraga
Pure Ar
Pure CF4
  Argon/CF4 scintillation

## Slide 6
VIS : Electron impact : excited CF4* dissociates to CF3* which emits in VIS.
Dissociation of CF4* is not the only way to get CF3* :
Charge transfer processes : ionised Ar+ contributes to production of CF4+ towards CF3* production.
Ar + CF4 → CF3+ + F + Ar
F.M. Brunbauer
  Argon/CF4 scintillation

## Slide 7
F.M. Brunbauer
  Other scintillating gas mixtures
  Light yield

## Slide 8
F.M. Brunbauer
F.M.F Fraga
  Gain

## Slide 9
PMT : High gain, fast response.
CCD (Charges-Coupled Devices) camera :
- Large number of pixels
- Significant readout time (tens of Hz)
EMCCD (Electron Multiplying CCD) camera :
- High signal-to-noise ratio in low-light conditions
- Charge multiplication through impact ionisation
- Limited image resolution due to smaller pixels
CMOS (Complementary Metal-Oxyde semiconductors) :
Very low noise : each pixel has a photosensitive region and an active amplifier.
- Shorter readout time
- Lower manufacturing cost than CDD sensors
- Rolling shutter effect : pixels are exposed alternatively
  Readout

## Slide 10
Hamamatsu CMOS camera
Readout noise
Dark current
Cooling Sensor temperature Dark current
Air - 20 °C 0.016 e- /pixels/s
Pixels
Number Size
4096 x 2304 4.6 µm x 4.6 µm
Minimum exposure time
Mode Rate
Standard 1 µs/frame
Ultra quiet 200 ms/frame
  Readout

## Slide 11
Outline
Scintillation study and optical readout
Applications
  Timeline
  Optical GEMs
  Optical TPCs
Glass Micromegas

## Slide 12
1990
2000
2010
2020
GEM scintillation with CF4
MICROMEGAS invention
Light emission with TEA and TMEA
Pressure and gain effect on light yield
GEM invention
Neutron imaging (He converter, low pressure)
Optical TPCs
Dose imager for radiotherapy
Dark matter experiment OTPCs
Glass Micromegas
  Timeline

## Slide 13
History of imaging with MPGDs
Glass Micromegas, Optical readout, deconvolution
  Radiography X
https://doi.org/10.1016/j.nima.2019.163320

## Slide 14
F. Takeshi
F.M. Brunbauer
σ = 351± 20 µm
  Optical GEM - Radiography X
10 Hz
2018
2019
σ = 280 µm

## Slide 15
F. Takeshi
F.M. Brunbauer
  Optical GEM - Tomography X
2019

## Slide 16
J. Borteldt
  Dose imager for radiotherapy
  Proton beam monitoring
F. Takeshi
2019
2020

## Slide 17
  Optical TPC - 2D scintillation detector for thermal neutrons
F.M.F Fraga
2002

## Slide 18
  Optical TPC - 2D scintillation detector for thermal neutrons
2009
20 cm
A. Roccaro

## Slide 19
CYGNO experiment
PMT
Camera
Drift gap
F. Petrucci
  Optical TPC
MPGD conference 2022
He + CF4

## Slide 20
E. Tilly, MPGD conference 2022
Migdal experiment
  Optical TPC
Ar + CF4

## Slide 21
Outline
Scintillation study and optical readout
Applications
Glass Micromegas
  X-ray characterization
  Activity measurement on tritiated cells
  Neutron imaging

## Slide 22
Performance of Micromegas on glass
Charge readout test in Argon+5%Iso:
  - gain above 104
  - energy resolution (FWHM) reaches 16%
Glass Micromegas
S. Aune, T. Benoit, M. Kebbiri
Coated glass with 150 nm of ITO (Indium Thin Oxide)
6 mm
55Fe energy spectrum – 5.9 keV
  X-ray characterization
https://doi.org/10.1016/j.nima.2022.167910

## Slide 23
6 mm
60 s full detector image with simple background suppression.
60 s exposure time bat radiography with simple background suppression and beam profile correction.
X-ray radiography (20 kV) – Ar/CF4(20%), CERN GDD
High gain: 1 min exposure time gives images with good contrast
  X-ray characterization

## Slide 24
Goals
Measurement of Point Spread Function (PSF)
Spreading origins : diffusion and optics
30 x 30 µm beam, Amplification
(Va=400 V, Vd=210 V)
https://doi.org/10.48550/arXiv.2303.17444
X-ray beam - 6keV - 50x50 µm
  Soleil synchrotron

## Slide 25
Diffusion
Signal spreading dependence on electric fields
  Soleil synchrotron
12/07/2023
25
GDR DI2I - Subatech
σ = 280 µm

## Slide 26
Goals
Micromegas mesh and pillar study
Glass Micromegas hexagonal mesh (50x50 µm x-ray beam)
Glass Micromegas Beta mesh (Ambient light picture)
  Soleil synchrotron

## Slide 27
MTF : 281 µm
MTF : 800 µm
PSF
Deconvolution
  Soleil synchrotron

## Slide 28
First deposit : tritiated glucose
Drug concentration ↔ sample activity (Bq)
Activity measurement limits and dynamic range → Activities: 0.1 Bq, 1 Bq and 10 Bq
Tritium deposits schema and picture
β
Cathode
Mesh
ITO
Glass
Light cover
Camera
VIS light
e-
OPTIMED-BETA set-up scheme
https://doi.org/10.1016/j.nima.2022.167910
  Activity measurement on tritiated cells
12/07/2023
28
GDR DI2I - Subatech

## Slide 29
All drops positions are well assessed
0.1 Bq drops are close to the background noise
720 frames of 5 s (60 min) added with simple background suppression - 20% of CF4
Integration method :
Light intensity profile
Reference | 0.09 | 1.76 | 9.8
Average | 0.086 | 0.84 | 11.74
σ | 0.026 | 0.18 | 1.28
Matching | 95% | 47% | 83%
Activity measurement (Bq) INTEGRATION
*
  Activity measurement on tritiated cells
12/07/2023
29
GDR DI2I - Subatech

## Slide 30
Clustering method :
200 ms frame with single beta events
  Activity measurement on tritiated cells
12/07/2023
30
GDR DI2I - Subatech

## Slide 31
Reference | 0.09 | 1.76 | 9.8
Measurement | 0.108 | 0.85 | 5.13
σ | 0.014 | 0.088 | 0.38
Matching | 83% | 48% | 52%
Activity measurement (Bq) CLUSTERING
  Activity measurement on tritiated cells
12/07/2023
31
GDR DI2I - Subatech
Clustering method :

## Slide 32
Acquisition modes:
  Event-by-event: track reconstruction:
  Potentially higher resolution (100 µm), better ɣ-to-n suppression
  Integrated: real-time radiography:
  Almost no data computation
Cathode : 10B4C neutron-to-charge converter
  Thermal neutrons absorbed by 2 µm thin 10B4C layer
  Conversion efficiency: 5%
  (α or Li) fragments cause strong ionisation
  Drawback: fragments long range in the gas (5 mm)
  Neutron imaging
12/07/2023
32
GDR DI2I - Subatech

## Slide 33
Neutron source (3 events/s on detector)
Drift field affects the diffusion in the gas
Diffusion spreads the light
50 V/cm drift field
800 V/cm drift field
2000 V/cm drift field
50 V/cm
800 V/cm
2000 V/cm
33
12/07/2023
33
GDR DI2I - Subatech
  Neutron imaging

## Slide 34
THANK YOU
A. Cools , S. Aune , F. Beau , F.M. Brunbauer , T. Benoit , E. Ferrer-Ribas , C. Malgorn , E. Oliveri , T. Papaevangelou , E.C. Pollacco , L. Ropelewski , A. Sari , F.J. Iguaz

## Slide 35
BACK UP

## Slide 36
LIGHT DETECTION DEVICES
Hamamatsu CMOS camera
Readout noise
Photon number resolving
Dark current
Cooling Sensor temperature Dark current
Air - 20 °C 0.016 e- /pixels/s
Pixels
Number Size
4096 x 2304 4.6 µm x 4.6 µm
Minimum exposure time
Mode Rate
Standard 1 µs/frame
Ultra quiet 100 ms/frame

## Slide 37
Tumor heterogeneity: different cell types inside a tumor
  Heterogeneity effect on drug targeting?
  Develop more efficient drugs
  Requires better detection sensibilities
Pharmaceutical needs at the cell level for drug development:
  Assess the drug distribution among cells
  At the cell level: Quantification of 3H concentration in single cell samples
Molecule labelling and tracking with tritium
37

## Slide 38
LIGHT DETECTION
38

## Slide 39
Cathode
Mesh
ITO
Glass
Light cover
Camera
VIS light
e-
Experimental set-up
OMNIS set-up schema
B4C
Neutron source
Slow neutron
α & 7Li
10 mm
  Neutron imaging
12/07/2023
39
GDR DI2I - Subatech

## Slide 40
10 mm drift gap
250 µm drift gap
12/07/2023
40
GDR DI2I - Subatech
Neutron source (10 events/s on detector)
  Neutron imaging

## Slide 41
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
β particle range in Ar-Isobutane gas mixture

## Slide 42
DETECTOR CHARACTERIZATION WITH X-RAYS
X-ray radiography
MTF measurement
60 sec exposure time lead target radiography with simple background suppression.

## Slide 43: Beta spectrum : CF4 Overall activity : 76 Bq

## Slide 46
  2D scintillation detector for thermal neutrons
A. Morozov
3H + CF4

## Slide 48
48
Soleil beam test (June 2023)
Beam collimator
Optical GEM
CMOS camera
Lens effects
Optical GEM and wavelength shifter
Wavelength shifter GEM (pure Ar)

## Slide 50
50
Production
Production at CEA Bulk Lab
Gain uniformity check
Planarity check : Laser diffraction measurement
T. Benoit
M. Vandenbroucke
Light intensity
Vertical scale x1000

## Slide 51
51