## Slide 1
http://pro.ganil-spiral2.eu/spiral2/instrumentation/s3
Super Separator Spectrometer S3
Opportunities for UK Physicists at GANIL/SPIRAL2
H. Savajols on behalf of the S3 collaboration
S3 has been funded by the French Research Ministry, National Research Agency (ANR), through the EQUIPEX (EQUIPment of EXcellence) reference ANR-10EQPX- 46, the FEDER (Fonds Européen de Développement Economique et Régional), the CPER (Contrat Plan Etat Région), and supported by the U.S. Department of Energy, Office of Nuclear Physics, under contract No. DE-AC02-06CH11357 and by the E.C.FP7-INFRASTRUCTURES 2007, SPIRAL2 Preparatory Phase, Grant agreement No.: 212692.
1

## Slide 2
Projet :
Budget ≈ 23.3 M€
FTE ≈ 450 (32,8 FTE 2022)
8 partner laboratories
Commissioning 2025
LINAC beams : He to U
1 mA, < 14,5 MeV/A (A/Q=3)
1 mA, < 7,5 MeV/A (A/Q=7)
Super Separator Spectrometer
2
Scientific collaboration:
27 Laboratories
11 countries : France, Finland, Germany, Hungary, Italy, Poland, Slovakia, Spain, Sweden, U.K., USA
Ions | Intensity (pµA) Phoenix V3 RFQ A/Q≤3 | Intensity (pµA) Phoenix V3 RFQ A/Q≤7 | Intensity (pµA) SC Ion Source RFQ A/Q≤7
18O | 80 | * | 375
19F | >15 | >40 | >40
36Ar | 16 | 70 | 45
40Ar | 3.6 | 70 | 45
36S | 2.3 | * | *
40Ca | 2.9 | 10 | 20
48Ca | 1.2 | 10 | 20
58Ni | 1.1 | 4 | 8
84Kr | 0.1 | 10 | 20

## Slide 3
Nuclei produced by
Fusion-Evaporation
(with refractory elements)
58Ni+46Ti100Sn +4n
I=10pµA  10/s
RIBF : 0.7/s
FAIR : 2/s & FRIB : 8/s
48Ca+238U282-283Cn+3,4n
(I=10pµA) 40evt/week
Heavy and Superheavy
Elements
Limit of the nuclear existence
Nuclear structure
Reaction mechanisms
Atomic properties
Proton Dripline & N=Z nuclei
Nuclear structure
Study the role of π-ν correlations
Deformation – shape coexistence
Exotic decay
Astrophysics rp-process
Fundamental interaction
Physics goals
Study of rare events in nuclear and atomic physics
Develop a comprehensive model of atomic nuclei – How do we understand the structure and stability of atomic nuclei?
Understand the origin of elements
Use of atomic nuclei to test fundamental symmetries and properties
3
http://u.ganil-spiral2.eu/chartbeams/
Notes: How deformation emerge from microscopic configuration

## Slide 4
Achromatic point
Primary beam dump
Target position
Secondary beam dump
Final focal plane
  Versatile multistep separator
  Momentum achromat + Mass separator
  Ion optics configuration: Q3DQ3Q3DQ3Q3EQ3Q3DQ3
  F1 : R16=1.15cm/%
  F2/F4 : R16 = R26 = 0
  F3 : R16 = -1.73 cm/% / -1.59 cm/%
High beam intensity
  High power target: >> 1pµA (= 6.1012p/s)
Two basic optical modes of operation:
High transmission vs high mass resolution
Basic properties and functionalities
Optics and performances
4
F0
F1
F2
F3
F4
High Resolution Mode (HRM)
m/q dispersion = 8 mm/%
3 charge states & M/𝚫M = 500
𝚫dp/p=16%
𝚫𝝦=45mrad
𝚫𝛗=140mrad)
100Sn transmissions 40% (10x10cm)
Convergent Mode (CM)
No mass resolution
6 charge states
𝚫dp/p=20%,
𝚫𝝦=90mrad,
𝚫𝛗=140mrad,
100Sn transmissions 65% (10x10cm)
Reference beam :
A=100, Q=24+, 𝛔p = 3.7%, 𝛔 θ = 18mrad
→ The momentum achromat (MA) optic is common to all modes

## Slide 5
Target system
High power rotating targets
3 × M-dipoles
Large H & V gaps
E-Dipole
20 cm gap & +/- 300 kV
Open slit in the anode
SC Multipoles
Dispersive zone
Open RT magnet & beam dump & Movable fingers
Super Separator Spectrometer
Infra / Interface
LEB
SIRIUS
SMT, PSS, Coldbox & LTC
DSSD, SSD, FEE/BEE, DAQ & Diagbox
LEB @ LPC & GISELE Laser Lab
Lot C68, Cooling system, Laser room …
5
Main equipment and detection setups
High selectivity > 1013 - High efficiency 50% - In flight mass separation > 1/450
Versatility & unique instrumentation (SIRIUS – LEB)

## Slide 6
6
Target station
  → on-line commissioning at GANIL in 2023 / on-line commissioning at LINAC planned end 2024
Room temperature magnets (3 magnetic dipoles & open multipole triplet)
  → power-up tests done 2023
Electric dipole (chamber, electrodes and 300kV power supplies installed)
  → first successful test (75 kV) 2023 & final conditioning beginning 2024
SMT, PSS & Cryogenics (7 PSS & 7 SMT delivered & cryo line installed and tested)
  → SMT1-4 tested, SMT5 misunderstood quenches/fast discharges to be investigated in 2023
  Many crashes of the cold box turbines since May 2022 (New cooling down sequence October 2023 !)
  → Finalised SMT tests in 2023-2024
  → Finalise 3D magnetic field measurement & alignment in 2023-2024
  → All SMT in final position, tested and connected Q3 2024
Beam dump (2 chambers, translation mechanisms, fingers and shielding delivered)
  → dump plates / cooling pipes assemblies installed end 2024
Status of the beamline

## Slide 7
Status of the beamline
Ready for beam commissioning 2025
7
Target station
Beam Dump
Electric Dipole
Superconducting Multipole Triplets
and Power-Supply Systems (x7)
Cryogenics
Open RT Triplet
Dipole 1
Dipole 2
Dipoles 3
Level of completion
Level of completion ≈ 85 %

## Slide 8
S3-SIRIUS (Spectroscopy & Indentification of Rare Ions Using S3)
Detections systems
8
, SF, e-, decay spectroscopy
Evolution of shell structure
Collective vs single-particle degrees of freedom
Deformation & shape coexistence
MQ & Z identification
Spectroscopy
Limits of the nuclear chart
Reaction mechanism
New isotopes
Fission branches & half lives, properties of fission fragments
Fission hindrances of single-particle and high-K states
Systematic measurement of cross sections & excitation
functions

## Slide 9
S3-LEB
(Low Energy Branch)
Detections systems
9
Laser & decay spectroscopy
Mass measurement
Nuclear Moments / Charge radii / Spin
Mass
Decay spectroscopy
Fundamental properties
Tasks
Provide pure & low energy beams
Provide access to species not available by other techniques

## Slide 10
152
Eshell
Calc.: A. Sobiszewski
120
114
108
162
184
SIRIUS
Limits of stability/isomers
250,249,…No
Search for new isotopes
252Rf
Odd Z isotopes – nuclear structure
fermium region
Isomers
254Rf, 260Sg
“day 1”
with injector1
S3 LEB
Atomic spectroscopy
(isomers, shapes and moments)
fermium isotopes
relativistic effects and the architecture of the periodic table
rutherfordium/dubnium isotopes
beyond
with NEWGAIN
2028
+ SC source
2030
Octupole deformation
uranium region
”day1 ” - preproposals
Science program ”day1” & beyond
Study of heavy nuclei
N = 126 shell closure
Ac - Th region
10
Courtesy of D. Ackermann (GANIL)
2018 LoIs

## Slide 11
N = Z
”day1 ” - preproposals
Known masses
Nucleon-Nucleon interaction around 100Sn?
Effective Single particle energy levels: 101Sn, 99In
T = 0 T = 1 Pairing interaction: 98In
Spin-aligned coupling scheme: 94Ag, 90Rh
How deformation emerge from microscopic
configuration ?
Q in Sn chain
Evolution of deformation around 80Zr (refractory elements)
Binding energies and Wigner term ?
From 80Zr-100Sn
rp-process
Study of N=Z nuclei
Science program ”day1” & beyond
SIRIUS
S3 LEB
New decay modes ?
Super-allowed α decay: 112Ba-108Xe-104Te
Cluster radioactivity: 114Ba, 112Ba
Courtesy of L. Caceres (GANIL)
11
2018 LoIs

## Slide 12
Collaboration & Scientific program
105 registered participants (13 countries)
Strong & diverse community ∼ 70 talks
Belgium
CERN-Isolde
Germany
Slovaquia
Finland
France
UK
Italia
Japan
Corean
Poland
Romania
United States
12
Revised S3 LoIs 2018
  SIRIUS : Some experiments have been performed but have open new questions / some of the program are
  still relevant (K-isomers, XS, fission, alpha-decay) / 48Ca shortage is an issue
  LEB : Scientific program is still relevant with high scientific impact
New idea and further developments
  Molecular laser spectroscopy at S3-LEB (start with stable Lanthanide molecule)
  New proposal to install a tape station for beta decay spectroscopy in 100Sn region at S3-LEB
  X-rays measurement with SIRIUS / Faster gas cell is needed in future (ANR FRIENDS3: V. Manéa IJCLAB)
General remarks
  S3 has a very strong and diverse community → Full synchronisation among all team is essential
  Important to identify our “starting niche” for select impactful results

## Slide 13
Optical commissioning :
  Progressive tuning of the elements with direct and scattering/stripped beams (Momentum achromat + Mass spectrometer)
  Tools : all diagnostics along the spectrometer + additional diagnostics at the focal plane (SIRIUS & LEB can be connected but not used)
Scientific commissioning :
  Optimize the rejection and the transmission for relevant kinematics to reach the required performances
    Converging Mode (CM)
    High Resolution Mode (HRM) important for the SIRIUS scientific program
  Setup : Diagnostic box in LEB mode + LEB / SIRIUS
SIRIUS and LEB commissioning with S3 beams in parallel with the 2 steps.
  Reference reactions with easy beams and targets to produce nuclei which large XS that are alpha emitters and easy to identify (asymmetric / very asymmetric / symmetric reactions)
  Direct comparison of spectrum quality and various other performances with cases that have also been studied elsewhere (e.g. using the gas-filled separator RITU at JYFL, the VASSILISA at JINR)
  Possibility of scientific data taking during the so-called commissioning for SIRIUS and LEB.
Separator Spectrometer commissioning
13
Global strategy
Given the complexity of S3 the commissioning and the associated focal plane detection, two years will be necessary to reach adequate performances to start day1 campaigns with experiments selected by the PAC (SIRIUS / LEB)

## Slide 14
Commissionning plan endorsed by S3 UCC (20 Juin)
14
Block 1 : Spectrometer optical commissioning
Block 2 (Converging Mode) : LEB
Reaction 1: asymmetric reaction 40Ar + 116Sn to produce erbium (N=82)
Block 3 (Coverging mode) : SIRIUS
Reaction 2: asymmetric reaction 40Ar + 174Yb to produce known actinides
Reaction 3: asymmetric reaction 40Ar + 180Hf to produce thorium (N=126)
Block 4 (Converging mode) : LEB
Reaction 4: asymmetric reaction 40Ar + 175Lu to produce actinium (N=126)
Reaction 5: symmetric reaction 50Cr + 58Ni to produce N = Z nuclei
Reaction 6: very asymmetric reaction 20Ne + 197Au to produce actinium (N=126)
Block 5 (Converging/ High Resolution modes) : SIRIUS
Reaction 7: very asymmetric reaction 22Ne + 206Pb to produce thorium
Reaction 8: repeat asymmetric reaction 40Ar + 116Sn to produce 151-152Er
Reaction 9: repeat asymmetric reaction 40Ar + 174Yb
Reaction 10: 40Ar + 209Bi to populate mendelevium isotopes 244-247Md
Milestone J6a : LINAC beam delivery up to the S3 target end 2024
  LHS3N accelerator beam line test up to LHS3N-CF24
  Beam spot optimisation on the target (S3N-CF12) and beam synchronisation

## Slide 15
Conclusion
15
Development of the S3 project is progressing well
  Spectrometer : ready for beam commissioning in 2025
  LEB : off-line tests at LPC completed / installation at S3 in 2024 for commissioning
  SIRIUS : in beam test at GANIL in 2023 / installation at S3 (room 51) in 2024 for source tests
Scientific program and campaigns setting
  Commissioning plan defined
  3 months day1 campaign selected for each set-up (SIRIUS & LEB) in 2018
  U.K. scientists involvement (6 LoIs)
    Decay Spectroscopy of 253Rf and 257Sg (Universities of Liverpool & York )
    Alpha-decay spectroscopy of odd-Z isotopes in fermium region (University of York)
    Search for new isotopes: 252Rf and 256Sg (University of Liverpool)
    Search for octupole deformation in 225-228U (University of Liverpool)
    Single-particle states and proton-neutron interaction in the 100Sn region studied through the neutron-deficient In nuclei (University of Manchester)
    Beta-delayed fission of neutron-deficient isotopes (University of York)
S3 will strongly benefit of NEWGAIN (Injector A/Q=7)
Notes: Question to the management/evaluation commitee :need for an official channel to submit proposals/LoIs – a clear time plan for the management