## Slide 1: From Nuclear Physics to Isotope Geochemistry: Identifying Anthropogenic Contamination Sources in the Environment
alkiviadis.gourgiotis@asnr.fr
SEPTEMBER 2025
Alkiviadis Gourgiotis

## Slide 2: Who are we: The French Authority for Nuclear Safety and Radiation Protection (ASNR)
  The ASNR oversees civil nuclear activities in France on behalf of the French State. It also carries out research, expert assessments, training, and public information in the fields of nuclear safety and radiation protection.
  Main missions of the ASNR:
    Oversight
    Regulation
    Expertise
    Research
    Emergency situations
    Information and dialog
    Training and development of a culture of radiation protection
ASNR sites: ASNR is spread over 10 sites across France and overseas:
The research conducted by ASNR has two main aims: to maintain and develop the knowledge and skills required for expert assessments in the various fields of nuclear safety and radiation protection, and to advance fundamental knowledge, in particular to understand the effects of ionizing radiation on health and the environment.
Our department: Radioactive Waste and Pollution Department (SPDR)
Our lab: Research Laboratory on Transfers in Contaminated Sites and Soils (LT2S)

## Slide 3: ASNR's Environmental Mission: Identification of contamination sources
As part of its expertise and environmental monitoring missions, ASNR carries out numerous studies related to contaminated sites.
Identifying the origin of radiological contamination --> help us to support decision-making and optimize current management strategies for contaminated sites and soils.

## Slide 4: historical overview
01

## Slide 5
L’atome
An atom → ancient Greek, ἄτομος [atomos] → that which cannot be divided
The atomist theory (Democritus) → supports the idea of matter made up of indivisible 'grains
The atom
From the discovery of isotopes to isotope geochemistry

## Slide 6
The scientific discovery of the atom dates back to Dalton, in 1803
Dmitri Mendeleïev : Periodic classification of the elements 1891
From the discovery of isotopes to isotope geochemistry

## Slide 7
Frederick Soddy 1913
Nature 1913
From the discovery of isotopes to isotope geochemistry

## Slide 8
Francis William Aston :
Measurement of isotopes starting from 1919
From the discovery of isotopes to isotope geochemistry

## Slide 9
From the discovery of isotopes to isotope geochemistry
IG → radioactive disequilibria as well as isotope variations (fractionations, mixing, etc.) as sources of information of the materials origin and the physicochemical processes in the nature.

## Slide 10: use of isotopes for tracing contamination SOURCES in the environment
02

## Slide 11: Uranium mines in France
Industrial exploitation from 1948 to 2001
At the end of 2018, 250 mining sites were listed at the national level

## Slide 12: U-mines The goal of the study
U-mine
wetland
Watercourses
Sediments
crust
(geochemical background)
[U] ~3 µg/g
+ Th, Ra, Pb
U mine
Chemical-processing plant
Tailling storage
U mining activities:
Sediments
[U] >100 µg/g
+ high Th, Ra, Pb
?
U-ore
[U] > 400 µg/g
+ RN (Th, Ra, Pb)
Contamination from mining activities
Weathering
and
erosion
2
Water catchment
U transfer:
Particles
Adsorbed U
Dissolved U
supply
(2) U supply:
sedimentntation
U6+(aq)=> U4+(s)
Complex U-OM
1
U transfer
(Th, Ra, Pb)
Red
Ox
Regenspurg, S. et al, Geochimica et Cosmochimica Acta 2010, 74, (7), 2082-2098
Peña, J. et al, Science of The Total Environment 2020, 727, 138368
Lefebvre, P. et al, Geochimica et Cosmochimica Acta 2022, 338, 322-346
Natural systems,
[U] up to 6000 ppm
The identification of the origin of env. contaminations  Optimizing current management methods for former mining sites
How can we do this ?
Using only concentration/activity  false positives
During the operation of the mining sites, and even after their closure (due to the radioactive materials that remain on site), radioactive substances may be transferred to the environment through atmospheric transport or mine drainage water.

## Slide 13: U-MINES: particulate transport Lead isotopes as a relevant tracer to highlight the environmental impact of uranium mining
U-ore  distinct lead isotopic signature
206Pb
208Pb
206Pb
208Pb
238
U
235
U
232
Th
206
Pb
207
Pb
208
Pb
204
Pb
Radiogenic Pb
Stable Pb isotopes

## Slide 14: U-MINES: particulate transport Lead isotopes as a relevant tracer to highlight the environmental impact of uranium mining
Study site: Rophin wetland (Puy-de-Dôme, Auvergne-Rhône-Alpes, France)
Beaumais et al. JHM 2022
Geng et al. JHM 2024
Specific area in which all the samples affected by mining materials are found
Morerau et al. Chemosphere 2022
Suspected contamination

## Slide 15
U-MINES: particulate transport Lead isotopes as a relevant tracer to highlight the environmental impact of uranium mining
SIMS 7F
Beaumais et al. JHM 2022
The benefit of particulate analysis  contaminations that may be masked by the high presence of natural materials

## Slide 16: U-MINES: dissolved transport U and Ra isotopes as a relevant tracer to highlight the environmental impact of uranium mining
 | (234U/238U) | (228Ra/226Ra)
Water in contact with U-ore subjected to congruent dissolution from mechanical treatment. | ~1 | <<0.1
Waters from natural weathering of rocks. | >>1 | ~1.2

## Slide 17: Nuclear ACCIDENTS and Global fallout

## Slide 18
Nuclear accidents and global fallout: the accidents of the NPP saint laurent des eaux
Two accidents occurred at Saint-Laurent-des-Eaux (EDF) in 1969 and 1980, both involving graphite-gas reactors (UNGG). They involved partial core meltdowns due to issues during fuel loading/unloading operations.

## Slide 19
GF
Chernobyl
Magre et al. Env. Pollution 2023
Zok et al. ES&T 2021
Nuclear accidents and global fallout:
The origin of radiocesium: global fallout versus Chernobyl
135Cs/137Cs

## Slide 20: The origin of the radioactivity observed in Saharan dusT

## Slide 21: The origin of the radioactivity observed in Saharan dusT

## Slide 22: Conclusions
Thanks to the knowledge acquired in nuclear physics on radioactive decay and to the isotopic abundances of man-made and/or natural materials etc, isotope geochemistry is today a field that supports environmental monitoring and regulatory decision-making.
It is important to continue work on new isotopic systems that better distinguish anthropogenic inputs from natural ones.
We must also anticipate the emergence of new potential contamination sources (SMRs, nuclear energy revival…).
Continued efforts are needed at low concentration levels: keeping up with analytical developments is essential.

## Slide 23: Thank you for your attention