## Slide 1: Measuring electric dipole moment of the muon using the frozen-spin technique
Pranas Juknevicius on behalf of the muEDM collaboration
Caen 2025

## Slide 2: Content
EDM searches
The frozen-spin method
Experiment design
  Muon injection
  Muon entrance detector
  Pulsed magnetic coil
  Cylindrical positron detectors
Conclusions

## Slide 3: Motivation – EDM and CP-violation

## Slide 4: Motivation – EDM and CP-violation
T
CP
EDM serves as probes of CP violation in the Standard Model.
Insufficient CP-violation to explain matter-antimatter asymmetry in the universe.

## Slide 5: Motivation – EDM and CP-violation
Insufficient CP-violation to explain matter-antimatter asymmetry in the universe.
EDM serves as probes of CP violation in the Standard Model.
Standard Model
CKM matrix provides CP-violation
Lepton EDM are tiny (4 loop)
Prediction of the muon EDM:
(Yamaguchi & Yamanaka, 2020)
T
CP

## Slide 6: Motivation – EDM and CP-violation
Current best experimental limit:
By BNL, Muon g-2 Collaboration see Bennett et al., 2009
Goal for muEDM collaboration:
Phase I :
Phase II :
muEDM Phase I
muEDM Phase II
BNL

## Slide 7: Content
EDM searches
The frozen-spin method
Experiment design
  Muon injection
  Muon entrance detector
  Pulsed magnetic coil
  Cylindrical positron detectors
Conclusions

## Slide 8: Frozen-spin method
Spin precession due to muon EDM
Larmor precession
4

## Slide 9: Frozen-spin technique
Muon orbit

## Slide 10: Frozen-spin technique
Muon orbit

## Slide 11: Frozen-spin technique
Muon orbit
Thomas BMT Equation
EDM contribution

## Slide 12: Frozen-spin technique
Muon orbit
Thomas BMT Equation
EDM contribution

## Slide 13: Frozen-spin technique
Muon orbit
Thomas BMT Equation
EDM contribution

## Slide 14: Frozen-spin technique
EDM contribution
In the frozen-spin condition the source for out of orbit plane spin precession proportional to only the muon EDM.

## Slide 15: How to measure muon spin direction?
Parity violating pion decay muons are polarized
Positrons from muon decay are preferentially ejected along the spin direction
Detecting emitted positron direction from a polarized muon beam  muon spin direction.
Experiment sensitivity to the muon EDM:

## Slide 16: Content
Motivation
The frozen-spin method
Experiment design
  Muon injection
  Muon entrance detector
  Pulsed magnetic coil
  Cylindrical detectors
Conclusions

## Slide 17: the muEDM experiment

## Slide 18
PSI High Intensity Proton Accelerator (HIPA)
Adelmann, A., Bainbridge, A.R., Bailey, I. et al. A compact frozen-spin trap for the search for the electric dipole moment of the muon. Eur. Phys. J. C 85, 622 (2025).
the muEDM experiment
muEDM team at PSI

## Slide 19: Content
Motivation
The frozen-spin method
Experiment design
  Muon injection
  Muon entrance detector
  Pulsed magnetic coil
  Cylindrical detectors
Conclusions

## Slide 20: Muon injection channel :: Magnetic mirror effect
Muon beam

## Slide 21
Muon beam
Muon injection channel :: Magnetic mirror effect
Challenges:
Non-uniform fringe field
~2T magnetic field
Strong gradient

## Slide 22
Muon beam
Challenges:
Non-uniform fringe field
~2T magnetic field
Strong gradient
Solution:
Superconducting injection channel
Muon injection channel :: Magnetic mirror effect

## Slide 23
Superconducting injection channel design
Cryo shield
Flexible copper thermal connections
Vacuum chamber

## Slide 24
Superconducting injection channel design
4 x Layered NbTi/Cu sheets w=0.7 mm
Copper half shells OD = 40 mm
Brass supporting tube ID = 16 mm
Cryo shield
Flexible copper thermal connections
Vacuum chamber

## Slide 25: Injection channel status
Vacuum pressure ~mBar.
T = 3.9K on superconducting injection channel holder.
Cooldown time ~35 hours.
Superconducting injection channel is being constructed @PSI.
First muon injection tests Dec 2025 beamtime.

## Slide 26: Content
Motivation
The frozen-spin method
Experiment design
  Muon injection
  Muon entrance detector
  Pulsed magnetic coil
  Cylindrical detectors
Conclusions

## Slide 27: Muon Entrance Trigger
Veto
Entrance
Magnetic kicker system
AND
⊗
NOT
Magnetic pulse is triggered only on muons with the correct trajectory
Only 0.4% of muons are in the acceptable phase space (Geant4 simulation)
Entrance Detector: Thin (≤100μm) scintillator
Veto Detector: Thick scintillating slab with holes
Entrance triggered was tested in 2024 beamtime
19.09.2025
12

## Slide 28: Magnetic kicker coil
Magnetic pulse characteristics:
Peak amplitude ~1mT
Pulse fullwidth ~50ns
Triggered <100ns
Tested in 2024 beamtime

## Slide 29
The Positron Tracker
Scintillating fiber detector:
~O(1000) scintillating fibers in hexagonal configuration
Fiber coincidence  positron detection
Able to reconstruct emitted positron trajectory
Coaxial cylinders with 17 mm and 21 mm radius

## Slide 30: Closing remarks
muEDM is a dedicated search for the muon EDM in a leptonic system with a novel frozen-spin method approach.
2025 commissioning systems:
Injection with SC channel
Kicker system for pulsed field
Cylindrical positron detectors
Demonstrate muon storage
2026 commissioning systems:
Electrodes for the frozen-spin
Demonstrate the frozen-spin method
Open for new collaborators!

## Slide 31
New physics in dipole moments
[1] The Muon g − 2 Collaboration, arxiv:2506.03069 [hep-ex] (2025) [2] Aliberti et al., arxiv:2505.21476 [hep-ph] (2025)
[3] Bennett et al., Phys. Rev. D 80, 052008 (2009)
[4] Ema, Gao & Pospelov, Phys. Rev. Lett. 128, 131803 (2022)
EFT description encodes heavy new physics in the Wilson coefficients of the dipole operator
Phase I explores CPV enhanced model space contributing strongly to [5,6]
Phase II will additionally probe CPV models contributing similarly to and [7,8]
The flavour diagonal terms are related to the g-2 and EDM
[5] Khaw et al., JHEP 234 (2023)
[6] Dermíšek et al., Phys. Rev. D 107 095043 (2023)
[7] Bigaran & Volkas, Phys. Rev. D 105 015002 (2022)
[8] Hamaguchi et al., JHEP 100 (2023)
Notes: reduce text - mostly broad, just say
eg. “Express Schiff moment in terms of dmu”
dont forget to introduce the muon in the plot
could hide the additional ones not mentioned
add the sensitivity we are targeting on the plot for context
worthwhile to explore full parameter space, with other flavour structures The leptonic EDMs are described through imaginary parts of Wilson coefficients of EFT dipole operators, such that limits directly constrain new physics without additional input.

## Slide 32
Magnetic field shielding using superconductors
Superconductor-based passive shielding and screening systems by N. Rotheudt et al
DOI 10.1088/1361-6668/adb7cc
z
Muon storage simulations show that successful storage can be achieved, when B field transversal components < 100 mT.

## Slide 33: Magnetic field shielding measurements
NbTi/Nb/Cu layered sheets
Used at CERN to successfully shield magnetic field up to 3.1T at 4.2K see ref: 10.1109/TASC.2018.2872860
S-Innovations 2G HTS tape 04-20Ag-5Cu-38H
Bismuth strontium calcium copper oxide (BSCCO2223)
Nb-47Ti

## Slide 34
Hall sensor
SC solenoid
REBCO shield
Force sensor
Material | Blim, mT | Force, N
NbTi AXIAL | 66 | 2
BSCCO2223 AXIAL | 50 | 2
REBCO 2 layers TRANS. | 200 | 8
REBCO 10 layers TRANS. | 600 | 12
4 layers of NbTi/Nb/Cu TRANS. | 3100 | ?

## Slide 35
Hall sensor
SC solenoid
REBCO shield
Force sensor
Material | Blim, mT | Force, N
NbTi AXIAL | 66 | 2
BSCCO2223 AXIAL | 50 | 2
REBCO 2 layers TRANS. | 200 | 8
REBCO 10 layers TRANS. | 600 | 12
4 layers of NbTi/Nb/Cu TRANS. | 3100 | ?

## Slide 36: The Experiment - Technical overview
Off-axis Injection tubes
Cryostat in vacuum
Vacuum cross for services
SC storage magnet
Magnet lifter
4K cryo head

## Slide 37: The Experiment - Technical overview
Bendable vacuum tube
Vacuum Chamber
Superconducting Injection tube
Cryo shield
Beam entrance
Flange for beam monitors feed-throughs
μ+

## Slide 38: The Experiment - Storage Parameters
Using G4beamline and surrogate models, we optimized the storage efficiency of muons up to ~0.4 %.

## Slide 39
Magnetic field shielding
Active magnetic field shielding:
Coils
Difficulties:
Non-uniform field
~2T magnetic field
Strong gradient
Passive magnetic field shielding
Ferromagnetic (<500mT)
Superconductors (>500mT)
Magnetic field lines in a ferromagnetic material.

## Slide 40
Magnetic field shielding
Magnetic field shielding using superconductors
Difficulties:
Cryogenic temperatures
Not easily accessible
Superconductor-based passive shielding and screening systems by N. Rotheudt et al
DOI 10.1088/1361-6668/adb7cc

## Slide 41
Magnetic field shielding
Magnetic field shielding using superconductors
Superconductor-based passive shielding and screening systems by N. Rotheudt et al
DOI 10.1088/1361-6668/adb7cc
Image taken from D.Barna et al see ref: 10.1109/TASC.2018.2872860

## Slide 42: COMSOL Multiphysics simulation
Muon storage simulations show that successful storage can be achieved, when B field transversal components < 100 mT.
z

## Slide 43: Magnetic field shielding measurements
Material | Blim, mT | Force, N
NbTi AXIAL | 66 | 2
BSCCO2223 AXIAL | 50 | 2
REBCO 2 layers TRANS. | 200 | 8
REBCO 10 layers TRANS. | 600 | 12
4 layers of NbTi/Nb/Cu TRANS. | 3100 | ?