## Slide 1
Results on the CROSSTEST@LNL experiment for NArCoS:
the Cross-talk problem
Brunilde Gnoffo
21-26 September 2025
Caen

## Slide 2
Brunilde Gnoffo
Outline
Description of NArCoS
Study of the identification capabilities
Study of the cross-talk problem
Conclusions and perspectives

## Slide 3
Brunilde Gnoffo
NARCOS: Neutron ARray for COrrelation Studies
NArCoS realized in Catania in the context of the ANCHISE (Array for Neutron and Charged particles with HIgh linear momentum SElection) project, approved and financed by national PRIN2020 funding call and in the context of INFN-CSN3.
A compact and segmented transportable apparatus  consisting of plastic scintillators  EJ276G (ex EJ299-33) (3x3x3cm3)
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., Nucl. Instrum. Methods A 1064 (2024) 169425

## Slide 4
Brunilde Gnoffo
NARCOS: Neutron ARray for COrrelation Studies
NArCoS realized in Catania in the context of the ANCHISE (Array for Neutron and Charged particles with HIgh linear momentum SElection) project, approved and financed by national PRIN2020 funding call and in the context of INFN-CSN3.
A compact and segmented transportable apparatus  consisting of plastic scintillators  EJ276G (ex EJ299-33) (3x3x3cm3)
Reading the light signal: Si-PM
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., Nucl. Instrum. Methods A 1064 (2024) 169425

## Slide 5
Brunilde Gnoffo
NARCOS: Neutron ARray for COrrelation Studies
NArCoS realized in Catania in the context of the ANCHISE (Array for Neutron and Charged particles with HIgh linear momentum SElection) project, approved and financed by national PRIN2020 funding call and in the context of INFN-CSN3.
A compact and segmented transportable apparatus  consisting of plastic scintillators  EJ276G (ex EJ299-33) (3x3x3cm3)
Reading the light signal: Si-PM
Modular, reconfigurable (in mechanic and electronic) ->64 detection cells
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., Nucl. Instrum. Methods A 1064 (2024) 169425

## Slide 6
Brunilde Gnoffo
NARCOS: Neutron ARray for COrrelation Studies
NArCoS realized in Catania in the context of the ANCHISE (Array for Neutron and Charged particles with HIgh linear momentum SElection) project, approved and financed by national PRIN2020 funding call and in the context of INFN-CSN3.
A compact and segmented transportable apparatus  consisting of plastic scintillators  EJ276G (ex EJ299-33) (3x3x3cm3)
Reading the light signal: Si-PM
Modular, reconfigurable (in mechanic and electronic) ->64 detection cells
Energy measurement from ToF (Δt≤ 500 ps and LToF≈1m)  TOF measured using the RF of the CS or with a MCP (in case of low intensity exotic beams) or kinematic coincidence
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., Nucl. Instrum. Methods A 1064 (2024) 169425

## Slide 7
Brunilde Gnoffo
NARCOS: Neutron ARray for COrrelation Studies
NArCoS realized in Catania in the context of the ANCHISE (Array for Neutron and Charged particles with HIgh linear momentum SElection) project, approved and financed by national PRIN2020 funding call and in the context of INFN-CSN3.
A compact and segmented transportable apparatus  consisting of plastic scintillators  EJ276G (ex EJ299-33) (3x3x3cm3)
Reading the light signal: Si-PM
Modular, reconfigurable (in mechanic and electronic) ->64 detection cells
Energy measurement from ToF (Δt≤ 500 ps and LToF≈1m)  TOF measured using the RF of the CS or with a MCP (in case of low intensity exotic beams) or kinematic coincidence
Discrimination of n/γ and light charged particles from PSD
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
Pagano E.V. et al., Nucl. Instrum. Methods A 1064 (2024) 169425

## Slide 8
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
The experiment was performed at CN accelerator of INFN-LNL laboratory using a proton beam of 5 MeV on a LiF target producing a neutron beam having energy En < 4.5 MeV (neutron experimental threshold 1.5 MeV)-> p + 7Li —-> 7Be + n

## Slide 9
Brunilde Gnoffo
NArcoS: SiPM and mechanics

## Slide 10
Brunilde Gnoffo
NArcoS: SiPM and mechanics
Each elementary cell of EJ276G or EJ276 (3x3x3 cm3) is read with a matrix of 25 SiPM (6x6 mm2) of 30 𝜇m of thickness (≈ 40k microcells). The SiPM matrix is coupled with the plastic and provided of its PAC and bias/temperature compensation circuit

## Slide 11
Brunilde Gnoffo
NArcoS: SiPM and mechanics
Each elementary cell of EJ276G or EJ276 (3x3x3 cm3) is read with a matrix of 25 SiPM (6x6 mm2) of 30 𝜇m of thickness (≈ 40k microcells). The SiPM matrix is coupled with the plastic and provided of its PAC and bias/temperature compensation circuit
Prototype Electronic Board for housing the 9 elementary cells with their electronic readout boards, with the out of the signals, test inputs, temperature monitoring and bias input

## Slide 12
Brunilde Gnoffo
NArcoS: SiPM and mechanics
Each elementary cell of EJ276G or EJ276 (3x3x3 cm3) is read with a matrix of 25 SiPM (6x6 mm2) of 30 𝜇m of thickness (≈ 40k microcells). The SiPM matrix is coupled with the plastic and provided of its PAC and bias/temperature compensation circuit
Prototype Electronic Board for housing the 9 elementary cells with their electronic readout boards, with the out of the signals, test inputs, temperature monitoring and bias input
Sampling frequency: 1 GHz
Trigger: internal
(only the central plastic detector)

## Slide 13
Brunilde Gnoffo
Variables used for the identification
10% of the Rise time ≤ FAST ≤ 10% of the Rise time+30 ns
10% of the Rise time+140 ns ≤ SLOW ≤ 10% of the Rise time+260 ns
10% of the Rise time ≤ TOTAL ≤ 10% of the Rise time+260 ns
TOT=FAST+SLOW
PIDTOT=SLOW/ TOT
PIDTOTAL= SLOW/TOTAL
Tau= slope of the falltime

## Slide 14
Brunilde Gnoffo
Tau vs TOTAL
PIDTOTAL vs TOTAL
Identification matrices
Pulse shape discrimination by using different variables, for one of the plastic detector.

## Slide 15
Brunilde Gnoffo
Figures of merit, in different energy ranges, at slice of 200 KeVee
for 0 < E < 1200 KeVee
FoM (distance between the two peaks divided by the sum of the FWHMs of each peak)
6 projections of the 2D Tau Vs Total matrix on the Y axis (Tau) for each of the energy intervals of the Total component in keVee (0,200); (200,400); (400,600); (600,800); (800.1000); (1000,1200).
Gnoffo B., Pagano E.V. et al., IL NUOVO CIMENTO 48 C (2025) 12

## Slide 16
Brunilde Gnoffo
Figures of merit, in different energy ranges, at slice of 200 KeVee
for 0 < E < 1200 KeVee
The value of the FoM is shown in each panel.
A good separation is obtained from 600 KeVee where the FoM is ≳1

## Slide 17
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
The experiment was performed at CN accelerator of INFN-LNL laboratory using a proton beam of 5 MeV on a LiF target producing a neutron beam having energy En < 4.5 MeV (neutron experimental threshold 1.5 MeV)-> p + 7Li —-> 7Be + n

## Slide 18
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
The experiment was performed at CN accelerator of INFN-LNL laboratory using a proton beam of 5 MeV on a LiF target producing a neutron beam having energy En < 4.5 MeV (neutron experimental threshold 1.5 MeV)-> p + 7Li —-> 7Be + n
Two configurations were tested

## Slide 19
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
The experiment was performed at CN accelerator of INFN-LNL laboratory using a proton beam of 5 MeV on a LiF target producing a neutron beam having energy En < 4.5 MeV (neutron experimental threshold 1.5 MeV)-> p + 7Li —-> 7Be + n
Two configurations were tested
The 3x3 Matrix (surface crosstalk)
3x3 Matrix

## Slide 20
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
y
z
x
The experiment was performed at CN accelerator of INFN-LNL laboratory using a proton beam of 5 MeV on a LiF target producing a neutron beam having energy En < 4.5 MeV (neutron experimental threshold 1.5 MeV)-> p + 7Li —-> 7Be + n
Two configurations were tested
The 3x3 Matrix (surface crosstalk)
The 3 clusters (linear crosstalk)
3x3 Matrix
3 clusters

## Slide 21
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Matrix configuration (surface crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the central plastic scintillator was in trigger

## Slide 22
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Matrix configuration (surface crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the central plastic scintillator was in trigger
Crosstalk probability: x 100 %

## Slide 23
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Matrix configuration (surface crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the central plastic scintillator was in trigger
Crosstalk probability: x 100 %
P (%) = prob (%) ± Erass (%) = (0.117 ± 0.008) %
P (%) ≈ 0.1 %

## Slide 24
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Cluster configuration (linear crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the plastic scintillator of the first cell of the central block was in trigger

## Slide 25
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Cluster configuration (linear crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the plastic scintillator of the first cell of the central block was in trigger
Crosstalk probability: x 100 %

## Slide 26
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Cluster configuration (linear crosstalk)
Neutrons in other plastics in the same event (with multiplicity equal to 2) are crosstalk (or background)
Only the plastic scintillator of the first cell of the central block was in trigger
Crosstalk probability: x 100 %
P (%) = prob (%) ± Erass (%) = (0.163 ± 0.005) %
P (%) ≈ 0.2 %

## Slide 27
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Crosstalk Measurement and comparison with MC based simulation
The simulated value was obtained form GEANT4 toolkit simulation (G. Santagati and L. Quattrocchi) and from MCNPX toolkit simulation (L. Quattrocchi) The two simulation software were in good agreement

## Slide 28
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Crosstalk Measurement and comparison with MC based simulation
The simulated value was obtained form GEANT4 toolkit simulation (G. Santagati and L. Quattrocchi) and from MCNPX toolkit simulation (L. Quattrocchi) The two simulation software were in good agreement
The differences between the measured and the simulated values are not very large in absolute terms, but they become significant in relative terms: a factor of 4 for the matrix configuration, and nearly an order of magnitude for the cluster configuration. Further investigation is therefore required

## Slide 29
Brunilde Gnoffo
Conclusions and Perspectives
The results of CROSSTEST exp. @LNL (end of 2023) were presented

## Slide 30
Brunilde Gnoffo
Conclusions and Perspectives
The results of CROSSTEST exp. @LNL (end of 2023) were presented
A good separation between neutron and gamma with a FoM of 1.2 at 4 MeV of neutrons with three different 2D identification matrix,

## Slide 31
Brunilde Gnoffo
Conclusions and Perspectives
The results of CROSSTEST exp. @LNL (end of 2023) were presented
A good separation between neutron and gamma with a FoM of 1.2 at 4 MeV of neutrons with three different 2D identification matrix,
The crosstalk value at 4.5 MeV of neutrons was measured for the matrix configuration is about P(%) = 0.1% and for the cluster configuration is about P(%) = 0.2%.

## Slide 32
Brunilde Gnoffo
Conclusions and Perspectives
New test are on going at LNS-INFN in order to measure the time resolution

## Slide 33
Brunilde Gnoffo
Conclusions and Perspectives
New test are on going at LNS-INFN in order to measure the time resolution
New experiments have to be performed in order to test the crosstalk at higher neutron energies in Catania at LNS-INFN and in Legnaro at LNL-INFN.

## Slide 34
Brunilde Gnoffo
Conclusions and Perspectives
New test are on going at LNS-INFN in order to measure the time resolution
New experiments have to be performed in order to test the crosstalk at higher neutron energies in Catania at LNS-INFN and in Legnaro at LNL-INFN.
MoReNA experiment. The goal of the experiment is to test the feasibility of using NArCoS for the study of molecular states with low neutron multiplicity, focusing on the decay channel 13C → n + 12C

## Slide 35
Brunilde Gnoffo
Conclusions and Perspectives
In its final version, the demonstrator will include 16 clusters, each consisting of an array of 4 elementary cells arranged in line along the beam axis and mounted on a 4×1 PCB motherboard.
New test are on going at LNS-INFN in order to measure the time resolution
New experiments have to be performed in order to test the crosstalk at higher neutron energies in Catania at LNS-INFN and in Legnaro at LNL-INFN.
MoReNA experiment. The goal of the experiment is to test the feasibility of using NArCoS for the study of molecular states with low neutron multiplicity, focusing on the decay channel 13C → n + 12C

## Slide 36
Brunilde Gnoffo
For more info see :
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 889 (2018) 83-
2) Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
3) Pagano E.V. et al., IL NUOVO CIMENTO 41 C (2018) 181
4) Pagano E.V. et al., JPS Conf. Proc. 32, 010096 (2020)
5) Pagano E.V. et al., IL NUOVO CIMENTO 43 C (2020) 12
6) Pagano E.V. et al., J. Phys.: Conf. Ser. 1643 (2020) 012037
7) Pagano E.V. et al., IL NUOVO CIMENTO 45 C (2022) 64
8) Pagano E.V. et al., Front. Phys. 10:1051058
9) Pagano E.V. et al., LNS Report (2022)
10) Pagano E.V., G. Politi, A. Simancas et al., Nucl. Instrum. Methods A 1064 (2024) 169425
11) Santagati G., Pagano E.V. et al., RAD Conference Proceedings, vol. 7, pp. 52-58, 2023
12) Santagati G., Pagano E.V. et al., IL NUOVO CIMENTO C, vol. 48, (2025) 13
13) Pagano E.V. et al., IL NUOVO CIMENTO C, vol. 48, (2025) 12
14 ) Quattrocchi L., Gnoffo B., Pagano E.V. et al., (Proceedings of the International Conference Applied Nuclear Physics 2024 to be published)
Gnoffo B., Pagano E.V. et al., IL NUOVO CIMENTO 48 C (2025) 12
Gnoffo B., Pagano E.V. et al., 2025 JINST 20
16) Gnoffo B., Pagano E.V. et al., on timing performances in preparations
17) Pagano E.V. et al., on croostalk al 4.5 MeV neutron in preparation

## Slide 37
B. Gnoffo1,2, E. V. Pagano3, C. Boiano4, G. Cardella2, A. Castoldi4,5, E. De Filippo2, E. Geraci1,2, C. Guazzoni4,5,G.Lanzalone3,6, C. Maiolino3, N.S. Martorana2,
S. Pirrone2, G. Politi1,2, L. Quattrocchi2,7, F. Risitano2,7, F. Rizzo1,3, P. Russotto3,
G. Saccà2, G. Santagati3,8, M.Trimarchi2,7and C. Zagami1,3
1Dipartimento di Fisica ed Astronomia, Università di Catania, Catania, Italy
2INFN, Sezione di Catania, Catania, Italy
3INFN, Laboratori Nazionali del Sud, Catania, Italy
4INFN, Sezione di Milano, Milano, Italy.
5Politecnico di Milano, Dip. Elettronica, Informazione e Bioingegneria, Milano, Italy
6Università di Enna ‘‘Kore’’, Enna, Italy.
7Dipartimento di Scienze MIFT, Università di Messina, Messina, Italy.
8 Istituto di Scienze del Patrimonio Culturale - Consiglio Nazionale delle Ricerche (ISPC-CNR), Catania, Italy

## Slide 38
Brunilde Gnoffo
For more info see :
Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 889 (2018) 83-
2) Pagano E.V. et al., N.S., Nucl. Instrum. Methods A, 905 (2018) 47-52
3) Pagano E.V. et al., IL NUOVO CIMENTO 41 C (2018) 181
4) Pagano E.V. et al., JPS Conf. Proc. 32, 010096 (2020)
5) Pagano E.V. et al., IL NUOVO CIMENTO 43 C (2020) 12
6) Pagano E.V. et al., J. Phys.: Conf. Ser. 1643 (2020) 012037
7) Pagano E.V. et al., IL NUOVO CIMENTO 45 C (2022) 64
8) Pagano E.V. et al., Front. Phys. 10:1051058
9) Pagano E.V. et al., LNS Report (2022)
10) Pagano E.V., G. Politi, A. Simancas et al., Nucl. Instrum. Methods A 1064 (2024) 169425
11) Santagati G., Pagano E.V. et al., RAD Conference Proceedings, vol. 7, pp. 52-58, 2023
12) Santagati G., Pagano E.V. et al., IL NUOVO CIMENTO C, vol. 48, (2025) 13
13) Pagano E.V. et al., IL NUOVO CIMENTO C, vol. 48, (2025) 12
14 ) Quattrocchi L., Gnoffo B., Pagano E.V. et al., (Proceedings of the International Conference Applied Nuclear Physics 2024 to be published)
15) Gnoffo B., Pagano E.V. et al., on timing performances in preparations
16) Pagano E.V. et al., on croostalk at 4.5 MeV neutron in preparation

## Slide 39
Brunilde Gnoffo
Gamma rays selection
Tau vs TOTAL
PIDTOTAL vs TOTAL
PIDTOT vs TOT
To select gamma rays, a cut around the corresponding line was made in each of the bidimensional matrices obtained during the runs in which 60Co source was used for the calibtration.

## Slide 40
Brunilde Gnoffo
Neutron selection
In the beam runs, to select neutrons, a cut around the corresponding line was made in each of the bidimensional matrices obtained after the subtracted gamma band selected as described above.

## Slide 41
Brunilde Gnoffo
Neutron energy spectra
Energy spectra in MeVee, of neutrons selected as descibed above, shown in black when the selection was made from the 2d plot tau vs TOTAL, in red for the selection made from the Pidtot vs TOT matrix and in green for the selection from Pidtotal vs TOTAL.

## Slide 42
Brunilde Gnoffo
Figures of merit
Figures of merit, in different energy ranges, at slice of 200 KeV for 0 < E < 1200 KeV
FoM (distance between the two peaks divided by the sum of the FWHMs of each peak)
Calculation procedure:
two separated gaussian fits for each peak in the corresponding interval
The 6 calculated parameters are used as the entrance parameter in a fit of the entire spectrum, by using as fitting function the sum of two gaussians, relative to the two corresponding intervals (red line in the plot)

## Slide 43
Brunilde Gnoffo
Results of CROSSTEST exp. @LNL (end of 2023)
Spokesperson(s): E.V. Pagano, G. Politi, P. Russotto, T. Marchi
Sampling frequency: 1 Gs/s Trigger: internal (only the central plastic detector)