## Slide 1: Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
European Nuclear Physics Conference 2025 - Caen, France
L. Arsini1,2, B. Caccia3, A. Ciardiello3, S. Giagu1,2, A. Sarti4, C. Mancini Terracciano1,2
1Department of Physics, Sapienza University of Rome, Rome, Italy. 2INFN, Section of Rome, Rome, Italy. 3Istituto Superiore di Sanità, Rome, Italy, 4Department of Basic and Applied Sciences for Engineering, Sapienza University of Rome, Rome, Italy
22/09/2025

## Slide 2: Treatment Planning Optimization
Choice of directions, energies and intensities of the beamlets
Fit dose medical prescription
to
Dose estimation
Plan Optimisation
2 steps
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Heavily depends on operator performance

## Slide 3: Differentiable approach
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Deep Learning driven
NOT a Knowledge-based DL model
Build a differentiable surrogate model for dose computation
Reproduce sub-optimal plans
Established RT only
Explainability?
Use powerful gradient-based optimizers
Treat all parameters jointly & automatically
GPU native

## Slide 4: Cylindrical approach
Three main advantages:
Reduce complexity without loss of generalisation: the cylinder follows the beam
Overcome problems related to the size of CT images
More resolution near the beamline
Dose data collected in a cylinder in the beam-eye view
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 5: Dose deposition in CT scans
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Monte Carlo
simulated dose
Density map in the cylinder
Deep Learning model

## Slide 6: Architecture
Graph NN and an original pooling
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
L. Arsini et al. Fast and precise dose estimation for very high energy electron radiotherapy with graph neural networks. Frontiers in Physics, 2024, 12, 1443306
L. Arsini et al. Nearest Neighbours Graph Variational AutoEncoder. Algorithms, 2023, 16(3), 143
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 7: DL prediction vs MC simulation
DL error ~ MC
Dose depth curve
In a 4 mm radius cylinder around the beam
(75% of the dose)
Test set example
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
L. Arsini et al. Frontiers in Physics 2024
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 8: Computation speed-up
Lorenzo Arsini - 08/01/2025
Deep Learning emulation of Physical Processes in Radiation Therapy
Monte Carlo simulation
Deep Learning emulation
~ 18 min
~ 5 ms
1M primaries
48 core CPU on HPC Cluster
1 NVIDIA V100 GPU
Can be reduced even more in batch mode

## Slide 9
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 10: Full Treatment Plan (Energy)
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
2 mm grid

## Slide 11: Proton dose engine
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Dose
Prediction Error

## Slide 12: Optimizing Spread Out Bragg Peak
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
SOBP Optimization
PTV
OAR
10 pencilbeams
Field
Pencil beam
Energy
Fluence
5 variables x pencil beam
Objective function:
Clinical volumetric + voxel constraints (L2)
Fluence

## Slide 13: Optimisation strategy
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
ADAM

## Slide 14: Optimisation strategy
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
ADAM

## Slide 15: Results with one field
The algorithm manages to find the parameters for the optimal solution
Producing a Spread Out Bragg Peak
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 16
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Two fields optimisation

## Slide 17
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France
Two fields optimisation
Final solution

## Slide 18: Benefits
Autoplanning algorithm
Optimize all beams parameters as continuous degrees of freedom Field and pencil-beam orientation, energy, fluence, shape, …
Possibility to explore more the parameter space
Speed and precision
Explainability
Possibly Better Treatments
Entire pipeline on GPU
Deep Learning not as a black-box
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 19: Opportunities
Robust optimisation
  It is possible to estimate the uncertainties voxel-wise
  Also the uncertainties are differentiable
Biological effectiveness it is possible to compute LET with no computational overhead
Could be included in the objective function
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 20: Next steps
Optimise the algorithm
Define stop strategies
Dose engine per field
Test on a clinical case
  Increase number of fields
  Use multiple GPUs
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini - 22/09/2025 EuNPC 2025 - Caen, France

## Slide 21: Thank you for your attention!
Dose engine for fast and accurate dose calculation
Cylindrical Graph Neural Network model:
From CT scan to dose deposition
Gradient based plan optimization on GPUs
lorenzo.arsini@uniroma1.it
Deep Learning–Driven Differentiable Autoplanning for Proton Therapy: A Proof-of-Concept
Lorenzo Arsini 22-09-2025