## Slide 1: (T)SDHCAL
I.Laktineh
IP2I, Lyon, France
On behalf of the French groups of
IP2I, LPCC, OMEGA
and 7 other groups from Spain, Belgium, S.Korea, China and Tunisia

## Slide 2
The structure proposed for the SDHCAL :
is very compact with negligible dead zones
Eliminates projective cracks
Minimizes barrel / endcap separation
(services leaving from the outer radius)
SDHCAL
The SDHCAL concept is based on exploiting Gaseous Detectors high granularity potential
For PFA applications. It was conceived and proposed for ILD@ILC
Semi-digital readout to improve on
power-pulsed electronics to reduce power consumption and eliminate active cooling
self-supporting mechanical structure to serve as absorber as well.
SDHCAL Technological Prototype was proposed in 2008 to be
as much as possible similar to the ILD module and able to study hadronic showers
Challenges
-Homogeneity for large surfaces
-Thickness of only few mms
-Lateral segmentation of 1 cm X 1 cm
-Services from one side
-Embedded power-cycled electronics
-Self-supporting mechanical structure

## Slide 3
10500 64-ch ASIC were tested and calibrated using a
dedicated (ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested.
They were assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with
their electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.

## Slide 4
10500 64-ch ASIC were tested and calibrated using a
dedicated (ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested.
They were assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with
their electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.
Published: JINST 10 (2015) P10039
48 layers (-6λI)
1 cm X 1 cm granularity
3-threshold, 500000 channels
Power-Pulsed
Triggerless DAQ system
Self-supporting mechanical structure
CALICE SDHCAL
Since 2012

## Slide 5
SDHCAL performance
The SDHCAL prototype was exposed to hadron, muon and electron
beams in 2012, 2015 , 2018 and 2022 on PS, H6 and H8 -SPS lines.
Power-pulsing using the SPS spill structure was used to reduce the
power consumption.
Self-triggering mode is used but external trigger mode is possible
The threshold information helps to improve on the energy rec.
by better accounting for the number of tracks crossing one pad
Data were taken in 2012, 2015, 2017, 2018 and 2022 with
continuously improved DAQ system.
Triggerless
Time-based clustering
Noise rate
Efficiency
Multiplicity

## Slide 6
SDHCAL Performance
Erec = α (Ntot) N1 + β (Ntot) N2 + γ (Ntot) N3
α , β , γ are quadratic functions of
They are computed by minimizing :
χ2= (Ebeam-Erec)2/Ebeam
Track segments reconstruction using 3D-Hough Transform helps
apply different treatment to the hits of these segments.
JINST 11 (2016) P04001
Hough-Transform
JINST 12 (2017) P05009
Track segments can also be used as in-situ calibration
and monitoring tools
JINST 15 (2020) P10009
Energy reconstruction
Particle identification
JINST 17 (2022) P07017

## Slide 7
ArborPFA, April algorithms:
they connect hits and then their clusters using distance and orientation information
then user tracker information (momentum)
to improve on the correction
CALICE note CAN054
Efficiency
Purity
ΔE
1 neutral of 10 GeV
1 neutral of 10 GeV
1 neutral of 10 GeV
Shower separations
R. Eté PhD thesis
L. BO (LIO postdoc)

## Slide 8
SDHCL for Circular Collider
New readout electronics:
  Continuous readout
  Precise time information  T-SDHCAL
Mechanics & services
  active cooling is mandatory
High rate capability
New friendly gases

## Slide 9
SDHCALT-SDHCAL

## Slide 10
Timing is an important factor to identify delayed neutrons and better reconstruct their energy
Timing can help to separate close-by showers and reduce the confusion for a better PFA application. Example: pi-(20 GeV), K-(10 GeV) separated by 15 cm.
1 ns resolution
100 ps resolution
Y
Y
Z
X
Y
X
X
Y

## Slide 11
Including time information in the simulation to separate hadronic showers ( 10 GeV neutral particle from 30 GeV charged particle) using techniques similar to ARBOR’s ones.
Timing for PFA

## Slide 12
DETECTOR
MultiGAP RPC is an excellent candidate.
5-gap of 200 µm each separating glass plates of 250 µm thick can provide
a time resolution of around 100 ps
New and easy way to build MRPC was recently developed.
Preliminary results show an efficiency > 93% with 5 gaps
The standard method to build MRPC is based on using fishing line

## Slide 13
2x 4-gap RPC with low resitivity glass

## Slide 14
Electronics readout
An ASIC with a fast preamplifier, precise discriminator and excellent TDC is needed
PETIROC 32-channel, high bandwidth preamp (GBWP> 10 GHz), <3 mW/ch, dual time and charge measurement (Q>50 fC)
jitter < 20 ps rms @ Q>0.3 pC
Internal TDC of 50 ps time resolution.
Another ASIC in TSMC 130 nm developed by OMEGA&WEEROC called LIROC with a time jitter < 10 ps is to be used in the future but it needs to be equipped with an internal TDC before (DRD6).

## Slide 15
Front-End Electronics for MRPC readout with high timing resolution
The system includes a front-end board (FEB), a detector interface card (DIF) and a data acquisition system(DAQ) based on ZCU102.
Top view
Bttom view
Small ASU
“Large” ASU
Board with 8 (could be extended to 12) Petircoc2B ASICs are conceived
Pads 2cm x 2cm, 256 channels
Local FPGA (Xilinx Spartan-6 TQFP) embedded on board
A board with 4 petiroc, 128 pads as well as the whole DAQ system was developed and being tested
50 cm x 33 cm

## Slide 16
(T)SDHCAL power consumption and cooling
The duty cycle of FCCee/CEPC is different from that of ILC and no power pulsing is possible.
The power consumption is therefore increased by a factor of 100-200 with respect to ILC and active cooling is needed.
Lyon and Shanghai groups worked on a simple cooling system for SDHCAL based on using water circulating into copper pipes
108 chips
Rectangular section tubes : 2x1 mm
Copper plate over: 1.5 mm
PCB plate under: 1.4 mm
symmetry
1.5 m
0.5 m
Flow in
Flow out
0.8 mW/chips with power pulsing, 80 mW/chips without power pulsing

## Slide 17
(T) SDHCAL power consumption and cooling
0.8 mW/chips with power pulsing, 80 mW/chips without power pulsing
The duty cycle of FCCee/CEPC is different from that of ILC and no power pulsing is possible.
The power consumption is therefore increased by a factor of 100-200 with respect to ILC and active cooling is needed.
Lyon and Shanghai groups worked on a simple cooling system for SDHCAL based on using water circulating into copper pipes.
Results are very encouraging but we need to confirm by producing a prototype

## Slide 18
(M)RPC are low-rate capability detectors due to the resistive nature of the electrodes. The capability could be significantly increased by developing low resistivity materials.
Dopped glass (by Tsinghua group) could be a solution
PVdF and PEEK are very stable and chemically inert thermoplastic
-New kind of PVdF developed with the help of PolyOne company,
doped with CNT  bulk resistivity of 1011-12 W.cm
-New charged PEEK developed with the help of Krefine company.
doped with Black Carbon bulk resistivity of 108-9 W.cm was achieved.
A few small detectors were made using doped PVdF plates of 2-3 mm thickness.
High efficiency was obtained with cosmic
Plates made with charged PEEK were produced
Some homogeneity due to extrusion need to be fixed before to have a final material.
High-Rate capability

## Slide 19
New friendly gases
The CERN gas group has identified friendly gases to replace TFE and SF6 for (M)RPC
TFE HFO1234ze
SF6 Nova4710 ( not good for Bakelite but ok for GRPC and MRPC)
Techniques of recycling the gas mixture is being constantly improved (>90%)
Techniques to recover the different exhaust gases (distillation…etc) are being developed and promising results have been obtained.
Recent results by our partners of GWNU showed that HFO1234ZE provides similar performances as TFE with no need to CO2 and SF6

## Slide 20
Conclusion
SDHCAL is ready for ILC
Many developments are needed to adapt SDHCAL for FCCee
Adding time information will certainly improve on SDHCAL already excellent performances
Finally, developing T-SDHCAL is also developing excellent muon chambers for FCCee.