## Slide 1: Développement de chambres à fission pour l'étude des actinides avec les détecteurs 4p SCONE@NFS et TAC@n_TOF
Workshop NACRE – IPHC Strasbourg – 22-23 Janvier 2024
M. Aiche4, M. Bacak1,5, A. Cahuzac1, G. Bélier2, D. Bernard3, E. Berthoumieux1, E. Dupont1, B. Fraïsse2, F. Gunsing1, L. Mathieu4, G. Noguère3, O. Sérot3, G. Tsiledakis1
1 Irfu/DPhN, CEA Paris-Saclay; 2 DPTA/SPN, CEA DAM Ile de France; 3 IRESNE/DER/SPRC CEA Cadarache; 4 LP2i Bordeaux; 5 TU Wien

## Slide 2: Contents
R&D fission chamber for fission tagging
Measurements performed and in preparation
  2016: 233U @n_TOF
  2021: 238U @NFS
  2023: 239Pu @NFS
  2025: 241Pu @n_TOF
Summary

## Slide 3: Fission Chamber for fission tagging
1

## Slide 4: Principle of fission tagging
with the n_TOF TAC
Fission tagging is necessary
  For studying g from fission (in coincidence mode)
  For studying capture (in anti-coincidence mode)
Samples are inside the fission chamber, which is inside the TAC
γ2
γ3
γ1
n
TAC detector (open)
Fission chamber
with SCONE
Fission tagging is necessary
  For studying n from fission (in coincidence mode)
  For studying (n,xn) reaction (anti-coincidence)
Samples are inside the fission chamber, which is inside SCONE

## Slide 5: Principle of fission tagging with the n_TOF Total Absorption Calorimeter (TAC)
Detection of g-rays by the TAC (4p segmented BaF2 calorimeter of 40 crystals)
𝐸𝑆𝑢𝑚 = 𝐸1 + 𝐸2 + 𝐸3 = 𝑆𝑛 + 𝐸𝑛
𝑚𝑐𝑟 = 3
ESum is the total g-ray energy deposited in the TAC
mcr is the number of crystals detecting a gamma
⇨ Selection cuts on Esum and mcr improve Signal/Bkgd
Fission tagging is necessary
  For studying fission (in coincidence mode)
  For studying capture (in anti-coincidence mode)
  For studying (n,xn) reaction (anti-coincidence)
Samples are inside the fission chamber, which is inside the TAC
γ2
γ3
γ1
n
TAC detector (open)
Fission chamber

## Slide 6: Fission Tagging development for the n_TOF TAC
TAC + FTMG-U235 [C. Guerrero et al., EPJA 48 (2012) 29]
Micromegas (MGAS) detectors / electronics outside the TAC
Background issue due to the MGAS thick Cu mesh in the beam
TAC + FICH-U233 [M. Bacak et al., NIMA 969 (2020) 163981]
Fission chamber
Fast electronics plugged directly on the chamber’s PCB
Minimum amount of material in the beam
TAC + FICH-Pu239 [J. Perkowski et al., in preparation]
Fission chamber with minimum material in the beam
Electronics moved off center (less background)
Additional gas in the beam (more background)

## Slide 7: Fission chambers for 233U and 241Pu
233U FICH [M. Bacak, NIMA 969 (2020) 163981]
Compact (L 12 cm x Ø 9 cm) Multi-plate chamber
- Total of ~46 mg of 233U
- 14 samples highly enriched in 233U (JRC-Geel)
- 14 ionization cells / Readout from 8 anodes
Fast signals (34 ns FWHM) for high a-count rates (>1 MBq per anode)
- Fast ionizing gas CF4 / Fast electronics (CEA/DAM/DIF)
New 241Pu FICH
Total of ~10 mg of 241Pu
6 to 8 samples only (more compact ⇨ less material in the beam)
Lower gas pressure (less material in the beam ⇨ less background)
Less massive (for reducing background from scattered neutrons)
Improved electronics (faster signals for sustaining higher a-count rates)

## Slide 8: Comparison/Evolution of fission chambers
(*) n_TOF-Pu241 with 15 mg samples (10 mg of 241Pu) of 70 MBq alpha-activity (assuming 2% 241Am)
 | LANL-Pu241 (2010) [1] | DAM-U238 (2016) [2] | n_TOF-U233 (2016) [3] | n_TOF-Pu239 (2020) [4] | DAM-Pu239 (2023) | n_TOF-Pu241(*) (2024)
Gas and drift velocity | 90%Ar-10%CH4 6 cm/us | CF4 11 cm/us | CF4 11 cm/us | 90%Ar-10%CF4 12 cm/us | CF4 11 cm/us | 90%Ar-10%CF4 12 cm/us
Gap and Voltage | 12 mm 250 V/cm | 2.5 mm 1300 V/cm | 3 mm 1400 V/cm | 4.5 mm 470 V/cm | 3 mm | ~3 mm
Drift time | ~200 ns | 23 ns | 27 ns | 37 ns | 27 ns | ~27 ns
Pressure | 1.65 bars | PA + 50 mbar | 1100 mbar | PA + epsilon | ~100 mbar | < PA
Deposit | ∅ 38 mm ~200 ug/cm2 (+ VYNS film) | ∅ 33 mm 585 ug/cm2 | ∅ 40 mm 264 ug/cm2 | ∅ 20 mm 300 ug/cm2 |  | ∅ 30 mm 265 ug/cm2
Cathodes | 4 (SS 12.5 um) | 19 (Ti 50 um) | 14 (Al 10 um) | 10 (Al 10 um) | 8 (Al 10 um) | 8 (Al 10 um)
Anodes | ? | 18 (Ti 50 um) | 8 (Al 20 um) | 10 (Al 10 um) | 4 (Al 1 or 2 um) | 8 (Al 10 um)
Cat. + An. |  | 1850 um | 300 um | 200 um | 86 um | 160 um
Windows | ? | Titanium (100 um) | Kapton (25 um) | Kapton (25 um) | Titanium (10 um) | Kapton (25 um)

## Slide 9: Fission Chamber references
[1] F. Tovesson, T.S. Hill, Cross Sections for 239Pu(n,f) and 241Pu(n,f) in the Range En = 0.01 eV to 200 MeV, Nuclear Science and Engineering 165 (2010) 224; https://doi.org/10.13182/NSE09-41
[2] J. Taieb et al., A new fission chamber dedicated to Prompt Fission Neutron Spectra measurements, NIMA 833 (2016) 1–7; http://dx.doi.org/10.1016/j.nima.2016.06.137
[3] M. Bacak et al., A compact fission detector for fission-tagging neutron capture experiments with radioactive fissile isotopes, NIMA 969 (2020) 163981; https://doi.org/10.1016/j.nima.2020.163981
[4] J. Perkowski et al., Multi-section ionization fission chamber for measurement of 239Pu(n,g) reaction in fission tagging method (paper in preparation)

## Slide 10: 233U @ n_TOF (2016)
PhD Thesis of Michael Bacak
2.1

## Slide 11: Measurement of 233U @ n_TOF in 2016
Why
U-233 capture cross section is important for reactors using the Th/U fuel cycle
Only two measurements are available because of U-233 radioactivity and low capture cross section with respect to fission
How
Development of a compact fission chamber to be coupled with the TAC
Fission-tagging measurement of the U-233 capture cross section
γ
γ
γ
n
TAC detector (open)
Fission chamber

## Slide 12: Measurement of 233U @ n_TOF in 2016
C
A
A
A
A
CC
CC
CC
Fission Chamber [M. Bacak, NIMA 969 (2020) 163981]
Compact (L 12 cm x Ø 9 cm)
Multi-plate chamber
  - 14 ionization cells
  - Readout from 8 anodes
Fast signals (34 ns FWHM) for high -count rates (>1 MBq per anode)
  - Fast ionizing gas CF4
  - Fast electronics (DAM/DIF)
  - Gap width: 3 mm @ 420 V
14 isotopically enriched (>99.9%) 233U samples (JRC-Geel)
    - Ø 4 cm
    - ~46 mg 233U total

## Slide 13: Measurement of 233U @ n_TOF in 2016
Data Taking
TAC and Fission Chamber operated in coincidence
Six weeks of measurement
950 TB of data
Analysis
Multi-parametric data analysis (coincidences, anti-coincidences, crystal multiplicity, Sum energy, gamma spectra)
Monte-Carlo simulations for various corrections (thresholds, background, efficiency)
Still fine-tuning the analysis while finalizing the publication

## Slide 14: Measurement of 233U @ n_TOF in 2016
Preliminary alpha-ratio [M. Bacak, EPJ Conf 239 (2020) 01043]
Overall consistency with evaluated libraries
Some deviations under investigations
Final paper still to be published
3 ≤ mcr ≤ 7
2.5 MeV ≤ ESum ≤ 7 MeV

## Slide 15: 238U @ NFS (2021)
2.2

## Slide 16: Measurement of 238U @ NFS in 2021
B. Fraïsse et al, JEFF Meeting, OECD/NEA, November 2023, JEF/DOC-2292

## Slide 17: Measurement of 238U @ NFS in 2021
From B. Fraïsse et al, JEFF Meeting, OECD/NEA, November 2023, JEF/DOC-2292

## Slide 18: Measurement of 238U @ NFS in 2021
From B. Fraïsse et al, JEFF Meeting, OECD/NEA, November 2023, JEF/DOC-2292

## Slide 19: Measurement of 238U @ NFS in 2021
From B. Fraïsse et al, JEFF Meeting, OECD/NEA, November 2023, JEF/DOC-2292
FICH inside SCONE (open)

## Slide 20: Measurement of 238U @ NFS in 2021
From B. Fraïsse et al, JEFF Meeting, OECD/NEA, November 2023, JEF/DOC-2292

## Slide 21: 239Pu @ NFS (2023)
2.3

## Slide 22: Fission chamber design
FICH DAM-Pu239 (8 deposits and 4 anodes)
Stack of biased anodes (in black) and grounded cathodes with deposit (in red)
Gap of 3 mm => stack of 3 cm

## Slide 23: Fission chamber design

## Slide 24: Mounting of the samples at JRC-Geel

## Slide 25: Fission chamber validation test
Gas pressure of 800 mbar
Good a-FF separation

## Slide 26: 241Pu @n_TOF (2025)
2.4

## Slide 27: Motivations
Plutonium is produced in reactors, 239Pu and 241Pu both contribute to energy production
241Pu xs are not well known because of its short half-life (~14 years) and the 241Am build-up

## Slide 28: Capture and fission cross sections
The fission cross section of 241Pu is at least three times larger than its capture cross section
There is only one time-of-flight measurement for capture, made by Weston at ORNL in the 70’s

## Slide 29: Radioactive decay of Pu and daughters
High activity (b > 99.99% with Q ~21 keV)
b decay populates 241gsAm only (i.e., no g)
Possible issue for capture xs interferences
Possible issue for a-background in the FICH
no g
~no g
Eg = 149 keV
Eg = 60 keV
a few gs
Eg = 312 keV
Parent nucleus | T1/2 | Decay mode | Daughter nucleus | T1/2
241Pu | 14.3 y | b- (~100%) | 241Am | 433 y
241Am | 433 y | a (100%) | 237Np | 2.1 My
238Pu | 87.7 y | a (100%) | 234U | 245 ky
239Pu | 24.1 ky | a (100%) | 235U | 704 My
240Pu | 6.6 ky | a (100%) | 236U | 23 My
242Pu | 373 ky | a (100%) | 238U | ~stable
244Pu | 81 My | a (100%) | N/A | 
237Np | 2.1 My | a (100%) | 233Pa | 27 d
233Pa | 27 d | b- (100%) | 233U | 159 ky
241Pu | 14.3 y | a (<<1%) | 237U | 6.75 d
237U | 6.75 d | b- (100%) | 237Np | 2.1 My

## Slide 30: Simulation of capture counting rates
Binning adapted to have a statistical precision better than ~3% (~103 counts/bin)
E < ~20 eV ⟹ 200 bpd (bins per decade) allow for good resolution and statistics
20 eV

## Slide 31: Alpha-activity from a 15 mg sample (~10 mg of 241Pu)
Composition calculated in 2025 four months after the last Am purification
Significant contributions from 238Pu, 240Pu, and especially 241Am
Total contribution from Pu isotopes is 30 MBq (in 4p)
241Am build-up would add between 20 MBq (1% build-up) and 40 MBq (2% build-up)
The new FICH should be able to handle such an a-background, i.e. up to ~5 MBq/channel (see tests at 14 MBq/channel in Laurent et al., NIMA 990 (2021) 164966)
 | Pu-238 | Pu-239 | Pu-240 | Pu-241 | Pu-242 | Am-241 | Total
Atom % | 0.07% | 4.3% | 16.6% | 65.3% | 12.4% | ~1% | 100%
a-activity (MBq) | 6.5 | 1.5 | 21 | 0.9 | 0.3 | ~20 | ~50

## Slide 32: Deposits of ~10 mg of 241Pu (15 mg of Pu)
Assuming a maximum activity in 4p of 70 MBq (30 MBq from Pu + 40 MBq from 2% 241Am)
- 1 anode for every deposit (on the cathode), i.e. alpha-activity in 2p only
- deposits of diameter 40 mm or 30 mm
=> 8 deposits of ∅ 30 mm should be ok (8 channels is the maximum with the “FICH-U3” design)
 |  | 4 anodes | 6 anodes | 8 anodes | 10 anodes
a-activity/channel |  | 8.8 MBq | 5.8 MBq | 4.4 MBq | 3.5 MBq
Deposit thickness | ∅ = 40 mm | 298 mg/cm2 | 200 mg/cm2 | 150 mg/cm2 | 
 | ∅ = 30 mm |  | 354 mg/cm2 | 265 mg/cm2 | 212 mg/cm2

## Slide 33: Fission chamber preliminary design
FICH n_TOF-Pu241 (8 deposits and 8 anodes)
Stack of biased anodes (in black) and grounded cathodes with deposits (in red)
Gap of 3 mm => two symmetric half-stacks of 19 mm
NB: the length of the chamber is constrained by the size of a preamp (which is ~37 mm)

## Slide 34: Fission chamber preliminary design
Compact configuration (-7 mm) with bottom connections for PA
-7 mm
-7 mm

## Slide 35: Absorber material preliminary study
The absorber of the TAC should:
moderate/absorb all scattered (and fission) neutrons
be transparent to gamma
not produce any problematic secondary gammas
Typical materials: LiH, Polyethylene (PE) with Li or B
Geant4 simulation shows that 4 cm B-PE with 5% B-nat is very efficient

## Slide 36: Summary
3

## Slide 37: Summary
Collaboration between DRF, DAM, DES, LP2i Bordeaux, IRSN (+JRC-Geel)
Development of Tagging Fission Chambers for high counting rates
  Compact FICH-U233 for TAC based on DAM design for high counting rate
  More compact FICH-U238 and FICH-Pu239 for SCONE based on FICH-U233
  FICH-Pu241 for TAC will be based on the latest developments
Measurements making use of these developments
  @n_TOF: 233U in 2016 (and 241Pu in 2025)
  @NFS: 238U in 2021 (and 239Pu…)

## Slide 38: Thank you for your attention