## Slide 2: A High-Energy Cosmic Ray Detector for the Owens Valley Radio Observatory Long-Wavelength Array
Kathryn Plant NASA Postdoctoral Fellow, JPL
2
Notes: Updates from the OVRO-LWA cosmic ray detection system

## Slide 3: Introduction to the OVRO-LWA
Frequency [MHz]
Power [dBm]
0
20
40
60
80
-80
-90
-100
-70
-60
-50
-40
-30
-20
Extrasolar space weather, epoch of reionization, solar astronomy, cosmic rays and more

## Slide 4: Cosmic ray composition measurements are key to understanding the Galactic to extragalactic transition.
log (E/eV)
Schroeder 2019
9 10 11 12 13 14 15 16 17 18 19 20
Observable by
OVRO-LWA
Notes: This plot combines composition measurements from several experiments. The observation that the heavy element fraction increases near the second knee, and then light elements dominate again at even higher energies is a key piece of evidence about transition to extragalactic sources.
These energies also have more differences between different experiments and so it will be useful for the OVRO LWA to contribute additional measurements.

## Slide 5: With the stage II array, Monroe et al. 2020 detected 8 cosmic rays with 40 hours of observing.
Antenna Position East-West [m]
Position North-South [m]
60
-60
-60
60
0
0
Power [arbitrary units
Notes: A previous graduate student Ryan Monroe detected 10 cosmic rays in 40 hours with a dedicated observing run with the earlier version of the array.
The movie on the left shows a cosmic ray arriving across the core array.
The dots mark antenna positions. The size and color of the dot correspond to the power in each antenna.
This demonstration of a radio only technique was a dedicated observing run that just used the core array and required stopping other observations.
I am developing firmware that will allow us to search for cosmic rays all the time, without interrupting other observations.

## Slide 6: Upgrading The OVRO-LWA
Notes: Things I had a role in but wasn’t the main person:
  Delay calibration
  Laser driver testing
  Miscellaneous hardware installation

## Slide 7: The OVRO-LWA underwent a major upgrade from 2019-2023.
352 dual polarization antennas
Expansion:
  288  352 dual polarization antennas
  1.5 km 2.4 km longest baselines km longest baselines
Junction box
ADC
Analog receiver electronics
Digital signal processing
Simplified LWA signal path

## Slide 8: The OVRO-LWA underwent a major upgrade from 2019-2023.
352 dual polarization antennas
Expansion:
  288  352 dual polarization antennas
  1.5 km 2.4 km longest baselines km longest baselines
All front-end electronics cleaned & tested
Junction box
ADC
Analog receiver electronics
Digital signal processing
Simplified LWA signal path

## Slide 9: The OVRO-LWA underwent a major upgrade from 2019-2023.
352 dual polarization antennas
Expansion:
  288  352 dual polarization antennas
  1.5 km 2.4 km longest baselines km longest baselines
All front-end electronics cleaned & tested
New RF over optical fiber modules
Junction box
ADC
Analog receiver electronics
Digital signal processing
Simplified LWA signal path

## Slide 10: The OVRO-LWA underwent a major upgrade from 2019-2023.
352 dual polarization antennas
Expansion:
  288  352 dual polarization antennas
  1.5 km 2.4 km longest baselines km longest baselines
All front-end electronics cleaned & tested
New RF over optical fiber modules
New analog receiver boards for better signal path isolation
Junction box
ADC
Analog receiver electronics
Digital signal processing
Simplified LWA signal path

## Slide 11: The OVRO-LWA underwent a major upgrade from 2019-2023.
352 dual polarization antennas
Expansion:
  288  352 dual polarization antennas
  1.5 km 2.4 km longest baselines km longest baselines
All front-end electronics cleaned & tested
New RF over optical fiber modules
New analog receiver boards for better signal path isolation
All new digital signal processing electronics: opportunity for commensal cosmic ray search
Junction box
ADC
Analog receiver electronics
Digital signal processing
Simplified LWA signal path

## Slide 12: My RFI rejection strategy leverages the array layout.
E-W position [km]
N-S position [km]
-1.2 -1 -0.8 -0.6 -0.4 -0.2 0 0.2 0.4
1
-1
0
-0.5
0.5
a)
b)
c)
Peak Electric field [millivolts/m]
c)
2
1.5
1
0.5
-200 0 200
E-W Position [m]
-200
200
0
N-S Position [m]
Simulated emission
Array layout color-coded by FPGA
Distant antennas veto RFI.
  Horizon
  Airplane reflections
Notes: Antennas are color coded by FPGA. Antennas marked X are veto antennas.
These sparser regions of the array are grouped into two higher-energy arrays, each with their own veto antennas.
Mention RFI is mostly from horizon, airplanes, or near field

## Slide 13
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
Buffer 20 microseconds x 64 antennas
Read out buffer and form ethernet packets
RFI Veto Logic
Trigger
64 timeseries from ADCs
To network switch
Transmit trigger to other boards
Cancel trigger
Filter, square voltages, and smooth power
Overview of the cosmic ray trigger firmware
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 14: Overview of the cosmic ray trigger firmware
Apply
cable delays
64 timeseries from ADCs
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 15
Apply
cable delays
64 timeseries from ADCs
Filter, square voltages, and smooth power
Overview of the cosmic ray trigger firmware
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 16: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
64 timeseries from ADCs
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 17: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Extend pulse over coincidence window
64 timeseries from ADCs
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 18: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
64 timeseries from ADCs
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 19: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
Trigger
64 timeseries from ADCs
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 20: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
RFI Veto Logic
Trigger
64 timeseries from ADCs
Transmit trigger to other boards
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 21: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
RFI Veto Logic
Trigger
64 timeseries from ADCs
Transmit trigger to other boards
Cancel trigger
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 22: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
Buffer 20 microseconds x 64 antennas
RFI Veto Logic
Trigger
64 timeseries from ADCs
Transmit trigger to other boards
Cancel trigger
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 23: Overview of the cosmic ray trigger firmware
Threshold pulse detector
Apply
cable delays
Sum over antennas
Extend pulse over coincidence window
Buffer 20 microseconds x 64 antennas
Read out buffer and form ethernet packets
RFI Veto Logic
Trigger
64 timeseries from ADCs
To network switch
Transmit trigger to other boards
Cancel trigger
Filter, square voltages, and smooth power
Notes: Here is an overview of the cosmic ray detection firmware. The SNAP2s buffer 20 microseconds of the time series output by the ADCs, with 5 ns time resolution.
The buffer is implemented as a circular buffer– whenever it gets to the last address it starts overwriting data from the beginning.
In parallel with the buffer, the firmware searches for pulses above a threshold, on the timeseries for each of the antennas processed by that SNAP2. If a threshold number of antennas have a pulse within the light travel time between those antennas, the detector logic outputs a trigger signal. The trigger can be cancelled by RFI rejection logic that I will describe on the next slide.
If the trigger is not cancelled by the RFI blocker, then the board stops writing new data to its buffer and reads out the buffered timeseries into ethernetpackets which are transmitted to a computer for the next stages of processing. Also, any board triggers all the others to read out their buffered data, so that the computer receives a snapshot from the whole array. Most of the RFI rejection occurs on this computer. The first stage of RFI rejection on the FPGAs only has to do well enough to keep the trigger rate low enough that the receiving computer can keep up and the readout dead time is small.
The readout deadtime is determined by how fast the receiving computer can process the ethernet packets, not the maximum speed that the SNAP2 boards can transmit the data. To avoid overwhelming the receiving computer, readout time takes 920 microseconds. Which we expect to result in less than 5% of observing time lost to dead time.
%Most of the RFI rejection
%Ryan found 500Hz RFI
%Limited to 50Hz, had slower readout on the old network so that was 13% dead time
%We will have 4.6% dead time at 50Hz event rate

## Slide 24: Bringing all signals to a central location is crucial to the cosmic ray detection strategy.
Combination of coaxial cable and RF over Fiber

## Slide 25
Goal of commissioning:
Optimize the tradeoff of balancing cosmic-ray sensitivity and RFI-rejection in:
  1. Detector settings
  2. Real-time event filtering software

## Slide 26: Example trigger and veto rates over one night
Time [hours since start]
0 2 4 5 8
Rate [Hz]
0 2 4 5 8
Time [hours since start]
Rate [Hz]
200
175
150
125
100
75
50
25
25000
20000
15000
10000
5000
Same data, zoom y-axis
Known, hourly RFI source
Triggers
Vetos
Raw events
Triggers
Vetos
Raw events

## Slide 27: Conclusion
Upgrade is complete
Commissioning in progress
Goal is to observe 1000s of cosmic rays over the next few years to make better composition estimates at the Galactic to extragalactic transition.