## Slide 1
Mathias Gerbaux, P. Ascher, Ph. Alfaurt, D. Atanasov, L. Daudin, R. Faure, M. Flayol, S. Grévy,
M. Hukkanen, A. Husson, B. Lachacinski, S. Pérard, E. Rey-Herme, M.Roche, A. de Roubin
DESIR Workshop – February 2024

## Slide 2
Let’s set the scene
Beams out of the accelerators are "dirty" ones:
Contaminated
Large emittance
Low energy experiments often demanding:
Low emittance needed
Some ask for a bunched beam
Ultra pure beam
Other experiments in DESIR
prepares beam for
purifies beam for
Mass measurement
purifies beam for
PIPERADE
GPIB
HRS
From S3
and SPIRAL1

## Slide 3
How it looks like at LP2iB
Ion source
3-keV line

## Slide 4
Foreword: emittance for dummies
In the transverse plane, equivalent to look at position and angle wrt beam axis
In the beam direction, equivalent to look at energy and time dispersion
Emittance
=
spread of the beam in the phase space
In the absence of dissipative forces emittance is conserved
Low emittance beams are desirable for efficient transmission through the beam lines

## Slide 5
y (mm)
z (mm)
Electric potential (V)
Why to use a radiofrequency cooler?
x
y
z
A static electric potential can not confine a charged particle in 3D but an RF one can!
25 DC segments surround the RF rods to guide the cooled ions towards the end of the RFQ.
Emittance of low energy RIB several 10 .mm.mrad
Typical needs for traps: a few .mm.mrad
Cooling needed!

## Slide 6
… and buncher
DC segments
RF rods
Buffer gas inlet

## Slide 7
Stability inside the RFQ
Stability of the motion depends on , , , and
When
best transmission usually obtained for
for the GPIB

## Slide 8
RF system
To the 2 pairs
of rods
Class A amplifier
Waveform
generator
Balun circuit
or

## Slide 9
Transverse emittance reduction
3
Transverse emittance reduction in compliance with expectations for continuous beams
Still to be measured for bunched beam but expected to be better
Measurements done with an electrical sweep type emittance scanner
  Before the GPIB (30 keV beam)
  After the GPIB at 30 keV and 3 keV
Measurements done with an electrical sweep type emittance scanner
  Before the GPIB (30 keV beam)
.mm.mrad at 30 keV / .mm.mrad at 3 keV

## Slide 10
Transmission efficiency
Bunching mode
Measurements are more challenging
Optimization of the ion trapping is crucial for large bunches
100 % transmission up to 106 ions/bunch
50 % transmission with 108 ions/bunch
Outdated results
Transmission for K+ ions is routinely over 75 %
Careful optical tuning yields transmission >90 %
Continuous mode
Transmission has little dependence on the beam current (up to nA)

## Slide 11
Energy and time dispersion measurement
Faraday
cup
MCP
Beam
Grounded grid
Retarding grid

## Slide 12
Work in progress!
Energy dispersion measurement currently limited by detection system (< 6 eV)
Minimum time dispersion currently down to 250 ns (FWHM) at 3 keV
Energy and time dispersion measurement

## Slide 13
Control and command system
All equipment are now controlled through EPICS PVs
User friendly interface with CSS

## Slide 14
Control and command system
All equipment are now controlled through EPICS PVs
User friendly interface with CSS
Pattern generator for the timing of the switchable electrodes handled for now either by the PTSD program (using EPICS) or old LabView program

## Slide 15
Rogowski probes to measure 4 kV
Recent developments
Improvement of the retarding grid system on the MCP
Autonomous CC developed for the Pantechnik pepper-pot emittance-scanner (EPICS compatible)

## Slide 16
Planned upgrades
New bipolar power-supplies and switches combination for the last DC segments
New insulators and holding systems for the grounded electrodes at entrance and exit of the GPIB
Gas purification system (presently grade 6 He bottle)

## Slide 17
Conclusion
GPIB should be sent fully operational to DESIR by 2025-2026
The GPIB delivered K and Rb beam to PIPERADE almost every work day in 2023 (sometimes 24/7)
Starting of the beam line automatized to a great extent
EPICS-isation almost complete
Continuous beam mode OK: transmission up to >90%, emittance reduction to 3 .mm.mrad at 30 keV
Characterization in bunched mode still in progress but promising (bunch duration <300 ns, transmission already correct for very large bunches)
Still to be done:
  Tailor bunches to fit needs of downstream setups
  Increase RF voltage up to 8 kVpp (?) to boost performances with large number of ions
  Reliable measurement of transmission and emittance (transverse and longitudinal) in bunching mode
M.Gerbaux et al, The General Purpose Ion Buncher: A radiofrequency quadrupole cooler-buncher for DESIR at SPIRAL2, Nucl. Instrum. Methods Phys. Res. A 1046 (2023) 167631

## Slide 18
Ph. Alfaurt
M. Aouadi (12/2017)
P. Ascher
D. Atanasov (12/2023)
L. Daudin
S. El Abbeir (06/2015)
R. Faure
M. Flayol
M. Gerbaux
S. Grévy
M. Hukkanen (07/2023)
A. Husson (12/2022)
B. Lachacinski
S. Perard (02/2024)
E. Rey-Herme
M. Roche
A. de Roubin (02/2022)
B. Thomas 06/2020)
The bunch of cool people working (or having worked) on the GPIB
D. Lunney (IJClab)
J.-C. Thomas (GANIL)
J.-F. Cam (LPC)
L. Lasne (Univ. Bordeaux)
Special thanks to…
The GPIB + PIPERADE team at

## Slide 20
Back-up

## Slide 21
Requirements
Transverse emittance | Extracted beam energy | Energy dispersion | Max intensity | Mode | Repetition rate | Bunch duration
> 10.mm.mrad | 3 - 30 keV | < 10 eV | 105 ppb | Continuous or bunched | 0.1 – 100 Hz | 1 - 10 µs
Transverse emittance | Extracted beam energy | Energy dispersion | Max intensity | Mode | Repetition rate | Bunch duration
 | 3 - 30 keV | < 10 eV | 105 ppb | Continuous or bunched | 0.1 – 100 Hz | 1 - 10 µs
What was asked for in the "technical specifications for DESIR beam" document :
And of course better if possible…

## Slide 22
What has been done / what is still to be done
High intensity : >108 ions/bunch or >100 pA (CW)
Extraction 30 keV | Continuous beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  |  | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity |  | 
 | 70 % < T < 93 % (with (nat)K) |  | .mm.mrad (to be repeated) |  | Not accessible |  |  | 
 | Bunched beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  | ToF dispersion | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity
 | X | X | Need ongoing developments on emittancemeter |  | X | X | < 10 µs (FWHM) | Need high attenuation
Extraction 30 keV | Continuous beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  |  | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity |  | 
 | 70 % < T < 93 % (with (nat)K) |  |  |  | Not accessible |  |  | 
 | Bunched beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  | ToF dispersion | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity
 | X | X | Need ongoing developments on emittancemeter |  | X | X | < 10 µs (FWHM) | Need high attenuation
Extraction 3 keV | Continuous beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  |  | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity |  | 
 | 70 % < T < 90 % (with (nat)K) |  | Need ongoing developments on emittancemeter (.mm.mrad) |  | Not accessible unless coupling with HRS |  |  | 
 | Bunched beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  | ToF dispersion | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity
 | Up to 100% | 50% (with 109 ions) | Need ongoing developments on emittancemeter |  | < 6 eV (currently limited by detector) | Need high attenuation | 250 ns - 1,5 µs (FWHM) | < 10 µs (FWHM)
Extraction 3 keV | Continuous beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  |  | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity |  | 
 | 70 % < T < 90 % (with (nat)K) |  |  |  | Not accessible unless coupling with HRS |  |  | 
 | Bunched beam |  |  |  |  |  |  | 
 | Transmission |  | Transverse emittance |  | Energy dispersion |  | ToF dispersion | 
 | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity | Low intensity | High intensity
 | Up to 100% |  | Need ongoing developments on emittancemeter |  | < 6 eV (currently limited by detector) | Need high attenuation | 250 ns - 1,5 µs (FWHM) | < 10 µs (FWHM)

## Slide 23
Specifications GPIB for DESIR
As in the "specifications techniques pour les faisceaux DESIR" document (2021)

## Slide 24
Why to use a cooler ?
Typical emittance of a few 10-keV RIB : several 10 .mm.mrad
Typical needs for traps: a few .mm.mrad
Collisions with buffer gas
Cooling needed!
Damping of the motion in all directions
Confinement needed to avoid Coulomb repulsion

## Slide 25
3-keV line
90° electrostatic deflector currently on a separate test-bench
Dedicated ion source
Detector tests (retarding grid, emittance-scanner)
Transmission measurement with low charge bunches
Optimization of energy dispersion measurement
Emittance measurement (aberrations ?)
Feasibility of ToF and energy measurement over whole intensity range ?
High intensity (>104 ions/bunch) → FC with Femto current transimpedance amplifier
Low intensity (<1000 ions/bunch) → MCP

## Slide 26
RF system
Function generator
20 dB
6 dB
Primary
winding
RFQ
Power
amplifier
Adjustable
ground
Tunable
capacitor
Secondary
windings
Directional
coupler
Osc. ch1
Osc. ch2
Osc. ch3
Osc. ch4
attenuator
attenuator

## Slide 27
A closer look at the mechanical design
Grounded
electrode
Inj1
Inj2
Inj3
DC segment 125
RF rod
Ext1
Ext2
Ext3
Grounded
electrode
RF feeding

## Slide 28
Hard or soft extraction