## Slide 1: The SHEXI demonstrator  Upgrade of SIRIUS GANIL CS 01/02/2024 K. Hauschild for the SIRIUS collaboration

## Slide 2
General motivations for SIRIUS
  Recap on type of measurements
Motivation for the upgrade
Fantasy resolutions
The SHEXI concept
What is needed for a proof-of-principle
Summary of the proof-of-principle funding request
Tow example experiments illustrating the power of full SHEXI
Outline

## Slide 3: (General) Physics Motivations
What are the limits ?
How many elements ?
(chemistry beyond row 7 ?)
Properties of nuclear matter at extreme Z and A
access through fine-structure a decay
and/or high-K isomeric states
Island of enhanced stability ?
MNT / pxn
Number of neutrons
Number of protons
Notes: The nuclei of interest int this current session are situated at the very top nuclear chart where the each isotope is represented as a function
of Z and N.
Of interest are the properties of matter in extreme conditions of mass and charge.
The actual limits of this chart corresponds to the basic question of how many elements actually exist.
One of the ways we obtain information on the structure of these nuclei is through fine-structure alpha decay coupled with coincident internal conversion electron and gamma-ray spectroscopy.
In axially deformed nuclei, the K quantum number is approximately conserved. Transitions that involve a change in K larger than the multipole order are usually forbidden and the so-called K isomers are formed. These K isomers can provide a unique fingerprint of the underlying single-particle structure. They also provide an experimental tool to access low-lying states that are not readily populated by alpha decay or difficult to observe at the target in prompt spectroscopy experiments either due to internal conversion or weak population.
Another interest in these K-isomers is that they might provide additional hindrance to fission wrt to the ground state and thus provide a mechanism for enhanced survival probability of super heavy nuclei.
And we are also interested in reaction mechanisms which could broaden the range of nuclei that we can study.

## Slide 4: SIRIUS detection system at the focal plane of S3
Implanted into 128x128 DSSD
ToF and ion tracking
Distance = 110.38 cm
Recoils from S3
1) Tracker, T(tr), x(tr), y(tr)
E(implant), T(implant), ID(x,y)
=> ToF,E + recoil marker

## Slide 5
SIRIUS detection system at the focal plane of S3
Signal in DSSD
(no tracker => decay)
Recoils from S3
1) Tracker, T(tr), x(tr), y(tr)
E(implant), T(implant), ID(x,y)
2) E(decay1), T(decay1), ID(x,y)
E(ge), T(ge), ID(ge)
E(tun), T(tun), ID(tun)
=> ToF,E + recoil marker
Position correlated event
(eg isomer decay)

## Slide 6: SIRIUS detection system at the focal plane of S3
Signal in DSSD
(no tracker => decay)
Recoils from S3
1) Tracker, T(tr), x(tr), y(tr)
E(implant), T(implant), ID(x,y)
2) E(decay1), T(decay1), ID(x,y)
E(ge), T(ge), ID(ge)
E(tun), T(tun), ID(tun)
3) E(decay2), T(decay2), ID(x,y)
E(ge), T(ge), ID(ge)
E(tun), T(tun), ID(tun)
=> ToF,E + recoil marker
Position correlated event
(eg isomer decay)
Position correlated event
(eg fine structure a decay)
E(decay1), T(decay1), ID(x,y)
E(ge), T(ge), ID(ge)
E(tun), T(tun), ID(tun)
E(decay2), T(decay2), ID(x,y)
E(ge), T(ge), ID(ge)
E(tun), T(tun), ID(tun)

## Slide 7: Main Motivation for the upgrade:
Z Identification of the isolated SHE.
S. Hofmann, EPJ Web of Conferences 182, 02054 (2018)
X-rays: energies characteristic of atomic number
 unique identification (historically K X-rays)

## Slide 8: SIRIUS upgrade SHEXI (Super Heavy Element X-ray Identification) R&D
48Ca+243Am  291Mc*
aL(43:M1) = 244
aL(86:E2) = 84
X-rays: energies characteristic of atomic number  unique identification (historically K X-rays)
Difficulties in SHE:
1) Excitation energies are compressed
 K X-rays unlikely (EB[Z=109]=178 keV)
2) Some nuclear transitions do not favour K X-rays
Based on D. Rudolph et al, Phys. Rev. Lett. 111 (2013) 112502
Physics Solution:
L X-rays (lower E) and always produced
but E(L,Z+1) – E(L,Z) ~ 0.4 keV for Z~110
aK(194:E1) = 0.099

## Slide 9: The fantasy 0.4 keV FWHM ?
Krings et al., Journal of Instrumentation 9 (2014) C05050
The “CUBE” ASIC preamplifier… designed for XFS
10 mm thick 39x32 mm2 Ge detector: pixel 7x7 mm2
4 mm thick 20x20 mm2 Ge detector: pixel 1x20 mm2

## Slide 10: SHEXI Concept
State-of-the-art ASICs from XGLab (0.4 keV FWHM)
Z identification of SHE
cooling
other side of DSSD:alpha/fission range
16 standard CSPs (HV)
(also needs developing/testing)
(ASIC range ~2.5 MeV: 1000 mV/MeV
 capacitance-matched DSSDs (1.5 mm thick)

## Slide 11: SHEXI Proof-of-principle: one 48x16 DSSD
DET
8 ASIC
16 CSP
x6
vacuum
cold
air
Power supply,
Reset logic
Bias + signal
conditioning
signal
buffered
signal
digitiser
  Xray ASIC Status
    24(of 48) ASICS bought
      Placed on 3 carriers boards
    We have the back-end to qualify the
    noise, rise-time, energy, etc.
Detector PCB
Detector design
approved by
Micronsemiconductor
3x 8-ASIC
boards bought
24 channels
need to be
instrumented
3 signal conditioning
boards bought
(but need housing)
16 CSP
and status
  TO DO
    Interconnection & adapters
    Vacuum feed-throughs
    EMC for bias boards needed
    Bias board (NUMEXO2 compat.)
Cost to complete tasks 34k

## Slide 12: SHEXI Proof-of-principle: one 48x16 DSSD [CSP]
DET
8 ASIC
16 CSP
x6
vacuum
cold
air
  Standard CSP
    Apply HV
    Escape alpha and fission fragments
      Range up to 100 MeV
    Ideally: conversion electrons
      Range down to 25 keV ?
       PIXELS:
K. Hauschild NIM A560 (2008) 388
254,255No
Can we use PSA to distinguish these event types ?
 FAST preamplifier rise time

## Slide 13: SHEXI Proof-of-principle: one 48x16 DSSD [CSP]
Spin-off from SIRIUS CSP modified for the GABRIELA DSSD  64 channel board
1)
range ~60 MeV, threshold ~50 keV, FWHM(a) ~14 keV, FWHM(e-) ~6 keV
(initial tests in 2018 following experimental runs)
2)
NetInstruments: 16-channel CSP - 100 MeV into 2Vpp
10 ns rise-time (<100 pF load)
pulser tests <3.9 keV FWHM
3)
Atomki low-power preamp – fast (<15 ns) (have schematics)
NIM A366 (1995) 146 base-line noise < 2 keV
does not use BF862 FET
Cost to complete tasks 23k
  TO DO
    CSP motherboards (#1 & #2)
    (1) new CSP version: reduce rise-time
    (2) produce a batch of CSP
    Feedthroughs, Interconnection & adapters (all)
    (#1 & #3) adapter board (NUMEXO)
    Improve trigger  lower threshold (DAQ)

## Slide 14: SHEXI Proof-of-principle: one 48x16 DSSD [PSA]
254,255No
Can we use PSA to distinguish these event types ?
 FAST preamplifier rise time
4x MSX03 detectors from Micron
(1.5 mm thick. ~7 pF)
8x CREMAT CR-110 preamps
no load  2 keV & 3 ns
NEED TO FINALISE DETECTOR PCB
Part of S. Kumar’s thesis
500 MHz digitiser ? 23.4 k
work around ? PA >
+2 ns
250 MHz
Digitiser
ch1
ch2
K. Hauschild et al. EXON 2018 Conference Procedings, p. 403

## Slide 15: Back-end electronics infrastructure
Vacuum chamber
Vacuum pumps
Cooling
DAQ Bay
eth
NIM
VME
PXIe
XY-theta table
(sources)
new controller: 15.5k
Storage: 2k
Recently EMC and shielding have been improved
Digital GABRIELA
R.S. Mukhin, et al., Part. Phys. Nucl. Lett. 18 (2021) 652.
R.S. Mukhin, et al., Acta Phys. Pol. B Proc. Suppl. 14 (2021) 75.

## Slide 16
Partner | Surame | First name | Role & responsibilities in the project | Work Packages (need updating) | ETP
IJCLab | HAUSCHILD | Karl | Coordinator, LabVIEW DAQ and DSP, experimental setup, Data analysis, student supervision | 1,(2.1),2.2,2.3,3.2,4.1,4.2,4.3 | 0.5
IJCLab | LOPEZ-MARTENS | Araceli | Data analysis, student supervision | 4.2,4.3 | 0.2
IJCLab | KARKOUR | Nabil | PCB design, EMC, system integration, student supervision | 2.3,3.1,3.2 | 0.25
IJCLab | GIBELIN | Laurent | PCB design, system integration | 2.3,3.2 | 0.25
IJCLab | LINGET | Denis | Maintenance of local infrastructure |  | 0.20
GANIL | KUMAR | Shayan | Experimental setup and data analysis, PSA. | 1,2.3,4.1,4.2,4.3 | 0.5
GANIL | PIOT | Julien | Ph.D. student supervisor @ GANIL |  | 0.05
GANIL | ACKERMANN | Dieter | Ph.D. student supervisor @ GANIL |  | 0.05
IPHC | DORVAUX | Olivier | Silicon detector Customer Acceptance Tests | 1 | 0.1
IPHC | MATHIEU | Cedric | Silicon detector Customer Acceptance Tests | 1 | 0.1
 |  |  |  | TOTAL (excl. IJCLab interns) | 2.2
HR
“CODEC” @IJCLab  Directorate was informed
Part of Shayan’s thesis

## Slide 17: What you get in 2 years: the SHEXI Proof-of-principle: fully instrumented 48x16 DSSD
16 CSP + carrier for alphas/fission frags
48 ASICs
for X-rays
NUMEXO2

## Slide 18: Summary of costs
Item | Cost [kE]
ASICs | 33.6
CSP | 23.5
PXIe-controller + storage (DAQ) | 17.5
500 MHz digitiser (PSA) | 23.4
Total | 98.0

## Slide 19: Reminder of why: detection efficiency of full array

## Slide 20: Conclude with two physics examples
NEWGAIN@GANIL: 5 pmA x 3.5 pb x 300 mg/cm2 x 45%
48Ca+243Am  291Mc*
SIRIUS (5xEXOGAM Ge) 180 days  ~500 289Mc
SHEXI: 45 days  ~125 288Mc
Near future: high-resolution conversion electron spectroscopy
255No  251Fm as an example:
GABRIELA data vs SHEXI simul
K. Rezynkina et al., Phys. Rev. C 97 (2018) 054332
typo in document

## Slide 21: Back-up

## Slide 22: PIONEER: Particle IdentificatiON for superheavy ElEment Research (ANR)
  → Replace 8x16 channel charge-sensitive GABRIELA preamplifiers
        with faster large dynamic range CSA 180 MeV with adjustable offset compatible with NI-5170 digitisers (DIGITAL GABRIELA)
    Status : 128 voies (sans les PAC) produites installation à IJCLAB Salle Beta 2 électronique retardée sur site (COVID puis plus de collaboration Russe)
Wassim (UL)
Nicolas, Lucy, Romain, Touria, Nicolas, William, Simon, Rayan, (4e année ESME)
Florian, Romane, Pauline (BTS ESME)
Spin-off from SIRIUS CSA

## Slide 23: PIONEER-64 @ FLNR
Gain=1.25  180 MeV in 5Vpp

## Slide 24: Back-up
2021/2

## Slide 25
Z
Energy [keV]
Extrapolation of known X-ray energies

## Slide 26
Energy [keV]
TTT6 leakage current @ 20oC
I [nA] | T [oC] | T [oC]
~10 | 20 | 20
5 | 13 | 10
2.5 | 6 | 0
1.25 | -1 | -10
~0.6 | -8 | -20
0.3 | -15 | -30
0.15 | -22 | -40