## Slide 1: Calibration with AuxTel: measure atmospheric transmission
- Status of the extraction of atmospheric transmission with CALSPEC spectrophotometric standards (Jérémy)
Continuous function -> Effective passbands
Atmospheric parameters: grey absorption, aerosols, ozone, PWV
Atmosphere monitoring for 2 years: water seasonal effects
- Perspectives
- using other spectra than CALSPEC standards (Corentin)
- AuxTel photometry (Sylvie)
- Best precision on the brightest stars: actual limitations
- Can we use this photometry to test atmospheric color-corrections?
- AuxTel, ComCam and after (Discussion: all)
note: ComCam will have only 3 filters in place, but ugriZy are all available
- AuxTel follow-up strategy with ComCam & LSST
- Atmospheric corrections (color / flux): ComCam & LSST

## Slide 2: Context: the AuxTel spectrograph mission measure the atmospheric transmission as a function of λ to derive the expected fluxes for each object under standard atmospheric conditions
Holographic disperser, a french proposal that was not in the initial project

## Slide 5: Science case for the best photometry: strong lensing time-delay
time delays of HE0435−1223: H0 to 3.8% precision from strong lensing
Estimate H0 from the measured delays and lens model

## Slide 6: AuxTel, the LSST hygrometer

## Slide 7: AuxTel
Rubin Auxiliary Telescope (AuxTel) primary objective is to characterize and monitor the local atmospheric transmission in parallel with the main Simonyi telescope:
1.2 m telescope on the next hill, equipped with a slitless spectrograph (LATISS)
In operation since 01/2020 as a pathfinder to test LSST systems and start characterising the atmosphere.

## Slide 8: Atmospheric transmission description
Atmospheric transmission can be decomposed in four components:
Rayleigh scattering in λ-4 proportional to on-site pressure
Ozone absorption band at ~600nm is quite stable (satellite observation)
Aerosols (<450nm) vary with human and natural activities
Water (non-linear absorption bands) varies daily and seasonally
ozone
aerosols
O2
O2
H2O
H2O
H2O
Precipitable Water Vapor (PWV) [mm]

## Slide 9: AuxTel spectrographs
Holographic disperser and mask
Blazed grating + quad-notch filter
Aperture photometry in 4 “blue” rectangles
Spectrum extraction by forward modelling

## Slide 10: AuxTel spectra
Spectrum extraction pipeline based on forward modelling (Spectractor)

## Slide 11: Seven months of South polar star observation
black: AuxTel spectrum divided by AuxTel throughput and CALSPEC spectrum
blue: Libradtran atmospheric model

## Slide 12: Hygrometry
18 months of AuxTel PWV
Zoom on 3 weeks
PWV=Precipitable Water Vapor

## Slide 13: Photometric repeatability on differential color measurements in Auxtel
Sensibility of photometry to atmospheric parameters
Sylvie Dagoret-Campagne, Marc Moniez
2024-06-12

## Slide 14: Photometric repeatability on Light curves context
> 20 mmag in G
Similar resolution
In R
> 40 mmag in Y
Official Photometric calibration not working well in Auxtel by now.
But how to show evidence for atmospheric parameter variations in Photometry ?
> 25 mmag in Z
requirements
5 mmag or less

## Slide 15: The zero-Point calibration problem
Different stages of calibration not easy to setup
Catalog matching photometry
FGCM
Per CCD zero-point
Ex : ZP Non-uniformity corrections
Try to extract photometry independently of complicated DM-pipeline calibration

## Slide 16: Focus on One Light Curve at a time
Instrumental aperture flux
Calibrated psf Magnitude
Calibration relies after the selection of isolated bright stars

## Slide 17: Example of selected one isolated bright star with DM object with a light-curve
Compare two close stars ( here distance : 45 arcsec)
And compare differential fluxes/colors
Star 1 – Star 2 on same exposure (get rid off Zero-point calibration)
Selection of exposures in different bands within less than 1 minute
Band g
Band r

## Slide 18: Relative flux ratio in the same band
Take away
1) psfMag better than aperture flux Mag
2) Instrinsic photometry measurement accuracy ~ 10 mmag (above req) in G,R when cancelling Zero Point
3) Atmospheric effect noticeable in band Y with 15 mmag ?
relative flux ratio
relative flux ratio

## Slide 19: Differential light curves in G,R with PSF Magnitude
Take away
40 mmag resolution on G-R is due to bad ZP calibration
12 mmag in band or relative color difference is the photometric accuracy excluding ZP effects
Shown:
Three «flux ratios» or magnitude differences
1) G(star 1)-G(star 2) : expect intrinsic photometric performances without atm effect and SED color effect
2) Color G-R on star 1 only from less 1min exposure
3) G-R color difference between the 2 stars

## Slide 20: Differential light curves in G,Y with PSF Magnitude
Take away
40 mmag resolution on G-Y is due to bad ZP calibration
  Not sensitive to PWV variations
10 mmag in band or relative color difference is the photometric accuracy excluding ZP effects
  Could try to detect PWV variations
Shown:
Three «flux ratios» or magnitude differences
1) G(star 1)-G(star 2) : expect intrinsic photometric performances without atm effext and SED color effect
2) Color G-Y on star 1 only from less 1min exposure
3) G-Y color difference between the 2 stars

## Slide 21: Differential light curves in R,Y with PSF Magnitude
Take away
40 mmag resolution on G-Y is due to bad ZP calibration
  Not sensitive to PWV variations
10 mmag in band or relative color difference is the photometric accuracy excluding ZP effects
  Could try to detect PWV variations
Shown:
Three «flux ratios» or magnitude differences
1) R(star 1)-R(star 2) : expect intrinsic photometric performances without atm effect and SED color effect
2) Color R-Y on star 1 only from less 1min exposure
3) R-Y color difference between the 2 stars

## Slide 22: Differential light curves in Z,Y with PSF Magnitude
Shown:
Three «flux ratios» or magnitude differences
1) Z(star 1)-Z(star 2) : expect slight atmospheric effect if SED slope is different for Star1 and Star 2
2) Color Z-Y on star 1 only from less 1min exposure
3) G-Y color difference between the 2 stars
Take away
40 mmag resolution on Z-Y is due to bad ZP calibration
  Not sensitive to PWV variations
15 mmag in band or relative color difference is the photometric accuracy excluding ZP effects
  Could try to detect PWV variations

## Slide 23: Problems encountered in photometry of isolated stars: Blending
Isolated star 1
Distance star1-star2 = 11 arcsec
Show a random flag deblend_skipped true or false depending on exposure

## Slide 24: Problems encountered in photometry of isolated stars: Big star footprint
Left : my cutout
Middle heavy footprint
Right : pixel mask

## Slide 25: Problems encountered in photometry of isolated stars: Bad PSF
Top : good uniform psf
Middle : non-uniform psf
Bottom : strange data/psf ratio

## Slide 26: Problems encountered in photometry of isolated stars: Bad PSF

## Slide 27: Isolated Bright stars for calibration : Star1-Star2 colors
color | g1-r1 | g2-r2 | g1-y1 | g2-y2 | r1-y1 | r2-y2 | z1-y1 | z2-y2
mean | 0.210940 | 0.70546 | 0.308111 | 1.216009 | 0.098398 | 0.512060 | -0.059711 | 0.016295
std | 0.032865 | 0.03095 | 0.043392 | 0.041790 | 0.057754 | 0.061969 | 0.051999 | 0.046869
Star 1
Star 2
Need to find two close stars
with much more difference in Z-Y to be sensitive to atmospheric variation impact due to SED color difference

## Slide 28: New AuxTel standards with Gaia
LSST LPCA group:
Philippe Gris, Nicoleta Pauna, Julie Leproux, Corentin Ravoux
With a lot of help from IJCLab team
LSST France meeting - 12 june 2024
Illustris TNG simulation

## Slide 29: Scientific goals (SNe Ia)
Impact of PWV (Precipitable water vapor) on SNe Ia bands
i,z,y bands interesting for high-redshift SNe Ia
Proposed DDF scenario has a lot of y-band visit: impact or correction of atmosphere variability
FGCM cross-verification/external data input
Figure from Martin
Standard atmosphere

## Slide 30: Gaia DR3 catalog
CALSPEC spectra does not cover DDF
Gaia = largest catalog of star spectra out of atmosphere
BP/RP spectrograph: low resolution at [330-1050]nm
RVS spectrograph: high resolution at [846-870]nm
Optimal coverage of the full LSST sky (including DDF)
g mag
CALSPEC stars and DDF
GAIA stars for PWV (g < 10)
BP/RP spectrum
RVS normalized spectrum
Wavelength [nm]
Wavelength [nm]

## Slide 31: Gaia DR3 spectrum
BP/RP spectrum of poorer resolution compared to CALSPEC but in the interest region of AuxTel
First test:
  Matching of spectra between CALSPEC and GAIA
  Quick modification of Spectractor with GAIA spectrum
HD160617 spectrum
Carrasco et al. 2021

## Slide 32: Spectractor with Gaia spectrum
Standard spectrum ∗ Gaussian smoothing ∗
Atmosphere model ∗ Auxtel transmission
AuxTel
CALSPEC
Spectractor =

## Slide 33: Spectractor with Gaia spectrum
AuxTel
GAIA
Standard spectrum ∗ Gaussian smoothing ∗
Atmosphere model ∗ Auxtel transmission
Spectractor =

## Slide 34: PWV measurement results
Comparison of Spectractor measurement between CALSPEC and GAIA
Agreement for most stars (PWV difference below 1 mm)
Can be improved with improved treatment of Gaia spectra

## Slide 35: What’s next ?
At the catalog stage:
Improve cross-matching between GAIA and CALSPEC
Remove the variables objects from the Gaia catalog (cross-matching, main sequence selection)
Uniform coverage of sources for all LSST sky
Focus on DDF
Catalog with different star types
At the spectrum stage:
Smoothing of the GAIA spectra to remove fluctuations (gaussian, or remove high order in the spectra decomposition)
Addition of spectrum error inside the Spectractor forward modeling
Proper GAIA implementation inside Spectractor (Astroquery, storing the selected source catalog)

## Slide 36: Annexe: with magnitudes

## Slide 37: Annexe: other fitted parameters

## Slide 38: Annexe: other fitted parameters

## Slide 39: Annexe: other fitted parameters

## Slide 40: Annexe: other fitted parameters

## Slide 41: Annexe: other fitted parameters

## Slide 42: Annexe: other fitted parameters

## Slide 43: Annexe: other fitted parameters

## Slide 44: Annexe: other fitted parameters

## Slide 45: Annexe: Gaia number of stars

## Slide 47: Calibration with AuxTel: Discussion / tentative planning