## Slide 1
Foundational Principle : Single Photoelectron Response
Modeling & Feasibility studies
Alexandra Kallitsopoulou, Thomas Papaevangelou PhD Candidate CEA/IRFU/Université Paris – Saclay
Thursday, 21st March 2024
Journées 2024 de l'atelier détecteurs gazeux
On behalf of PICOSEC Micromegas Collaboration
GANIL

## Slide 2: Outline
Introduction to the PICOSEC Micromegas technology
Modeling the Timing characteristics
Feasibility studies using alternative digitizers
Conclusions

## Slide 3: The PICOSEC Micromegas Technology

## Slide 4: What is our motivation?
Tracking challenges for HL-LHC:
      LHC will go to higher energy & luminosity
        5x nominal instaneous luminosity  Increased particle densities
        20x current integrated luminosity  Increased radiation damage
      What are the needs:
        Reduction of mixing different events due to pile-up
        Track to vertex association  3D tracking with timing information
Timing with a few 10’s of Picosecond
      Extra detector requirements:
          Large area coverage
          Resistance to aging effects
          Multi-pad readout tracking
Giant improvement ~ 3 orders of magnitude compared to standard MPGDs
      Detector Technologies
  Gaseous detectors
    Resistive Plate Chambers (RPCs) (σt ~ 30 ps)
    Micro-Pattern Gaseous Detectors (σt ~ 1 ns)
Notes: The motivation is to achieve timing with a few 10s of a picosecond. The idea is rising from the need of high-rate experiments to deal with pile-up phenomena.
For example, HL LHC estimates per average of 140 pp interaction per bunch crossing, which means that event reconstruction is not straightforward. The new 4D tracking era can include timing as an extra parameter for triggering or event selection.
    On average 140 p-p interactions per bunch crossing
    Necessary timing resolution ~20ps
But this push to the limits of existing detector designs. We have to be able to scale up the modules, be resistant to aging, and read out multi-channels.
For this, some technologies already have reached a fraction of 20 ps.
For example, Avalanche PD has a big gap and high resistivity they cannot survive at such a high rate.

## Slide 5: The PICOSEC Micromegas Technology
Y. Giomataris, P. Rebourgeard, J.P. Robert and G. Charpak, “Micromegas: A high-granularity position sensitive gaseous detector for high particle-flux environments”, Nuc. Instrum. Meth. A 376 (1996) 29
J.Bortfeldt, et al., “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, https://doi.org/10.1016/j.nima.2018.04.033
Limitations of the Micromegas Timing Potential
  Stochastic nature of ionization
  Randomness of last ionization
  Time jitter of a few ns
Additional Components
  Cherenkov radiator +
  Solid converterPhotocathode Prompt photoelectrons
Modifications in MM Geometry
  Smaller Drift Gap
    Elimination of the stochastic nature of ionization
  Higher applied Drift VoltagePre-avalanche
Notes: So the idea of the stochastic nature of ionization means that the incident particle can cause ionizations randomly in the gas.
In the picosec in order to minimize this probability of direct ionization we use smaller drift gap. But we still have somehow to create our signals. For this we have a radiator, as for the relativistic particle that crosses this will create Cherenkov photons and those will then be converted by the photocathode material to photoelectrons.
This very small drift gap offers a great advantage to apply even higher electric field in creasing the probability of creating an avalanche even from the 1st stage, i.e preamplification

## Slide 6: Modeling the Timing

## Slide 7: Single Photoelectron Measurements
Different Detector technologies
  Bulk Micromegas  1cm
  MicroBulk Micromegas  1cm
  The Sensor:
COMPASS Gas :
  80% Ne – 10% CF4-10%C2H6
Single Channel Prototypes
  Bulk Micromegas  1cm
  119μm drift gap,
  CsI photocathode deposited on Al layer (275/525V – High Gain)
Laser Beam (IRAMIS/CEA)
  Fast Photodiode  Reference
  UV Ultra short laser pulses
  Controlled number of photoelectrons
  Perform measurements independently of the photocathode material
  Laser repetition rate up to 10kHz - 5MHz spot  = 2mm
Notes: Since the very first tests, single prototypes are always the basis of the prof of principle of the detector technology.
Through the years there has been different designs, not only on the readout layer but also on the vessel containing it, in order to optimize the detector response.
In the R&D phase we have to quantify the effect of every single component of the detector that might affect its timing resolution. This stage comprises of testing different photocathode materials as well as the gas composition.

## Slide 8: Standard Waveform Analysis
Experimental Data used in this work
  2 Data-Set collected
    Spe-Set ( single photoelectrons)
    Exp-Set (multi-photoelectrons ~7.8 p.e.)
The Standard CFD Technique
  Adjust a curve to the experimental data
    Fitting the leading edge of the waveform with logistic function
  Timing at 20% of peak amplitude for all signals
  (SAT – Signal Arrival Time)
  Subtract the PICOSEC signal from the PD0 signal
  Distribution of SAT  RMS = Timing resolution
Photodiode
Amplitude[V]
Time[ns]
Electron peak
Ion tail
Timing Resolution: 18.3 ± 0.2 ps
Notes: To demonstrate the timing algorithms we are going to use data coming from the Laser Test taken with a single pad prototype, with 119μm drift gap, CsI photocathode and operating in
High field of 525 drift and 275 anode voltage.
The signals of both the picosec and the photodiode can be seen in the upper right. PICOSEC Signal is a two component signal, comprising of the fast drifting electron peak and the slow ion tail.
On the other hand, the Photodiode’s signal is more sharp with clear electron peak.
The standard timing algorithm procedure starts by adjusting a curve to both the signals of the photodiode and the PICOSEC, which is the logistic function.
The Signal Arrival Time is extracted by this fit at 20% of peak maximum, and then we subtract PICOSEC Value from the respective photocathode value.
After correcting for dynamical errors we can came up with a SAT distribution, which is fitted with a double Gaussian and its RMS defined the timing resolution, which for this data set is set to 18.3 ps
This procedure and the results we achieved will be our reference analysis, and with this we will compare our new algorithms for their validity and consistency.

## Slide 9: Correcting for Dynamical Errors
In principle, CFD method DOES NOT suffer from time walk effects
  However we observe dependence on signal amplitude
    Its origin has nothing to do with offline analysis procedure BUT
    Results from the microscopic behavior of the avalanche
      Photoelectrons drift with different velocities than the total avalanche
  Calibration curve
g
Notes: Talking about dynamical errors we mean that the dependence of SAT on the signal amplitude. But in principle the CFD technique does not suffer from time walk effects.
This dependence can be seen by splitting the data into bins of peak size(amplitude or charge), fitting each data set with Gaussian and then by shorting SAT values in rising values of the size.
On the left you can see the results for the data set we used, this small dependence has nothing to do with the offline analysis procedure, but instead it reveals the pulse formation dynamics, and the microscopic behavior of the avalanche, and the fact that the avalanche drifts with different velocity than its electrons individually. Even though we have reduced more the drift gap to create avalanches as early as possile, this is still a remaining effect. For this reason, we parametrize this dependence with a power law and correct for this. While on the other hand the constant thr thechnique truly suffers from time walk effects
And the effect is corrected on the offline analysis.

## Slide 10: Important Observables
J.Borteldt, et al. “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, Nuc. Instrum. Meth. A (2021)https://doi.org/10.1016/j.nima.2018.04.033
Data taking & Output
  Signal Arrival Time has a dependence on Electron peak charge
  Timing resolution improves with
    Higher drift field &
    Smaller gap(<50ps for 120μm for single pe)
L.Sohl-PhD Thesis “Development of a PICOSEC Micromegas for fast timing in high rate (archives-ouvertes.fr)
L.Sohl-PhD Thesis “Development of a PICOSEC Micromegas for fast timing in high rate (archives-ouvertes.fr)
Notes: Continuing the collaboration with IRAMIS laser Facility, the way of better understanding of the detector was open. Some detailed studies having the control of number of photoelectrons, resulted to very important statements of detector response.
And say which one are those…
Great achievement of those measurements was that we observed some important statements of the detector response.
The dependence of SAT with electron peak charge in different operation Voltages, The grater the drift voltage the smaller the SAT
In parallel it is evident that timing resolution improves with higher field and smaller gap reaching even a resolution of 50 ps for 120μm gap and

## Slide 11: Understanding the Timing
Simulation Studies Summary
Modeling the behavior:
  Phenomenological model describing the dynamical and statistical properties of the detector signal
SAT vs charge shape
  Independent of Drift Voltage/Field!
Large signals arrive earlier than smaller ones!
Resolution vs charge
  Independent of Drift Voltage/Field!
The purpose of the simulation was to simulate the observed effects
and investigate the mechanisms producing them
Notes: Physics
  Synchronous Cherenkov photons
  Synchronous Photoelectrons from the photocathode
  Photoelectron conversion(Townset Coeff)
  Preamplification Avalanche
  Transport through the mesh
  Amplification Avalanches

## Slide 12: Understanding the Timing
J.Borteldt, et al. “Modeling the timing characteristics of the PICOSEC Micromegas Detector”, Nuc. Instrum. Meth. A (2021) https://doi.org/10.1016/j.nima.2021.165049
  Modeling Aspects:
  SAT time walk seen in single pe data is explained:
    SAT reduces with avalanche length
    Long avalanches  big e-peak charge
    SAT reduces with e-peak charge
  SAT & Timing resolution are determined by:
    The drift path of the primary photoelectron
             number of photoelectrons in avalanche & its length
The purpose of the simulation was to simulate the observed effects
and investigate the mechanisms producing them
Simulation Studies using GARFIELD++
Notes: Physics
  Synchronous Cherenkov photons
  Synchronous Photoelectrons from the photocathode
  Photoelectron conversion(Townset Coeff)
  Preamplification Avalanche
  Transport through the mesh
  Amplification Avalanches

## Slide 13: Understanding the Timing
  Modeling Aspects:
  SAT time walk seen in single pe data is explained:
    SAT reduces with avalanche length
    Long avalanches  big e-peak charge
    SAT reduces with e-peak charge
  SAT & Timing resolution are determined by:
    The drift path of the primary photoelectron
             number of photoelectrons in avalanche & its length
The purpose of the simulation was to simulate the observed effects
and investigate the mechanisms producing them
Agreement between simulation & experimental data
Simulation Studies using GARFIELD++
Notes: Physics
  Synchronous Cherenkov photons
  Synchronous Photoelectrons from the photocathode
  Photoelectron conversion(Townset Coeff)
  Preamplification Avalanche
  Transport through the mesh
  Amplification Avalanches

## Slide 14: Feasibility Study for Online Timing

## Slide 15: Timing with Artificial Neural Networks
  Architecture:
    Feed Forward Neural Network
    One input layer
    Two hidden layers with 64 neurons each
    Output layer
    ReLU activation Function for all nodes
    Cost Function  Mean squared error
Timing resolution :
24.20.6 ps
  First Indication:
    Using particle beam data
    Check if we reproduce the same results as the offline analysis
    K-fold validation technique to Train and Test the ANN

## Slide 16: Timing with Artificial Neural Networks
  Architecture:
    Feed Forward Neural Network
    One input layer
    Two hidden layers with 64 neurons each
    Output layer
    ReLU activation Function for all nodes
    Cost Function  Mean squared error
  Use of the same Laser Beam Data:
    Need of a wide sample of data for the Training process
    Starting from the single photoelectron data set
    Train with emulated multi photoelectron pulses
    Test with the real multi photoelectron pulses
Take advantage of the Single Photoelectron data
that indicate small time walk dependence

## Slide 17: The Simulation Model
    EXP-Set contains ~7.8 photoelectrons
    Log-likelihood estimation method
    Convolution fit of
      Poissonian x Polya distribution using
= 7.8 pes
EXP-set data points
Convolution fit
  Creating Multi-photoelectron pulses:
    Multiplicity N of single p.e.
      According to a Poissonian with mean of 7.8
    N waveforms selected randomly among the SPE-set
    Each shifted in time to t-reference being zero
      Same clock for triggering and digitization
    3rd degree polynomial interpolation between digitization to estimate relative position
Ν = 5
Sum of N single pulses
Single pes waveforms

## Slide 18: The Simulation Model
Ν = 5
Sum of N single pulses
Single pes waveforms
Negative Effect
  Having the same digitization
  This process eliminates any time jitter that would occur naturally.
  Additional random digit shift ± 50ps (25 ps)
  Creating Multi-photoelectron pulses:
    Multiplicity N of single p.e.
      According to a Poissonian with mean of 7.8
    N waveforms selected randomly among the SPE-set
    Each shifted in time to t-reference being zero
    3rd degree polynomial interpolation between digitization to estimate relative position
Notes: Supposing that PICOSEC-MM (including the front-end electronics) is a
linear device, the detector response to N-photoelectrons should be emulated
by the sum of N single-pe waveforms. Then, for the simulation of waveforms
as those comprising the EXP-set, we implement the following algorithm:
A multipicity, N, of single-pe is chosen according to a Poissonian dis-
tribution with mean value equal to 7.8.
. N waveforms are selected randomly among the ones of the SPE-set.
. Each of the selected single-pe waveforms is shifted in time, in order the
respective reference time (dened by the reference photodiode) to be
at zero.
. A common set of time coordinates have been used for all single-pe
waveforms, where zero corresponds to the reference time.
. A local 3rd degree polynomial interpolation between digitization points
is used, on each single-pe signal, to estimate the relative position

## Slide 19: The Simulation Model II - Evaluation
  Challenges
    Limited number of SPE pulses
    Emulated pulses will share the same SPE waveforms
    Should share similar properties with the EXP-set
      Electron peak size
      Timing Resolution
Simulated pulses
EXP-set pulses
  Noise contribution
    Cumulative property
    Due to interpolation between digitization points
    Electron peak charge is more reliable parameter

## Slide 20: The Simulation Model II - Evaluation
  Timing Properties
    Offline Analysis
    Timing with CFD @ 20% of Peak Maximum
    Data with noise correspond to RMS of random noise
    Photodiode noise data correspond to the resolution of the device  due to synchronization
    Worse than the EXP-set resolution by 3ps
    Noise affects the resolution
Timing resolution :
21.30.6 ps
Simulated pulses
EXP-set pulses
EXP with noise
EXP with diode noise

## Slide 21: Feed the ANN
  Alternative Digitizers
    Red points represent the input layer (3.2 ns)
    Threshold trigger at 100mV
      Provide the timestamp
    The starting point simulates the behavior of the SAMPIC starting digitization ( 64ch/sample)
  Validation of ANN – Challenges
    Use only the EXP-set
    K-fold cross validation
    Increase the danger of bias
    Good first indication
Timing resolution :
18.50.6 ps

## Slide 22: Feed the ANN
  Validation of ANN – Solution
    Use Unknown events
      The Simulation Model Pulses
    Reduce further the probability of bias
      Generate the Simulation Model Pulses with a uniform distribution of Npes

## Slide 23: Results and Tests
Timing resolution :
18.50.6 ps
Simulated data EXP-Set data
Strong evidence that ANN works properly
Timing resolution :
21.30.5 ps
Timing resolution:
23.6 0.5 ps (offline)
24.7 0.6 ps (ANN)
Test with “Noisy” Data
Test with Simulated Data
Test with less digitization points
Prove that ANN is not a black box
Train the ANN with uniform number of photoelectrons
Test with real experimental data – aka. Exp-Set
50ps SP(20GS/s)
200ps SP(5GS/s)
Timing resolution:
19.1 0.5 ps

## Slide 24: Conclusions
PICOSEC detection concept overcomes timing limitations of gaseous detectors
We demonstrated the physical processes adapting on its operation
The development of signal processing algorithms explore the properties of the detector and offer the ability for online precise timing
An ANN for real timing signal processing, is able to provide precise timing and can be used for fast event selection
Main demand of adequate training samples → Simulation model
It was proven that the ANN learns a signal analysis procedure and it is consistent and unbiased
Notes: EvetyNo Robusteness
Gain can affect robustness and timing
Adjusted according to application demands

## Slide 25: The PICOSEC Micromegas Collaboration
AUTH (Greece) I. Angelis, K. Kordas, C. Lampoudis, I. Maniatis, I. Manthos, K. Paraschou, D. Sampsonidis, A. Tsiamis, S. E. Tzamarias
CEA-IRFU, LIST, LIDYL(France) S. Aune, D. Desforge, I. Giomataris, T. Gustavsson, A. Kallitsopoulou, M. Kebbiri, P. Legou, T. Papaevangelou, M. Pomorski, E. Scorsonne
CERN (Switzerland) J. Bortfeldt, F. Brunbauer, C. David, K.J. Floethner, M. Lupberger, M. Lisowska, H. Müller, E. Oliveri, G. Orlandini, F. Resnati, L. Ropelewski, L. Scharenberg, T. Schneider, M. van Stenis, R. Veenhof
HIP (Finland) F. Garcı́a
LIP (Portugal) M. Gallinaro
NCSR Demokritos, (Greece) G. Fanourakis
NTUA (Greece) Y. Tsipolitis
Stony Brook University (USA) P. Garg
Jefferson Lab (USA) K. Gnanvo
USTC (Hefei, China) J. Liu, B. Qi, X. Wang, Z. Zhang, Y. Zhou
University of Zagreb(Croatia) M. Kovacic, A. Utrobicic
University of Pavia (Italy) D. Fiorina
Univeristy of Virginia (USA) S. White
12 institutes from 9 countries
46 collaborators

## Slide 26
A relevant series of publication (and contribution to conferences)
Notes: Giving a relevant series of publications and contribution to conferences…

## Slide 27: In the end, it’s all a matter of timing…

## Slide 28: Thank you for your attention
CEA SACLAY
91191 Gif-sur-Yvette Cedex
France
alexandra.kallitsopoulou@cea.fr
thomas.papaevangelou@cea.fr

## Slide 29: BackUp Slides

## Slide 30: Detailed simulation
http://ikee.lib.auth.gr/record/297707
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 31: Detailed simulation
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 32: Detailed simulation
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 33: Detailed simulation
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 34: Phenomenological model: A deeper looking under the hood
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 35
https://indico.ph.liv.ac.uk/event/266/attachments/799/1097/Liverpool_picosec_seminar.pdf

## Slide 36: Finding the Number of Photoelectrons – Deconvolution Algorithm
Assuming that the number of photons (n) in the Cherenkov radiator follows a Poisson Distribution :
Each of these photons has either the probability to interact in the photocathode or to escape :
The probability to observe k photoelectrons is the convolution of the Poisson and Binomial resulting to a new Poissonian
Every single photoelectron is distributed via Polya distribution, thus the multi-photoelectron charge distribution should be fitted with the convolution of Poissonian and N-Polya
Using Log-Likelihood estimation for the number of photoelectrons we conclude to the desired value of 7.8 p.e.
https://iopscience.iop.org/article/10.1088/1742-6596/1498/1/012014/meta

## Slide 37: The Simulation Model II
Limited number of single pulses
  The Simulated pulses share the same Spe waveforms
  Should follow the same behavior as the Exp-set
  Reproduce and compare the distributions of electron peak size
RMS single pes = 0.0046
RMS SM pulses = 0.013
Simulated pulses
EXP-set pulses
Noise Contribution
  Noise has the cumulative property
  Affect the determination of Epeak max
  Add a limitation to our model
Notes: Having the model developed we have now to test if it carries the same properties as the EXP-set.
First we compare the e peak charge and amplitude distributions, and we see that the peak charge in h better agreement between the two sets, so we will use this parameter for our parametrizations.

## Slide 38: Investigating the Extra timing Error
Simulated pulses
EXP-set pulses
EXP with noise
EXP with phd noise
Noise is added as a function of the number of photoelectrons
  Which defines the SIZE of the waveform
Number of photoelectrons as a function of electron peak SIZE
  Fit with a 4th degree polynomial
On an event-by-event basis
  Corresponding noise is:
Data with noise corresponds to RMS of random noise
Data with random noise and error of reference device resolution
  We are sensitive due to synchronization process

## Slide 39
Particle Beams @ CERN SPS H4 Beamline
  Muons (80-150GeV)
    8cm diameter of beam
    muons/spill (measured rate ~kHz/)
The Setup
  Use GEMs for tracking
  Use MCP PMTs as timing reference devices and for triggering
  Detectors Under Test
  Electronics: Commercial/Custom-made preamplifiers
  Digitizers – Lecroy scopes
Detector Testing - Particle beams
J.Borteldt, et al. “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, Nuc. Instrum. Meth. A (2021)https://doi.org/10.1016/j.nima.2018.04.033
11 p.e.
Timing Resolution  RMS of Signal Arrival Time Distribution
First timing measurement @ Particle Beam ( 2017 )
  Single Prototype : Thin Gap (200μm) with MgF2 & CsI photocathode
Notes: Although all the important information about the optimization of the detector can be very well understood from a laser test, through the years the better understanding was coming by also supplementary measurements in particle beams, which is a more realistic case for the detector operation