## Slide 1
Presenter Name
Date
Journées 2024 de l'atelier détecteurs gazeux
Signal induction in particle detectors containing resistive elements
Djunes Janssens
djunes.janssens@cern.ch
March 22nd, 2024

## Slide 2: Introduction
An (incomplete) list of resistive detectors:
Multi-gap Resistive Plate Chambers (MRPC)
Surface Resistive Plate Counter (sRPC)
MicroCAT’s two-dimensional interpolating readout
μ-Resistive WELL
μ-Resistive plate WELL
Small-pad resistive Micromegas
Resistive Micromegas
Resistive PICOSEC Micromegas
Un-depleted-silicon sensors
Resistive silicon detectors
4D Diamond sensor
The use of resistive technologies in experiments makes it necessary to understand and characterize their response for the design and optimization of the next generation of particle detectors and their application.
Image taken from G. Bencivenni et al., Nucl. Instrum. Meth. A 958 (2020) 162050.
  Example: Fast grounding μ-Resistive-WELL
RPC
MPGD
Solid-state

## Slide 3
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
Ph.D. thesis: https://cds.cern.ch/record/2890572
Introduction
  Outline:
  Ramo-Shockley theorem
  Ramo-Shockley theorem extension for conductive media
  Signals in the presence of a thin resistive layer
  Numerical approach
  Resistive strip MicroMegas
  Other applications
  Summary
We use Garfield++ and a finite element method to numerically calculate the signal formation in detectors with resistive elements by applying an extended form of the Ramo-Shockley theorem.

## Slide 4: Ramo-Shockley theorem

## Slide 5
  The Ramo-Shockley theorem allows the current on any electrode induced by an externally impressed charge density to be calculated using a so-called weighting potential .
4
S. Ramo, PROC. IRE 27, 584 (1939).
W. Shockley, Journal of Applied Physics. 9 (10): 635 (1938).
This static can be calculated using the following step:
Remove the drifting charges
Put the electrode at potential Vw
Grounding all other electrodes
Ramo-Shockley theorem

## Slide 6
Ramo-Shockley theorem
Endpoint of the electrodes on the readout
Induced signal on the strip electrodes
electron
ion
  Using this framework, the induced current sourced by a point charge q can be calculated in a single using the calculated the weighting potential of the electrode.
  GEM
Garfield++ simulation of GEM amplification
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
, where

## Slide 7: Ramo-Shockley theorem extension for conductive media

## Slide 8: Resistive materials
  The materials inside the detector can have a finite conductivity , e.g,. in Resistive Plate Chambers, un-depleted silicon sensors, and resistive strip bulk Micromegas.
  The (nonuniform) conductivity, reciprocal with the volume resistivity, establishes the connection between the local electric field and the local current density.

## Slide 9: Ramo-Shockley theorem extension for conducting media
E. Gatti, G. Padovini and V. Radeka, Nuclear Instruments and Methods in Physics Research 193 (1982) 651.
W. Riegler, Nucl. Instrum. Meth. A 535 (2004), 287-293.
W. Riegler, Signals in Particle Detectors, CERN’s Academic Training Lecture (2019)
Simplify calculations using dynamic :
Solving Maxwell’s equations:
  For detectors with resistive elements, the time dependence of the signals is not solely given by the movement of the charges in the drift medium but also by the time-dependent reaction of the resistive materials.

## Slide 10: Ramo-Shockley theorem extension for conducting media
  The time-dependent weighting potential is comprised of a static prompt and a dynamic delayed component:
V
Direct induction
Reaction from resistive material
The current induced by a point charge q is given by:
where .
V

## Slide 11: Delayed component of the signal
  A charge q moves at a constant velocity through the gas gap before reaching the bulk resistive layer that separates it from the anode.
The dynamics is governed by the time constant:
Here we took .

## Slide 12: Delayed component of the signal
  A charge q moves at a constant velocity through the gas gap before reaching the bulk resistive layer that separates it from the anode.
The dynamics is governed by the time constant:
Here we took .
RPC regime
Only prompt!

## Slide 13: Resistive plane MicroMegas

## Slide 14
  Given a parallel-plate type geometry with a grounded resistive layer separated from the pad electrodes by an insulating layer.
d3
ε1
wx
d1
ε2
Q
a
b
Q
wx
wy
(x0, y0)
  The induced charge on each pad can be analytically calculated to study the effect of the size of the resistive layer:
  with the infinite number of time constants given by
Time-dependent part
Charge diffusion in a thin resistive layer

## Slide 15: Charge diffusion in a thin resistive layer
  The size of the resistive layer does play a role in the evolution of the signal. For the initial part of the induced current for a large-area resistive detector can be approximated by a smaller counterpart.
Q
0.5 mm
a
a
Here we took R = 1 MΩ/□.

## Slide 16: Charge diffusion in a thin resistive layer
full solution
QTel
  The full solution of a charge diffusing in an infinite extending resistive layer can be understood in terms of an Rc time constant as it reduces to the solution to the Telegraph equation for late times (t>Rc).
Here we took R = 1 MΩ/□ and wx = 200 μm.

## Slide 17: Signal ‘spreading’ in a thin resistive layer
  Unipolar shaper
As an example of a unipolar shaper, we took the APV25 with parameters taken from this link
Let's examine a Townsend avalanche occurring within the amplification gap of a Micromegas detector, resulting in a signal being generated on the readout strips.

## Slide 18: Numerical approach

## Slide 19: Numerical approach
  Using a finite element method approach, the weighting potential is calculated numerically.
Image taken from S. Hassani RD51 Mini-Week slides.
D. Janssens et al., Nucl. Instrum. Meth. A 1040 (2022)
D. Janssens et al, JINST 18 (2023) 08, C08010
Accurately represent the boundary conditions by coordinate mapping of the model to the full active area.
The contribution of external impedance elements is included by incorporating it on the level of the weighting potential.
COMSOL Multiphysics: https://www.comsol.ch

## Slide 20
Resistive strip MicroMegas
  The resistive strips in the geometry of this MicroMegas facilitate the sharing of the signal over many neighboring readout strips strips running orthogonal to them.
resistive strips
pillar
T. Alexopoulos, et al., Nucl. Instrum. Meth. A 640 (2011) 110.
M. Byszewski and J. Wotschack, JINST 7 C02060 (2011).

## Slide 21
Resistive strip MicroMegas
  To calculate the dynamic weighting potential, a voltage ramp is placed on the readout strip under investigation.
D. Janssens et al, JINST 18 (2023) 08, C08010.
  Calculated dynamic weighting potential

## Slide 22
Resistive strip MicroMegas
  APV25
  Leading strip (5)
  Next-to-leading strip (6)
  After having calculated the signals induced on the strip electrodes, the electronics with which the detector is read out needs to be considered.
For a result on the ion tail length: D. Janssens,”Ion mobility in a MicroMegas detector: a puzzle between measurement and simulation”, RD51 Collaboration Meeting.

## Slide 23
Resistive strip MicroMegas
-
-
For the comparison we look at the average induced current response of neighboring strips. This averaging is performed over muon events positioned between the leading and the next-to-leading strip.

## Slide 24: Applications
(Multi-gap) Resistive Plate Chamber (MRPC)
Small-pad resistive MicroMegas
Resistive strip bulk MicroMegas
Resistive PICOSEC MicroMegas
MicroCAT resistive interpolating readout
3D Diamond Detector
Resistive Silicon Detector (RSD)
  During the doctoral project we have applied this numerical methodology to a wide range of detector geometries ranging from gas-based detectors to solid-state sensors.
MicroCAT resistive interpolating readout
  Correction map
  Map of non-uniform resistivity

## Slide 25: Summary
  With resistive materials becoming increasingly more common in particle detector designs, it was therefore prudent to keep the capabilities of simulation tools such as Garfield++ aligned with this technological advancement.
  We discussed the numerical approach used for applying the extended form of the Ramo-Shockley theorem to the calculation of induced signals in resistive particle detectors.
  The numerical approach was benchmarked using resistive strip MicroMegas detectors with 2D strip readouts.
  This methodology can be applied to a wide range of resistive (large active area) detector structures within the families of gas detectors, MPGDs, and solid-state sensors, which can improve our understanding of their response and optimize them for specific applications.
  Merci de votre attention!

## Slide 26: Backup slides

## Slide 27: Charge between two conductive half-spaces in the quasi-static limit
  The solution of the potential is given by
  where the charge seemingly ‘decays’ with a time constant
  The total charge that flows though two half domes in the top and bottom half-space is
  which come from currents flowing in the media to compensate the charge
  When positioning a charge q at t = 0 at the interface of two half-space conductive media, the environment will ‘react’.

## Slide 28: Resistive particle detectors
  Resistive structures affect the performance of the detector:
  Discharge protection by offering an increased impedance to ground
  Signal formation is altered in the presence of a resistive material which can be used to increase the detector’s accuracy
  Rate-capability limitation of the detector due to an Ohmic voltage drop across the resistive material
  Introduces thermal noise into the system
Video taken from: A. Utrobicic’s presentation at the 6th MPGD conference (2019).
Plots taken from: T. Alexopoulos, et al., Nucl. Instrum. Meth. A 640 (2011) 110.

## Slide 29
Resistive strip MicroMegas: measurement
  During the RD51 test beam campaigns at the CERN SPS H4 beamline we measured the induced signal in two different resistive strip bulk MicroMegas detectors. These were placed in a tracking telescope and read out using APV25 ASICs.

## Slide 30: Noise in detectors containing resistive elements
What about the noise in structures with distributed passive materials? The self-impedance Z(ω) of the terminal will contribute to its noise power spectrum.
H. Nyquist, Physical Review 32 (1928) 110.168
J.B. Johnson, Physical Review 32 (1928) 97.169
D. Janssens and W. Riegler, submitted to Nucl. Instrum. Meth. A, NIMA-D-23-01244.
Simulated ENC for a pad electrode in a resistive MM

## Slide 31: MicroCAT resistive position interpolation readout
  The MicroCAT’s two-dimensional interpolating readout structure allows for a reduced number of electronic readout channels without loss of spatial resolution.
F. Bartol et al. J. Phys. III France, 6 (1996), p. 337
A. Sarvestani et al., Nucl. Instrum. Meth. A 410 (1998) 238–258
D. Janssens et al., Nucl. Instrum. Meth. A 1040 (2022)

## Slide 32
MicroCAT resistive position interpolation readout
  During production, the resistivity can fluctuate on the surface of the resistive layer. This could make the timing response or reconstruction capability of your detector non-uniform over the active area.
R. Arcidiacono et al., arXiv:2211.13809v1 [physics.ins-det]
  Correction map
  Map of non-uniform resistivity

## Slide 33: Signal in a non-resistive Micromegas
  Let us consider a Townsend avalanche inside the amplification gap of a Micromegas detector that induces a signal on the anode plane.
V

## Slide 34: Electron/ion pair on a resistive layer
  The convolution of the weighting vector H over the trajectory of the charged particle is performed in Garfield++.
As a benchmark we can take an ion traversing the gas gap at a constant velocity v = g/T above an infinitely extending resistive layer.
D. Janssens et al., Nucl. Instrum. Meth. A 1040 (2022)
The analytical solution can be found in W. Riegler, JINST 11 (2016) 11, P11002

## Slide 35: Capacitive-coupling between electrodes
  The cross-talk between the bottom of the GEM foil and readout needed to be considered in the LHC experiments for various instances.
ALICE TPC
Slide borrowed from R. Münzer’s Detector Seminar
Slide borrowed from J.A. Merlin’s contribution to the RD51 Coll. Meetings.
CMS GEM
See also the LHCb blocking capacitor of the GEM muon system

## Slide 36: Impedance between terminals
  When working with resistive materials, the voltages and currents between the terminals are related through the admittance matrix.
  Given external impedance elements connected to our terminals, we can view them ‘as part of the detector medium’.
*
The dynamic can be calculated for a connected electrode using the following steps:
Remove the drifting charges
Connect the external circuit to the terminals
Put a potential Vw at time t = 0 on at the point where you want to know the signal
Gatti E., Padovini G., Radeka V., Nucl. Instrum. Methods, 193 (1982), pp. 651-653
*

## Slide 37: Impedance between terminals
An RPC-type geometry is one of the few resistive geometries that can be represented by a discrete electrical circuit. We can calculate the cross-coupling when attaching external impedances.
R2
R1

## Slide 38: Impedance between terminals
Alternatively, we can view the external impedance elements as a part of the detector medium and absorb them into the weighting potential.
This will show up as a time-dependent contribution on top of the one already provided from the resistive layer.
COMSOL’s electrical circuit interface: link
R1
R2
Vwϴ(t)

## Slide 39: Charge diffusion on a thin resistive layer
  Comparison of the induced signal on neighboring channels between the full solution and the one form the Telegraph equation.
Cathode
ε1
Pads
Resistive layer
wx
ε2
Q
Full solution
QTel only with c to the anode
QTel

## Slide 40
Transmission line model
  We can derive an analytical expression for the current flowing from an electrode capacitively coupled to ground, which is capacitively coupled to a transmission line on which a charge q is injected at t = 0.
  Here we have made some assumptions: Rs ≪ Cs, no transconductance (G = 0), and inductance (L = 0).
  A numerical approach of this problem can be found in J. Galán, JINST 7 (2012) C04009.
x0 = 0.6 l
  Time constant:

## Slide 41: Resistive PICOSEC MicroMegas
Considering the position of the plateau where the leading edge of the signal is minimally affected by the delayed component, the rate capability estimation, and the protection against discharges, a surface resistivity of 20 MΩ/□ was chosen, and the prototype was produced.
Simulated amplification drop from pion beam
Simulated voltage drop across the resistive layer
mimimum for timing
mimimum for protection
rate capability

## Slide 42: Resistive PICOSEC MicroMegas
Measurement of timing resolution
After production, the timing performance of the resistive multi-pad detector on the pad level was measured to be below 25 ps for Minimum Ionizing Particles.
MCP-PMT
timing reference
PICOSEC MM
µ
Signal waveform