## Slide 1: Detecting gravitational waves from space
An introduction to LISA Instrument
Dr. Henri Inchauspé Institute for Theoretical Physics, KU Leuven LISA School 2025, Les Houches
Flash me to get some more course material !

## Slide 2
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy
The novel ASTRONOMY of the gravitational Universe
Flash me to get some more course material !

## Slide 3: LISA to observe the GW Universe !
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy
LISA is a gravitational waves detector in space
LISA is a spaced-based gravitational waves astrophysical observatory

## Slide 4: GW170817
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy
https://en.wikipedia.org/wiki/GW170817#cite_note-55
Hubble picture of the identified host galaxy NGC4993 () with inset showing GRB170817A over 6 days. Credit: NASA and ESA
The GW170817 signal as measured by the LIGO and Virgo gravitational wave detectors. Signal is invisible in the Virgo data. Achieved localization within .
Artist's impression of strontium emerging from a neutron star merger. https://www.eso.org/public/news/eso1917/
First direct evidence that BNS mergers significantly contribute to heavy atoms nucleosynthesis
Short Gamma Ray Burst identification
Stringent constraints on scalar-tensor theories of Gravity.
First successful EM follow-up of GW event by Fermi-GBM and Integral
https://gwosc.org/audio/

## Slide 5: Multi-Wave length (EM) astronomy
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy
A single Universe, but a multitude of perspective, across the EM spectrum.
And now with gravitational waves.

## Slide 6: Multi-band Gravitational Waves Astronomy
And the GW astronomy of the millihertz
Similar picture for GW astronomy: different band, unique perspective on the Universe.
The lower, the heavier: Astro systems scale grows as frequency decreases.
Probing physics at early time and high energy far from reach by other means.
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy

## Slide 7: LISA and the GW astronomy of the millihertz
Space-based observation open up the millihertz band.
Very rich and diverse:
Supermassive Black Holes Binaries mergers (SMBHBs)
Extreme-Mass Ratio Inspirals (EMRIs)
Galactic Binaries (White Dwarves). Stellar mass black holes coalescence. (Continuous)
Stochastic Backgrounds (Astro, Cosmo)
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Astronomy

## Slide 8
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
LISA: Europe largest science space MISSION ever
Flash me to get some more course material !

## Slide 9: The space-based observatory LISA
Largest laser interferometer never built
Millihertz band imposes to go to space:
    To deploy solar system scale arm length.
    To get free from terrestrial noise ( seismic, acoustic, Newtonian noise)
Detection principle:
Oscillatory deformation of collection of free-falling observes.
Laser interferometry, with unequal and time-varying arms : TDI
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Animation: Ricardo Waibel (ITP, Heidelberg University)
Orbits: H. Halloin (APC, UPCité)
Milky Way map: JPL, NASA
Notes: Longueur de bras déployée =
Pas de perturbations terrestres

## Slide 10
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
First challenge: Free-falling, inertial test masses

## Slide 11: LISA Pathfinder, paving the way to GW detection in space
Constructing references of inertia in space
Main goal: Measuring residual differential acceleration between two « free-floating » test masses. = Measurement of quality of free-fall for the test-masses. (Test mass 1 free-fall, test-mass 2 suspended)
Understanding physical origins of the residual noise.
Two main novelties / breakthroughs:
  sub-picometer metrology in space: laser interferometry
  test-mass wireless discharging (UV lamp via photoelectric effect)
At low frequency: 3 orders of magnitude gain in sensitivity.
Various experiments: enhancing / stimulating a specific coupling and probing impact on the start acceleration.
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 12: Acceleration noise: physical origin
Brownian noise
Actuation noise + Mystery noise (low frequency)
OMS sensing noise (high frequency)
Spectral representation of differential acceleration noise of LISA Pathfinder test masses and post-processing removal of residual coupling components with the satellite.
April 2016
February 2017
April 2016

## Slide 13
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Second challenge: A 2.5 million of km arm length interferometer

## Slide 14: Long-range laser interferometry
2.5 million of km ranging with… picometer precision !!!
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Mirror-to-mirror measurement performed in 3 steps:
Local test-mass to local satellite.
Local satellite to distant satellite.
Distant satellite to distant test-mass.
LISA: now the test masses are on-board different SC, and 2.5 million of km apart.
Large arm = large effective deformation + larger wavelength.
Laser power emitted 1W, received pW. Cannot been reflected back —> transponder scheme
Arm-length defined by orbits: unequal and time-varying.
Laser frequency noise 8 orders of magnitude above target GW strain !

## Slide 15: Time-Delay Interferometry (TDI)
Laser frequency noise largely dominates the single link measurements.
Classical Michelson scheme: one single primary laser split across nearly equal optical path: at recombination, the noise is coherent and cancels out !
Impossible with LISA. Needs to compose our interferences in post-processing:
6 Inter-Spacecraft Interferometers (ISI): beatnotes frequency time-series are measured and down-streamed.
6 Test-Mass Interferometers (TMI) to measure the S/C noisy motion w.r.t. local inertial reference frames.
They are delayed and linearly combined to make the laser noise coherently added and suppressed.
This is Time-Delay Interferometry (TDI).
LISA mission
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 16
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
LISA response model to GW

## Slide 17
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
From van der Steen et al. 2025

## Slide 18
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
From van der Steen et al. 2025
Single-link response
LISA GW Response (Python code, Bayle et al.)

## Slide 19
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
From van der Steen et al. 2025
Photon geodesic equations
1. Zeroth order:
2. Linear order:

## Slide 20: GW in TT gauge
Small oscillatory perturbation of spacetime metric propagating across space.
Propagates two degrees of freedom.
In TT gauge (coordinate systems), the dynamical, non-zero components are contained in the spatial part of the metric, and orthogonal to the propagation axis (transverse wave).
Far from the source: plane waves
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 21: Plane wave solutions
Wave traverse: space deformation occurring on plane orthogonal to k, and decomposable into polarization basis:
All points of plane orthogonal to the propagation vector k have same amplitudes and phase at time t:
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 22: Plane wave solutions
Wave traverse: space deformation occurring on plane orthogonal to k, and decomposable into polarization basis:
All points of plane orthogonal to the propagation vector k have same amplitudes and phase at time t:
LISA response
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 23
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Beatnotes and interferences
Flash me to get some more course material !

## Slide 24: Heterodyne interferometry
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 25: Heterodyne interferometry
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 26: Heterodyne interferometry
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 27: Heterodyne interferometry
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 28: Heterodyne interferometry + GW
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 29: Heterodyne interferometry + GW
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 30: Heterodyne interferometry + GW
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 31: Heterodyne interferometry + GW
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 32: Heterodyne interferometry + GW + White Noise
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 33: Heterodyne interferometry + GW + White Noise
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 34: Heterodyne interferometry + GW + White Noise
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 35: Heterodyne interferometry + GW + White Noise
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 36: Doppler shift and frequency plan
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
LISA constellation flexing yearly.
Relative velocity between SC along line of sight
DC / out-of-band Doppler shift of laser beams to account for.
Frequency plan to keep a stable beat note frequency range.

## Slide 37
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Working around laser noise
Flash me to get some more course material !

## Slide 38: Time-Delay Interferometry
Suppressing primary noises
LISA detection
Laser frequency noise: fluctuations about 8 orders of magnitude above GW strain typical amplitude.
Direct Michelson interferometry impossible: arm length asymmetric and variations driven by spacecraft orbits.
Strategy: measure beat-note frequencies real-time across the constellation, and synchronize / build interferences on-ground !
Key post-processing: Time-Delay Interferometry (TDI)
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 39: Time-Delay Interferometry
Second Generation TDI
LISA detection
First generation TDI 1.5.
Suppresses laser noise exactly for unequal, static arm-length:
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 40: Time-Delay Interferometry
Second Generation TDI
LISA detection
Second generation TDI 2.0
16 links combination.
Second round-trip reverse of both beams to « accumulate » time-varying delays symmetrically.
First order correction to time-varying arm-lengths.
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 41
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
The quieter place in the solar system
Flash me to get some more course material !

## Slide 42: From LISA Pathfinder to LISA
Locking S/C trajectory on quiet test masses
LISA detection
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
  … since the S/C motion is locked on the super quiet test masses.
  At low frequency, the S/C as quiet as the test masses. > 1 ton spacecraft stable at level essentially when control gain is stiff.
  S/C and test mass control: 15 DOFs to bring to target point, stabilize and optimize the jitter.
  Target points:
  Attitude control: MOSA pointing distant MOSAs (telescope and S/C rotation)
  Drag-Free control: S/C thrusts to follow a virtual average test masses.
  Suspension control: differential TM motion corrected with electrostatic forces

## Slide 43
x1, x2 ==> Inteferometer (IFO) ~pm.Hz-1/2
y1, y2, z1, z2 ==> Capacitive sensing (GRS)
~nm.Hz-1/2
Incidence angle of long-range beam ==> S/C attitude measurement Differential Wavefront Sensing (DWS)
< nrad.Hz-1/2
TMs actuated via capacitive (electrostatic) system
ONLY when unavoidable
and NOT along x1 or x2 axes
S/C actuated via micro-propulsion (and locked on TMs = Drag-Free)

## Slide 44: Acceleration noise: noise budget for LISA
Main goal: Measuring residual differential acceleration between two « free-floating » test masses. = Measurement of quality of free-fall for the test-masses. (Test mass 1 free-fall, test-mass 2 suspended)
Understanding physical origins of the residual noise.
Two novelties / breakthroughs:
  sub-picometer metrology in space: laser interferometry
  test-mass wireless discharging (UV lamp via photoelectric effect)
At low frequency: 3 orders of magnitude gain in sensitivity.
Various experiments: enhancing / stimulating a specific coupling and probing impact on the start acceleration.
Back slides
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Same models and parameters are scaled to LISA to build the noise budget.
Spectral representation of differential acceleration noise of LISA Pathfinder test masses and post-processing removal of residual coupling components with the satellite.

## Slide 45
Back slides
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches

## Slide 46: Example: chirp signal from BH mergers
Back slides
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
Late inspiral
Merger
Ringdown

## Slide 47: Three steps optical measurement
Back slides
Dr. Henri Inchauspé, Institute for Theoretical Physics, KU Leuven - LISA School 2025, Les Houches
LISA: indirect differential measurement from mirror to mirror:
  TMI 21: tracking spacecraft SC1 motion w.r.t. local ( inertial) masses TM21 along line of sight.
  ISI 21 and (ISI 12): tracking SC1 to SC2 optical path variation (including relative motion, but also GW)
  TMI 12: tracking spacecraft SC2 motion w.r.t. local ( inertial) masses TM12 along line of sight.
  Combining everything within TDI to suppress out the S/C noisy motion.
(ISI: Inter Spacecraft Interferometer TMI: Test Mass Interferometer)