## Slide 1: Monitoring & POWER SUPPLIES

## Slide 2: MONITORING & interlock
TNTC
x8
Press
x2
T / Hum
SHT85
ADC
x8
ATOM Lite 1
FPGA
ATOM Lite 2
ADC
x2
I2C
Interlock
Power Supplies
I2C
I2C
Monitoring_board
Vidor_board
ALARM HARD (to FPGA)
INTERLOCK SIGNAL (if several successive ALARM HARD)
ALARM SOFT (to DCS)
CAEN_IT_board
DCS

## Slide 3: Vidor board
Inputs signals :
  ALARM_T from 8 Temperature channels
  ALARM_H from 1 Humidity channel
  ALARM_P from 2 Pressure channel
  Logic Level 1=OK 0=nOK
Outputs signals :
  IT30 to switch OFF the LP Supplies channels 3 to 0
  IT47 to switch OFF the LP Supplies channels 7 to 4
Flexible point-to-point routing (red wires)

## Slide 4: Populated PCB
ALARM_H
ALARM_T
ALARM_P
Power connectors
IT_30
IT_74
1 = OK = led on
Pull-Down
Pull-up
Led power on

## Slide 5: Simulation
It is difficult to read anything about this simulation but the principle is as follows: in order to avoid an unwanted INTERLOCK, one of the ALARMS must be at 0 for at least 9 ms for it to be triggered.
An ALARM is on going.
INTERLOCK remains ON (ALARM too short)
INTERLOCK goes down (ALARM too long)